## Slide 1: Obstetrical forceps
Dr Asma Hassan

## Slide 2: History
In use for three centuries
Enormous changes and evolutions

## Slide 3: Types
Wrigley's
Simpson's
kielland

## Slide 4: Wrigley's forceps
Short in length
Suitable for the delivery of head
Often called as outlet forceps
Most frequently used

## Slide 7: Simpson’s forceps
Same basic structure except it is longer in length
Used to deliver head in OA position
When head is slightly at higher place at level of ischial spine
Also known as mid cavitory forceps
Can cause significant trauma as internal rotation not yet happened at this level

## Slide 8: Simpson’s Contd.
Should be used with caution by experienced obstetrician
At many occasion vacuum extractor or even c section is is preferred

## Slide 10: Kielland’s forceps
Rotational forceps
In use since 1916
Used to assist rotation from OP to OL position
may cause maternal and fetal trauma

## Slide 11: Architecture (Wrigley's and Simpson's)
Blade
Shank
Lock
Handle

## Slide 12: A. Blade
To grip baby head
Average length is 16 cm
Further divide into parts
Fenestra, fetal curve, pelvic curve

## Slide 13: 1. Fenestra
Opening in its main body
Facilitates the application of blades with compression
Makes blade lighter

## Slide 14: 2.Cephalic or fetal curve
Inward curve
Made to hold the fetal head
Radius of 11.25 cm
When the two blades are put together the distance between the tips is 3cm
Widest distance is 9cm smaller measurement cause trauma larger ones cause slipping of head

## Slide 15: 3.Pelvic curve
Upward curve in blades
Radius of 17.5 cm
To adapt the shape of birth canal
Improves the relationship of blade to fetal skull

## Slide 16: B. The shank
Area between the blade and the lock
Shorter are in case of Wrigley's as compared to Simpson's
In Simpson’s, usually 6.5 cm
Should be at least one finger in order to exert traction

## Slide 17: C.The lock
When the lock is in place then the left blade rests lower than right one

## Slide 18: D. The handle
Wrigley’s has short and smooth handle
Simpson has large with finger grip
Smooth handle is preferred because it discourages undue compressions and excessive traction

## Slide 19: The end