## Slide 1
Data Processing
and Control
Chapter 14
© 2008 Pearson Education
Notes: <number>

## Slide 2
Digital Electronics-II; M Sc IV (Phy-21406) & BS VIII (Phy-01806)
Read the following from the textbook (digital fundamentals by T L Floyd 11th edition)
14–1 The Computer System
14–2 Practical Computer System Considerations
14–3 The Processor: Basic Operation
14–4 The Processor: Addressing Modes
14–5 The Processor: Special Operations
14–6 Operating Systems and Hardware
14–7 Programming
This will complete this chapter.
Prof. Dr. Aftab Ahmad

## Slide 3
Summary
Computer Block Diagram
The central processing unit (CPU) controls the operations by issuing a fetch to memory for an instruction, then executes it.
Memory stores instructions and data until needed by the CPU.
The ports are the I/O connections to the peripherals.
The buses are groups of conductors with a common purpose.
Peripherals are devices for inputting or outputting information.
Notes: <number>

## Slide 4
Summary
Software
Software is all of the instructions that determine what operations are performed.
System software is the operating system of the computer and acts as the system manager.
Application software includes the various programs used to accomplish a task.
The BIOS is a portion of the operating system called “firmware” because it is a permanent part of the system software in ROM (read-only memory).
Notes: <number>

## Slide 5
Summary
Microprocessors
Four blocks are common to all microprocessors. These are:
ALU
  Performs arithmetic and logic operations
Instruction decoder
  Translates the programming instruction into an address where microcode resides for executing the instruction
Register array
  A group of temporary storage locations within the processor, each with special features
Control unit
  Synchronizes the processing of instructions
Arithmetic logic unit (ALU)
Instruction decoder
Register array
Control unit
Microprocessor
Notes: <number>

## Slide 6
Summary
Microprocessor Buses
Three buses for microprocessors allow data, addresses and instructions to be moved.
The address bus is used by the microprocessor to specify a location in memory or external device. Some processors have 64 address lines and can access 1.8 x 1019 locations.
The data bus transfers data and instruction codes to and from memory and I/O ports.
The control bus coordinates operations and communicates with external devices.
Notes: <number>

## Slide 7
Summary
Microprocessor Programming
Microprocessors work with an instruction set that allows it to function. Although the instruction set within the processor is binary, programmers work with English-like commands, which are divided into seven groups. These are:
Data transfer
Arithmetic and logic
Bit manipulation
Loops and jumps
Strings
Subroutines and interrupts
Control
Notes: <number>

## Slide 8
Summary
Multicore Processors
The Intel microprocessors up through the Pentium were all single core processors, meaning they had only one microprocessor in an IC.
Many newer processors have more than one core on a single IC. Multicore processors can execute more than one instruction at a time. This process is also called multiprocessing.
System bus
Processor core
Processor core
Cache
Cache
two processors work on an image at the same time to adjust the contrast. The work is sectioned so that each processor works on only one part.
Example
An example of multiprocessing is when
Notes: <number>

## Slide 9
Summary
Multitasking
Multitasking is a technique that allows a computer to perform more than one task. Unlike multiprocessing, the work only appears to be simultaneous because of the speed of the processor.
One type of multitasking parcels time slices on the processor for each program – this is called preemptive multitasking. Another type of multitasking is done when the program controls the processor – this is called cooperative multitasking.
Multithreading is a variation on multitasking, where different parts of the same program are executed simultaneously.
Notes: <number>

## Slide 10
Summary
Operations
Microprocessors execute programs by repeatedly cycling through three basic steps:
Execution unit
EU
Executes instructions
Bus interface unit
BIU
Fetches instructions
Reads operands
Writes results
System buses
8086/8088 Microprocessor
Fetch
Decode
Execute
The processor has two internal units, the EU and the BIU, as shown in the figure:
Notes: <number>

## Slide 11
Summary
Operations
While the EU is executing instructions, the BIU is fetching the next instruction from memory, and storing the next instruction in a high speed memory called the cache.
Execution unit
EU
Executes instructions
Bus interface unit
BIU
Fetches instructions
Reads operands
Writes results
System buses
8086/8088 Microprocessor
In the Pentium processors, two execution units (EUs) allow instructions that are independent of each other to execute at the same time.
The following slide shows the architecture of the 8088 processor …
Notes: <number>

## Slide 12
Summary
Notes: <number>

## Slide 13
Summary
Addressing
Intel chose a innovative way of generating 20-bit physical addresses in the 8088 and subsequent processors.
The physical address is formed by combining a 16-bit address in a segment register with a 16-bit address in a general register. The addresses “overlap” as shown, with an implied 00002 on the right side of the segment register (shown in blue).
16-bit segment base address
16-bit offset address
20-bit physical address
Segment register
General register
Notes: <number>

## Slide 14
Summary
Addressing
Segment/offset addressing allows 64k blocks of code to be relocated in memory by changing only the segment address.
Example
Assume IP = 20A016 and CS=B20016.
What is the location of the start and end of the block?
What physical address is formed?
Solution
The addressing is diagramed:
Contents of CS
implied
Contents of IP
a) The start of the block is at B200016;
it ends at B200016 + FFFF16 = C1FFF16
b) The physical address is B200016 + 20A016 = B40A016
64 kB block
Notes: <number>

## Slide 15
Summary
The Execution Unit
The EU decodes instructions, generates control signals, and executes instructions. The general registers and flags are key elements from an assembly language programming view.
Data set
Pointer and index set
Accumulator
Base index
Count
Data
Stack pointer
Base pointer
Destination index
Source index
Interrupt enable
Direction
Trap
Carry
Parity
Aux carry
Zero
Sign
Overflow
Control flags
Status flags
15 8 7 0
As processors have evolved, the register set has expanded, both in number size and number. The following slide shows part of that evolution…
Notes: <number>

## Slide 16
Summary
The Execution Unit
Accumulator
Base index
Count
Data
Stack pointer
Base pointer
Source index
Destination index
Instruction pointer
Code segment
Data segment
Extra segment
Stack segment
32-bit names
EAX
EBX
ECX
EDX
ESP
EBP
EDI
ESI
EIP
EFlags
Name
The software model of later processors includes expanded registers, buses, math coprocessors and the ability to do “pipelining”. Pipelining is a technique where the processor begins executing the next instruction before the previous instruction has been completed.
Notes: <number>

## Slide 17
Summary
Computer Programming
Assembly language was developed to make a simpler interface between the machine and the programmer. Assembly language is useful today for many operations because it executes fast and efficiently, but it must be written for a specific processor and takes more time to write programs.
Early computers were programmed in machine language, which was the only instructions the computer could execute. Machine language is tedious to write and prone to errors.
Most programming today is done in a high-level language, which can run on various machines. It is easier to write and maintain high-level programs.
Notes: <number>

## Slide 18
Summary
Computer Programming
High-level languages can run on any machine; the source code is converted to machine code by a compiler. (In some cases an interpreter is used; it converts source code line-by-line.)
Assembly language must written for the specific processor it will be used on and the programmer must understand the register structure of the processor. An assembler converts the source code to the machine code.
High-level language program
(Source program)
Machine language program
(Object program)
Machine language program
(Object program)
Assembly language program
(Source program)
Assembler
Compiler
Notes: <number>

## Slide 19
Summary
Assembly Programming
Assembly language is suited to instrumentation and control applications such as found in a production facility. It is also used to write device drivers for peripheral devices because necessary instructions are not readily available in high-level languages.
In assembly language, there are two types of instructions – assembler directives and executable instructions. Assembler directives provide the assembler with various types of information such as space requirements, or where to begin executing instructions. Executable instructions can be directly translated to machine code and include arithmetic and other operations.
Example
dw 30 ;an assembler directive that reserves space for 30 as a word
sub ax,bx ;an executable instruction - subtract (bx) from (ax)
The following slide lists categories of executable instructions…
Notes: <number>

## Slide 20
Summary
Instruction type Examples Syntax
Transfer Move (copy) MOV destination, source Input IN destination, port number
Arithmetic Add with Carry ADC destination, source
Subtract SUB destination, source
Bit Manipulation Invert bits NOT register
Shift left (logical) SHL register, quantity
Arithmetic Add with Carry ADC destination, source
Subtract SUB destination, source
Loops and Jumps Unconditional jump JMP destination
Jump if no carry JNC destination
Strings Input a string INS port number
Subroutines Call a procedure CALL label
and Interrupts Interrupt INT number
Processor Control Clear carry flag CLC
Notes: <number>

## Slide 21
Summary
Internal Interfacing
It is often necessary to communicate with various devices in systems. Often, the devices are connected together with a bus and access to the bus is controlled by a bus controller or bus arbitrator to avoid conflicts.
To avoid having two or more devices “talking” on a common bus, tristate buffers are commonly used. These are buffers with three states: HIGH, LOW, and high impedance (disconnected). An enable line determines if the device is enabled or disconnected.
Active HIGH enable line
HIGH
HIGH
LOW or HIGH
HIGH
HIGH
HIGH
Disconnected (high-Z)
Notes: <number>

## Slide 22
Selected Key Terms
Port
Interrupt
Assembly language
Tristate
A physical interface on a computer through which data are passed to or from a peripheral.
A computer signal or instruction that causes the current process to be temporarily stopped while a service routine is run.
A programming language that uses English like words and has a one-to-one correspondence to machine language.
A type of output on logic circuits that exhibits three states: HIGH, LOW, and high Z; used to interface the outputs of a source device to a bus.
Notes: <number>

## Slide 23
1. In a computer, the address bus is a
a. one way bus from the CPU
b. one way bus to the CPU
c. two way bus between the CPU and memory
d. two way bus between the CPU and ports
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 24
2. A example of software that resides in ROM (firmware) is
a. assembly language
b. application software
c. the BIOS
d. all of the above
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 25
3. The part of a microprocessor that translates the programming instruction into an address where microcode resides is the
a. ALU
b. instruction decoder
c. register array
d. control unit
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 26
4. The part of a microprocessor that fetches the next instruction from memory is called the
a. ALU
b. BIU
c. EU
d. bus controller
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 27
5. The figure illustrates the segment/offset method of addressing used in Intel processors. The advantage of this method is
a. code can be easily relocated
b. a smaller address bus can be used
c. addresses can be “pipelined”
d. the clock speed can be increased
© 2008 Pearson Education
Quiz
16-bit segment base address
16-bit offset address
20-bit physical address
Notes: <number>

## Slide 28
6. An advantage to assembly language is that it is
a. fast and efficient
b. easier to write programs
c. can be used on any processor
d. all of the above
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 29
7. Information given to an assembler such as where to begin executing instructions is provided by
a. the BIOS
b. system programs
c. executable instructions
d. assembler directives
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 30
9. For the circuit shown, the output will be
a. LOW
b. HIGH
c. high impedance
d. not enough information to tell
© 2008 Pearson Education
Quiz
HIGH
LOW
?
Notes: <number>