## Slide 1
Signal Conversion
and Processing
Chapter 12
Notes: <number>

## Slide 2
Digital Electronics-II; M Sc IV (Phy-21406) & BS VIII (Phy-01806)
Read the following from the textbook (digital fundamentals by T L Floyd 11th edition)
12–1 Analog-to-Digital Conversion
12–2 Methods of Analog-to-Digital Conversion
12–3 Methods of Digital-to-Analog Conversion
12–4 Digital Signal Processing
This will complete this chapter.
Prof. Dr. Aftab Ahmad

## Slide 3
Use full Video Lectures
On the homepage of YouTube search for “digital electronics lectures”
There are so many video lectures available on the following site.
https://www.youtube.com/results?search_query=digital+electronics+lectures
e.g. Select the following
Electronics - Digital Circuits and Systems (40 videos)
Lectures by Prof. S. Srinivasan https://www.youtube.com/playlist?list=PL803563859BF7ED8C
OR
https://www.youtube.com/playlist?list=PL-IC1WV1OE4kamEu_SGzh3hadrZPoXaSh
Digital Electronics by Dinesh Arya
157 videos
https://www.youtube.com/playlist?list=PLWPirh4EWFpHk70zwYoHu87uVsCC8E2S-
255 videos (useful to understand any topic of digital electronics)
Select the relevant topic which you want to understand.
These lecture will help you a lot. Share tis message with all fellows.

## Slide 4
Summary
Most input signals to an electronic system start out as analog signals. For processing, the signal is normally converted to a digital signal by sampling the input.
Sampling
Before sampling, the analog input must be filtered with a low-pass anti-aliasing filter. The filter eliminates frequencies that exceed a certain limit that is determined by the sampling rate.
Notes: <number>

## Slide 5
Summary
To understand the need for an anti-aliasing filter, you need to understand the sampling theorem which essentially states:
Anti-aliasing Filter
where fsample = sampling frequency
fa(max) = highest harmonic in the analog signal
Stated as an equation, fsample > 2fa(max)
In order to recover a signal, the sampling rate must be greater than twice the highest frequency in the signal.
If the signal is sampled less than this, the recovery process will produce frequencies that are entirely different than in the original signal. These “masquerading” signals are called aliases.
Notes: <number>

## Slide 6
Summary
The anti-aliasing filter is a low-pass filter that limits high frequencies in the input signal to only those that meet the requirements of the sampling theorem.
Anti-aliasing Filter
Unfiltered analog frequency spectrum
Overlap causes aliasing error
fc
Filtered analog frequency spectrum
f
fsample
Sampling frequency spectrum
The filter’s cutoff frequency, fc, should be less than ½ fsample.
Notes: <number>

## Slide 7
To process naturally occurring analog quantities with a digital system, the analog signal is converted to digital form after the anti-aliasing filter.
Summary
Analog-to-Digital Conversion
The first step in converting a signal to digital form is to use a sample-and-hold circuit. This circuit samples the input signal at a rate determined by a clock signal and holds the level on a capacitor until the next clock pulse.
A positive half-wave from 0-10 V is shown in blue. The sample-and-hold circuit produces the staircase representation shown in red.
0 V
10 V
Notes: <number>

## Slide 8
Summary
The second step is to quantize these staircase levels to binary coded form using an analog-to-digital converter (ADC). The digital values can then be processed by a digital signal processor or computer.
0 V
10 V
Example
What is the maximum unsigned binary value for the waveform?
Solution
10 V = 10102 V. The table lists the quantized binary values for all of the steps.
Peak = 10 V
Analog-to-Digital Conversion
Notes: <number>

## Slide 9
Summary
Most signals have higher frequency harmonic and noise. For most ADCs, the sampling and filter cutoff frequencies are selected to be able to reconstruct the desired signal without including unnecessary harmonics and noise.
Anti-aliasing Filter
An example of a reasonable sampling rate is in a digital audio CD. For audio CDs, sampling is done at 44.1 kHz because audio frequencies above 20 kHz are not detectable by the ear.
Question
What cutoff frequency should an anti-aliasing filter have for a digital audio CD?
Answer
Less than 22.05 kHz.
Notes: <number>

## Slide 10
Summary
Sample-and-Hold and ADC
Following the anti-aliasing filter, is the sample-and-hold circuit and the analog-to-digital converter. At this point, the original analog signal has been converted to a digital signal.
Many ICs can perform both functions on a single chip and include two or more channels. For audio applications, the AD1871 is an example of a stereo audio ADC.
Samples held for one clock pulse
0 1 0 0 0 1 0 1
1 1 0 0 1 0 1 0
Notes: <number>

## Slide 11
Summary
Analog-to-Digital Conversion Methods
The flash ADC:
The flash ADC uses a series high-speed comparators that compare the input with reference voltages. Flash ADCs are fast but require 2n – 1 comparators to convert an analog input to an n-bit binary number.
Question
How many comparators are needed by a 10-bit flash ADC?
Answer
1023
Notes: <number>

## Slide 12
Summary
Analog-to-Digital Conversion Methods
The dual-slope ADC:
1. The dual-slope ADC integrates the input voltage for a fixed time while the counter counts to n.
2. Control logic switches to the VREF input.
-V
HIGH
HIGH
2. A fixed-slope ramp starts from –V as the counter counts. When it reaches 0 V, the counter output is latched.
Notes: <number>

## Slide 13
Summary
Analog-to-Digital Conversion Methods
The successive approximation ADC:
1. Starting with the MSB, each bit in the successive approximation register (SAR) is activated and tested by the digital-to-analog converter (DAC).
2. After each test, the DAC produces an output voltage that represents the bit.
3. The comparator compares this voltage with the input signal. If the input is larger, the bit is retained; otherwise it is reset (0).
SAR
DAC
Vout
Parallel binary output
CLK
D0
D1
D2
D3
Serialbinary output
Input signal
Comparator
(MSB)
(LSB)
The method is fast and has a fixed conversion time for all inputs.
Notes: <number>

## Slide 14
Summary
Analog-to-Digital Conversion Methods
An integrated circuit successive approximation ADC is the ADC804. This popular ADC is an 8-bit converter that completes a conversion in 64 clock periods (100 s).
The completion is signaled by the INTR line going LOW.
Notes: <number>

## Slide 15
Summary
Analog-to-Digital Conversion Methods
The sigma-delta ADC:
With sigma-delta conversion, the difference between two samples of the analog input signal integrated and quantized. The density of 1s at the output is proportional to the input signal.
Notes: <number>

## Slide 16
Summary
Analog-to-Digital Conversion Methods
One option for the sigma-delta method is to count the one-bit quantized output for a set interval. The output of the counter is latched with the parallel binary code.
Sigma-delta ADCs can have high resolution and have advantages for rejecting noise signals (such as 60 Hz power line interference). They are available in ICs with internal programmable amplifiers. For these reasons, they are widely used in instrumentation applications.
Notes: <number>

## Slide 17
Summary
Digital-to-Analog Conversion Methods
Binary-weighted-input DAC:
The binary-weighted-input DAC is a basic DAC in which the input current in each resistor is proportional to the column weight in the binary numbering system. It requires very accurate resistors and identical HIGH level voltages for accuracy.
The MSB is represented by the largest current, so it has the smallest resistor. To simplify analysis, assume all current goes through Rf and none into the op-amp.
MSB
LSB
8R
4R
2R
R
Rf
Vout
Analog output
D0
D1
D2
D3
Notes: <number>

## Slide 18
Summary
Digital-to-Analog Conversion Methods
Example
A certain binary-weighted-input DAC has a binary input of 1101. If a HIGH = +3.0 V and a LOW = 0 V, what is Vout?
Solution
+3.0 V
+3.0 V
+3.0 V
0 V
120 k
60 k
30 k
15 k
10 k
Rf
Vout = Iout Rf = (−0.325 mA)(10 k) =
−3.25 V
Vout
Notes: <number>

## Slide 19
Summary
Digital-to-Analog Conversion Methods
R-2R ladder:
The R-2R ladder requires only two values of resistors. By calculating a Thevenin equivalent circuit for each input, you can show that the output is proportional to the binary weight of inputs that are HIGH.
2R
R
R
R
2R
2R
2R
2R
Rf = 2R
Inputs
D0
D1
D2
D3
Each input that is HIGH contributes to the output:
Vout
where VS = input HIGH level voltage
n = number of bits
i = bit number
R1
R3
R5
R7
R2
R4
R6
R8
For accuracy, the resistors must be precise ratios, which is easily done in integrated circuits.
Notes: <number>

## Slide 20
Summary
Digital-to-Analog Conversion Methods
Rf = 50 k
0 V
+5.0 V
Vout
R1
R3
R5
R7
R2
R4
R6
R8
Example
An R-2R ladder has a binary input of 1011. If a HIGH = +5.0 V and a LOW = 0 V, what is Vout?
50 k
25 k
Solution
50 k
50 k
50 k
50 k
25 k
25 k
+5.0 V
+5.0 V
D0
D1
D2
D3
Applying superposition, Vout =
−3.43 V
Apply to all inputs that are HIGH, then sum the results.
Notes: <number>

## Slide 21
Summary
Resolution and Accuracy of DACs
The R-2R ladder is relatively easy to manufacturer and is available in IC packages. DACs based on the R-2R network are available in 8, 10, and 12-bit versions. The resolution is an important specification, defined as the reciprocal of the number of steps in the output.
Question
What is the resolution of the BCN31 R-2R ladder network, which has 8-bits?
Answer
28 – 1 = 255
1/255 = 0.39%
The accuracy is another important specification and is derived from a comparison of the actual output to the expected output. For the BCN31, the accuracy is specified as ±½ LSB = 0.2%.
Notes: <number>

## Slide 22
Summary
Reconstruction Filter
Reconstruction Filter
Output of the DAC
Final analog output
After converting a digital signal to analog, it is passed through a low-pass “reconstruction filter” to smooth the stair steps in the output. The cutoff frequency of the reconstruction filter is often set to the same limit as the anti-aliasing filter, to block higher harmonics due to the digitizing process.
Notes: <number>

## Slide 23
Summary
A digital signal processor (DSP) is optimized for speed and working in real time (as events happen). It is basically a specialized microprocessor with a reduced instruction set.
Digital Signal Processing
After filtering and converting the analog signal to digital, the DSP takes over. It may enhance the signal in some predetermined way (reducing noise or echoes, improving images, encrypting the signal, etc.). The signal can then be converted back to analog form if desired.
Notes: <number>

## Slide 24
Selected Key Terms
Nyquist frequency
Quantization
Analog-to-digital converter (ADC)
DSP
Digital-to-analog converter (DAC)
The highest signal frequency that can be sampled at a specified sampling frequency; a frequency equal or less than half the sampling frequency.
The process whereby a binary code is assigned to each sampled value during analog-to-digital conversion.
A circuit used to convert an analog signal to digital form.
Digital signal Processor; a special type of microprocessor that processes data in real time.
A circuit used to convert a digital signal to analog form.
Notes: <number>

## Slide 25
1. If an anti-aliasing filter is not used in digitizing a signal the recovery process
a. is slowed
b. may include alias signals
c. will have less noise
d. all of the above
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 26
2. An anti-aliasing filter should have
a. fc more than 2 times the Nyquist frequency
b. fc equal to the Nyquist frequency
c. fc more than ½ fsample
d. fc less than ½ fsample
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 27
3. The number of comparators required in a 10-bit flash ADC is
a. 255
b. 511
c. 1023
d. 4095
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 28
4. The block diagram is for a successive-approximation ADC. The top block is
a. an SAR
b. a DAC
c. an ADC
d. a comparator
© 2008 Pearson Education
Quiz
Vout
CLK
D0
D1
D2
D3
Serialbinary output
Input signal
(MSB)
(LSB)
Parallel binary output
Notes: <number>

## Slide 29
6. A sigma-delta circuit is a form of
a. DSP
b. DAC
c. ADC
d. SAR
© 2008 Pearson Education
Quiz
Notes: <number>

## Slide 30
7. The circuit shown is a
a. DSP
b. DAC
c. ADC
d. SAR
© 2008 Pearson Education
Quiz
8R
4R
2R
R
Rf
Vout
Notes: <number>

## Slide 31
8. For the circuit shown, the input on the far left is for the
a. analog input
b. clock
c. LSB
d. MSB
© 2008 Pearson Education
Quiz
2R
R
R
R
2R
2R
2R
2R
Rf = 2R
Inputs
Vout
R1
R3
R5
R7
R2
R4
R6
R8
Notes: <number>