## Slide 1
Functions of
Combinational Logic
Chapter 6
© 2009 Pearson Education
Notes: <number>

## Slide 2
Digital Electronics-I; M Sc III (Phy-21306) & BS VII (Phy-01706)
Read the following from the textbook (digital fundamentals by T L Floyd 11th edition)
6–1 Half and Full Adders
6–2 Parallel Binary Adders
6–3 Ripple Carry (excluding Look-Ahead Carry Adders)
6–4 Comparators
6–5 Decoders
6–6 Encoders
6–7 Code Converters
6–8 Multiplexers (Data Selectors)
6–9 Demultiplexers
6–10 Parity Generators/Checkers (excuding Data Transmission System with Error Detection)
This will complete this chapter.
Prof. Dr. Aftab Ahmad

## Slide 3
Useful Video Lectures
On the homepage of YouTube search for “digital electronics lectures”
There are so many video lectures available on the following site.
https://www.youtube.com/results?search_query=digital+electronics+lectures
e.g. Select the following
Electronics - Digital Circuits and Systems (40 videos)
Lectures by Prof. S. Srinivasan https://www.youtube.com/playlist?list=PL803563859BF7ED8C
OR
https://www.youtube.com/playlist?list=PL-IC1WV1OE4kamEu_SGzh3hadrZPoXaSh
Digital Electronics by Dinesh Arya
157 videos
https://www.youtube.com/playlist?list=PLWPirh4EWFpHk70zwYoHu87uVsCC8E2S-
255 videos (useful to understand any topic of digital electronics)
Select the relevant topic which you want to understand.
These lecture will help you a lot. Share tis message with all fellows.

## Slide 4
Basic rules of binary addition are performed by a half adder, which has two binary inputs (A and B) and two binary outputs (Carry out and Sum).
Summary
Half-Adder
The inputs and outputs can be summarized on a truth table.
A
B

Cout
The logic symbol and equivalent circuit are:
A
B

Cout

Notes: <number>

## Slide 5
Summary
Full-Adder
By contrast, a full adder has three binary inputs (A, B, and Carry in) and two binary outputs (Carry out and Sum). The truth table summarizes the operation.
A full-adder can be constructed from two half adders as shown:
A
B

Cout

A
B

Cout

A
B
Sum
Cout
Cin
A
B

Cout

Cin
Symbol
Notes: <number>

## Slide 6
Summary
Full-Adder
A
B

Cout

A
B

Cout

Example
Solution
For the given inputs, determine the intermediate and final outputs of the full adder.
1
1
0
1
0
The first half-adder has inputs of 1 and 0; therefore the Sum =1 and the Carry out = 0.
The second half-adder has inputs of 1 and 1; therefore the Sum = 0 and the Carry out = 1.
The OR gate has inputs of 1 and 0, therefore the final carry out = 1.
1
0
1
Sum
Cout
Notes: <number>

## Slide 7
Summary
Full-Adder
A
B

Cout

A
B

Cout

1
1
0
1
0
1
0
1
Sum
Cout
Notice that the result from the previous example can be read directly on the truth table for a full adder.
Notes: <number>

## Slide 8
Summary
Parallel Adders
Full adders are combined into parallel adders that can add binary numbers with multiple bits. A 4-bit adder is shown.
A
B

Cout
Cin
A
B

Cout
Cin
A
B

Cout
Cin
A
B

Cout
Cin
A1 B1

C0



C1
C2
C3
C4
A2 B2
A3 B3
A4 B4
The output carry (C4) is not ready until it propagates through all of the full adders. This is called ripple carry, delaying the addition process.
Notes: <number>

## Slide 9
Summary
Parallel Adders
The logic symbol for a 4-bit parallel adder is shown. This 4-bit adder includes a carry in (labeled (C0) and a Carry out (labeled C4).
The 74LS283 is an example. It features look-ahead carry, which adds logic to minimize the output carry delay. For the 74LS283, the maximum delay to the output carry is 17 ns.
Binary number A
Binary number B
Input carry
4-bit sum
Output carry
1
2
3
4
1
2
3
4
1
2
3
4
C0
C4

Notes: <number>

## Slide 10
Summary
Comparators
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them. In the simplest form, a comparator can test for equality using XNOR gates.
Example
Solution
How could you test two 4-bit numbers for equality?
AND the outputs of four XNOR gates.
A1
B1
A2
B2
A3
B3
A4
B4
Output
Notes: <number>

## Slide 11
Summary
Comparators
IC comparators provide outputs to indicate which of the numbers is larger or if they are equal. The bits are numbered starting at 0, rather than 1 as in the case of adders. Cascading inputs are provided to expand the comparator to larger numbers.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
Cascading inputs
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
The IC shown is the 4-bit 74LS85.
Notes: <number>

## Slide 12
Summary
Comparators
IC comparators can be expanded using the cascading inputs as shown. The lowest order comparator has a HIGH on the A = B input.
Outputs
A1
A0
A2
A3
B1
B0
B2
B3
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
A5
A4
A6
A7
B5
B4
B6
B7
+5.0 V
COMP
A = B
A < B
A > B
A = B
A < B
A > B
0
0
3
3
A
A
LSBs
MSBs
Notes: <number>

## Slide 13
Summary
Decoders
A decoder is a logic circuit that detects the presence of a specific combination of bits at its input. Two simple decoders that detect the presence of the binary code 0011 are shown. The first has an active HIGH output; the second has an active LOW output.
A1
A0
A2
A3
X
Active HIGH decoder for 0011
A1
A0
A2
A3
X
Active LOW decoder for 0011
Notes: <number>

## Slide 14
Summary
Decoders
Assume the output of the decoder shown is a logic 1. What are the inputs to the decoder?
Question
Notes: <number>

## Slide 15
Summary
Decoders
IC decoders have multiple outputs to decode any combination of inputs. For example the binary-to-decimal decoder shown here has 16 outputs – one for each combination of binary inputs.
Question
For the input shown, what is the output?
Notes: <number>

## Slide 16
Summary
Decoders
A specific integrated circuit decoder is the 74HC154 (shown as a 4-to-16 decoder). It includes two active LOW chip select lines which must be at the active level to enable the outputs. These lines can be used to expand the decoder to larger inputs.
CS2
A1
A0
A2
A3
CS1
X/Y
EN
74HC154
Notes: <number>

## Slide 17
Summary
Decoders
BCD-to-decimal decoders accept a binary coded decimal input and activate one of ten possible decimal digit indications.
A1
A0
A2
A3
Example
Solution
Assume the inputs to the 74HC42 decoder are the sequence 0101, 0110, 0011, and 0010. Describe the output.
All lines are HIGH except for one active output, which is LOW. The active outputs are 5, 6, 3, and 2 in that order.
Notes: <number>

## Slide 18
Summary
BCD Decoder/Driver
Another useful decoder is the 74LS47. This is a BCD-to-seven segment display with active LOW outputs.
The a-g outputs are designed for much higher current than most devices (hence the word driver in the name).
BCD inputs
Outputs to seven segment device
GND
VCC
BCD/7-seg
BI/RBO
BI/RBO
LT
RBI
LT
RBI
74LS47
Notes: <number>

## Slide 19
Summary
BCD Decoder/Driver
Here the 7447A is an connected to an LED seven segment display. Notice the current limiting resistors, required to prevent overdriving the LED display.
Notes: <number>

## Slide 20
Summary
BCD Decoder/Driver
Blanked
Blanked
The 74LS47 features leading zero suppression, which blanks unnecessary leading zeros but keeps significant zeros as illustrated here. The BI/RBO output is connected to the RBI input of the next decoder.
Depending on the display type, current limiting resistors may be required.
Notes: <number>

## Slide 21
Summary
BCD Decoder/Driver
Blanked
Blanked
Decimal point
Trailing zero suppression blanks unnecessary trailing zeros to the right of the decimal point as illustrated here. The RBI input is connected to the BI/RBO output of the following decoder.
Notes: <number>

## Slide 22
Summary
Encoders
An encoder accepts an active logic level on one of its inputs and converts it to a coded output, such as BCD or binary.
The decimal to BCD is an encoder with an input for each of the ten decimal digits and four outputs that represent the BCD code for the active digit. The basic logic diagram is shown. There is no zero input because the outputs are all LOW when the input is zero.
A1
A0
A2
A3
1
2
3
4
5
6
7
8
9
Notes: <number>

## Slide 23
Summary
Encoders
A1
A0
A2
A3
Example
Solution
Show how the decimal-to-BCD encoder converts the decimal number 3 into a BCD 0011.
The top two OR gates have ones as indicated with the red lines. Thus the output is 0111.
1
2
3
4
5
6
7
8
9
0
0
0
0
0
0
0
0
1
0
0
1
1
Notes: <number>

## Slide 24
Summary
Encoders
The 74HC147 is an example of an IC encoder. It is has ten active-LOW inputs and converts the active input to an active-LOW BCD output.
This device is offers additional flexibility in that it is a priority encoder. This means that if more than one input is active, the one with the highest order decimal digit will be active.
Decimal input
BCD output
GND
VCC
HPRI/BCD
74HC147
The next slide shows an application …
Notes: <number>

## Slide 25
Summary
Encoders
VCC
BCD complement of key press
Keyboard encoder
HPRI/BCD
74HC147
The zero line is not needed by the encoder, but may be used by other circuits to detect a key press.
Notes: <number>

## Slide 26
Summary
Code converters
There are various code converters that change one code to another. Two examples are the four bit binary-to-Gray converter and the Gray-to-binary converter.
Example
Show the conversion of binary 0111 to Gray and back.
Solution
0
0
0
1
1
1
Binary-to-Gray Gray-to-Binary
MSB
LSB
MSB
LSB
1
0
0
0
1
0
0
1
1
1
Notes: <number>

## Slide 27
A multiplexer (MUX) selects one data line from two or more input lines and routes data from the selected line to the output. The particular data line that is selected is determined by the select inputs.
Summary
Multiplexers
Two select lines are shown here to choose any of the four data inputs.
Data
select
Data
inputs
Data
output
D1
D0
D2
D3
S1
S0
Question
Which data line is selected if S1S0 = 10?
D2
1
0
Notes: <number>

## Slide 28
A demultiplexer (DEMUX) performs the opposite function from a MUX. It switches data from one input line to two or more data lines depending on the select inputs.
The 74LS138 was introduced previously as a decoder but can also serve as a DEMUX. When connected as a DEMUX, data is applied to one of the enable inputs, and routed to the selected output line depending on the select variables. Note that the outputs are active-LOW as illustrated in the following example…
Summary
Demultiplexers
74LS138
Data select lines
Enable
inputs
Data outputs
Notes: <number>

## Slide 29
Determine the outputs, given the inputs shown.
Summary
Demultiplexers
Example
74LS138
Data select lines
Enable
inputs
Data outputs
A
0
Y
0
Y
1
Y
2
Y
3
Y
4
Y
5
Y
6
Y
7
A
1
A
2
G
1
G
2A
G
2B
LOW
LOW
The output logic is opposite to the input because of the active-LOW convention. (Red shows the selected line).
Solution
Notes: <number>

## Slide 30
Summary
Parity Generators/Checkers
Parity is an error detection method that uses an extra bit appended to a group of bits to force them to be either odd or even. In even parity, the total number of ones is even; in odd parity the total number of ones is odd.
11010011
S with odd parity =
S with even parity =
01010011
Example
The ASCII letter S is 1010011. Show the parity bit for the letter S with odd and even parity.
Solution
Notes: <number>

## Slide 31
Summary
Parity Generators/Checkers
The 74LS280 can be used to generate a parity bit or to check an incoming data stream for even or odd parity.
Checker: The 74LS280 can test codes with up to 9 bits. The even output will normally be HIGH if the data lines have even parity; otherwise it will be LOW. Likewise, the odd output will normally be HIGH if the data lines have odd parity; otherwise it will be LOW.
Generator: To generate even parity, the parity bit is taken from the odd parity output. To generate odd parity, the output is taken from the even parity output.
74LS280
Data inputs
 Even
 Odd
Notes: <number>

## Slide 32
Selected Key Terms
Full-adder
Cascading
Ripple carry
Look-ahead carry
A digital circuit that adds two bits and an input carry bit to produce a sum and an output carry.
Connecting two or more similar devices in a manner that expands the capability of one device.
A method of binary addition in which the output carry from each adder becomes the input carry of the next higher order adder.
A method of binary addition whereby carries from the preceding adder stages are anticipated, thus eliminating carry propagation delays.
Notes: <number>

## Slide 33
Selected Key Terms
Decoder
Encoder
Priority encoder
Multiplexer (MUX)
Demultiplexer (DEMUX)
A digital circuit that converts coded information into a familiar or noncoded form.
A digital circuit that converts information into a coded form.
An encoder in which only the highest value input digit is encoded and any other active input is ignored.
A circuit that switches digital data from several input lines onto a single output line in a specified time sequence.
A circuit that switches digital data from one input line onto a several output lines in a specified time sequence.
Notes: <number>

## Slide 34
1. For the full-adder shown, assume the input bits are as shown with A = 0, B = 0, Cin = 1. The Sum and Cout will be
a. Sum = 0 Cout = 0
b. Sum = 0 Cout = 1
c. Sum = 1 Cout = 0
d. Sum = 1 Cout = 1
© 2009 Pearson Education
Quiz
A
B

Cout

A
B

Cout

0
1
0
Sum
Cout
Notes: <number>

## Slide 35
2. The output will be LOW if
a. A < B
b. A > B
c. both a and b are
correct
d. A = B
© 2009 Pearson Education
Quiz
A1
B1
A2
B2
A3
B3
A4
B4
Output
Notes: <number>

## Slide 36
3. If you expand two 4-bit comparators to accept two 8-bit numbers, the output of the least significant comparator is
a. equal to the final output
b. connected to the cascading inputs of the most
significant comparator
c. connected to the output of the most significant
comparator
d. not used
© 2009 Pearson Education
Quiz
Notes: <number>

## Slide 37
4. Assume you want to decode the binary number 0011 with an active-LOW decoder. The missing gate should be
a. an AND gate
b. an OR gate
c. a NAND gate
d. a NOR gate
© 2009 Pearson Education
Quiz
A1
A0
A2
A3
X
?
Notes: <number>

## Slide 38
5. Assume you want to decode the binary number 0011 with an active-HIGH decoder. The missing gate should be
a. an AND gate
b. an OR gate
c. a NAND gate
d. a NOR gate
© 2009 Pearson Education
Quiz
A1
A0
A2
A3
X
?
Notes: <number>

## Slide 39
6. The 74138 is a 3-to-8 decoder. Together, two of these ICs can be used to form one 4-to-16 decoder. To do this, connect
a. one decoder to the LSBs of the input; the other decoder to the MSBs of the input
b. all chip select lines to ground
c. all chip select lines to their active levels
d. one chip select line on each decoder to the input MSB
© 2009 Pearson Education
Quiz
Notes: <number>

## Slide 40
7. The decimal-to-binary encoder shown does not have a zero input. This is because
a. when zero is the input,
all lines should be LOW
b. zero is not important
c. zero will produce
illegal logic levels
d. another encoder is used
for zero
© 2009 Pearson Education
Quiz
A1
A0
A2
A3
1
2
3
4
5
6
7
8
9
Notes: <number>

## Slide 41
8. If the data select lines of the MUX are S1S0 = 11, the output will be
a. LOW
b. HIGH
c. equal to D0
d. equal to D3
© 2009 Pearson Education
Quiz
Data
select
Data
inputs
Data
output
D1
D0
D2
D3
S1
S0
Notes: <number>