## Slide 1
Basic Concepts
Computer Architecture & Assembly Language

## Slide 2: Virtual Machines
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 3: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 4: Specific Machine Levels

## Slide 5: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language (Level 4)

## Slide 6: Assembly Language
Level 3
Instruction mnemonics that have a one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 7: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 8: Digital Logic
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors

## Slide 9: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 10: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 11: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 12: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1  2n-1) + (Dn-2  2n-2) + ... + (D1  21) + (D0  20)
D = binary digit
binary 00001001 = decimal 9:
(1  23) + (1  20) = 9

## Slide 13: Translating Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101

## Slide 14: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 15: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 16: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 17: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 18: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (D3  163) + (D2  162) + (D1  161) + (D0  160)
Hex 1234 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,660.
Hex 3BA4 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,268.

## Slide 19: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 20: Converting Decimal to Hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 21: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 22: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 2E
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 23: Signed Integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 24: Forming the Two's Complement
Negative numbers are stored in two's complement notation
Represents the additive Inverse
Note that 00000001 + 11111111 = 00000000

## Slide 25: Binary Subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
Practice: Subtract 0101 from 1001.

## Slide 26: Ranges of Signed Integers
The highest bit is reserved for the sign. This limits the range:
Practice: What is the largest positive value that may be stored in 20 bits?

## Slide 27: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 28: Numeric Data Representation
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"

## Slide 29: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 30: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 31: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 32: AND
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 33: OR
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 34: Operator Precedence
Examples showing the order of operations:

## Slide 35: Truth Tables (1 of 3)
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 36: Truth Tables (2 of 3)
Example: X  Y

## Slide 37: Truth Tables (3 of 3)
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 38
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal