## Slide 1
Computer Architecture & Assembly Language
General Concepts

## Slide 2: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 3: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 4: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 5: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
Instruction Execution Cycle

## Slide 6: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  address placed on address bus
  Read Line (RD) set low
  CPU waits one cycle for memory to respond
  Read Line (RD) goes to 1, indicating that the data is on the data bus

## Slide 7: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 8: How a Program Runs

## Slide 9: Multitasking
OS can run multiple programs at the same time.
Multiple threads of execution within the same program.
Scheduler utility assigns a given amount of CPU time to each running program.
Rapid switching of tasks
  gives illusion that all programs are running at once
  the processor must support task switching.

## Slide 10: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 11: Modes of Operation
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 12: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 13: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 14: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.

## Slide 15: Accessing Parts of Registers
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 16: Index and Base Registers
Some registers have only a 16-bit name for their lower half:
Source index
Destination Index
Base pointer
Stack pointer

## Slide 17: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 18: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 19: Status Flags
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4
Parity
  sum of 1 bits is an even number

## Slide 20: Floating-Point, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations

## Slide 21: Intel Microprocessor History
Intel 8086, 80286
IA-32 processor family
P6 processor family
CISC and RISC

## Slide 22: Early Intel Microprocessors
Intel 8080
  64K addressable RAM
  8-bit registers
  CP/M operating system
  S-100 BUS architecture
  8-inch floppy disks!
Intel 8086/8088
  IBM-PC Used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)

## Slide 23: The IBM-AT
Intel 80286
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  80287 floating point unit

## Slide 24: Intel IA-32 Family
Intel386
  4 GB addressable RAM, 32-bit registers, paging (virtual memory)
Intel486
  instruction pipelining
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 25: 64-bit Processors
Intel64
  64-bit linear address space
  Intel: Pentium Extreme, Xeon, Celeron D, Pendium D, Core 2, and Core i7
IA-32e Mode
  Compatibility mode for legacy 16- and 32-bit applications
  64-bit Mode uses 64-bit addresses and operands

## Slide 26: Intel Technologies
HyperThreading technology
  two tasks execute on a single processor at the same time
Dual Core processing
  multiple processor cores in the same IC package
  each processor has its own resources and communication path with the bus

## Slide 27: Intel Processor Families
Currently Used:
Pentium & Celeron – dual core
Core 2 Duo - 2 processor cores
Core 2 Quad - 4 processor cores
Core i7 – 4 processor cores

## Slide 28: CISC and RISC
CISC – complex instruction set
  large instruction set
  high-level operations
  requires microcode interpreter
  examples: Intel 80x86 family
RISC – reduced instruction set
  simple, atomic instructions
  small instruction set
  directly executed by hardware
  examples:
    ARM (Advanced RISC Machines)
    DEC Alpha (now Compaq)

## Slide 29: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 30: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 31: Real-Address mode
1 MB RAM maximum addressable
Application programs can access any area of memory
Single tasking
Supported by MS-DOS operating system

## Slide 32: Segmented Memory
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment

## Slide 33: Calculating Linear Addresses
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0

## Slide 34: Your turn . . .
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.

## Slide 35: Your turn . . .
What segment addresses correspond to the linear address 28F30h?
Many different segment-offset addresses can produce the linear address 28F30h. For example:
28F0:0030, 28F3:0000, 28B0:0430, . . .

## Slide 36: Protected Mode (1 of 2)
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows

## Slide 37: Protected mode (2 of 2)
Segment descriptor tables
Program structure
  code, data, and stack areas
  CS, DS, SS segment descriptors
  global descriptor table (GDT)
MASM Programs use the Microsoft flat memory model

## Slide 38: Flat Segment Model
Single global descriptor table (GDT).
All segments mapped to entire 32-bit address space

## Slide 39: Multi-Segment Model
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program

## Slide 40: Paging
Supported directly by the CPU
Divides each segment into 4096-byte blocks called pages
Sum of all programs can be larger than physical memory
Part of running program is in memory, part is on disk
Virtual memory manager (VMM) – OS utility that manages the loading and unloading of pages
Page fault – issued by CPU when a page must be loaded from disk

## Slide 41: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 42: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 43: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 44: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 45: Intel 965 Express Chipset

## Slide 46: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required
* This link may change over time.

## Slide 47: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 48: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 49: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 50: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 51: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 52: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 53: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 54: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 55: Programming levels
Assembly language programs can perform input-output at each of the following levels: