## Slide 1
Computer Architecture & Assembly Language
Assembly Language Fundamentals

## Slide 2: Chapter Overview
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 3: Basic Elements of Assembly Language
Integer constants
Integer expressions
Character and string constants
Reserved words and identifiers
Directives and instructions
Labels
Mnemonics and Operands
Comments
Examples

## Slide 4: Integer Constants
Optional leading + or – sign
binary, decimal, hexadecimal, or octal digits
Common radix characters:
  h – hexadecimal
  d – decimal
  b – binary
  r – encoded real
Examples: 30d, 6Ah, 42, 1101b
Hexadecimal beginning with letter: 0A5h

## Slide 5: Integer Expressions
Operators and precedence levels:
Examples:

## Slide 6: Character and String Constants
Enclose character in single or double quotes
  'A', "x"
  ASCII character = 1 byte
Enclose strings in single or double quotes
  "ABC"
  'xyz'
  Each character occupies a single byte
Embedded quotes:
  'Say "Goodnight," Gracie'

## Slide 7: Reserved Words and Identifiers
Reserved words cannot be used as identifiers
  Instruction mnemonics, directives, type attributes, operators, predefined symbols
  See MASM reference in Appendix A
Identifiers
  1-247 characters, including digits
  not case sensitive
  first character must be a letter, _, @, ?, or $

## Slide 8: Directives
Commands that are recognized and acted upon by the assembler
  Not part of the Intel instruction set
  Used to declare code, data areas, select memory model, declare procedures, etc.
  not case sensitive
Different assemblers have different directives
  NASM not the same as MASM, for example

## Slide 9: Instructions
Assembled into machine code by assembler
Executed at runtime by the CPU
We use the Intel IA-32 instruction set
An instruction contains:
  Label (optional)
  Mnemonic (required)
  Operand (depends on the instruction)
  Comment (optional)

## Slide 10: Labels
Act as place markers
  marks the address (offset) of code and data
Follow identifer rules
Data label
  must be unique
  example: myArray (not followed by colon)
Code label
  target of jump and loop instructions
  example: L1: (followed by colon)

## Slide 11: Mnemonics and Operands
Instruction Mnemonics
  memory aid
  examples: MOV, ADD, SUB, MUL, INC, DEC
Operands
  constant
  constant expression
  register
  memory (data label)
Constants and constant expressions are often called immediate values

## Slide 12: Comments
Comments are good!
  explain the program's purpose
  when it was written, and by whom
  revision information
  tricky coding techniques
  application-specific explanations
Single-line comments
  begin with semicolon (;)
Multi-line comments
  begin with COMMENT directive and a programmer-chosen character
  end with the same programmer-chosen character

## Slide 13: Instruction Format Examples
No operands
  stc ; set Carry flag
One operand
  inc eax ; register
  inc myByte ; memory
Two operands
  add ebx,ecx ; register, register
  sub myByte,25 ; memory, constant
  add eax,36 * 25 ; register, constant-expression

## Slide 14: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 15: Example: Adding and Subtracting Integers
TITLE Add and Subtract (AddSub.asm)
; This program adds and subtracts 32-bit integers.
INCLUDE Irvine32.inc
.code
main PROC
mov eax,10000h ; EAX = 10000h
add eax,40000h ; EAX = 50000h
sub eax,20000h ; EAX = 30000h
call DumpRegs ; display registers
exit
main ENDP
END main

## Slide 16: Example Output
Program output, showing registers and flags:
EAX=00030000 EBX=7FFDF000 ECX=00000101 EDX=FFFFFFFF
ESI=00000000 EDI=00000000 EBP=0012FFF0 ESP=0012FFC4
EIP=00401024 EFL=00000206 CF=0 SF=0 ZF=0 OF=0

## Slide 17: Suggested Coding Standards (1 of 2)
Some approaches to capitalization
  capitalize nothing
  capitalize everything
  capitalize all reserved words, including instruction mnemonics and register names
  capitalize only directives and operators
Other suggestions
  descriptive identifier names
  spaces surrounding arithmetic operators
  blank lines between procedures

## Slide 18: Suggested Coding Standards (2 of 2)
Indentation and spacing
  code and data labels – no indentation
  executable instructions – indent 4-5 spaces
  comments: right side of page, aligned vertically
  1-3 spaces between instruction and its operands
    ex: mov ax,bx
  1-2 blank lines between procedures

## Slide 19: Program Template
TITLE Program Template (Template.asm)
; Program Description:
; Author:
; Creation Date:
; Revisions:
; Date: Modified by:
INCLUDE Irvine32.inc
.data
; (insert variables here)
.code
main PROC
; (insert executable instructions here)
exit
main ENDP
; (insert additional procedures here)
END main

## Slide 20: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 21: Assembling, Linking, and Running Programs
Assemble-Link-Execute Cycle
Listing File
Map File

## Slide 22: Assemble-Link Execute Cycle
The following diagram describes the steps from creating a source program through executing the compiled program.
If the source code is modified, Steps 2 through 4 must be repeated.

## Slide 23: Listing File
Use it to see how your program is compiled
Contains
  source code
  addresses
  object code (machine language)
  segment names
  symbols (variables, procedures, and constants)

## Slide 24: Map File
Information about each program segment:
  starting address
  ending address
  size
  segment type

## Slide 25: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 26: Defining Data
Intrinsic Data Types
Data Definition Statement
Defining BYTE and SBYTE Data
Defining WORD and SWORD Data
Defining DWORD and SDWORD Data
Defining QWORD Data
Defining TBYTE Data
Defining Real Number Data
Little Endian Order
Adding Variables to the AddSub Program
Declaring Uninitialized Data

## Slide 27: Intrinsic Data Types (1 of 2)
BYTE, SBYTE
  8-bit unsigned integer; 8-bit signed integer
WORD, SWORD
  16-bit unsigned & signed integer
DWORD, SDWORD
  32-bit unsigned & signed integer
QWORD
  64-bit integer
TBYTE
  80-bit integer

## Slide 28: Intrinsic Data Types (2 of 2)
REAL4
  4-byte IEEE short real
REAL8
  8-byte IEEE long real
REAL10
  10-byte IEEE extended real

## Slide 29: Data Definition Statement
A data definition statement sets aside storage in memory for a variable.
May optionally assign a name (label) to the data
Syntax:
  [name] directive initializer [,initializer] . . .
  value1 BYTE 10
All initializers become binary data in memory

## Slide 30: Defining BYTE and SBYTE Data
value1 BYTE 'A' ; character constant
value2 BYTE 0 ; smallest unsigned byte
value3 BYTE 255 ; largest unsigned byte
value4 SBYTE -128 ; smallest signed byte
value5 SBYTE +127 ; largest signed byte
value6 BYTE ? ; uninitialized byte
Each of the following defines a single byte of storage:
MASM does not prevent you from initializing a BYTE with a negative value, but it's considered poor style.
If you declare a SBYTE variable, the Microsoft debugger will automatically display its value in decimal with a leading sign.

## Slide 31: Defining Byte Arrays
list1 BYTE 10,20,30,40
list2 BYTE 10,20,30,40
BYTE 50,60,70,80
BYTE 81,82,83,84
list3 BYTE ?,32,41h,00100010b
list4 BYTE 0Ah,20h,‘A’,22h
Examples that use multiple initializers:

## Slide 32: Defining Strings (1 of 3)
A string is implemented as an array of characters
  For convenience, it is usually enclosed in quotation marks
  It often will be null-terminated
Examples:
str1 BYTE "Enter your name",0
str2 BYTE 'Error: halting program',0
str3 BYTE 'A','E','I','O','U'
greeting BYTE "Welcome to the Encryption Demo program "
BYTE "created by Kip Irvine.",0

## Slide 33: Defining Strings (2 of 3)
To continue a single string across multiple lines, end each line with a comma:
menu BYTE "Checking Account",0dh,0ah,0dh,0ah,
"1. Create a new account",0dh,0ah,
"2. Open an existing account",0dh,0ah,
"3. Credit the account",0dh,0ah,
"4. Debit the account",0dh,0ah,
"5. Exit",0ah,0ah,
"Choice> ",0

## Slide 34: Defining Strings (3 of 3)
End-of-line character sequence:
  0Dh = carriage return
  0Ah = line feed
str1 BYTE "Enter your name: ",0Dh,0Ah
BYTE "Enter your address: ",0
newLine BYTE 0Dh,0Ah,0
Idea: Define all strings used by your program in the same area of the data segment.

## Slide 35: Using the DUP Operator
Use DUP to allocate (create space for) an array or string. Syntax: counter DUP ( argument )
Counter and argument must be constants or constant expressions
var1 BYTE 20 DUP(0) ; 20 bytes, all equal to zero
var2 BYTE 20 DUP(?) ; 20 bytes, uninitialized
var3 BYTE 4 DUP("STACK") ; 20 bytes: "STACKSTACKSTACKSTACK"
var4 BYTE 10,3 DUP(0),20 ; 5 bytes

## Slide 36: Defining WORD and SWORD Data
Define storage for 16-bit integers
  or double characters
  single value or multiple values
word1 WORD 65535 ; largest unsigned value
word2 SWORD –32768 ; smallest signed value
word3 WORD ? ; uninitialized, unsigned
word4 WORD "AB" ; double characters
myList WORD 1,2,3,4,5 ; array of words
array WORD 5 DUP(?) ; uninitialized array

## Slide 37: Defining DWORD and SDWORD Data
val1 DWORD 12345678h ; unsigned
val2 SDWORD –2147483648 ; signed
val3 DWORD 20 DUP(?) ; unsigned array
val4 SDWORD –3,–2,–1,0,1 ; signed array
Storage definitions for signed and unsigned 32-bit integers:

## Slide 38: Defining QWORD, TBYTE, Real Data
quad1 QWORD 1234567812345678h
val1 TBYTE 1000000000123456789Ah
rVal1 REAL4 -2.1
rVal2 REAL8 3.2E-260
rVal3 REAL10 4.6E+4096
ShortArray REAL4 20 DUP(0.0)
Storage definitions for quadwords, tenbyte values, and real numbers:

## Slide 39: Little Endian Order
All data types larger than a byte store their individual bytes in reverse order. The least significant byte occurs at the first (lowest) memory address.
Example:
val1 DWORD 12345678h

## Slide 40: Adding Variables to AddSub
TITLE Add and Subtract, Version 2 (AddSub2.asm)
; This program adds and subtracts 32-bit unsigned
; integers and stores the sum in a variable.
INCLUDE Irvine32.inc
.data
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
finalVal DWORD ?
.code
main PROC
mov eax,val1 ; start with 10000h
  add eax,val2 ; add 40000h
  sub eax,val3 ; subtract 20000h
  mov finalVal,eax ; store the result (30000h)
  call DumpRegs ; display the registers
  exit
main ENDP
END main

## Slide 41: Declaring Unitialized Data
Use the .data? directive to declare an unintialized data segment:
  .data?
Within the segment, declare variables with "?" initializers:
  smallArray DWORD 10 DUP(?)
Advantage: the program's EXE file size is reduced.

## Slide 42: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 43: Symbolic Constants
Equal-Sign Directive
Calculating the Sizes of Arrays and Strings
EQU Directive
TEXTEQU Directive

## Slide 44: Equal-Sign Directive
name = expression
  expression is a 32-bit integer (expression or constant)
  may be redefined
  name is called a symbolic constant
good programming style to use symbols
COUNT = 500
.
.
mov ax,COUNT

## Slide 45: Calculating the Size of a Byte Array
current location counter: $
  subtract address of list
  difference is the number of bytes
list BYTE 10,20,30,40
ListSize = ($ - list)

## Slide 46: Calculating the Size of a Word Array
Divide total number of bytes by 2 (the size of a word)
list WORD 1000h,2000h,3000h,4000h
ListSize = ($ - list) / 2

## Slide 47: Calculating the Size of a Doubleword Array
Divide total number of bytes by 4 (the size of a doubleword)
list DWORD 1,2,3,4
ListSize = ($ - list) / 4

## Slide 48: EQU Directive
Define a symbol as either an integer or text expression.
Cannot be redefined
PI EQU <3.1416>
pressKey EQU <"Press any key to continue...",0>
.data
prompt BYTE pressKey

## Slide 49: TEXTEQU Directive
Define a symbol as either an integer or text expression.
Called a text macro
Can be redefined
continueMsg TEXTEQU <"Do you wish to continue (Y/N)?">
rowSize = 5
.data
prompt1 BYTE continueMsg
count TEXTEQU %(rowSize * 2) ; evaluates the expression
setupAL TEXTEQU <mov al,count>
.code
setupAL ; generates: "mov al,10"

## Slide 50: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 51: Real-Address Mode Programming (1 of 2)
Generate 16-bit MS-DOS Programs
Advantages
  enables calling of MS-DOS and BIOS functions
  no memory access restrictions
Disadvantages
  must be aware of both segments and offsets
  cannot call Win32 functions (Windows 95 onward)
  limited to 640K program memory

## Slide 52: Real-Address Mode Programming (2 of 2)
Requirements
  INCLUDE Irvine16.inc
  Initialize DS to the data segment:
      mov ax,@data
      mov ds,ax

## Slide 53: Add and Subtract, 16-Bit Version
TITLE Add and Subtract, Version 2 (AddSub2r.asm)
INCLUDE Irvine16.inc
.data
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
finalVal DWORD ?
.code
main PROC
  mov ax,@data ; initialize DS
  mov ds,ax
  mov eax,val1 ; get first value
  add eax,val2 ; add second value
  sub eax,val3 ; subtract third value
  mov finalVal,eax ; store the result
  call DumpRegs ; display registers
  exit
main ENDP
END main