## Slide 1: Digital Logic & Design Lec #1&2
M.C.s 1st Semester
IUB

## Slide 2: What is DLD?
Digital logic design is a system in electrical and computer engineering that uses simple number values to produce input and output operations. As a digital design engineer, you may assist in developing cell phones, computers, and related personal electronic devices. Continue reading to find out what training can develop skills in function algorithms and binary conversion.

## Slide 3: Applications
Digital logic design forms the foundation of electrical engineering and computer engineering. Digital logic designers build complex electronic components that use both electrical and computational characteristics such as power, current, logical function, protocol, and user input. Digital logic design is used to develop hardware, such as circuit boards and microchip processors. This hardware processes user input, system protocol, and other data in navigational systems, cell phones, or other high-tech systems.

## Slide 4: Is digital logic design important in computer science engineering?
Yes it is an important subject in computer science. Example: If you want to learn computer organization and architecture you got to have a decent command over Digital Logic.
Digital Logic is a subject where we learn about the designing of combinational and sequential logic circuits (Hardware components of a computer),Boolean Algebra, Basic gates etc. which inturn is helpful in designing of a computer.

## Slide 5: Digital And Analog Signals
Analog and digital signals are used to transmit information, usually through electric signals. In both these technologies, the information, such as any audio or video, is transformed into electric signals. The difference between analog and digital technologies is that in analog technology, information is translated into electric pulses of varying amplitude. In digital technology, translation of information is into binary format (zero or one) where each bit is representative of two distinct amplitudes.

## Slide 6: Characteristics of Digital Signal
1. Bit interval
It is the time required to send one single bit
2. Bit rate
(i) It refers to the number of bit intervals in one second.
(ii) Therefore bit rate is the number of bits sent in one second as shown in fig.
(iii)Bit rate is expressed in bits per second (bps).
(iv)Other units used to express bit rate are Kbps, Mbps and Gbps.
1 kilobit per second (Kbps) = 1,000 bits per second
1 Megabit per second (Mbps) = 1,000,000 bits per second
1 Gigabit per second (Gbps) = 1,000,000,000 bits per second

## Slide 7: Period, Frequency, Duty Cycle
Period (T)
Time between waves or oscillation
Measure in seconds/ milisecond
Frequency
How many oscillation or waves per unit time
f= 1/T
Measure in Hz

## Slide 8
Duty cycle
We need to determine the plus width (Tw) for period digital waves form
Duty cycle= Tw/T x100%
Where is the duty cycle,is the pulse width (pulse active time), and is the total period of the signal. Thus, a 60% duty cycle means the signal is on 60% of the time but off 40% of the time
The "on time" for a 60% duty cycle could be a fraction of a second, a day, or even a week, depending on the length of the period

## Slide 11: Number Systems
Binary to Decimal Conversion
Sum-of-Weights
  Expression base number & weights
  Sum terms
  Paper and pencil method
Sum of non-zero terms
  Mental Arithmetic, quick method
  Sum of weights of non-zero terms

## Slide 12
Sum-of-Weights
100112
(1 x 24) + (0 x 23) + (0 x 22) + (1 x 21)
+ (1 x 20)
Terms 16, 0, 0, 2 and 1
19
Add weights of non-zero terms
Weights increase/decrease by power of 2
100112 = 16 + 2 + 1 = 19
1011.1012 = 8 + 2 + 1 + 1/2 + 1/8
= 11 + 5/8
= 11.625

## Slide 13
Decimal to Binary Conversion
Sum-of-Weights method used in reverse
  Highest binary weight less than the decimal number
  Subsequent smaller weights that add up to decimal number
Repeated division by 2
  Paper and pencil method
  Number repeatedly divided by 2

## Slide 14: Decimal to Binary Conversion using Sum-of-Weights

## Slide 15: Binary-Decimal fraction conversion
Binary to Decimal Conversion
  Sum-of-Weights method
  Weights decrease by a factor of 2
  0.11012 weights ½, ¼, 1/16
  Sum up to 0.8125
Decimal to Binary Conversion
  Repeated Multiplication by 2
  example

## Slide 16
Decimal to Binary Conversion
  Repeated multiplication by 2

## Slide 17: Octal Number System
Base 8
0, 1, 2, 3, 4, 5, 6, 7
Representing Binary in compact form
  11011000001102 = 154068

## Slide 19: Binary-Octal Conversion
Binary to Octal Conversion
  11010110101110010110
  011 010 110 101 110 010 110
  3 2 6 5 6 2 6
Octal to Binary Conversion
  1726
  001 111 010 110

## Slide 20: Hexadecimal Number System
Base 16
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Representing Binary in compact form
  11011000001102 = 1B06 H
Binary to Hexadecimal Conversion
  11010110101110010110
  1101 0110 1011 1001 0110
  D 6 B 9 6
Hexadecimal to Binary Conversion
  FD13
  1111 1101 0001 0011