## Slide 1: Lecture 3 to 10
DLD
MCS1
IUB

## Slide 2: Binary Arithmetic
Binary Addition
Binary Subtraction
Binary Multiplication
Binary Division

## Slide 3: Binary Addition
Four Basic rules for binary addition

## Slide 5: Binary Subtraction
Four Basic rules for binary subtraction

## Slide 7: Binary Multiplication
Four Basic rules for binary multiplication

## Slide 8
1101 (13)
x 101 (5)
1st product term 1101
2nd product term 0000
3rd product term 1101
Product 1000001 (65)

## Slide 9: Binary Division
10
101 | 1101
101
011
000
11

## Slide 10: Signed and Unsigned Numbers
Unsigned Binary Numbers
Signed Binary Numbers
  Most significant bit represents sign
  0 represents a positive number
  1 represents a negative number

## Slide 11: Compliments of Binary
1’s complement form
2’s complement form
Binary number 01101 (13)
1’s complement 10010
+ 1
2’s complement 10011 (-13)

## Slide 12: The Gray Code
The Gray code does not have any weights assigned to its bit positions. The Gray Code
is not a positional code. The Gray code is different from the unsigned binary code as
successive values of Gray code differ by only one bit. Table 4.5 shows the Gray Code
representation of Decimal numbers 0 to 9.

## Slide 14: ASCII Code
The ASCII Code (American Standard Code for Information Interchange) is a 7-bit code
representing 128 unique codes which represent the alphabet characters A to Z in lower case
and upper case, the decimal numbers 0 to 9, punctuation marks and control characters.
• ASCII codes 011 0000 (30h) to 011 1001 (39h) represents numbers 0 to 9
• ASCII codes 110 0001 (61h) to 111 1010 (7Ah) represent lower case alphabets a to z
• ASCII codes 100 0001 (41h) to 101 1010 (5Ah) represent upper case alphabets A to Z
• ASCII codes 000 0000 (0h) to 001 1111 (1Fh) represent the 32 Control characters

## Slide 15: LOGIC GATES
The Digital Systems should be able to process or perform operations on the numbers
that are represented in the Binary Number System. The simplest operations that come to mind
are the arithmetic operations like add and subtract. There are many more operations and
functions that Digital Systems are able to perform.
Digital Logic Gates provide the basic building blocks; these Logic Gates perform
different operations on the Binary information. These Logic Gates are used in different
combinations to implement large complex systems. Digital Logic Gates are represented and
identified by unique symbols. These symbols are used in circuit diagrams to describe the
function of a digital circuit.

## Slide 17
NAND Gate
The NAND Gate performs a function that is equivalent to the function performed by the combination of an AND gate and a NOT gate
NOR Gate
The NOR Gate performs a function that is equivalent to the function performed by a combination of an OR gate and a NOT gate

## Slide 18
Exclusive-OR Gate
The Exclusive-OR Gate or XOR Gate performs a function that is equivalent to the combination of NOT, AND and OR gates. XOR gates are extensively used in digital applications; therefore XOR gates are available as basic components. Most commonly used XOR Gates have two inputs

## Slide 19
Exclusive-NOR Gate
The Exclusive-NOR Gate or XNOR Gate performs a function that is equivalent to the combination of NOT, AND and OR gates. XNOR gate is extensively used in digital applications; therefore XNOR gates are available as basic components. Most commonly used XNOR Gates have two inputs

## Slide 20: Boolean Algebra
Definitions
1. Variable
A variable is a symbol usually an uppercase letter used to represent a logical quantity.
A variable can have a 0 or 1 value.
2. Complement
A complement is the inverse of a variable and is indicated by a bar over the variable.
Complement of variable X is X’ . If X = 0 then X’ = 1 and if X = 1 then X’ = 0.
3. Literal
A Literal is a variable or the complement of a variable.
Boolean Addition
Boolean Addition operation is performed by an OR gate. In Boolean algebra the expression defining Boolean Addition is a sum term which is the sum of literals.
A + B, A + B, A’ + B’ + C’

## Slide 21
Boolean Multiplication
Boolean Multiplication operation is performed by an AND gate. In Boolean algebra the
expression defining Boolean Multiplication is a product term which is the product of literals.
A.B , A.B , A’.B’.C

## Slide 22: Laws of Boolean Algebra
The basic laws of Boolean Algebra are the same as ordinary algebra and hold true for any number of variables.
1. Commutative Law for addition and multiplication
2. Associative Law for addition and multiplication
3. Distributive Law
1. Commutative Law for Addition and Multiplication
• Commutative Law for Addition A + B = B + A
• Commutative Law for Multiplication A.B = B.A

## Slide 23
2. Associative Law for Addition and Multiplication
• Associative Law for Addition A + (B + C) = (A + B) + C
• Associative Law for Multiplication A.(B.C) = (A.B).C

## Slide 24
3. Distributive Law
• Distributive Law A.(B + C) = A.B + A.C

## Slide 25: Rules of Boolean Algebra

## Slide 26: Demorgan’s Theorems
DE Morgan's First Theorem states: The complement of a product of variables is equal to the sum of the complements of the variables.