## Slide 1
Memory Hierarchy Terminology
Miss: data needed by the processor is not found in the upper level and has to be retrieved from a block in the lower level
Miss Rate =
= 1 - (Hit Rate)
Miss Penalty is the sum of the time:
(i) to replace a block in the upper level
(ii) to deliver the block the processor

## Slide 2
Cache Memory Performance
Average Access Time:
Hit Time x Hit Rate + Miss Penalty x Miss Rate
CPU Execution Time
(CPU Clock Cycles + Memory Stall Cycles) x clock cycle time
Memory Stall Cycles
= Number of Misses x Miss Penalty
= IC x (Misses / Instructions)x Miss Penalty
= IC x [(Memory Access / Instructions)] x Miss Rate x Miss Penalty

## Slide 3
Improving Cache Performance
1. Reduce the miss penalty,
2. Reduce the miss rate,
3. Reduce miss Penalty or miss rate via Parallelism
4. Reduce the time to hit in the cache

## Slide 4
Reducing Miss Penalty
1. Multilevel Caches
2. Critical Word first and Early Restart
3. Priority to Read Misses Over write Misses
4. Merging Write Buffers
5. Victim Caches

## Slide 5
1: Multilevel Caches
Multiple levels of caches
Tradeoff between cache size (cache effectiveness and cost (access time) a small fastest memory is used as level-1 cache

## Slide 6
2: Critical word first and early restart
Early Restart: Request the words in a block in normal order
As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
Critical Word First: “Request the missed word from memory first; and the memory sends it to the CPU as soon as it arrives”
The CPU continues filling the rest of the words in the block afterwards

## Slide 7
3: Priority to Read Miss over the Write misses
Uses the Write-buffer for writing the data.
The write-buffers ensure that write to memory does not stall the processor;

## Slide 8
4: Merging Write Buffer
Small write-buffer may end up stalling processor if they fill up; and the Processor needs to wait till write committed to memory
This problem is resolved by Merging cache-block entries in the write buffer

## Slide 9
5: Victim Caches
Another way to reduce the miss penalty is to remember what was discarded as it may needed again.
This method reduces the miss penalty since the discarded data has already been fetched so it can be used again at small cast
The victim cache contains only discarded blocks because of some earlier miss

## Slide 10
Reducing Miss Rate
1. Larger Block Size
2. Larger Caches
3. Higher Associativity
4. Way Prediction and Pseudo-associativity
5. Compiler Optimization

## Slide 11
Reducing Miss Penalty and Rate via Parallelism
1. Non-blocking Caches:
2. Hardware Prefetch
3. Software (compiler controlled) Prefetch

## Slide 12
Reducing Hit Time
Small and Simple Caches
Avoiding Address translation during Indexing
Pipelined Cache Access
Trace Caches

## Slide 13
Improving Main Memory Performance
Wider Main Memory
Simple Interleaved Memory
Independent Memory Banks

## Slide 14
1: Wider Main Memory

## Slide 15
2: Interleaved Memory

## Slide 16
3: Independent Memory Banks