## Slide 1: Computer Architecture

## Slide 2
An I/O system works on the principle of producer-server model
I/O System

## Slide 3
Producer: the device that generates request to be serviced
Queue: the area where the tasks accumulate waiting to be serviced
Server: the device performing the requested service
Producer-Server model
I/O device
Server
I/O
controller
Producer
Queue
Arrivals
departures

## Slide 4
Diversity: Which I/O device can connect to the CPU
Capacity: How many I/O devices can connect to the CPU
Latency: Overall response time to complete a task
Bandwidth: Number of task completed in specified time - throughput
Performance Parameters

## Slide 5
Entry Time: the time for user to enter a command
System Response Time: time between when user enters the command and system responds
Think Time: the time from reception of the command until the user enters the next command
Time Parameters

## Slide 6
Instruction Set Architecture – ISA
Instruction Set Architecture – ISA which is the interface between the hardware-software
It plays a vital role in understanding the computer architecture

## Slide 7
Instruction Set Architecture – ISA
The design of hardware and software can’t be initiated without defining ISA
It describes the instruction word format and identifies the memory addressing for data manipulation and control operations

## Slide 8
Instruction Set Architecture – ISA
Major Choices of ISA:
Stack Architecture:
Accumulator Architecture
General Purpose Register Architecture
 Register – memory
 Register – Register (load/store)
 Memory – Memory Architecture

## Slide 9
Stack Architecture (Zero-Address machine)
TOS
ALU
Processor
Memory
. . . .
Both the operands are implicitly on the TOS
Thus, it is also referred to as Zero-Address machine
The operand may be either an input (orange shade) or result from the ALU (yellow shade)
All operands are implicit (implied or inherited)
The first operand is removed from the stack and the second operand is replaced by the result

## Slide 10
Stack Architecture (Zero-Address machine)
To execute: C=A+B
PUSH A
PUSH B
ADD
POP C
ADD instruction has implicit operands for the stack – operands are written in the stack using PUSH instruction

## Slide 11
Accumulator Architecture
ALU
Processor
Memory
. . . .
. . . .
An accumulator is a special register within the CPU that serves both as both the as the implicit source of one operand and as the result destination for arithmetic and logic operations.
Thus, it accumulates or collect data and doesn’t serve as an address register at any time
Limited number of accumulators - usually only one – are used
The second operand is in the memory, thus accumulator based machines are also called 1-address machines
They are useful when memory is expensive or when a limited number of addressing modes is to be used

## Slide 12
Accumulator Architecture
To execute: C=A+B
Load A
ADD B
Store C
ADD instruction has implicit operand A for the accumulator, written using LOAD instruction; and the second operand B is in memory at address B

## Slide 13
General Purpose Register Architecture
Many general purpose registers are available within CPU
Generally, CPU registers do not have dedicated functions and can be used for a variety of purposes – address, data and control
A relatively small number of bits in the instruction is needed to identify the register
In addition to the GPRs, there are many dedicated or special-purpose registers as well, but many of them are not “visible” to the programmer
GPR architecture has explicit operands either in register or memory thus there may exist:
- Register – memory architecture
- Register – Register (Load/Store) Architecture
- Memory – Memory Architecture

## Slide 14
General Purpose Register Architecture
Register – Memory Architecture
R1
ALU
Memory
. . . .
. . . .
R3
R2
. . . .
. . . .
Processor
One explicit operand is in a register and one in memory and the result goes into the register
The operand in memory is accessed directly

## Slide 15
General Purpose Register Architecture
Register – Memory Architecture
To execute: C=A+B
Load R1, A
ADD R3, R1, B
Store R3, C
ADD instruction has explicit operand A loaded in a register and the operand B is in memory and the result is in register

## Slide 16
General Purpose Register Architecture
Register – Register Architecture
R1
ALU
R3
R2
. . . .
. . . .
Processor
The explicit operands in memory are first loaded into registers temporarily and
Are transferred to memory by Store instruction

## Slide 17
General Purpose Register Architecture
Register – Register Architecture
To execute: C=A+B
Load R1, A
Load R2, B
ADD R3, R1, R2
Store R3, C
ADD instruction has implicit operands A and B loaded in registers
Both the explicit operands are not accessed from memory directly, i.e., Memory – Memory Architecture is obsolete

## Slide 18
General Purpose Register Architecture
Register-Register
Advantages
Simple, fixed-length instruction decoding
Simple code generation
Similar number of clock cycles / instruction
Disadvantages
Higher Instruction count than memory reference
Lower instruction density leads to larger programs

## Slide 19
General Purpose Register Architecture
Register- Memory
Advantages
Data can be accessed without separate Load first
Instruction format is easy to encode
Disadvantages
Operands are not equivalent since a source operand (in a register) is destroyed in operation
Encoding a register number and memory address in each instruction may restrict the number of registers
CPI vary by operand location

## Slide 20
General Purpose Register Architecture
Memory- Memory
Advantages
Most compact
Doesn’t waste registers for temporary storages
Disadvantages
Large variation in instruction size
Large variation in work per instruction
Memory bottleneck by memory access

## Slide 21: Evolution of Instruction Sets
Single Accumulator (EDSAC 1950)
Accumulator + Index Registers (Manchester Mark I, IBM 700 series 1953)
Separation of Programming Model from Implementation 1963-64
High-level Language Based (B5000 1963)
Concept of a Family (IBM 360 1964)
General Purpose Register Machines
Complex Instruction Sets Computer
(Vax, Intel 432 1977-80)
Load/Store Architecture
Reduced Instruction Set Computer
(Mips,Sparc,HP-PA,IBM RS6000, . . .1987)
(CDC 6600, Cray 1 1963-76)

## Slide 22
Types and Size of Operands
Types of an Operand
- Integer
- Single-precision floating point
- Character
Size of Operand
- Character 8-bit
- Half word 16-bit
- Single precision FP or Word 32-bit
- Double precision FP or 64-bit
double word

## Slide 23
Instruction Set Operations
Arithmetic and Logic
- Integer add, sub, and, or, multiply, divide
Data Transfer
- Load, store and
- Move instructions with memory addressing
Control
- Branch, Jump, procedure call and return

## Slide 24
Instruction Set Operations
System
- operating system call, Virtual Memory Management
Floating point
- Add, multiply, divide and compare
Decimal
- BCD add, multiply and Decimal to Character Conversion
String
- String move, compare and search
Graphics
- Pixel and vertex operations, compression / de-compression operations

## Slide 25
Operand Addressing Modes
- Immediate
- Register
- Direct or Absolute
- Indirect
An “effective address” is the binary bit pattern issued by the CPU to specify the location of operands in CPU (register) or the memory
Addressing modes are the ways of providing access paths to CPU registers and memory locations
Commonly used addressing modes are:

## Slide 26
Operand Addressing Modes
Immediate ADD R4, # 24H
Reg[R4] Reg[R4] + 24 H
Data for the instruction is part of the instruction itself
Used to hold source operands only; cannot be used for storing results

## Slide 27
Operand Addressing Modes
- Register ADD R4, R3
Reg[R4] Reg[R4] + Reg[R3]
Operand is contained in a CPU register
No memory access needed , therefore it is fast

## Slide 28
Operand Addressing Modes
Direct (or absolute) ADD R1,(1000)
Reg[R1] Reg[R1] + Mem[1000]
The address of the operand is specified as a constant, coded as part of the instruction
Limited address space (2operand field size) locations

## Slide 29
Operand Addressing Modes
Indirect Addressing modes
The address of the memory location where the data is to be found is stored in the instruction as the operand, i.e., the operand is the address of an address
Large address space ( 2 memory word size) available
Two or more memory accesses are required

## Slide 30
Types of Indirect addressing modes:
Register Indirect
Register Indirect Indexed
- Effective memory address is calculated by adding another register (index register) to the value in a CPU register (usually referred to as the base register)
Useful for accessing 2-D arrays
Register Indirect plus displacement
- Similarly, “based” refers to the situation when the constant refers to the offset (displacement) of an array element with respect to the first element. The address of the first element is stored in a register
Memory Indirect

## Slide 31
Operand Addressing Modes
Register Indirect ADD R4, (R1)
Reg[R4] Reg[R4] + Mem[Reg[R1]]

## Slide 32
Operand Addressing Modes
Register Indirect Indexed
ADD R4, (R1+R2)
Reg[R4] Reg[R4] + Mem[Reg[R1]+Reg[R2]]

## Slide 33
Operand Addressing Modes
Register Indirect plus displacement
ADD R4,100(R1)
Reg[R4] Reg[R4] + Mem[100+Reg[R1]]

## Slide 34
Operand Addressing Modes
Memory Indirect
ADD R4,@(R1)
Reg[R4] Reg[R4] + Mem[Mem[Reg[R1]]

## Slide 35
Operand Addressing Modes
Auto-increment
ADD R1, (R2)+
Reg[R1] Reg[R1] + Mem[Reg [R2]]
Reg[R2] Reg[R2] + d
register are automatically incremented to point to the next consecutive memory location.

## Slide 36
Operand Addressing Modes
Auto-decrement
ADD R1, (R2)-
Reg[R2] Reg[R2] - d
Reg[R1] Reg[R1] + Mem[Reg [R2]]

## Slide 37
Operand Addressing Modes
Scaled ?