## Slide 1: Computer Architecture

## Slide 2
Computer Instructions Encoding
Type of the operation
Place to find the source operand (s)
Place to store the results
Place to find the next instruction
op code
source 2
destination
next address
source 1

## Slide 3
Instruction Word Types
Variable Length
Fixed Length Format
Hybrid Length

## Slide 4
Variable Length
Operation is specified in one field, Op-code
Can support any number of operands
Typical Examples: VAX, Intel 80x86
Operation and
number of
operands
Address
Specifier # 1
Address
Specifier #n
Address
Field # n
Address
field # 1

## Slide 5
Fixed Length Format
Always has same number of operands
It generally generates the largest code size
Fields may be used for different purposes, if necessary
Typical Examples: Alpha, MIPS, PowerPC, SPARC
Operation
code
Address
field # 1
Address
field # 3
Address
field # 2

## Slide 6
Hybrid Length
Multiple formats are specified by the op-code
It generally generates the optimum code size
Typical Examples: IBM 360/370, MIPS16
Operation
code
Address
specifier
Address
field
Operation
code
Address
Specifier # 1
Address
field
Address
Specifier # 2
Operation
code
Address
specifier
Address
field # 2
Address
field # 1

## Slide 7
Comparison of instruction formats
Assume that
A single byte is used for the op code
The size of the memory address space is 16 Mbytes
A single addressable memory unit is a byte
Size of operands is 24 bits
Data bus size is 8 bits

## Slide 8
4-address instruction
Code size = 1+3+3+3+3 = 13 bytes
# of bytes accessed from memory
13 bytes for instruction fetch +
6 bytes for source operand fetch +
3 bytes for storing destination operand
Total = 22 bytes
op code
source 2
destination
next address
source 1
1 byte
3 bytes
3 bytes
3 bytes
3 bytes

## Slide 9
3-address instruction
Code size = 1+3+3+3 = 10 bytes
# of bytes accessed from memory
10 bytes for instruction fetch +
6 bytes for source operand fetch +
3 bytes for storing destination operand
Total = 19 bytes
1 byte
3 bytes
3 bytes
3 bytes
op code
source 2
destination
source 1

## Slide 10
2-address instruction
Code size = 1+3+3 = 7 bytes
# of bytes accessed from memory
7 bytes for instruction fetch +
6 bytes for source operand fetch +
3 bytes for storing destination operand
Total = 16 bytes
op code
destination
source 1
source 2
1 byte
3 bytes
3 bytes

## Slide 11
1-address instruction
Code size = 1+3= 4 bytes
# of bytes accessed from memory
4 bytes for instruction fetch +
3 bytes for source operand fetch +
0 bytes for storing destination operand
Total = 7 bytes
1 byte
3 bytes
op code
source 2

## Slide 12
0-address instruction
Code size = 1 bytes
# of bytes accessed from memory
1 bytes for instruction fetch +
6 bytes for source operand fetch +
3 bytes for storing destination operand
Total = 10 bytes
1 byte
op code

## Slide 13
Comparison of instruction count
F = (B + C)*D – E
0-Address 1-Address 2-Address 3-Address PUSH B LDA B LOAD F, B ADD F, B, C PUSH C ADD C ADD F, C MUL F, F, D ADD MUL D MUL F, D SUB F, F, E PUSH D SUB E SUB F, E MUL STA F PUSH E SUB POP F
8 5 4 3

## Slide 14
RISC - Reduced Instruction Set Computer
CISC - Complex Instruction Set Computers
OISC - One Instruction Set Computer
URISC - Ultimate Reduced Instruction Set Computer
MISC - Minimal Instruction Set Compute
NISC - No instruction set computing
Different ISA

## Slide 15
MIPS -Microprocessor Without Interlocked Pipeline Stages
RISC ISA

## Slide 16
MIPS
MIPS is a fixed length, 32/64-bit LOAD/STORE Architecture
Contains 32 GPR each of 32-bit
Supports:
3-address, reg-reg arithmetic instruction
displacement instructions with address offset 12-16 bits
immediate data 8-bit and 16-bit and
register indirect
data size 8-, 16-, 32- and 64-bit integer
64-bit IEEE 754 floating point

## Slide 17
MIPS ISA
Instructions:
Data Transfer: load, store,
register-register move
Arithmetic: add, subtract, and shift
Compare: equal, not-equal, less
Branch: PC-relative, jump and call/return

## Slide 18
MIPS ISA
Types of an Operand
- Integer
- Single-precision floating point
- Character
Size of Operand
- Character 8-bit
- Half word 16-bit
- Single precision FP or Word 32-bit
- Double precision FP or 64-bit
double word

## Slide 19
http://goo.gl/xILH8w
http://goo.gl/O0uXXv
MIPS ISA