## Slide 1: Basic building blocks of a computer
Central Processing Unit
Subsystems:
Memory
Input / Output
Buses

## Slide 2: Basic building blocks of a computer
Data
Path
CONTROL
At a “higher level” a CPU can be viewed as consisting of two sub-systems

## Slide 3
Design Process
CPU
Datapath
Control
ALU
Regs
Shifter
Nand
Gate

## Slide 4
Design Process
Datapath:
The path that facilitates the transfer of information from one part (register/memory/ IO) to the other part of the system
Control:
The hardware that generates signals to control the sequence of steps and direct the flow of information through the datapath

## Slide 5
Design Process
Top Down
complex functions (behaviors)
into more primitive functions
Bottom-up
composition of primitive building blocks into more complex assemblies
CPU
Datapath
Control
ALU
Regs
Shifter
Nand
Gate

## Slide 6
Performing an Operation
Each instruction of a program is performed in two phases:
- Instruction Fetch
- Instruction Execute
Each phase is divided into number of steps, called Micro-operation
A micro-operation is completed in a fixed time interval
The number of micro-operations is determined by the datapath implementation

## Slide 7
Datapath Implementations
The datapath is the arithmetic organ of the Von- Neumann’s stored-program organization
It consists of registers, internal buses, arithmetic units and shifters
Typically, the datapath may be implemented as:
- Unibus structure
- 2-bus structure
- 3-bus structure

## Slide 8
Unibus structure

## Slide 9
Unibus structure
It consists of a register file having 32 registers each of 32-bit and internal bus connecting the arithmetic and shifter unit to the register file
Other registers (PC, IR, MAR, MBR, A, C) have a load control line too
Additionally, registers MAR and MBR have other circuitry connecting them to the external CPU bus

## Slide 10
2-bus structure

## Slide 11
2-bus structure
Registers and arithmetic and logic unit are identical to uni-bus structure
The structure contains two internal buses called the in-bus and out-bus
The in-bus carries data to be written into registers and out-bus carries data read out from the registers
The output of ALU is directly connected to the in-bus instead of through register C as in Uni-bus structure

## Slide 12
3-bus structure

## Slide 13
3-bus structure
Registers and arithmetic and logic unit are identical to uni-bus and 2-bus structure
The structure contains three internal buses called the A-bus, B-bus and C-bus
The register file contains two read ports connected to A-bus and B- bus and one write port connected to C-bus
The registers A and C are provided as the A input and C output of ALU are connected the bus A and C respectively

## Slide 14
Instruction Operations
Instruction Fetch
Instruction Decode and Register Read
Execute
Memory (Read/write)
Write (to register file)
I fetch
ID/Reg
Exec
Mem
Wr
Ifetch
Reg/Dec
Exec
R-type

## Slide 15
Single Cycle Data Path
Clk
Cycle
I fetch
ID/Reg
Exec
Mem
Wr

## Slide 16
Multiple Cycle Data Path
I fetch
ID/Reg
Exec
Mem
Wr
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Clk
Clk

## Slide 17
Pipelining
Program Flow
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
IFetch
Dcd
Exec
Mem
WB
Time
1st Inst.
2nd Inst.
3rd Inst

## Slide 18
Pipelining
Time
(clock cycles)
I.Mem
I
n
s
t
r.
O
r
d
e
r
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I.Mem
Reg
D. Mem
ALU
I.Mem
Reg
D. Mem
Reg
ALU
I.Mem
Reg
D.Mem
Reg
ALU
D.Mem
Reg
CC1
CC3
CC2
CC5
CC4
CC6
CC8
CC7
CC9
Reg
Reg

## Slide 19
Hazards
Structural Hazards
Data Hazards
Control Hazards

## Slide 20
Structural Hazards
Attempt to use the same resource two different ways at the same time

## Slide 21
Structural Hazards
Mem
Time (clock cycles)
Instr 1 Load
Instr 2
Instr 3
Instr 4
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Instr 5
I
n
s
t
r.
O
r
d
e
r

## Slide 22
Eliminating Structural Hazards?
Structural hazards can be eliminated or minimized by either using the stall operation or adding multiple functional units

## Slide 23
Insert Stall To Avoid Structural Hazards
Time (clock cycles)
Instr 1
Instr 2
Instr 3
Stall
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Instr 4
I
n
s
t
r.
O
r
d
e
r
Bubble

## Slide 24
Structural Hazards
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type

## Slide 25
Insert Stall To Avoid Structural Hazards
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Exec
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Pipeline
Bubble
Ifetch
Reg/Dec
Exec
Wr

## Slide 26
Delay R-type’s Write by One Cycle
Clock
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Mem
Wr
Load
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Mem
Wr
R-type
Ifetch
Reg/Dec
Exec
Wr
R-type
Mem
Exec
Exec
Exec
Exec
1
2
3
4
5

## Slide 27
Data Hazards
Attempt to use item before it is ready
Instruction depends on result of prior instruction still in the pipeline
Add R1 ,R2,R3
Sub R4, R1 ,R3

## Slide 28
Data Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Add R1,R2,R3
Sub R4,R1,R3
IF
ID/RF
EX
MEM
WB
ALU
Im
Reg
Dm
Reg
ALU
Im
Reg
Dm
Reg

## Slide 29
Data Hazard Solution- Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Add R1,R2,R3
Sub R4,R1,R3
IF
ID/RF
EX
MEM
WB
ALU
Im
Reg
Dm
Reg
ALU
Im
Reg
Dm
Reg
STALL
STALL
STALL

## Slide 30
Data Hazard Solution - Forwarding
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Add R1,R2,R3
Sub R4,R1,R3
IF
ID/RF
EX
MEM
WB
ALU
Im
Reg
Dm
Reg
ALU
Im
Reg
Dm
Reg

## Slide 31
Control Hazards
Control hazard occurs when one attempt to take action before condition is evaluated

## Slide 32
Control Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ADD
BEQ
LOAD
ALU
IF
Reg
Mem
Reg
ALU
IF
Reg
Mem
Reg
ALU
Reg
Mem
Reg
IF

## Slide 33
Control Hazards Solution Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ADD
BEQ
Target Inst.
ALU
IF
Reg
Mem
Reg
ALU
IF
Reg
Mem
Reg
ALU
Reg
Mem
Reg
IF
Stall
Stall
Stall

## Slide 34
Control Hazards Solution
Redo Fetch after branch
Delayed branching
Branch prediction
Multiple Streams