## Slide 1
Pipelining

## Slide 2
Hazards
Structural Hazards
Data Hazards
Control Hazards

## Slide 3
Structural Hazards
Attempt to use the same resource two different ways at the same time

## Slide 4
Data Hazards
Attempt to use item before it is ready
Instruction depends on result of prior instruction still in the pipeline
Add R1 ,R2,R3
Sub R4, R1 ,R3

## Slide 5
Control Hazards
Control hazard occurs when one attempt to take action before condition is evaluated

## Slide 6
Data Hazards
Three Generic Data Hazards
Read After Write (RAW):
Write After Read (WAR):
Write After Write (WAW):

## Slide 7
Data Hazards
Read After Write (RAW):
add r1,r2,r3
sub r4,r1,r3

## Slide 8
Data Hazards
Write After Read (WAR):
  sub r4,r1,r3
add r1,r2,r3

## Slide 9
Data Hazards
Write After Write (WAW):
  sub r1,r4,r3
add r1,r2,r3

## Slide 10
Data Hazard Solution- Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Add R1,R2,R3
Sub R4,R1,R3
IF
ID/RF
EX
MEM
WB
ALU
Im
Reg
Dm
Reg
ALU
Im
Reg
Dm
Reg
STALL
STALL
STALL

## Slide 11
Data Hazard Solution - Forwarding
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Add R1,R2,R3
Sub R4,R1,R3
IF
ID/RF
EX
MEM
WB
ALU
Im
Reg
Dm
Reg
ALU
Im
Reg
Dm
Reg

## Slide 12
Scheduling
DIV.D F0,F2,F4
ADD.D F10,F0,F8
SUB.D F12,F8,F14

## Slide 13
Scheduling
DIV.D F0,F2,F4
ADD.D F6,F0,F8
SUB.D F8,F10,F14
MUL.D F6,F10,F8

## Slide 14
Scheduling
Static Scheduling – Compiler based
Dynamic Scheduling – Hardware based

## Slide 15
Dynamic Scheduling: Score boarding Technique
Score-
Board
Registers
Integer Unit
FP Adder
FP Divide
FP Mul
FP Mul
Data Buses
Control/status

## Slide 16
Components of Scoreboard
Instruction Status
Functional Unit Status
Register Result Status

## Slide 17
Components of Scoreboard
Instruction Status
    Issue:
Read Operand:
Execute:
Write Result:

## Slide 18
Components of Scoreboard
Functional Unit Status
Busy:
OP: e.g. ADD or SUB etc.
Registers:
  Fi – Destination register Number
  Fj, Fk – Source registers number
  Qj and Qk - FU producing source register
  Rj, Rk -source registers are ready and not

## Slide 19
Components of Scoreboard
Register Result Status
Registers associated with which FU