## Slide 1
Scoreboard
It is accomplished by dividing the ID stage into two parts
  Issue the instruction in-order
  Read operand out-of-order
Structural and data dependencies are checked at ID stage
No forwarding
Prevent WAW hazard
Wait for WAR hazard

## Slide 2
Scheduling Approach:
Scoreboard
CDC 6600 (1963)
Tomasulo's Algorithm
IBM 360/91 (1966)

## Slide 3
Control Hazards
Control hazard occurs when one attempt to take action before condition is evaluated
Stall
Redo Fetch after branch
Delayed branching
Branch prediction
Multiple Streams

## Slide 4
Delayed branching
Redefine branch behavior to take place after the next instruction by introducing other instruction (may be No-OP) which is always executed

## Slide 5
Branch prediction
The two possible predictions are:
- Predict Branch not-taken
- Predict branch taken

## Slide 6
Dynamic Branch prediction
1-bit Dynamic Branch Prediction
2-bit Dynamic Branch Prediction

## Slide 7
Dynamic Branch prediction
1-bit Dynamic Branch Prediction
If the prediction is wrong, then invert prediction-bit
In a loop, 1-bit BHT will cause two mispredictions in a row

## Slide 8
Dynamic Branch prediction
2-bit Dynamic Branch Prediction
2 bits are used to encode 4-states in the system (counter) Say:
States 00 and 01 for Predict Not-Taken
States 10 and 11 for Predict Taken

## Slide 9
2-bit Dynamic Branch Prediction

## Slide 10
(m,n) Predictor Branch prediction
• In general, (m,n) predictor means record last m branches to select between 2m history talbes each with n-bit counters
Old 2-bit BHT is then a (0,2) predictor
(2,2) predictor

## Slide 11
Branch Target Buffer (BTB)
This is accomplished by introducing a Cache that contains the address of the next instruction if branch is taken as well as not-taken
This cache is known as the Branch-Target Cache or Branch-Target Buffer (BTB)