## Slide 1
Memory System

## Slide 2
Classification Of Memory Systems
Classification of memory systems based on different attributes and their design Attributes:
Material – Semiconductor, magnetic, optical
Accessing – Random, Sequential, Hybrid
Store/Retrieve – ROM, RAM

## Slide 3
Random-Access Memory (RAM)
Key features
RAM is packaged as a chip.
Basic storage unit is a cell (one bit per cell).
Multiple RAM chips form a memory
Types of RAM
Static RAM (SRAM)
Dynamic RAM (DRAM)

## Slide 4
Static RAM (SRAM)
Each cell stores bit with a six-transistor (Diode) circuit.
Retains value indefinitely, as long as it is kept powered.
Relatively insensitive to disturbances such as electrical noise.
Faster and more expensive than DRAM.

## Slide 5
Dynamic RAM (DRAM)
Each cell stores bit with a capacitor and transistor.
Value must be refreshed every 10-100 ms.
Sensitive to disturbances.
Slower and cheaper than SRAM.

## Slide 6
SRAM vs DRAM Summary
Tran. Access
per bit time Persist? Sensitive? Cost Applications
SRAM 6 1X Yes No 100x cache memories
DRAM 1 10X No Yes 1X Main memories,
frame buffers

## Slide 7
Enhanced DRAMs
1: Fast Page Mode DRAM (FPM DRAM)
In normal DRAM, we can only read and write M-bit at time because only one row and one column is selected at any time by the row and column address
2: Extended data out DRAM (EDO DRAM)
It is the Enhanced FPM DRAM with more closely spaced CAS signals (Channel-associated signaling)

## Slide 8
Enhanced DRAMs
3: Synchronous DRAM (SDRAM)
It is driven with rising clock edge instead of asynchronous control signals.
4: Double Data Rate synchronous DRAM (DDR SDRAM)
It is Enhancement of SDRAM that uses both clock edges as control signals.

## Slide 9
Enhanced DRAMs
5: Video RAM (VRAM)
It is like FPM DRAM, but output is produced by shifting row buffer; and is
Dual ported to allow concurrent reads and writes

## Slide 10
Nonvolatile Memories
Types of ROMs
Programmable ROM (PROM)
Erasable programmable ROM (EPROM)
Electrically erasable PROM (EEPROM)
Flash memory
Firmware
Program stored in a ROM
Boot time code, BIOS (basic input/output system)
graphics cards, disk controllers.

## Slide 11
CPU-Memory Gap

## Slide 12
Memory Hierarchy
memory hierarchy is organized into several levels
Fast memory is expensive and cheap memory is slow
Organize memory in hierarchy, based on the Concept of Caching; and Principle of Locality

## Slide 13
Memory Hierarchy
Control
Datapath
Memory
Processor
Memory
Memory
Memory
Memory
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:

## Slide 14
Memory Hierarchy

## Slide 15
Hierarchy List
Register File Level 0 Datapath
L1 Level 1 Cache on Chip
L2 Level 2 External Cache
Main memory Level 3 System Board DRAM
Disk cache Level 4 Disk drive
Disk Level 5 Magnetic disk
Optical Level 6 CDs etc-
Tape Level 7

## Slide 16
Principle of Locality
Programs access a relatively small portion of the address space at any instant of time
Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon

## Slide 17
Principle of Locality
sum = 0;
for (i = 0; i < n; i++)
sum + = a[i];
return sum;
Spatial Locality:
All the array-elements a[ i ]
All the instructions of the loop
Temporal Locality
The data, sum

## Slide 18
Cache Organization
Main Memory

## Slide 19
Cache Organization

## Slide 20
Cache Addressing – Direct Addressing
8
9
14
3
4
10
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
4
10
00
01
10
11
0000
0100
1000
1100
0001
0101
1001
1101
0010
0110
1010
1110
0011
0111
1011
1111
00yy
01yy
10yy
11yy
xx00
xx01
xx10
xx11

## Slide 21
Memory Hierarchy Terminology
Hit: the data the processor wants to access appears in some block in the upper level
Hit Rate: the fraction of memory access that are found in the upper level
Hit Time: Time to access the upper level which consists of
(i) RAM access time
(ii) Time to determine if this is hit or miss

## Slide 22
Memory Hierarchy Terminology
Miss: data needed by the processor is not found in the upper level and has to be retrieved from a block in the lower level
Miss Rate = 1 - (Hit Rate)
Miss Penalty is the sum of the time:
(i) to replace a block in the upper level
(ii) to deliver the block the processor

## Slide 23
Cache Hit and Miss
Request
14
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
12
d
0
1
2
3
4*
CPU

## Slide 24
Placement and Replacement Policies
Cache design that defines the relationship of cache addresses with the higher level memory addresses
Placement policy that determines where can the new block go? And
Replacement policy that defines which block should be evicted?

## Slide 25
Types of misses
Cold (compulsory) miss
occurs when the cache is empty; at the beginning of the cache access
Capacity miss
occurs when the set of active cache blocks (working set) is larger than the cache
Conflict miss
occurs when the level k cache is large enough, but multiple data objects all map to the same level k block.