## Slide 1: Specification of Standard Track
Prepared By:
Shafqat Ali

## Slide 2: Standard Track

## Slide 3: Standard Track
Standard Track distance is 400 meter.
One Standard Track has 3 parts.
(i) Straight (ii) Curve (iii) diameter
One Standard Track has 8 lanes.
(The difference between two lines is called lane)
Now a days Standard Track has maximum 9 lanes and minimum 6 lanes.
Ideal length of Standard track 170 meters.
Ideal width of Standard track 93 to 95 meters.

## Slide 4: Standard Track
Ideal Straight of Standard track 79 to 85 meters.
Ideal curve of Standard track 137 to 139 meters.
1st lane difference is 1.12 meters.
Other all lanes difference is 1.22 meters.
The 1st player run 0.30 meter away from inside of line.
The other player run 0.20 meter away from inside of line.

## Slide 5: Standard Track
Example 1
Lay out the Standard Track with the help of 81 m Straight.
Solution :
Total Distance of Track = 400 m
Straight = 81 m
Total Straight = 81 + 81 = 162 m
Track Distance = Total Straight + Total Curve

## Slide 6: Standard Track
Total Curve ( C ) = Total Distance – Total Straight
C = 400 – 162
C = 238 m
Where C = 2∏R (R = Radius )
R = C × 1/ 2∏ (∏ = 22/7 )
R = 238 × ½ × 7/22
R = 37.86 m
Running Radius = 37.86 m

## Slide 7: Standard Track
Marking Radius = Running Radius – 0.30 m
Marking Radius = 37.86 – 0.30
Marking Radius = 37.56 m
Diameter = 2 × R
Diameter = 2 × 37.56
Diameter = 75.12 m
Width = Diameter + Lanes
Width = 75.12 + 16(1.22)
Width = 75.12 + 19.52
Width = 94.64 m
If the width of ground is 94.64 m then we mark the Standard Track of 400 m with the help of 81 m Straight.

## Slide 8: Standard Track
Example 2
Lay out the Standard Track with the help of 84 m Straight.
Solution :
Total Distance of Track = 400 m
Straight = 84 m
Total Straight = 84 + 84 = 168 m
Track Distance = Total Straight + Total Curve

## Slide 9: Standard Track
Total Curve ( C ) = Total Distance – Total Straight
C = 400 – 168
C = 232 m
Where C = 2∏R (R = Radius )
R = C × 1/ 2∏ (∏ = 22/7 )
R = 232 × ½ × 7/22
R = 36.90 m
Running Radius = 36.90 m

## Slide 10: Standard Track
Marking Radius = Running Radius – 0.30 m
Marking Radius = 36.90 – 0.30
Marking Radius = 36.60 m
Diameter = 2 × R
Diameter = 2 × 36.60
Diameter = 73.22 m
Width = Diameter + Lanes
Width = 73.22 + 16(1.22)
Width = 73.22 + 19.52
Width = 92.74 m
If the width of ground is 92.74 m then we mark the Standard Track of 400 m with the help of 84 m Straight.

## Slide 11: Standard Track
Example 3
Lay out the Standard Track with the help of 80 m Straight.
Solution :
Total Distance of Track = 400 m
Straight = 80 m
Total Straight = 80 + 80 = 160 m
Track Distance = Total Straight + Total Curve

## Slide 12: Standard Track
Total Curve ( C ) = Total Distance – Total Straight
C = 400 – 160
C = 240 m
Where C = 2∏R (R = Radius )
R = C × 1/ 2∏ (∏ = 22/7 )
R = 240 × ½ × 7/22
R = 38.18 m
Running Radius = 38.18 m

## Slide 13: Standard Track
Marking Radius = Running Radius – 0.30 m
Marking Radius = 38.18 – 0.30
Marking Radius = 37.88 m
Diameter = 2 × R
Diameter = 2 × 37.88
Diameter = 75.76 m
Width = Diameter + Lanes
Width = 75.76 + 16(1.22)
Width = 75.76 + 19.52
Width = 95.28 m
If the width of ground is 95.28 m then we mark the Standard Track of 400 m with the help of 80 m Straight.

## Slide 14: Standard Track
Example 4
Lay out the Standard Track with the help of 95 m width.
Solution :
Width of the Ground = 95 m
Diameter = Width of the Ground – Lanes
Diameter = 95 – 16 (1.22)
Diameter = 95 – 19.52
Diameter = 75.48

## Slide 15: Standard Track
Diameter = 2 × Radius
Marking Radius = Diameter/2
Marking Radius = 75.48/2
Marking Radius = 37.74 m
Actual Radius = Marking Radius + 0.30 m
Actual Radius = 37.74 + 0.30
Actual Radius = 38.04 m

## Slide 16: Standard Track
C = 2∏R (R = Radius )
C = 2 × 22/7 × 38.04
C = 1673.76/7
C = 239.1085 m
Total Distance of Track = 400 m
Total Distance of Track = Total Straight – Total curve
Total Straight = Total Distance – Total Curve
Total Straight = 400 – 239.1085
Total Straight = 160.8914
One Straight = 160.8914/2
One Straight = 80.4457 m

## Slide 17: Standard Track
Length = Straight + 2R + Lanes
Length = 80.4457 + 2(38.04) + 16(1.22)
Length = 80.4457 + 76.08 + 19.52
Length = 176.0457
If the length of ground is 176.0457 then we mark the Standard Track of 400 m with the help of 95 m width.

## Slide 18: Standard Track
Example 5
Lay out the Standard Track with the help of 93 m width.
Solution :
Width of the Ground = 93 m
Diameter = Width of the Ground – Lanes
Diameter = 93 – 16 (1.22)
Diameter = 93 – 19.52
Diameter = 73.48

## Slide 19: Standard Track
Diameter = 2 × Radius
Marking Radius = Diameter/2
Marking Radius = 73.48/2
Marking Radius = 36.74 m
Actual Radius = Marking Radius + 0.30 m
Actual Radius = 36.74 + 0.30
Actual Radius = 37.04 m

## Slide 20: Standard Track
C = 2∏R (R = Radius )
C = 2 × 22/7 × 37.04
C = 232.82 m
Total Distance of Track = 400 m
Total Distance of Track = Total Straight – Total curve
Total Straight = Total Distance – Total Curve
Total Straight = 400 – 232.82
Total Straight = 167.17
One Straight = 167.17/2
One Straight = 83.58 m

## Slide 21: Standard Track
Length = Straight + 2R + Lanes
Length = 83.58 + 2(37.04) + 16(1.22)
Length = 83.58 + 74.08 + 19.52
Length = 177.18
If the length of ground is 177.18 then we mark the Standard Track of 400 m with the help of 93 m width.

## Slide 22
THANK YOU!!!