## Slide 1: Capsule Filling Machine
20/06/2019

## Slide 2: Capsule Overview
Capsule is an EDIBLE solid dosage form in which the drug (with or without excipients) is enclosed in a hard or a soft soluble shell.
The word capsule is derived from the latin word that means “small box”
Capsules Types
Hard Gelatin Capsules
Filled with powder ingredients
Soft Gelatin Capsules
Filled with Liquid ingredients
Filled with semisolid ingredients
Introduction

## Slide 3: Hard Capsule Production

## Slide 4
Methods of Filling Hard Gelatin Capsules:
Punch Method
Capsule Machines
manual and semi-automatic filling machines
automatic filling machines
Used by the pharmacists To hand fill capsules at the prescription counter

## Slide 5: Punch Method
The ingredients are triturated to the same particle size and then mixed by geometric dilution. The powder is placed on the powder paper or ointment slab and smoothed with spatula to a height approximately half the length of the capsule body.
The base of the capsule is held vertically and the open end is repeatedly pushed or "punched" into the powder until the capsule is filled; the cap is then replaced to close the capsule.
Each filled capsule is weighed using an empty capsule as a counterweight.
Powder is added or removed until the correct weight has been placed in the capsule. The filled capsule is tapped so that no air spaces are visible within the contents.
Hard Capsule Manufacturing

## Slide 6: Manual Filling Machines
Capsules machines are available for filling 50, 100, and 300 capsules at a time.
Each manufacturer's machine is slightly different in its operation, but the series of operations is the same.

## Slide 7: The parts of a capsule filling machine are:
  Scraper
Capsule Loader
Cap Holder
Base Plates
Manual Filling Machines
  Comb

## Slide 8
To begin, the cap holder is placed on the base plates
Then the capsule loader is filled with capsules.
The loader will align the capsules so that the bottoms faces down in the base plate.
The loader is used twice, since it only can hold 50 capsules at a time
The cap holder contains the caps, and the bodies of the capsules are in the base plates.
Manual Filling Machines

## Slide 9
Tight the retention screws on the base plates to hold the capsule bodies as the cap holder is removed. So the caps will not fall out
The cap holder is removed taking the caps with it
while the capsule bodies remain in the base plates.
Loose the retention screws which allows the capsule bodies to completely descend into the base plates.
Manual Filling Machines

## Slide 10
Manual Filling Machines
The powder mixture is poured onto the base plates, and the scraper is used to spread the powder over the capsules
The comb is used to pack the capsules.
The cap holder is fitted back onto the base plates, and the capsule cap are pushed only the capsule bodies.
When the cap holder is removed, the capsules are removed from the base plates...
Finally capsules are ready to be analyzed and dispensed.

## Slide 11: Semiautomatic Filling Machines
The auger feeding system is used:
Empty capsules are fed into a pair of ring holders, the caps being retained in one half and the bodies in the other.
The body holder is placed on a variable-speed revolving turntable;
the powder hopper is pulled over the top of this plate, which revolves underneath it.
In the hopper a revolving auger forces powder down into the capsule bodies.
  The weight of powder filled into the body is dependent mainly upon the time the body is underneath the hopper during the revolution of the plate holder.
  The output range varied from 5000 to 150000 per hour depending on the type of motion of the machine used (Intermittent or continuous motion)

## Slide 12
Automatic Filling Machine
Dosator-Type Machines
Tamping Finger and Dosing Disc

## Slide 13: Dosator -Type Machines
Most frequently used type in industry. This consists of a dosing tube inside which there is a movable spring-loaded piston, thus forming a variable-volume chamber in the bottom of the cylinder.
The tube is lowered open end first into a bed of powder, which enters the tube to fill the chamber and form a plug. This can be further consolidated by applying a compression force with the piston.
The assembly is then raised from the powder bed and positioned over the capsule body.
The piston is lowered, ejecting the powder plug into the capsule body.
The weight of powder filled can be adjusted by altering the position of the piston inside the tube and by changing the depth of the powder bed.
A dosing tube or dosator -type machine

## Slide 14: Tamping Finger and Dosing Disc
The dosing disc forms the bottom of a revolving powder hopper.
This disc has in it a series of sets of accurately drilled holes in which powder plugs are formed by several sets of tamping fingers.
At each position the fingers push material into the holes, building up a plug before the index on to the next position.
At the last position the finger pushes the plug through the disc into a capsule body.
The powder fill weight can be varied by the amount of insertion of the fingers into the disc, by changing the thickness of the dosing disc, and by adjusting the amount of powder
in the hopper. The machines that use this system are all intermittent in motion
A dosing disc and tamping finger machine

## Slide 15: Capsule Sealing
One manufacturer makes distinctive-looking capsules by sealing them with a colored band of gelatin.
Capsules may also be sealed through a heat-welding process that fuses the capsule cap to the body through the double wall thickness at their juncture.
Another process uses a liquid wet-ting agent that lowers the melting point in the contact areas of the capsule’s cap and body and then thermally bonds the two parts using low temperatures

## Slide 16: Cleaning and Polishing Capsules
On a small scale, capsules may be cleaned individually or in small numbers by rubbing them with a clean gauze or cloth.
On a large scale, many capsule-filling machines are affixed with a cleaning vacuum that removes any extraneous material from the capsules as they exit the equipment.

## Slide 17: Conclusion and Summary

## Slide 18: Thank You