## Slide 1: PACKAGING LINE AND EQUIPMENT OF PHARMACEUTICAL INDUSTERY

## Slide 2: Index:
Packaging – introduction
Packaging line:
Manual vs. automated
Process of packaging line
factors that defines automated packaging machine better than manual packaging
Packaging machinery:
Function of packaging machines
Type of machines
Conclusion
References

## Slide 3: introduction:
What dose packaging means?
is the technology of enclosing or protecting products for distribution, storage, sale and use.
Function of packaging :
Protection and preservation
Product information
Promotion of corporate identity
Forms part of sales promotion
Adds to appeals of product

## Slide 4: Packaging line:
Packaging Line is a coordinated system, formed by single or multiple equipment, that performs packaging of goods for transport, warehousing, logistic and sale.

## Slide 5: Manual vs automated packaging line
There are two major processes done in packaging that are manual and automated. Some companies use manual process while some use automated process for packaging. There is one major difference between manual and automated packaging process that manual packaging is the complex process as compared to automated packing process. The automatic packaging process use packaging machines but manual packaging processes is done manually.

## Slide 6: factors that defines automated packaging machine better than manual packaging.
 | manual | Automated
Level of production | Speed and time manufactural loss | provide more speed and produce additional packaged product in a day
Packaging line impact | manual process not provides greater speed and high impact. | automated packaging procedure gives highest and based on stability between gains in speed and price.
Packaging cost | cheaper | More expensive than manual
Packaging operation | manual packaging operations provides complex packaging and un-reliable results. | Packaging automation process provides reliable results.

## Slide 7: Packaging line process
filling equipment
Labeling / Serialization Equipment
packaging Equipment
palletizer
Putting goods – tablet, liquid, powder, item etc. into unit container – box, bottle etc
Label or serialize unit container
Palletization for storage and transportation
Putting unit container into bigger container – could be several levels

## Slide 8: Packaging equipment
Packaging machinery is used throughout all packaging operations, involving primary packages to distribution packs. This includes many packaging processes: fabrication, cleaning, filling, sealing, combining, labeling, overwrapping, palletizing.
Function:
Improve labor productivity
Ensure packaging quality.
Handle specialized requirements, such as vacuum packaging, inflatable packaging, skin packaging and pressure filling.
Reduce labor and improve working conditions for bulky/heavy products.
Protect workers from health effects brought by dust, toxic/hazardous products and prevent environmental contamination.
Reduce packaging costs and save storage costs for loose products, such as cotton, tobacco, silk, linen, etc., by simply using compression packaging.
Reliably ensure product hygiene by eliminating hand contact with food and medicines.

## Slide 9: Type of machineries
General filling machines:
1.Tablet fillers
2.Pressure filling
sealing machines:
3.Blister packaging machine
4.Vacuum packaging machine
Labeling:
5. Wrap labeling machine
6. Top labeling machine
End of line section:
7.Sleeve wrappers and bundles
8.Palletizing

## Slide 10: 1- tablet filler
Designed for products that’s counted by pieces instead of weight. These are designed for small bottles, but the hopper of filler is set up to permit scan counting of tablets.

## Slide 11: 2-pressure filler
pressure filler can be configured for automatic or semi-automatic operation with from 2 - 14 heads (depending on bottle size) and from one ounce to 2.5 gallon.
works as follows:
Conveyor brings the bottles into position
Conveyor stops
Heads lower into bottles
Variable speed pump starts filling with overflow returning to the supply tank as bottles are filled
After filling pump stops to relieve pressure
Conveyor starts and another set of bottles indexes in, as filled bottles index out

## Slide 12: 3. Blister packaging machines
Blister packaging machines this equipment is mainly used for packaging disposable medical products, such as disposable syringe, needle, infusion set, and medical health consumable.

## Slide 13: 4. Vacuum packaging
Vacuum packaging method of packaging that remove the air from the package .
This specific machine has a sealing length of 1020 mm
Used for solid, granule and fluid

## Slide 14: 5. Wrap labeling
Wrap Labeling Machines are built for labeling round products with either a partial wrap or full wrap. Wrap labeling machines range from semi-automatic labeling machines to high speed labeling machines capable of running up to 260 bottles/minute.

## Slide 15: 6. Top labeling
Top label applicators are by far the most versatile equipment offer. Whether you are labeling bakery goods, tops of jars, boxes, or lay flat goods like chipboard or books, this equipment is up to the task.

## Slide 16: 7. Sleeve wrapping machines
Sleeve wrapping machines are distinguishable from other types of shrink bundles in that the two ends of the package have an opening (often called "bulls eyes”) and the products are bundled together for shipment.

## Slide 17: 8.Palletizing
automatic palletizers arrange boxes and bags on pallet. There are several types of palletizer equipment including low table, high table and robotic. In most applications each tier is loaded ninety degrees to the previous tier in order to better stabilize the load.

## Slide 18: References
www.busch-machinery.com
https://abltechnology.wordpress.com
https://www.pharmaceuticalmachinery.in
Books:
Yam, K.L., "Encyclopedia of Packaging Technology", John Wiley & Sons, 2009,
Soroka, W, "Fundamentals of Packaging Technology", Chapter 19 – Packaging Machinery, IoPP, 2002,