## Slide 1: SEMI-SOLID PREPARATIONS (ointments, creams, gels, pastes)

## Slide 2: Topics to be covered..
Definitions & basic introduction
Industrial processing
Storage and packaging conditions
References

## Slide 3: Definition & Basic introduction
Semi solid pharmaceutical system comprise a body of product, which when applied to skin or accessible mucous membrane it tends to alleviate or treat a pathological condition or other protection from harmful environment.

## Slide 4: Ideal properties of semi solid preparations

## Slide 5: Ointments
Are homogenous, translucent, viscous, semi solid product ,primarily made of oil, intended for external use to skin or mucous membranes.
It may be medicated (active drug ) or not.
They soft and melt at body temperature.
Uses:
Emollient
Application for
active ingredient on skin.
Occlusive.
Examples:
Garamycin, nitro-bid, vira-A

## Slide 6: Ointment CONT..
Ointment Bases
Oleaginous Bases ( mineral oils, petrolatum)
Absorption Bases ( hydrophilic petrolatum )
Water-Removable Bases
Water-Soluble Bases
Preparation of Ointments
Incorporation
Fusion
Compendial Requirements for Ointments
Microbial Content
Minimum Fill
Packaging, Storage, and Labeling
Additional Standards

## Slide 7: Equipments used in preparing ointments
Incorporation:
mix together ( mortal & pestle, spatula & slab ).
Roller mill
Levigating the powder ( reduction of size in suspending agent in compatible with ointment base ).
Fusion:
In a porcelain dish, all or some components of the ointment are melted together and cooled with constant stirring until congealed, then add the non-melting substances as the ointment is being cooled and stirred.

## Slide 8: Equipments used..

## Slide 9: Creams
Viscous semi solid emulsion with opaque appearance as Contrasted with translucent ointments.
Consistency depends on whether the cream is W/O or O/W.

## Slide 10: Pastes
Contains high percentage of insoluble solid (usually 50% or more)
How to make them?
Pastes are usually prepared by incorporating solids directly into congealed system by levigation with a portion of base to form paste like mass.
To achieve this you need only mortal and pestle.
They have good adhesion on skin & less greasy.

## Slide 11: Gel / jelly
Gels are aqueous colloidal system of hydrated forms of insoluble medicaments.
We use gelling agent in it ( tragacanth, gelatin )
Jellies are transparent or translucent non greasy semisolid and contain more water than gels.
We use a thickening agent here ( carbomer , propylene glycol )
Used for medication, lubrication and carrier for spermicidal agents to be used intra vaginally with diaphragm.

## Slide 12: Gel / jellies
Equipments used:

## Slide 13: Formulation of semi-solids
Ingredients used to prepare semi-solid dosage forms:
Active pharmaceutical ingredients
Bases :
  compatible with skin PH
  non-irritating, good stability
Preservatives ( methyl hydroxy benzoate )
Humectants:
  Increase the solubility of active ingredients
  to elevate its skin preparation
  Elevate the hydration of the skin
Anti oxidants
Emulsifier ( alkyl sulphate, quaternary amonium comp., polyoxy ethylene ).
Gelling agent
Buffers ( sodium acetate, sodium citrate ).

## Slide 14: Mixing of oil and aqueous phase
Sigma blade mixer
The mechanism of mixing is shearing. The sigma shaped blades creates high shear.
Advantages:
  It creates a minimum dead space during
  mixing.
  It is used for wet granulation process.
Disadvantages:
    It works at a fixed speed.

## Slide 15: Mixing of oil and aqueous phases
Colloidal miller
It consists of two steel discs, one disc rotates and another one is stationary. When the material is passed through these discs they get sheared. Thus coarse particles are break down to small particles due to shear.
Advantages:
  It can be used in the production
  of sterile products.
Disadvantages:
    It is not used for dry milling.

## Slide 16: Packaging for ointments ( jars & tubes )
Prepare the ointment
Select an ointment jar that will just hold all the formulation.
Begin by taking some of the ointment and fill the bottom of the jar.
Use spatula to put ointment into cervices.
stab the spatula into the ointment couple of times to reveal air.
Wipe off ointment from the threads of the jar.
Cap the jar.
Sanitize the equipments with detergents flushed with chlorinated water followed by bacteria-free water rinse.
Label the final package.
Storage:
Store it in a tightly closed and completely filled container.
Changing temp. can lead to crystallization.
Usually dispensed in jars of glass or plastic material or collapsible tubes.

## Slide 17: Packaging for ointments ( jars & tubes )
Tube filling machine

## Slide 18: References
Remington: the science and practice of pharmacy.
Pharmaceutics: the study of dosage form design by Aulton
Ansel’s pharmaceutical dosage form and drug delivery system