## Slide 1: HEZARDS
  WHAT DOES A INDUSTRIAL HAZARD MEANT?
Hazard is a term associated with a substance,
That is likely to cause injury to a personnel, (or)
One which may lead to loss of property, products etc;
(or)
A substance that might prove fatal to the personnel.
  DEFENITION OF INDUSTRIAL SAFETY
Industrial safety refers to reduce the risk of injury or loss and danger to persons, property from the industrial hazards.

## Slide 2
Toxic corrosive chemicals, fire explosions and personnel falling into accident are major health and safety hazards encountered in the operations of chemical and pharmaceutical industries.
Identification of hazards and employing protective measures to control the hazards are important to protect the people from their consequences.

## Slide 3: OBJECTIVES OF INDUSTRIAL SAFETY
Understand the harmful effects of industrial hazards
Define the relationship between hazard and risk
Explore the routes of exposure to industrial hazards
Shed lights on type of toxicity by industrial hazards
Know the most toxic environmental hazardous substances.

## Slide 4: INDUSTRIAL HAZARD V/S RISK
Hazard is the potential of a substance to cause damage.
Toxicity is the hazard of a substance which can cause poisoning.
Risk is a measure of the probability that harm will occur under defined conditions of exposure to a chemical. (Patrick et al., 1986).

## Slide 5: WHAT IS AN ACCIDENT ???
“An accident is an unplanned & uncontrolled event which causes or is likely to cause an injury”.
It is some thing which un-expected , un-predictable or intended or not desired.
An accidents may cause a result of some unsafe activity, act, working condition etc ,…..
Notes: 5

## Slide 6
Hazards may arise when impure or contaminated chemicals are used.
By products may accumulate relatively high concentrations in parts of the plant and cause un expected effects.
In pharmaceutical industry most of the dermatitis can be attributed to synthetic drugs, especially phenothiazines.

## Slide 7: Industrial Hazards
Large exposures to chemicals can affect human health directly or indirectly.
disrupting ecological systems that exist in rivers, lakes, oceans, streams, and wetlands
The release of chemicals into the environment can have global impacts
Chemicals can be transported throughout the atmosphere and are not bound by borders

## Slide 8: Industrial Hazards
All the changes that occur in the environment affect people.
Ultimately people can be exposed to any substance that enters the environment

## Slide 9: Routes of Industrial hazards Entry into the Body
There are three main routes by which hazardous chemicals enter the body:
absorption through the respiratory tract through inhalation.
absorption or injection through the skin or eyes.
absorption through the digestive tract. This can occur through eating or smoking with contaminated hands or in contaminated work areas.

## Slide 10: Types of Hazards Toxicity
Acute poisoning is characterized by rapid absorption of the substance and the exposure is sudden & severe. Normally, a single large exposure is involved. Examples: carbon monoxide or cyanide poisoning.
Chronic poisoning is characterized by prolonged or repeated exposures of a duration measured in days, months or years. Symptoms may not be immediately apparent, but tend to build up in the body as a result of chronic exposure. The effects are not seen until a critical body burden is reached. Examples: lead or mercury poisoning or pesticide exposure.

## Slide 11: 2.TYPES OF HAZARDS
Fire hazards
Chemical hazards
Electrical hazards
Mechanical hazards and
pharmaceutical hazards.

## Slide 12: FIRE HAZARDS
Fire:
The self-sustaining process of rapid oxidation of a fuel which produces heat and light.
Fire is an exothermic chemical reaction between oxygen and fuel at certain temperature.
Three things essential for the combustion of fire are
Fuel (any combustible material)
Oxygen (At concentrations above 23 % in air, the situation becomes dangerous due to the increased fire hazard)
Temperature.

## Slide 13: SOURCES OF FIRE HAZARDS
Fuels include solids, liquids, vapours and gases.
solid fuels
wood, fabrics, synthetic materials, packing materials, papers
etc.,.
Liquid fuels
flammable liquids (e.g., nitrophenol, ammonium nitrate and pottassium chlorate, paint and oil soaked rags, cotton or cellulose soaked with sulphuric acid etc.,.).
Other sources include flame, sparks, spontaneous ignition and self combustible chemicals. (Khanna,1992).

## Slide 14
Causes
Smoking in the factory
Defective heating equipment, electrical equipment & wiring.
Explosive gas leakage.
Inadequate protection of electric motors
Sparking of electric wires & equipment
Fire & explosion hazards

## Slide 15: DETECTION OF FIRE HAZARDS
Many automatic fire detection systems are used today in industry.
Some include
Thermal expansion detectors,
Heat sensitive insulation,
Photoelectric fires,
Ionization or radiation sensors and
Ultraviolet or I .R detectors.
These sound an alarm through which fire flames are detected.

## Slide 16: FIRE ALARMS
FIRE SENSORS

## Slide 17: PREVENTION OF FIRE HAZARDS
Well planned design and layout
Proper ventilated systems
Chemical data sheets
Proper training of personnel
Proper maintenance of surroundings
use of fire extinguishers, alarms ,sensors, detectors
Fire fighting equipment
Sprinkler systems

## Slide 18
Halotron 1 Fire extiguisher
Non-Magnetic stored pressure deionized water mist fire extinguisher
ABC Dry chemical fire extinguisher
Carbon dioxide (CO2) Portable fire extinguisher
K Class Wet chemical extinguisher.
Spinkler systems

## Slide 19: CHEMICAL HAZARDS
Many chemicals can cause severe burns, if these coming to contact with living tissue or other routes like inhalation.
  Living tissue may be destroyed by chemical reactions such as dehydration, digestion, oxidation etc.
Eye and mucus membrane of the throat are particularly susceptible to the effect of corrosive dust, mist and gases.
Chloroform, benzene, chlorinated hydro carbons, low boiling fractions of petroleum are some of the common organic solvents used in pharmaceutical industry.(Muir,2002).

## Slide 20: SOURCES OF CHEMICAL HAZARDS
AIR BORN TOXICS
Irritants
Ipecac,podophyllumetc .,.
Asphyxiants
Carbondioxide, monoxide, methane, ethane, hydrogen cyanide,
hydrogen sulphide, helium,nitrogen etc.,.
Narcotics/anaesthetics
Acetone, ether, chloroform, methyl-ethyl ketone etc.,.
CARCINOGENS
Coaltar, cresote oil, anthracene oil, parafin oils, chromium,
nickel, cobalt etc.,.

## Slide 21: Heavy Metals
Metals comprise three-fourths of the elements in the periodic table.
A few of the metals are essential for life. Most of the known metals are quite toxic to living organisms when present in excess.

## Slide 22: Exposure to Heavy Metals
Breathing vapors
Industrial Activities & Waste
Contaminated Solis
Notes: 22
Heavy metals and AhR ligands are common environmental co-contaminants of hazardous waste sites and are co-released from sources such as fossil fuel combustion and municipal waste incineration and as components of tobacco. Both AhR ligands and heavy metals are ranked highly as the most hazardous xenobiotics in the environment, prepared by Canadian Environmental Protection Act (CEPA) and the Agency for Toxic Substances and Disease Registry and the Environmental Protection Agency.

## Slide 23: Mechanisms of Heavy Metals Toxicities
Inhibition of heme biosynthesis, heme is the essential structural component of hemoglobin, myoglobin and cytochromes (Pb)
Binds to sulfhydryl groups (-SH groups) of proteins and enzymes.
Interfering with essential metals ions (Zn, Ca, Na) on their channels

## Slide 24: Treatment strategies
Removal of the subject from the source(s) of exposure.
Treatment with chelating agents, such as EDTA, Succimer, and Cysteine and N-Acetyl Cysteine (NAC)
Administration of some antioxidants, Vitamin C, E

## Slide 25: Formaldehyde
Formaldehyde is also known as methanal, is a gas with a strong pungent smell.
Formaldehyde readily results from the incomplete combustion of carbon-containing materials.
Formaldehyde is produced industrially by the catalytic oxidation of methanol. It may be found in the smoke from forest fires, in automobile exhaust, and in tobacco smoke.
Formaldehyde is readily oxidized by atmospheric oxygen to form formic acid

## Slide 26: Formaldehyde
Most formaldehyde is used in the production of polymers and other chemicals, in many construction materials, including carpet, and spray-on insulating foams.
formaldehyde is one of the more common indoor air pollutants.
Formaldehyde is classified as a probable human carcinogen by the U.S. Environmental Protection Agency. The International Agency for Research on Cancer

## Slide 27: Formaldehyde Toxicities
Carcinogenicity: although the risk is small or non-existent, the possibility that formaldehyde is a human carcinogen cannot be excluded.
Urinary Tract Disease: dysuria, suprapubic pain, ureteric and bladder fibrosis, hydronephrosis, vesicoureteral reflux
Hypersensitivity : Hypersensitivity to formaldehyde has had several manifestations
  acute exacerbation of eczema after injection of hepatitis B vaccine containing formaldehyde
  Skin pruritus, burning, and redness

## Slide 28: Treatment of Formaldehyde Toxicities
Treat signs and symptoms; no known antidote
Contaminated skin should be washed with soap and water
After ingestion water, milk, and/or charcoal, should be given
Acidosis, resulting from metabolism of formaldehyde to formic acid, may require IV NaHCO3 or Na lactate.
If seizure occurred, IV benzodiazepines or barbiturates could be given.

## Slide 29: Methanol
Methyl alcohol is used as a pharmaceutical and industrial solvent.
It is also used as `wood naphtha' to denature ethanol in the preparation of industrial methylated spirits.
Methyl alcohol is also used as an extraction solvent in food processing.
Methyl alcohol is readily absorbed from the gastrointestinal tract and distributed throughout the body fluids.

## Slide 30: Methanol Toxicity
Characteristic symptoms of methyl alcohol poisoning are caused by toxic metabolites and develop after a latent period of about 12 to 24 hours, or longer
metabolic acidosis with rapid, shallow breathing
visual disturbances which often proceed to irreversible blindness,
severe abdominal pain, gastrointestinal disturbances, pain in the back and extremities
coma which in severe cases may terminate in death due to respiratory failure or, rarely, to circulatory collapse

## Slide 31: Treatment of Methanol Toxicities
Gastric lavage may be considered if the patient presents within 1 hour of ingesting methyl alcohol
Activated charcoal is probably of little use as it does not absorb significant amounts of methyl alcohol
Metabolic acidosis should be corrected immediately with intravenous sodium bicarbonate.
Haemodialysis may be indicated to increase the removal of methyl alcohol and its toxic metabolites

## Slide 32: SAFETY ASPECTS IN CHEMICAL HAZARDS
Application of barrier creams before commencing the work has been found useful in protecting individuals from hazardous
chemicals.
While using the high vapor pressure solvents and grinding of
vegetable drugs (e.g., capsicum and podophyllum) safety goggles are to be worn. Because these will effects the eyes.

## Slide 33
We must know the exposure limits and toxicity of different chemicals.
chemicals | Exposure limit (ppm)
Ethyl alcohol | 1000ppm
acetone | 1000ppm
Methyline chloride | 125ppm
Isopropyl alcohol | 400ppm

## Slide 34: MECHANCAL HAZARDS
These are associated with powers-driven machine, whether
automated or manually operated by steam, hydraulic and/or
electric power introduced new hazards into work place.
Mechanical hazards are exacerbated by the large number and different designs of equipment, crowded work place conditions and different interaction between workers and equipment.
Hazardous electrical energy must be released or controlled before working on active equipment.
High sound levels may be generated by manufacturing equipment (e.g., ball mill) there by increasing their exposure to noise.
Injuries like cutting, tearing, shearing, puncturing and crushing
may occur with moving machinery. (Barbara et al.,2005).

## Slide 35: Mechanical hazards
Accidents usually take place by the combination of unsafe condition & carelessness.
Most of industrial accidents are due to
Faulty inspection
Inability of employee
Poor discipline
Lack of concentration
Unsafe practice
Mental & physical unfitness for job
Faulty equipment or improper working condition
Improper training regarding the safety aspects

## Slide 36
Building planning
Floors must be of non-slippery type.
Enough space for employees to work.
Passages between working places.
Proper arrangements of temperature control; like fans, A.C., heaters.

## Slide 37
Protection of head by using hard hats/helmets.
Protection of ears by using earmufffs and plugs.
Protection of face by using face marks, face shields.
Personal protective devices

## Slide 38
Point of operation devices-photoelectric devices, radiofrequency
devices, pull back devices, restraint devices and safety trip
devices.
Feeding and ejection systems-automatic feed system, semi
automatic, automatic and semiautomatic ejection systems.
Robot safeguards.
LOCKOUT/TAGOUT SYSTEMS
Padlock systems
Tagout systems.
(Shah Prakashan,2007).

## Slide 39: SAFETY ASPECTS IN MECHANICAL HAZARDS
All the operators should be trained in safe operation, maintainance and emergency procedures to take care when accidents occur.
Inspection ,adjustment repair and calibration of safe guards
should be carried out regularly.
Ear protection devices must be used to prevent the excessive noise.
Effort should be made to reduce the noise to a safe level.

## Slide 40: ELECTRICAL HAZARDS
Electrical hazards occurs when a person come in contact with
the conductor carrying current and simultaneously contacts
with the ground, usually known to be work place hazard.
SOURCES OF ELECTRCAL HAZARDS
Short circuts
Electrostatic hazards
spark hazards
Combustible and explosive materials
Improper wiring
Insulation failure

## Slide 41: SAFETY ASPECTS IN ELECTRICAL HAZARDS
Ensure that power has been disconnected from the system working with it.
Do not wear conductive material like such as metal jewellary.
Perodically inspect insullation.
Verify circuit voltages.
Use only explosion proof devices and non sparkling switches in flammable liquid storage areas.
All electrical parts should confirm ISI specifications.
Ensure all flexible wires and power cables are properly insulated.
Installation of earth trip devices for all electrical equipments.
Safe guarding is essential for all electrical equipments. (Niosh,1986).

## Slide 42: PHARMACEUTICAL HAZARDS
Hazardous drugs that pose a potential health risk to health care workers who may be exposed during drug manufacturing, packing and storage.
CRITERIA FOR DEFINING HAZARDOUS DRUGS
Drugs that meet one or more of the following criteria should be hazardous.
Carcinogenicity.
Teratogenicity.
Reproductive toxicity.
Organ toxicity at lower doses.

## Slide 43
ROUTES OF EXPOSURE TO HAZARDOUS DRUGS
Inhalation of an aerosolized drug.
Dermal absorption.
Ingestion.
Injection.
TYPES OF HAZARDS TOXICITY
Acute poisoning.
Chronic poisoning.(Akunuru,1997).

## Slide 44: SAFETY ASPECTS IN PHARMACEUTICAL HAZARDS
Personal protective equipment for hazardous drug handling
Disposable gowns made of fabric that has low permeability
to the agents in use, with closed fonts and cuffs,intended for
single use.
Powder free gloves, labeled and tested for drugs used with
chemotherapy , made of latex, nitrile or neoprene.
Face and eye protection when splashing is possible.
Approved respirator when there is a risk of inhaling drug aerosols. The labelling of solvents to indicate their properties and health and fire hazards, is an extremely important method for controlling the hazards.
Substitution of more harmful material by one which is less danger to health.

## Slide 45
To prevent or reduce dangerous expose to toxic materials.
Gas releases should be vented outside buildings and away work areas and other populated areas.
Exhausts and ventilations should be provided to remove emissions.
Every bulk drug and pharmaceutical unit must prepare its disaster management plan.

## Slide 46: 3.SAFETY ASPECTS IN PHARMA INDUSTRY
Standard operating procedures
Handling of hazardous materials
Water supply and drainage
Floors and floor coverings
Emergency exits
Back up plan if anything goes wrong
Specially trained personnel
Health polices and insurance
Written procedures
Safety audits
Risk analysis
Appropriate training and education to employee
Regular monitoring of workplace
Written documentation of policies
Create awareness of the environment.

## Slide 47: Classification of signs according to use – (1) Danger signs.
The DANGER header is used when there is a hazardous situation which has a high probability of death or severe injury. It should not be considered for property damage unless personal injury risk is present.

## Slide 48: 2) Caution signs. (i)
The CAUTION header is used to indicate a hazardous situation which may result in minor or moderate injury. However, Caution should not be used when there is a possibility of death or serious injury.

## Slide 49: (3) Safety instruction signs
General Safety Signs (SAFETY FIRST, BE CAREFUL, THINK) should indicate general instructions relative to safe work practices, reminders of proper safety procedures, and the location of safety equipment.

## Slide 50: (4) Biological hazard signs.
The biological hazard warning shall be used to signify the actual or potential presence of a biohazard and to identify equipment, containers, rooms, materials, experimental animals, or combinations thereof, which contain, or are contaminated with, viable hazardous agents.

## Slide 51
THANK YOU