## Slide 1: PHARMACEUTICAL PACKAGING
PHARMACEUTICAL PACKAGING
Notes: PRESENTED BY
SHRIRAM GOSWAMI
<number>

## Slide 2
INTRODUCTION
Packaging is the science, art and technology of enclosing or protecting products for distribution, storage, sale, and use.
Packaging also refers to the process of design, evaluation, and production of packages.
Pharmaceutical packaging can be defined as the economical means of providing presentation, protection, identification , information, convenience ,compliance , integrity and stability of the product .

## Slide 3
FUNCTIONS OF PACKAGING
  Product Identification:- Packaging greatly helps in identification of products.
  Product Protection:- Packaging protects the contents of a product from spoilage, breakage, leakage, etc.
  Facilitating the use of product:- Packaging should be convenience to open, handle and use for the consumers.
  Product Promotion:- Packaging is also used for promotional and attracting the attention of the people while purchasing.

## Slide 4: TYPES OF PACKAGING Primary packaging- is the material that first envelops the product and hold it. This usually is the smallest unit of distribution or use. Ex. Aerosol spray can, blister packs, bottle

## Slide 5: Secondary packaging - Is outside the primary packaging perhaps used to group primary package together. Ex. Boxes, cartons

## Slide 6: Tertiary packaging- is used to bulk handling and shipping. Ex. Barrel, container, edge protector

## Slide 7
TYPES OF PACKAGING MATERIALS USED FOR PHARMACEUTICAL PACKAGING
Glass
Plastics
Rubbers
Paper/card boards
Metals

## Slide 8
THE CHOICE OF PACKAGING MATERIAL WILL DEPEND UPON:
The degree of protection required
Compatibility with the dosage form
Customer convenience e.g. size, weight of dosage form,
Filling method
Sterilization method to be employed and cost

## Slide 9
GLASS:
Glass has been widely used as a drug packaging material
Advantages
They are transparent.
They have good protection power.
They can be easily labelled.
Economical
Variety of sizes and shapes
Disadvantages
Glass is fragile so easily broken.
Release alkali to aqueous preparation

## Slide 10
TYPES OF GLASS
Type I—Highly resistant borosilicate glass
Type II—Treated soda lime glass
Type III—soda lime glass
NP—soda glass (non parenteral usage)

## Slide 11
Type of Glass | Main constituents | Properties | Uses
Type-1 Borosilicate glass | SiO2  80% B2O3  12 Al2O3 - 2% Na2O+CaO - 6% | Has high melting point so can withstand high temperature Resistant to chemical substances Reduced leaching action | Laboratory glass apparatus For injections and for water for injection.
Type-II Treated soda-lime glass | Made of soda lime glass. The surface of which is treated with acidic gas like SO2 (i.e. dealkalised) at elevated temperature (5000C) and moisture. | The surface of the glass is fairly resistant to attack by water for a period of time. Sulfur treatment neutralizes the alkaline oxides on the surface, thereby rendering the glass more chemically resistant. | Used for alkali sensitive products Infusion fluids, blood & plasma. large volume container
Type-III Regular soda-lime glass | SiO2 Na2O CaO | It contains high concentration of alkaline oxides and imparts alkalinity to aqueous substances Flakes separate easily. May crack due to sudden change of temperature. | For all solid dosage forms (e.g. tablets, powders) For oily injections Not to be used for aqueous injection Not to be used for alkali-sensitive drugs.

## Slide 12
Type of Glass | Main constituents | Properties | Uses
Neutral Glass | SiO2  72-75% B2O3  7-10% Al2O3  6% Na2O  6-8% K2O  0.5  2% BaO  2-4% | They are softer and can easily be moulded Good resistance to autoclaving Resistant to alkali-preparations (with pH upto 8) Lower cost than borosilicate | Small vials (<25 ml) Large transfusion bottles
Colored glass | Glass + iron oxide | Produce amber colour glass Can resist radiation from 290 400 450nm UV Visible | For photosensitive products.

## Slide 13
PLASTIC
Plastics may be defined as any group of substances, of natural or synthetic origins, consisting chiefly of polymers of high molecular weight that can be moulded into a shape or form by heat and pressure.
Advantages
Less weight than glass,
flexible
Variety of sizes and shapes
Essentially chemically inert, strong, rigid Safety use, high quality, various designs
Extremely resistant to breakage
Disadvantages
Absorption permeable to moisture
Poor printing,

## Slide 14
TYPES OF PLASTICS
Thermosetting type –
When heated they may become flexible but they do not become liquid
e.g. Urea formaldehyde (UF),Phenol formaldehyde ,Melamine formaldehyde (MF), Epoxy resins (epoxides), Polyurethanes (PURs)
Thermoplastics type-
On heating they are soften to viscous fluid which harden again on cooling.
e.g. Polyethylene{HDPE – LDPE}, Polyvinylchloride(PVC),Polystyrene Polypropylene, Nylon(PA), Polyethylene terepthalate(PET) ,Polyvinylidene chloride(PVdC), Polycarbonate Acrylonitrile butadiene styrene(ABS)

## Slide 15: Additives of plastics
Stabilizers
Prevent side reaction during polymerization
octyl tin to stabilize PVC
Antioxidants
Plastics are vulnerable to oxidation
N,N’-di--napthyl-p-phenylene diamine
Pigments
Decorative purpose, protect from UV radiations
4-biphenyl salicylate

## Slide 16: Additives of plastics
Fillers
are often employed to make the product cheap but in some cases may be essential for correct product performance.
Whiting, asbestos and mica
Plasticizers
They act by directly reducing the attractive forces between polymer chains.

## Slide 17: Plastic Material
High Density Polyethylene (HDPE)
Inert,
low cost,
low water vapour transmission,
Detergents, , bleaches, milk, foods, cleansing powders, drugs & cosmetics.
Low Density Polyethylene (LDPE)
Squeeze property, inertness, low cost
Cosmetics, personal products, foods

## Slide 18: Plastic Material
Polystyrene
Clarity, stiffness, low cost.
petroleum jelly.
Rigid polyvinylchloride (PVC)
Clarity, , retention of non-polar molecules
Shampoo, bath oil, detergent
Polypropylene
Inert, low cost
Drugs, cosmetics, syrups, juices

## Slide 19: Plastic Material
Polyamide (Nylon6,10)
Good barrier for non-polar molecules, tough, good
O2-barrier, sterilizable.
Foods, drugs, cosmetics, aerosols
Polycarbonate
Very tough, clear, sterilizable
Drugs, cosmetics.

## Slide 20: Plastic Material
Polyethylene terephthlate (PET)
Excellent strength, good barrier for gas and aroma.
Bottle for carbonated waters, mineral waters, mouth washes, cosmetics.

## Slide 21: DRUG-PLASTIC CONSIDERATION
Five separate categories
Permeation
Leaching
sorption
Chemical reaction
Alteration in physical properties of plastic or product

## Slide 22: DRUG-PLASTIC CONSIDERATION
Permeation
The transmission of gases, vapours or liquids through
plastic packaging materials can have an adverse effect
on the shelf-life of a drug.
Nylons are hydrophilic in nature, and are poor barrier for water while hydrophobic materials as polyethylene provide much better barriers.
Formulation containing volatile ingredients may change when stored in plastic container

## Slide 23: DRUG-PLASTIC CONSIDERATION
LEACHING
Additives those are added in the plastics may leach into the content
Release of a constituent from the plastic container to the drug product may lead to drug contamination, may catalyse some reaction in the solution - decomposing the drug.
Particular dyes may migrate into a parenteral solution and cause a toxic effect.

## Slide 24: DRUG-PLASTIC CONSIDERATION
Sorption
This process involves the removal of constituents from the drug product by the packaging material.
Drug substances of high potency are administered in small doses. In this case losses due to sorption may significantly affect the therapeutic efficacy of the preparation
A common problem is the loss of preservatives

## Slide 25: DRUG-PLASTIC CONSIDERATION
MODIFICATION
The physical and chemical alteration of the
packaging material by the drug product is called
modification
Deformation in polyethylene containers is often caused by permeation of gases and vapours from the environment or by loss of content through the container walls
Oils have a softening effect on polyethylene and PVC

## Slide 26
Plastic bottles made from PP, HDPE and PS
Plastic pouches of HDPE
Bottle- PET and spray- PP
EXAMPLES OF PLASTIC PACKAGES

## Slide 27
METALS :
Metals are used for construction of containers. The metals commonly used for this purpose are aluminium ,tin plated steel, stainless steel, tin and lead
Advantages:
They are impermeable to light, moisture and gases.
They are made into rigid unbreakable containers
They are light in weight compared to glass containers.
Labels can printed directly on to their surface.
Disadvantages:
They are expensive.
They react with certain chemicals

## Slide 28
COLLAPSIBLE TUBES METAL
The collapsible metal tube is an attractive container that permits controlled amounts to be dispensed easily, with good reclosure, and adequate protection of the product.
It is light in weight and unbreakable and lends itself to high speed automatic filling operations.
Most commonly used are tin, aluminium and lead.

## Slide 29
Tin:
Tin containers are preferred for food, pharmaceuticals and any product for which purity is considered.
Tin is the most chemically inert of all collapsible metal tubes .
Aluminium:
Aluminium tubes offer significant savings in product shipping costs because of their light weight .
They are attractive in nature
Lead:
Lead has the lowest cost of all tube metals and is widely used for non food products such as adhesives, inks. paints and lubricants.
Lead should never be used alone for anything taken internally because of the risk lead poison .
With internal linings, lead tubes are used for products such as chloride tooth paste.

## Slide 30: CLOSURE AND CLOSURE LINERS
closures are devices and techniques used to close or
seal a bottle, jar ,jug , tube, can etc.
closures tightly pack the containers to exclude oxygen, carbondioxide, moisture, microorganism, prevent the loss of water, and other volatile substances from the product.

## Slide 31
Purpose of closures :
Many containers and packages require a means of closing. It can be a separate device or seal or sometimes a integral lock. Depending on the contents and container, closures have several functions:
Keep the container closed and the contents contained for the specified shelf life until time of opening
Provide a barrier to dirt, oxygen, moisture, etc. Control of permeation is critical to many types of products: foods, chemicals, etc.
Keep the product secure from undesired premature opening
Provide a means of reclosing or reusing the container
Assist in dispensing and use of product
Allow reasonable ease to open the container by the intended user. The force or torque required to open a closure is an important consideration for packaging engineers
Many types of packaging with their closures are regulated for strength, safety, security, communication, recycling, and environmental requirements.

## Slide 32
Types of closures
(a)RUBBER CLOSURES
(b)CAPS & OVERSEALS
screw cap
crown cap
Snap on
Friction fit
(c)SPECIAL TYPES
Tamper-evident
Dispensing
Child-resistant

## Slide 33
RUBBER:
Rubber is used mainly for the construction of closure meant for vials, transfusion fluid bottles, dropping bottles and as washers in many other types of product.
BUTYL RUBBER:
Advantages:
Water absorption is very low.
They are relatively cheaper compared to other synthetic rubbers.
Disadvantages:
Slow decomposition takes place above 130 ▫ C.
Oil and solvent resistance is not very good.
NITRILE RUBBER:
Advantages : Oil resistant due to polar nitrile group. Heat resistant.
Disadvantages:
Absorption of bactericide and leaching of extractives are considerable.
CHLOROPRENE RUBBERS :
Advantages: Oil resistant. heat stability is good.

## Slide 34
RUBBER CLOSURES

## Slide 35: CLOSURE AND CLOSURE LINERS
Threaded Srew Cap:
When the screw-cap is placed on the neck of the container, its threads engage with the corresponding threads molded on the neck of the bottle. A liner in the cap seals the opening of the container.
Screw-caps are commonly made of metals (tinplate or aluminium) and plastics (thermoplastics and thermosetting). Metal caps are usually coated on the inside with an enamel or lacquer for resistance against corrosion.

## Slide 36
CAPS AND OVERSEALS :
These are used to secure the rubber closure to the container in order to maintain the integrity of the seal under normal conditions of handling and storage.It includes:
Screw cap
A screw cap or closure is a common type of closure for bottles, jars, and tubes
Common screw closures: Plastic bottle with plastic screw cap, Dispensing closure for salad dressing (with inner seal), Break-away closure for syrup, Dispensing pump closure, Dispensing closure (with inner seal), Spray pump, Metal closure on glass jar, Child resistant closure, Cap on toothpaste, Measuring cap

## Slide 37: CLOSURE AND CLOSURE LINERS
Crown caps:
This style of cap is commonly used as a crimped closure for beverage bottles and remains unchanged for more than 50 years. Crown-caps are made of metals.

## Slide 38
Crown cap
Crown caps
Main article: Bottle cap
Beverage bottles are frequently closed with crown beverage caps. These are shallow metal caps that are crimped into locking position around the head of the bottle.
Bottle cap
For the Nestlé candy, see Bottle Caps (candy).
A generic 21-teeth crown cork bottle cap

## Slide 39
Bottle caps are a type of closure used to seal the openings of bottles of many types. They can be small circular pieces of metal, usually steel with plastic backings, and for plastic bottles a plastic cap is used instead. A bottle cap is typically colorfully decorated with the logo of the brand of beverage. Caps can also be plastic, sometimes with a pour spout. Flip-Top caps like Flapper closures provide controlled dispensing of dry products
Other types
pull-off bottle cap
plastic bottle screw cap used to seal a plastic bottle
Bottle closure

## Slide 40
Snap on
Friction fit
Some closures snap on . For opening , the top is designed to pry off, or break off, or have a built in dispenser

## Slide 41
TAMPER RESISTANT PACKAGING:
The requirement for tamper resistant packaging is now one of the major considerations in the development of packaging for pharmaceutical products.
Tamper resistant package is one having an indicator to entry in which, if missing, can reasonably be expected to provide visible evidence to consumers that tampering has occurred.
FDA approves the following configurations as tamper resistant packaging: Film wrappers, Blister package, Strip package, Bubble pack, Shrink seals, and bands Oil, paper, plastic pouches, Bottle seals, Tape seals, Breakable caps, Aerosol containers

## Slide 42
Special types of clousres
Tamper evident
Layers of tamper resistance: carton with adhesive, shrink band, cap, innerseal
Main article: Tamper resistant
Main article: Tamper-evident
Resistance to tampering is required for some types of products. Container closures can be one of several layers of packaging to deter tampering and to provide evidence of attempts at tampering.Various types of tamper evident packagings are listed.They are-

## Slide 43
Film wrappers breakable cap ring systems
Blister packs sealed tubes
Bubble packs plastic blind end sealed tubes
Heat shrunk bands or wrappers sealed cartons
Paper foil for plastic packs aerosol containers,and
Bottle with inner mouth seals metal and composite cans
Tape seals
Dispensing
A wide variety of convenience dispensing features can be built in to closures. Spray bottles and cans with aerosol spray have special closure requirements. Pour spouts, measuring attachments, sifting devices, etc. are common.
Child-resistant
Main article: Child-resistant packaging
Child-resistant packaging or C-R packaging has special closures designed to reduce the risk of children ingesting dangerous items. This is often accomplished by the use of a special safety cap. It is required by regulation for prescription drugs, over-the-counter medications, pesticides, and household chemicals.

## Slide 44
Examples .
spray bottle
coffee tin – square can with friction fit closure
rubber stoppers on flasks

## Slide 45
spray duster with long tube for dispensing
Closure and roll-on device for deoderant
Bottle of Geritol with a child resistant cap

## Slide 46: CLOSURE LINERS
a liner may be defined as any material that is inserted in a cap to effect a seal between the closure and the container.
Factors in selecting a liner:
Chemical inertness  should be chemically inert
Appearance, thickness etc.
Gas and water-vapour transmission rates  should be low.
heat resistance  e.g. during autoclaving should be thermostable.

## Slide 47: CLOSURE LINERS
Shelf-life  should not change their shape during storage
Economics  should be cheap.
Liners are classified into two types:
(a) Homogeneous liner:
These are one-piece liner available either as a disk or as a ring.
they are widely used for pharmaceuticals because their properties are uniform and can withstand high-temperature sterilization.

## Slide 48: CLOSURE LINERS
Heterogeneous or Composite liners:
These are composed of layers of different materials chosen for specific requirements, In general the composite liner consists of two parts: a facing and a backing. Usually, the facing is in contact with the product, and the backing provides the cushioning and sealing properties required.

## Slide 49
BLISTER PACKAGE:
Blister package provides excellent environmental protection, and efficacious appearance.
It also provides user functionality in terms of convenience , child resistance and tamper resistance
The blister package is formed by heat softening a sheet of thermoplastic resin and vacuum drawing the soften sheet of plastic into a contoured mold .
After cooling the sheet is released from the mold and proceeds to the filling station of the machine. It is then lidded with heat sealable backing material
Peel able backing material is used to meet the requirements of child resistance packaging.
The material such as polyester or paper is used as a component of backing lamination.
Materials commonly used for the thermo formable blister are PVC, polyethylene combinations , polystyrene and polypropylene.

## Slide 50
STRIP PACKAGE
A strip package is a form of unit dose packaging that is commonly used for the packaging of tablets and capsule .
A strip package is formed by feeding two webs of a heat sealable flexible through heated crimping roller.
The product is dropped into the pocket formed prior to forming the final set of seals. A continuous strip of packets is formed in general.
The strip of packets is cut into desired number of packets.
Different packaging materials used are: paper/polyethylene/foil/PVC.

## Slide 52: Quality Assurance Aspects Of Packaging
To ensure that patients and consumers receive high-quality drugs, the quality management system must take the following considerations into account if the required quality of packaging is to be obtained:
  — the requirements of the national authorities and the relevant legislation
  — the product
  — the production process
  — the manufacturers’ internal policies (safety, marketing, etc.).
Bad packaging which is the result of deficiencies in the quality assurance system for packaging can have serious consequences, and packaging defects can create problems that may result in drug recalls. Such defects may include breakage, and problems relating to printing or inks, or errors on labels and package inserts (patient information leaflets). The use of GMP and quality control will prevent the release of a defective medicinal product.
Packaging processes and equipment need validation/qualification in the same way as any other part of processing within a pharmaceutical facility.
07/31/26
<number>

## Slide 53: SYMBOLS USED ON PACKAGES AND LABELS
Many types of symbols for package labeling are nationally and internationally standardized.
Fragile
This way up
Keep away from sunlight
Keep away from water