## Slide 1: Introduction
Parenterals are the sterile dosage forms, administered by routes other than the oral route.
These preparations bypass the gastrointestinal tract and liver and directly enter the systemic circulation.
The finished products are forwarded to the quality control department where the various quality control tests are performed.

## Slide 2
Manufacturing of products
Sterilization of products
Online testing
Capping/ outer sealing
Inspection
Quarantine
Finishing, labeling and packaging
warehouse
Market

## Slide 3: Quality Control Tests Of Parenterals
Leakage Test
Clarity Test
Pyrogen Test
Sterility Test

## Slide 4: Leakage Test (with methylene blue solution)
The ampoules are immersed in vacuum chamber consisting of 1% methylene blue solution
A vacuum of about 27 inch Hg is created for about 15 to 30 min.
This causes the solution to enter the ampoules with defective sealing.
The vacuum is released and ampoules are observed.
If a leakage is present, the solution in the ampoules appear blue color.

## Slide 5
Leakage Test machine

## Slide 6: Clarity Test
Test to detect the particulate matter.
1. Visual method
2. Microscopic count method
3. Light obstruction method
4. Coulter counter method

## Slide 7: Visual method
The containers are examined against strong illuminated screen.
Black background is used for the detection of light colored particles and white background for dark colored particles.

## Slide 8
Visual Inspection machine

## Slide 9: Microscopic count method
Membrane filters and microscopes are used.

## Slide 10: Light obstruction method
Tungsten lamp produces a constant collimated beam of light that pass through a small rectangular passageway and impinges onto a photodiode.
Liquid can flow through the passageway between the light source and photodiode.
If a single particle transverses the light beam there results a reduction in normal amount of light received by the photodiode .
This reduction of light and the measurable decrease in the output from the photodiode is proportional to the area of the particle interrupting the light flow

## Slide 11: Light obstruction method
This method uses an electronic counter that produces a light beam of high intensity.
The solution is allowed to pass under this bright light.
A shadow is formed if a particle is present.
The particles are counted by the no. of shadows.

## Slide 12
Coulter Counter counts the particles in a sample based on the change
in the electrical resistance. Particle size detection limit in this
instrument is from 0.1 to 1000 micrometer.
The powder sample requires pretreatment such as dispersion in an electrolyte to form a very dilute suspension.
The Suspension is usually subjected to ultrasonic agitation to avoid particle agglomerates.
Coulter Counter method
A dispersant may also be added to aid particle deagglomeration. Passage of particle causes the change in electrical resistance in between the electrodes which is proportional to the volume of particle.
The change in resistance is converted into voltage pulse which is amplified and processed electronically and split into the particle size distribution into many different size-range.
.Particles below 0.2 µm can also be detected.

## Slide 14: Pyrogen Test
The term pyrogen frequently refers to gram negative bacterial endotoxin.
Pyrogen is a general term for any substance that causes fever after IV administration / inhalation .
Microbial substances which act as pyrogen includes bacteria , fungi , plasmodia , viruses, staphylococcal endotoxin.
The amount of USP reference standard endotoxin needed to initiate pyrogenicity in humans and rabbits is about 1ng/kg.
Naturally occurring bacterial endotoxin contain the lipid, carbohydrate and protein makeup of the outer cell membrane of gram negative bacteria.

## Slide 15: Sources of pyrogen contamination
solvent - possibly the most important source
the medicament
the apparatus
the method of storage between preparation and sterilization

## Slide 16: Animals and equipment
selection of animals (healthy, adult, not less than 1.5 kg)
housing of animals
equipment and material used in test (glassware, syringes, needles)
retaining boxes (comfortable for rabbits as possible)
thermometers (standardized position in rectum, precision of 0.1°C)

## Slide 17: Housing of Rabbits

## Slide 18: Preliminary Test
  intravenous injection of sterile pyrogen-free saline solution
  to exclude any animal showing an unusual response to the trauma (shock) of injection
  any animal showing a temperature variation greater than 0.6C is not used in the main test

## Slide 19: Main Test
  group of 3 rabbits
  preparation and injection of the product:
    warming the product
    dissolving or dilution
    duration of injection: not more than 4 min
    the injected volume: not less than 0.5 ml per 1 kg and not more than 10 ml per kg of body mass
  determination of the initial and maximum temperature
    all rabbits should have initial T: from 38.0 to 39.8C
    the differences in initial T should not differ from one another by more than 1C

## Slide 20: The result of pyrogen test:
No. Of Rabbits | Individual Temp. rise(0C) | Rise in group(0C) | Inference
3 | 0.6 | 1.4 | Pass
3 + 5 = 8 | 0.6 | 3.7 | Pass

## Slide 21: Sterility Test
Sterility testing attempts to reveal the presence or absence of viable micro-organisms in a sample number of containers taken from batch of product. Based on results obtained from testing the sample a decision is made as to the sterility of the batch.
Sterility testing is made after the product exposition to the one of the possible sterilization procedures

## Slide 22: Principle
Sterility test is based on the principle that when microorganisms are supplied with nutrient medium and water, and incubated at favorable temperatures, they multiply.
The presence of micro organisms can be identified by turbidity in the clear medium.

## Slide 23: Culture Media
The culture media used for sterility test must be capable of promoting the growth of a wide range of microorganisms.
Types of media-
1. Fluid thioglycollate medium (for anaerobic bacteria).
2. Soyabean-casein digest medium (for aerobic bacteria and fungi).
Incubation of media: 14 days at 30-350C

## Slide 24: Fluid Thioglycolate Medium
Ingredients | Quantity for 1000 ml
L- cysteine | 0.5 g
Sodium chloride | 2.5 g
Dextrose | 5.5 g
Agar | 0.75 g
Yeast extract | 5.0 g
Pancreatic digest of casein | 15.0 g
Sodium thioglycollate | 0.5 g
Resazurin(0.1 % fresh solution) | 1.0 ml
Distilled water | Upto 1000 ml

## Slide 25: Soyabean - Casein Digest Medium
Ingredients | Quantity for 1000 ml
Pancreatic digest of casein | 17 g
Peptic digest of soyabean meal | 3 g
Sodium chloride | 5 g
Dibasic potassium phosphate | 2.5 g
Dextrose | 2.5 g
Distilled water | Upto 1000 ml

## Slide 26: Minimum sample size related to batch size
No. of items in the batch | Min. no. of item recommended to be tested
Injectable preparations | 
a) upto 100 containers | 10% or 4 containers whichever is greater
b) 101-500 containers | 10 containers
c) > 500 containers | 2% or 20 containers which ever is less
Ophthalmic and other non - Injectable preparations | 
a) upto 20 containers | 5% or 2 containers whichever is greater
b) > 200 containers | 10 containers

## Slide 27
No of items in the batch | Min no. of items recommended to be tested
Bulk Solids | 
a) <4 containers | All containers
b) 4 – 50 containers | 20% or 4 containers whichever is greater
c) > 50 containers | 2% or 20 containers whichever is greater
Surgical Dressings | 
a)< 100 packages | 10% or 4 packages whichever is greater
b) > 100 but < 500 packages | 10 packages
c) > 500 packages | 2% or 20 packages whichever is less

## Slide 28: For injectable preparations
Quantity of each container | Min Quantity to be used for each culture medium
For liquids | 
a) < 1 ml | Total contents of a container
b) 1 ml – 4 ml | Half the contents of a container
c) 4 ml – 20 ml | 2 ml
d) 20 – 100 ml | 10% of contents of a container
e) > 100 ml | NLT half of the containers
For solids | 
a) < 50 mg | Total contents of a container
b) 50 mg – 200 mg | Half the contents of a container
c) > 200 mg | 100 mg

## Slide 29: Test methods
The test methods for the sterility of the products are:
Membrane filtration method
Direct inoculation of the culture medium

## Slide 30: Membrane Filtration Method
Appropriate for : (advantage)
  filterable aqueous preparations
  alcoholic preparations
  oily preparations
  preparations miscible with or soluble in aqueous or oily (solvents with no antimicrobial effect)
solutions to be examined must be introduced and filtered under aseptic conditions

## Slide 31: Selection of the filters
pore size of 0.45 m
effectiveness established in the retention of micro-organisms
appropriate composition
the size of filter discs is about 50 mm in diameter

## Slide 32
sterilization of filtration system and membrane filtration of
examined solution under aseptic conditions.
Filtration of the sample through a membrane filter having the nominal size of 0.45µ and a diameter of 47mm.
After filtration the membrane is removed aseptically from the metallic holder and divided into two halves.
The first half is transferred into 100 ml of culture media meant for fungi and incubated at 20˚ to 25 ˚c for not less than seven days.
The other half is transferred into 100ml of fluid thioglycolate medium and incubated at 30 to 35 ˚c for not less than 7 days.

## Slide 33: Scheme for sterility test by membrane filtration

## Slide 34: Direct inoculation of the culture medium
suitable quantity of the preparation to be examined is transferred directly into the appropriate culture medium
volume of the product is not more than 10% of the volume of the medium
suitable method for aqueous solutions, oily liquids, ointments an creams

## Slide 35: Scheme for sterility test by direct inoculation method

## Slide 36: Interpretation of the results
The culture media is examined during and after the incubation period to detect the possible microbial growth.
a) the sample passes the test if microbial growth is not found.
b) If microbial growth is present, a retest is performed. If growth absent. Then sample passes the test.
If microbial growth is present in the retest also, identify the organisms.
If same organisms are found as in the first test, then the sample fails the test.
If different organisms are found, retest is performed using twice the number of samples. Passes if microbial growth is not found.

## Slide 37
Powdered glass Test:
Use crushed glass containers in 250-ml conical flask, add 50 ml high purity water, cap the flask with borosilicate glass beaker
Place the containers in the autoclave and close it securely hold temperature at 1210c±20c for 30 min., counting from the time this temperature is reached.
cool the flask, decant the water from the flask into a clean vessel, and wash the residual powdered glass with high purity water, add 5 drops methyl red solution, titrate immediately with 0.02 N sulfuric acid .
Record the volume of 0.02N Sulfuric acid used to neutralize the extract from 10 g of the prepared specimen of glass.
Test for packaging containers
Type | Type of test | Size (ml) | ml of 0.02N H2SO4
ˡ | Powder glass | All | 1.0
ˡˡ | Water attack | 100/less Over 100 | 0.7 0.2
ˡˡˡ | Powder glass | All | 8.5
Non parenteral | Powder glass | All | 15.0

## Slide 38: Parenteral Formulation

## Slide 39: Parenteral Formulation
Drug
Vehicles
a) aqueous
b) water immiscible and non aqueous
Antioxidants
Buffering agents

## Slide 40: Parenteral Formulation
Tonicity adjustment agents
Inert gases
Chelating agents

## Slide 41: Parenteral Formulation
Drug
careful evaluation must be made of every combination of drugs
physical and chemical properties of drugs
molecular weight, solubility, purity , chemical reactivity
outstanding formulation can be justified to launch in market ( extensive documentation by FDA

## Slide 42: 1.Vehicles a) aqueous vehicles
TYPES | COMMENTS
Purified water USP | Pharmaceutical solvent
Water for injection WFI | Used to prepare pharmaceutical products.
Sterile water for injection USP | Single dose containers, used to reconstitute sterile solids or solutions
Bacteriostatic water for injection USP | Multiple and single doses
Sterile water for irrigation USP | 1 liter or large, for irrigation only

## Slide 43: Aqueous vehicle
test for quality of water is total solid contents, gravimetric evaluation of dissociated and undissociated organic and inorganic substance present in water
electrolyte measurement of conductivity of water ( measure the conductance)
water contain minimum amount of organic compounds (Toxic, nutrition of microorganisms)

## Slide 44: b) Water miscible vehicles
They are used when
Drug is insoluble in water
Drug is susceptible to hydrolysis
Indication: when these are used as vehicles, then formulation should not be diluted with water as precipitation may occur .
Example glycerin propylene glycol
ethanol Glycerine
PEG ethylalcohol

## Slide 45: Non aqueous solvents
Non aqueous solvents characteristics
must not be irritant, toxic or sensitizings
Not exert any adverse reactions
Polarity, Density, Viscosity, Miscibility, Toxicity ,

## Slide 46: Non aqueous solvents
Fixed vegetables oils are used
Prolong drug release at site of administration can be achieved when converted to oily suspension
Examples,
Seasame oil isopropyl myristate
Cotton seed oil benzyl benzoate
Peanut oil propylene glycol

## Slide 47: Solvent Selection
Solution is preferred in parenteral therapeutic agents
It is compatible with body fluids, biological response is predictable
Therapeutic active agent ranges from highly polar to non polar
Alkaloids nature drugs required non polar solvents

## Slide 48: Solvent Selection
Solvents to be injected must be of low toxicity
Ether is highly irritant to body tissue, use with combination of other solvents
Compound dissolve in water are often subject to degradative reactions, such as hydrolysis, oxidation
Minimize the reactions by stabilize the pH of solution

## Slide 49: Solvent Selection
Epinephrine in solution goes to oxidation reaction can be minize if its pH maintain upto at 3 or less
Atropine sulphate rapidly hydroyzes in solutions but if pH is maintaned at about pH 3 or 4, hydrolysis does not occur
The use of mixed solvent system reduces degradative reactions

## Slide 50: Solvent Selection
Pentobarbital is easily hydrolyzed in water
pentobarbital sodium is soluble and stable if we use 60% polyethylene glycol and 10% ethanol in water at pH of 8

## Slide 51: ANTIOXIDANTS
Protect the therapeutic agents susceptible to oxidation
by blocking oxidation chain reaction

## Slide 52: ANTIOXIDANTS
True antioxidants | Reducing agents
Tocopheral (.05- .075) | Ascorbic acid, ( 0.02- .1)
BHA (butylated hydroxy anisole) (.005- .02) | Sodium bissulfite ( 0.1-0.15)
BHT (butylated hydroxy toulene) (.005- .02) | Sodium metabisulphite (0.1-0.15) Thiourea (0.005)

## Slide 53: Buffering agents
Changes in pH occur during storage
dissolution of glass constituents
release of constituents from rubber
plastic components in contact with
product

## Slide 54: Buffering agents
As most drugs are weak acids and bases. They are subject to partial ionization under a given pH.
Buffers are used to maintain and adjust pH in order to increase stability
Examples
acetate
glutamates
citrates
Glutamates
Phosphates

## Slide 55: Tonicity adjustment Agents
Compounds contributing isotonicity of the product reduces the pain of injection
Tonicity adjusters are the last ingredients added in the formulation

## Slide 56: Tonicity adjustment Agents
Dextrose
Sodium chloride
Potassium chloride

## Slide 57: CHELATING AGENTS
Chelating agents may be added to bind with traces of heavy metals ,which it free, catalyzes the degradative reactions
The heavy metals extracted from rubber closures
Thimerosal in poliomyelitis vaccine
Thimerosal is unstable in presence of cupric ion, breakdown products of which destroy the antigenicity of vaccine

## Slide 58: CHELATING AGENTS
EDTA
EXAMPLES
Di sodium edetate

## Slide 59: Inert Gases
Displace the oxygen from solution and reduce the possibility of oxidative changes in the formulation
During autoclaving, sodium bicarbonate injection decompose into carbonate, carbon dioxide and water. Saturation of solution by carbon dioxide inhibits this reaction and stabilized the solution
Nitrogen, argon and carbon dioxide

## Slide 60: Antimicrobial preservatives
Antibacterial agents in bacteriostatic concentration must be included in formulation of product packaged in multiple dose vials
The requirement of activity, stability, and effectiveness of antibacterial agents in parenterals have been reviewed in published papers

## Slide 61: Antimicrobial preservatives
Benzyl alcohol 0.5-10.0 %
Benzethonium chloride 0.01%
Butyl paraben 0.015 %
Chlorobutanol 0.25-0.5%
Methyl paraben 0.1-0.125%
Propyl paraben 0.005- 0.035%
Thimerosol 0.001-0.02%

## Slide 62: Production Process
Steps from accumulation and combining of ingredients of the formula to the enclosing of product in the individual container for distribution.
For assurance of successful manufacturing operations, all process steps must be written(SOP) after being shown to be effective.
Any change must go through same approval steps as the original written SOP

## Slide 63: Production Process
In initial step, Formulation ingredients, container components and processing equipments, after approval are drawn from respective areas.
The ingredients are compounded according to master formula in an environmental designed to maintain a high level of cleanless.

## Slide 64: Production Process
Process equipments and container components are cleaned according to the required specification
Assembled in a clean environment, preferably are sterilized and depyrogenated prior to use
all equipments and supplies introduce into a septic filling area should be sterile.

## Slide 65: Production Process
all supplies must be introduced into aseptic area in such a manner that a septic state of these rooms is maintained
The product is sealed in its final container within aseptic room.
Product is transferred to packaging area.
this area is maintained clean but no need to meet the standards imposed for aseptic rooms

## Slide 66: Production Process
Packaged products are placed in quarantine storage until all tests have been completed and in process control records have been evaluated
The product may be released for distribution

## Slide 67: Environmental Control
The standard of environmental control is vary, depending on the area ( Packaging, compounding, filling)
the entire area used for preparation of product prepared aseptically in rigid controlled environment
if the product is to be terminally sterilized, somewhat less rigid biologic control of the compounding and filling area may be acceptable.

## Slide 68: Environmental Control
Traffic control
A careful designed arrangements to control and minimize traffic, particularly in and out of aseptic area, is essential.
Personnel should be permitted to enter aseptic area only after following rigidly prescribed procedures
removing street clothes
washing their hand

## Slide 69: Environmental Control
Traffic control
donning gowns, hats, shoes, facemasks
gloves
Once they have entered into aseptic area, not permitted to move in and out of the area without regowning.

## Slide 70: Environmental Control
Surface Disinfectants
After thorough cleaning, all surfaces should be disinfected, at least in the aseptic area
Ultraviolet lights reduces the viable micro organism present in the surface or in the air

## Slide 71: Environmental Control
Air control
Air is exchanged frequently ( personnel)
More than one pre filters may be used in series
First one quite large, next one of somewhat smaller in size, to remove the contaminated air

## Slide 72: Environmental Control
Air control
High Efficiency Particulate Air (HEPA)
At least 99.97% efficient in removing particles of 0.3 Um size and larges
Air passing through these units can be rendered virtually free from foreign matters
Clean air in dirstributed to the required areas by means of metal ducts.
Hepa filters installed at point where clean air enters the controlled room

## Slide 73: Environmental Control
Air control
Class 100 clean room
A room in which the particle count in the air is not more than 100 per cubic foot of 0.5 um and larger in size
The airflow must be uniform in velocity and direction through out any given cross section of area
Specified for most critically aseptic area

## Slide 74: Environmental Control
Air control
Class 10,000 Clean room
One in which the particle count is not more than 10,000 per cubic foot of 0.5Um and larger in size
Buffer areas around aseptic area ( handling, pre cleaned containers, process filtration and aseptic gowning of personnel

## Slide 75: Environmental Control
Air control
Class 100,000 Clean room
One in which the particle count is not more than 100,000 per cubic foot of 0.5Um and larger in size
Laboratories, stock staging area, finish packaging

## Slide 76: Environmental monitoring method
Biological evaluation
Settling plates method
Gravitational fallout in a given time on a
given area
Uncomplicated and low cost
only heavier particles settle

## Slide 77: Environmental monitoring method
Slit sampler
Measured volume of air drawn through slit and impacted on nutrient agar as plate turns
Measured volume of air sampled
sampling related to time, as palte turns
velocity of impaction likely to have lethal effect on vegetative cells

## Slide 78: Environmental monitoring method
Cascade sieve sampler
Measured volume of air cascade through up to six plates of decreasing pore size and impacted on nutrient agar plates, with smallest particles collected on last plate
Measured volume of air sampled
permit gradation of particle by size

## Slide 79: Environmental monitoring method
Membrane filter sampler
Measured volume of air drawn through membrane filter with particles retained on surface and filter then incubated on nutrient agar plate
Used for microscopic particle counting
Addition step of membrane being placed
Vaccum source required

## Slide 80: Sterilization
Sterilization can be defined as any process that effectively kills or eliminates transmissible agents (such as fungi, bacteria, viruses) from a surface, equipment, foods, medications, or biological culture medium.

## Slide 81: METHODS OF STERILIZATION
The various methods of sterilization are:
1. Physical Method
a. Thermal (Heat) methods
b. Radiation method
c. Filtration method
2. Chemical Method
a. Gaseous method

## Slide 82: PHYSICAL METHODS:
1. HEAT STERILIZATION:
Heat sterilization is the most widely used and
reliable method of sterilization, involving
destruction of enzymes and other essential cell
constituents.
This method of sterilization can be applied only to
the THERMO STABLE PRODUCTS
i) Dry Heat (160-1800˚C) Sterilization for thermo
stable products
ii) moist heat (121-1340 ˚C) sterilization is used for
moisture- resistant materials.
Notes: The process is more effective in hydrated state where under conditions of high humidity, hydrolysis and denaturation occur, thus lower heat input is required. Under dry state, oxidative changes take place, and higher heat input is required.

## Slide 83
The efficiency with which heat is able to inactivate microorganisms is dependent upon
i) The degree of heat,
ii) The exposure time

## Slide 84: THERMAL (HEAT) METHODS
Thermal methods includes:
i) Dry Heat Sterilization
1. Flaming
2. Hot air oven
ii) Moist Heat Sterilization
1.Dry saturated steam – Autoclaving
2. Boiling water/ steam at atmospheric pressure
3. Hot water below boiling point

## Slide 85: Dry Heat Sterilization
It employs higher temperatures in the range of 160-180˚C and requires exposures time up to 2 hours, depending upon the temperature employed.
The benefit of dry heat includes good penetrability and non-corrosive nature which makes it applicable for sterilizing glass wares and metal surgical instruments. It is also used for sterilizing non-aqueous thermo stable liquids and thermo stable powders.

## Slide 86
Dry heat destroys bacterial endotoxins (or pyrogens) which are difficult to eliminate by other means and this property makes it applicable for sterilizing glass bottles which are to be filled aseptically

## Slide 87: Moist Heat Sterilization
Moist heat sterilization involves the use of steam in the range of 121-134˚C. Steam under pressure is used to generate high temperature needed for sterilization. Saturated steam acts as an effective sterilizing agent.

## Slide 89: Autoclave
Autoclaves use pressurized steam to destroy microorganisms, and are the most dependable systems available for the decontamination of laboratory waste and the sterilization of laboratory glassware, media, and reagents. For efficient heat transfer, steam must flush the air out of the autoclave chamber.
Generally the conditions employed are
Temperature upto121-134˚C for 15-20 min under 15 lbs pressure,based on type of metiral used.

## Slide 90: Radiation Sterilization
Many types of radiation are used for sterilization like electromagnetic radiation (e.g. gamma rays and UV light), particulate radiation (e.g. accelerated electrons).The major target for these radiation is microbial DNA.
Radiation sterilization with high energy gamma rays or accelerated electrons has proven to be a useful method for the industrial sterilization of heat sensitive products.

## Slide 91: Radiation Sterilization
Radiation sterilization is generally applied to articles in the dry state; including surgical instruments, sutures, unit dose ointments, plastic syringes and dry pharmaceutical products.
UV light, with its much lower energy, and poor penetrability finds uses in the sterilization of air, for surface sterilization of aseptic work areas, for treatment of manufacturing grade water, but is not suitable for sterilization of pharmaceutical dosage forms.

## Slide 92: Filtration Sterilization
Filtration process does not destroy but removes the microorganisms. It is used for both the clarification and sterilization of liquids and gases as it is capable of preventing the passage of both viable and non viable particles.
The major mechanisms of filtration are sieving, adsorption and trapping within the matrix of the filter material.
Ex:HEPA FILTERS

## Slide 93: Filtration Sterilization
Sterilizing grade filters are used in the treatment of heat sensitive injections and ophthalmic solutions, biological products and air and other gases for supply to aseptic areas. They are also used in industry as part of the venting systems on fermentors, centrifuges, autoclaves and freeze driers. Membrane filters are used for sterility testing

## Slide 94: LAMINAR AIR FLOW CHAMBER

## Slide 95: LAMINAR AIR FLOW CHAMBER

## Slide 96: CHEMICAL STERILIZATION METHOD
GASEOUS METHOD
The chemically reactive gases such as formaldehyde, (methanol, H.CHO) and ethylene oxide (CH2)2O possess biocidal activity. Ethylene oxide is a colorless, odorless, and flammable gas.
The mechanism of antimicrobial action of the two gases is assumed to be through alkylations of sulphydryl, amino, hydroxyl and carboxyl groups on proteins and amino groups of nucleic acids.

## Slide 97
S.no | METHOD | MECHANISM | MERITS | DEMERITS | APPLICATIONS
1 | Heat sterilization | Destroys bacterial endo toxins | Most widely used and reliable method of sterilization, involving destruction of enzymes and other essential cell constituents | Can be applied only to the thermo stable products | Dry heat is applicable for sterilizing glass wares and metal surgical instruments and moist heat is the most dependable method for decontamination of laboratory waste and the sterilization of laboratory glassware, media, and reagents.

## Slide 98
S.no | METHOD | MECHANISM | MERITS | DEMERITS | APPLICATIONS
1 2 | Gaseous sterilization Radiation sterilization | Alkylation Ionization of nucleic acids | Penetrating ability of gases. It is a useful method for the industrial sterilization of heat sensitive products | Gases being alkylating agents are potentially mutagenic and carcinogenic. . | Ethylene oxide gas has been used widely to process heat-sensitive devices. Radiation sterilization is generally applied to articles in the dry state; including surgical instruments, sutures, prostheses, unit dose ointments, plastics

## Slide 99
S.no | METHOD | MECHANISM | MERITS | DEMERITS | APPLICATIONS
1 | Filtration sterilization | Does not destroy but removes the microorganisms | It is used for both the clarification and sterilization of liquids and gases as it is capable of preventing the passage of both viable and non viable particles | Does not differentiate between viable and non viable particles | This method is Sterilizing grade filters are used in the treatment of heat sensitive injections and ophthalmic solutions, biological products and air and other gases for supply to aseptic areas

## Slide 100: Pharmaceutical Importance of Sterilization
Moist heat sterilization is the most efficient biocidal agent. In the pharmaceutical industry it is used for: Surgical dressings, Sheets, Surgical and diagnostic equipment, Containers, Closures, Aqueous injections, Ophthalmic preparations and Irrigation fluids etc.
Dry heat sterilization can only be used for thermo stable, These include products like; Dry powdered drugs, Suspensions of drug in non aqueous solvents, Oils, fats waxes, soft hard paraffin silicone, Oily injections, implants, ophthalmic ointments and ointment bases etc.

## Slide 101: Pharmaceutical Importance of Sterilization
Gaseous sterilization is used for sterilizing thermolabile substances like; hormones, proteins, various heat sensitive drugs etc.
U.V light is perhaps the most lethal component in ordinary sunlight used in sanitation of garments or utensils.
Gamma-rays from Cobalt 60 are used to sterilize antibiotic, hormones, sutures, plastics and catheters etc.

## Slide 102: Pharmaceutical Importance of Sterilization
Filtration sterilizations are used in the treatment of Heat sensitive injections and ophthalmic solutions, biological products, air and other gases for supply to aseptic areas.
They are also used in industry as part of the venting systems on fermentors, centrifuges, autoclaves and freeze driers. Membrane filters are used for sterility testing.

## Slide 103: Areas in Parenteral processing
Different sectional areas required for sterile preparations are as follows:
Clean-up section
Compounding section
Aseptic section
Quarantine section
Packing and labeling section

## Slide 104: Layout of parenteral processing

## Slide 105: Clean-up area
The cleaning area has walls and ceilings made up of film coating materials is involved in cleaning of bottles, vials or ampoules.
Air inside the clean area should be free from dust and microorganisms.
This is ensured through high efficiency (95%) filters.
Air existing in the clean area should be frequently replace

## Slide 106: Compounding section
This area contains stainless steel cabinets and counters and is involved in the actual compounding.
Unlike aseptic area, maintenance of sterile conditions is not essential, but necessary measures should be adopted to control the dust generated from raw material during weighing and compounding.

## Slide 107: Aseptic area
In this area, strict control measures should be adopted to avoid contamination of the preparations.
The stainless steel counters and cabinets should be such that they should not allow dirt particles to accumulate.
Mixing and storage of the compounded preparations should be done outside the aseptic area.
The compounded preparations are then transferred to the aseptic area through pipelines where the filling operation is carried out.

## Slide 108: Quarantine section
This area consists of a store where the in-process batches as well as approved batches are stored separately.
This area has limited access and is under the control of a responsible person.
Without the consent of the incharge, other personnel cannot enter into this particular area.

## Slide 109: Packing and labeling section
In this area, the batches are packed and labeled.
Packing is carried out by packaging machines, while labels are obtained by over printing devices.
At a time, only one product labels are printed.
Parenteral packing plays a vital role in the production of sterile preparations.
Packing should be carried out in such a manner that the sterility of the product is maintained.

## Slide 110: Requirements for design of aseptic area
Aseptic techniques are defined as a set of procedures carried out to obtain an environment with minimal contamination from pathogenic microorganisms.
These procedures are carried out under controlled conditions.
The main goal of aseptic technique is to provide protection against infections.

## Slide 111: 1.Site of premises
Aseptic area should be designed at a site away from stairs, lift shafts , corridors and general manufacturing area as these areas are capable of providing routes by which microorganisms may travel.
Each stage of the production should be carried out in separate rooms of aseptic area.
Store rooms should be adjacent to aseptic area where all sterile equipments and products can be stored.

## Slide 112: 2.Size of premises
Aseptic area should be constructed in such a manner that maximum number of personnels can work at a time.
The rooms should be large and spacious by which overall effect of microorganisms can be reduced which ultimately results in minimal contamination.

## Slide 113: 3.Windows
Large windows with transparent glass are suitable for aseptic area.
These windows should remain closed and ventilation should be provided artificially by air filtration system.
These type of windows are used to prevent heat loss from glass material.

## Slide 114: 4.Doors
Entrance should have double doors with an air-lock system.
In this way, air entering from outside into the aseptic area can be prevented .
Even sliding and swing doors can be used.

## Slide 115: 5.Floors, walls and bench tops
The floor, walls and bench tops should be,
Easy to clean
Smooth with no cracks and pores
Impervious to cleaning agents like disinfectants etc
Chemically resistant to solvents, dyes, strong acids or alkalies.

## Slide 116: Floor
It should be made up of the following materials,
Terrazzo
Linoleum
plastics

## Slide 117: Contd…
Terrazzo:
It is a mixture of cement and marble which is mostly used as flooring material in aseptic area.
Advantages:
it can withstand harsh cleaning.
The water used for cleaning purpose can be removed easily by sloping the floor towards the gully, which is present at one side of the aseptic room.

## Slide 118: Contd…
Disadvantages:
Expensive
Noisy, cold and gets slippery when wetted.
It gets easily attacked by acids.
It gets easily stained by dyes.

## Slide 119: Contd…
(b).Linoleum
Linoleum of heavy grade is best suited for flooring. It is available in the form of sheets and tiles.
Advantages:
easy to clean
Inexpensive
Disadvantages:
Polished surfaces get slippery when wetted.

## Slide 120: Contd…
Plastics:
Polyvinyl chloride of non-slip and matt-finish grade is ideally for aseptic area. The joints of sheets & tiles can be welded.
Advantages:
Easy to clean
Inexpensive
Available in many colors

## Slide 121: Walls and ceiling
They should have surfaces made up of,
Tiles – they are smooth, non-absorbent in nature and tend to crack on prolonged usage. They can be easily cleaned.
Glass paint – this type of paint is applied on smooth plaster. These plaster walls get easily damaged.
Plastic laminate – this type of material I used to cover the walls and ceiling of an aseptic room. However, it is expensive.

## Slide 122: Tops of working bench
The tops of the working benches should be made up either of the following materials.
Stainless steel – the screws used in benches should be located under the surface of the bench to avoid accumulation of the dust.
Plastic laminates – they are available in various bright colors.

## Slide 123: Contd…
Advantages:
low cost and less noisy compared to stainless steel.
Resistant to heat.
Resistant to reagents
Disadvantages:
May get stained with dyes.

## Slide 124: Types of laminar flow systems
laminar air flow systems are generally of three types.
Vertical flow system
Horizontal flow system

## Slide 125: Laminar air flow hoods
The underlying principle of a laminar air flow hood is that a constant flow of HEPA filtered air at a rate of approximately 90 linear feet per minute physically sweeps the work area and prevents the entry of contaminated air
The hood workspace is used to prevent the contamination of compounded sterile products and parenteral preparations
The space between the HEPA filter and sterile product being prepared is referred to as the critical work surface
HEPA filter - High Efficiency Particulate Air filter removes 99.97% of all air particles 0.3mm or larger

## Slide 126: Laminar Air Flow Hoods
Prefilter
Hepa Filter
Room Air
Filtered Air
Horizontal Laminar Air Flow Hood
Horizontal Laminar Air Flow Hood

## Slide 127: Laminar Air Flow Hoods (cont.)
Vertical Laminar Flow Hood

## Slide 128: Laminar Air Flow Hoods (cont.)
All aseptic manipulations should be performed at least SIX inches within the hood to prevent the possibility of contamination from room air entering the hood.
6 inches
inside hood

## Slide 129: Laminar Air Flow Hoods (cont.)
A laminar flow hood should be left operating continuously
If hood is turned off it must run for 30 minutes to reestablish laminar air flow and then be cleaned prior to use
Before use, all interior working surfaces of the laminar flow hood should be cleaned from back to front away from the HEPA filter
Back to Front
Away from HEPA filter

## Slide 130: Laminar Air Flow Hoods (cont.)
The HEPA filter is located in the fragile mesh between thin metal strips at the back of the hood behind the HEPA filter screen
Nothing should be permitted to come in contact with the HEPA filter
  NO cleaning solution
  NO aspirate from syringes
  NO glass from ampules
  NO fluids, even if sterile
  DO NOT touch HEPA filter

## Slide 131: Laminar Air Flow Hoods
Only products essential to product preparation should be placed in the laminar flow hood to minimize the potential for contamination
No Paper, Pens, Calculators or Labels in the Hood

## Slide 132: Laminar Air Flow Hoods
Eating, drinking, and smoking is always prohibited
Talking or coughing should be directed away from the hood to minimize air flow turbulence
A mask covering mouth and nose must be worn while working in the hood
The use of a laminar flow hood alone without the observance of aseptic technique, cannot insure product sterility

## Slide 133: Sources of contamination and methods of prevention
Contamination, in broad sense, is the presence of minor unwanted particulate matter called contaminants in atmosphere, physical body, work station etc.
Right from production to packaging almost every sector of pharmaceutical industry comes across contamination.
The most common sources of contamination fall into the following three main categories:
Atmospheric contamination
Fluid contamination
Transfer contaminants

## Slide 134: 1.Atmospheric contamination
Atmospheric conditions during manufacturing as well as during storage affects the quality of final preparation.
Atmosphere in and around the industrial area contains potential contaminants like dust, silica etc and gases like Co2 , water vapor etc.
Besides the above mentioned contaminants, microorganisms like P.aeruginosa, A.niger etc.
These contaminants may get incorporated into the end product either during the process of manufacturing or during purification.

## Slide 135: Contd…
Prevention:
Prior to its entry into the working area, the air should be initially passed through a suitable prefilter then treated with an electrostatic precipitator and finally through HEPA filters.
Periodic removal of air-borne dust settled on walls, floors and ceilings is essential.

## Slide 136: 2.Fluid contamination
Besides serving as the most common solvent in pharmaceutical industry, water also serves as the greatest solvent in pharmaceutical industry.
Although, it is deprived of most of the contaminants yet it contains pyrogens and traces of sulphates, chlorides and carbonates of Ca, Mg and Na.
Therefore, usage of water for washing the machineries and working areas may leave traces of these contaminants.

## Slide 137: Contd…
Prevention:
Almost all of the pharmaceutical operations should be carried out using purified water obtained upon deionization, distillation, ion-exchange, reverse osmosis, filtration or other similar processes.
For the preparation of parenterals, water for injection, sterile water for injection or bacteriostatic water for injection must be employed.

## Slide 138: 3.Transfer contaminants
Transfer contaminants refer to the contaminants sourced from personnel and wheels of trolleys used for transport of goods.
Personnel working in aseptic areas, if suffering from cold, allergies, dermatological conditions or any similar illness carry multiple microorganisms which upon expulsion into atmosphere via sneezing, coughing, talking etc., can lead to contamination.
For example, atmospheric dust particles may get entangled with the fibres of the clothes which can get dislodged due to body movements and lead to contamination.

## Slide 139: Contd…
Prevention:
Personnel should be well trained and periodically evaluated in the principles of aseptic processing and techniques to be employed before participating in the preparation of sterile products.
Apart from gown, the personnel area also required to put on face mask, head cap, gloves, foot covers and even goggle to ensure complete coverage of all skin areas.
The entrance of most of the working areas is equipped with air blowers that aid in removing any loose dirt, lint from uniform of the operators.

## Slide 140: Contd…
Those mechanical pars of the equipments that come in contact with the parenteral products should be demountable which enables their easy cleaning and sterilization.
All the apparatus and their carriers being carried to the aseptic areas should be sterilized by suitable methods.

## Slide 141: Requirements for aseptic area
Conditions to be maintained in aseptic area are as follows,
Environmental control
Traffic control
General cleaning
Clean rooms
Cleaning of air

## Slide 142: Environmental control
The environmental control maintained is different for different areas.
Stringent environmental control is required before and during the processing of parenterals to assure an area free from contamination and where there is no accumulation of dust particles, lint, viable microorganisms etc.
Production environment is constantly monitored and evaluated to assure that the required aseptic conditions are maintained.

## Slide 143: Contd…
Various evaluation tests are available to evaluate the environmental control.
Particle count
Slit to agar (STA) sampler
Rodac plates

## Slide 144: Contd…

## Slide 145: Contd…

## Slide 146: 2.Slit to Agar (STA) Sampler
This device consists of a rotating agar plate comprising of a slit through which measured amount of air is accumulated by applying vacuum.
This air comes in contact with the surface of the agar plate.
Viable microorganisms stick to the surface of the agar plate and start growing in the form of colonies that are counted as colony forming units (CFUs).

## Slide 147: Slit to agar sampler

## Slide 148: 3.Rodac plates
These plates consists of nutrient agar with a convex surface which is rolled on the surface to be tested.
Microorganisms stick to the surface of agar following which the plates are incubated.

## Slide 149: Rodac plates