## Slide 1: Chapter 11: Design Technology

## Slide 2: Outline
Automation: synthesis
Verification: hardware/software co-simulation
Reuse: intellectual property cores
Design process models

## Slide 3: Introduction
Design task
  Define system functionality
  Convert functionality to physical implementation while
    Satisfying constrained metrics
    Optimizing other design metrics
Designing embedded systems is hard
  Complex functionality
    Millions of possible environment scenarios
    Competing, tightly constrained metrics
  Productivity gap
    As low as 10 lines of code or 100 transistors produced per day

## Slide 4: Improving productivity
Design technologies developed to improve productivity
We focus on technologies advancing hardware/software unified view
  Automation
    Program replaces manual design
    Synthesis
  Reuse
    Predesigned components
    Cores
    General-purpose and single-purpose processors on single IC
  Verification
    Ensuring correctness/completeness of each design step
    Hardware/software co-simulation
Reuse
Specification
Implementation
Automation
Verification

## Slide 5: Automation: synthesis
Early design mostly hardware
Software complexity increased with advent of general-purpose processor
Different techniques for software design and hardware design
  Caused division of the two fields
Design tools evolve for higher levels of abstraction
  Different rate in each field
Hardware/software design fields rejoining
  Both can start from behavioral description in sequential program model
  30 years longer for hardware design to reach this step in the ladder
    Many more design dimensions
    Optimization critical
Implementation
Assembly instructions
Machine instructions
Logic gates
Logic equations / FSM's
Register transfers
Sequential program code (e.g., C, VHDL)
Compilers
(1960s,1970s)
Assemblers, linkers
(1950s, 1960s)
Behavioral synthesis
(1990s)
RT synthesis
(1980s, 1990s)
Logic synthesis
(1970s, 1980s)
Microprocessor plus program bits
VLSI, ASIC, or PLD implementation
The codesign ladder

## Slide 6: Hardware/software parallel evolution
Software design evolution
  Machine instructions
  Assemblers
    convert assembly programs into machine instructions
  Compilers
    translate sequential programs into assembly
Hardware design evolution
  Interconnected logic gates
  Logic synthesis
    converts logic equations or FSMs into gates
  Register-transfer (RT) synthesis
    converts FSMDs into FSMs, logic equations, predesigned RT components (registers, adders, etc.)
  Behavioral synthesis
    converts sequential programs into FSMDs
Implementation
Assembly instructions
Machine instructions
Logic gates
Logic equations / FSM's
Register transfers
Sequential program code (e.g., C, VHDL)
Compilers
(1960s,1970s)
Assemblers, linkers
(1950s, 1960s)
Behavioral synthesis
(1990s)
RT synthesis
(1980s, 1990s)
Logic synthesis
(1970s, 1980s)
Microprocessor plus program bits
VLSI, ASIC, or PLD implementation
The codesign ladder

## Slide 7: Increasing abstraction level
Higher abstraction level focus of hardware/software design evolution
  Description smaller/easier to capture
    E.g., Line of sequential program code can translate to 1000 gates
  Many more possible implementations available
    (a) Like flashlight, the higher above the ground, the more ground illuminated
      Sequential program designs may differ in performance/transistor count by orders of magnitude
      Logic-level designs may differ by only power of 2
    (b) Design process proceeds to lower abstraction level, narrowing in on single implementation
(a)
(b)
idea
implementation
back-of-the-envelope
sequential program
register-transfers
logic
modeling cost increases
opportunities decrease
idea
implementation

## Slide 8: Synthesis
Automatically converting system’s behavioral description to a structural implementation
  Complex whole formed by parts
  Structural implementation must optimize design metrics
More expensive, complex than compilers
  Cost = $100s to $10,000s
  User controls 100s of synthesis options
  Optimization critical
    Otherwise could use software
  Optimizations different for each user
  Run time = hours, days

## Slide 9: Gajski’s Y-chart
Each axis represents type of description
  Behavioral
    Defines outputs as function of inputs
    Algorithms but no implementation
  Structural
    Implements behavior by connecting components with known behavior
  Physical
    Gives size/locations of components and wires on chip/board
Synthesis converts behavior at given level to structure at same level or lower
  E.g.,
    FSM → gates, flip-flops (same level)
    FSM → transistors (lower level)
    FSM X registers, FUs (higher level)
    FSM X processors, memories (higher level)
Behavior
Physical
Structural
Processors, memories
Registers, FUs, MUXs
Gates, flip-flops
Transistors
Sequential programs
Register transfers
Logic equations/FSM
Transfer functions
Cell Layout
Modules
Chips
Boards

## Slide 10: Logic synthesis
Logic-level behavior to structural implementation
  Logic equations and/or FSM to connected gates
Combinational logic synthesis
  Two-level minimization (Sum of products/product of sums)
    Best possible performance
      Longest path = 2 gates (AND gate + OR gate/OR gate + AND gate)
    Minimize size
      Minimum cover
      Minimum cover that is prime
      Heuristics
  Multilevel minimization
    Trade performance for size
    Pareto-optimal solution
      Heuristics
FSM synthesis
  State minimization
  State encoding

## Slide 11: Two-level minimization
Represent logic function as sum of products (or product of sums)
  AND gate for each product
  OR gate for each sum
Gives best possible performance
  At most 2 gate delay
Goal: minimize size
  Minimum cover
    Minimum # of AND gates (sum of products)
  Minimum cover that is prime
    Minimum # of inputs to each AND gate (sum of products)
F = abc'd' + a'b'cd + a'bcd + ab'cd
Sum of products
4 4-input AND gates and
1 4-input OR gate
→ 40 transistors
a
b
c
d
F
Direct implementation

## Slide 12: Minimum cover
Minimum # of AND gates (sum of products)
Literal: variable or its complement
  a or a’, b or b’, etc.
Minterm: product of literals
  Each literal appears exactly once
    abc’d’, ab’cd, a’bcd, etc.
Implicant: product of literals
  Each literal appears no more than once
    abc’d’, a’cd, etc.
  Covers 1 or more minterms
    a’cd covers a’bcd and a’b’cd
Cover: set of implicants that covers all minterms of function
Minimum cover: cover with minimum # of implicants

## Slide 13: Minimum cover: K-map approach
Karnaugh map (K-map)
  1 represents minterm
  Circle represents implicant
Minimum cover
  Covering all 1’s with min # of circles
  Example: direct vs. min cover
    Less gates
      4 vs. 5
    Less transistors
      28 vs. 40
11
1
0
0
0
0
0
1
0
1
0
0
0
0
0
0
ab
cd
00
01
11
10
00
01
10
1
1
0
0
0
0
0
1
0
1
0
0
0
0
0
0
ab
cd
00
01
11
10
00
01
11
10
1
F=abc'd' + a'cd + ab'cd
a
b
c
d
F
2 4-input AND gate
1 3-input AND gates
1 4 input OR gate
→ 28 transistors
K-map: sum of products
K-map: minimum cover
Minimum cover
Minimum cover implementation

## Slide 14: Minimum cover that is prime
Minimum # of inputs to AND gates
Prime implicant
  Implicant not covered by any other implicant
  Max-sized circle in K-map
Minimum cover that is prime
  Covering with min # of prime implicants
  Min # of max-sized circles
  Example: prime cover vs. min cover
    Same # of gates
      4 vs. 4
    Less transistors
      26 vs. 28
1
0
0
0
0
0
1
0
1
0
0
0
0
0
0
ab
cd
00
01
11
10
00
01
11
10
1
K-map: minimum cover that is prime
Minimum cover that is prime
F=abc'd' + a'cd + b'cd
1 4-input AND gate
2 3-input AND gates
1 4 input OR gate
→ 26 transistors
F
a
b
c
d
Implementation

## Slide 15: Minimum cover: heuristics
K-maps give optimal solution every time
  Functions with > 6 inputs too complicated
  Use computer-based tabular method
    Finds all prime implicants
    Finds min cover that is prime
    Also optimal solution every time
    Problem: 2n minterms for n inputs
      32 inputs = 4 billion minterms
      Exponential complexity
Heuristic
  Solution technique where optimal solution not guaranteed
  Hopefully comes close

## Slide 16: Heuristics: iterative improvement
Start with initial solution
  i.e., original logic equation
Repeatedly make modifications toward better solution
Common modifications
  Expand
    Replace each nonprime implicant with a prime implicant covering it
    Delete all implicants covered by new prime implicant
  Reduce
    Opposite of expand
  Reshape
    Expands one implicant while reducing another
    Maintains total # of implicants
  Irredundant
    Selects min # of implicants that cover from existing implicants
Synthesis tools differ in modifications used and the order they are used

## Slide 17: Multilevel logic minimization
Trade performance for size
  Increase delay for lower # of gates
  Gray area represents all possible solutions
  Circle with X represents ideal solution
    Generally not possible
  2-level gives best performance
    max delay = 2 gates
    Solve for smallest size
  Multilevel gives pareto-optimal solution
    Minimum delay for a given size
    Minimum size for a given delay
size
delay
multi-level minim.
2-level minim.

## Slide 18: Example
Minimized 2-level logic function:
  F = adef + bdef + cdef + gh
  Requires 5 gates with 18 total gate inputs
    4 ANDS and 1 OR
After algebraic manipulation:
  F = (a + b + c)def + gh
  Requires only 4 gates with 11 total gate inputs
    2 ANDS and 2 ORs
  Less inputs per gate
  Assume gate inputs = 2 transistors
    Reduced by 14 transistors
      36 (18 * 2) down to 22 (11 * 2)
  Sacrifices performance for size
    Inputs a, b, and c now have 3-gate delay
Iterative improvement heuristic commonly used
F
b
c
e
a
d
f
g
h
2-level minimized
F
b
c
e
a
d
f
g
h
multilevel minimized

## Slide 19: FSM synthesis
FSM to gates
State minimization
  Reduce # of states
    Identify and merge equivalent states
      Outputs, next states same for all possible inputs
      Tabular method gives exact solution
        Table of all possible state pairs
        If n states, n2 table entries
        Thus, heuristics used with large # of states
State encoding
  Unique bit sequence for each state
  If n states, log2(n) bits
  n! possible encodings
  Thus, heuristics common

## Slide 20: Technology mapping
Library of gates available for implementation
  Simple
    only 2-input AND,OR gates
  Complex
    various-input AND,OR,NAND,NOR,etc. gates
    Efficiently implemented meta-gates (i.e., AND-OR-INVERT,MUX)
Final structure consists of specified library’s components only
If technology mapping integrated with logic synthesis
  More efficient circuit
  More complex problem
  Heuristics required

## Slide 21: Complexity impact on user
As complexity grows, heuristics used
Heuristics differ tremendously among synthesis tools
  Computationally expensive
    Higher quality results
    Variable optimization effort settings
    Long run times (hours, days)
    Requires huge amounts of memory
    Typically needs to run on servers, workstations
  Fast heuristics
    Lower quality results
    Shorter run times (minutes, hours)
    Smaller amount of memory required
    Could run on PC
Super-linear-time (i.e. n3) heuristics usually used
  User can partition large systems to reduce run times/size
  1003 > 503 + 503 (1,000,000 > 250,000)

## Slide 22: Integrating logic design and physical design
Past
  Gate delay much greater than wire delay
  Thus, performance evaluated as # of levels of gates only
Today
  Gate delay shrinking as feature size shrinking
  Wire delay increasing
    Performance evaluation needs wire length
  Transistor placement (needed for wire length) domain of physical design
  Thus, simultaneous logic synthesis and physical design required for efficient circuits
Wire
Transistor
Delay
Reduced feature size

## Slide 23: Register-transfer synthesis
Converts FSMD to custom single-purpose processor
  Datapath
    Register units to store variables
      Complex data types
    Functional units
      Arithmetic operations
    Connection units
      Buses, MUXs
  FSM controller
    Controls datapath
  Key sub problems:
    Allocation
      Instantiate storage, functional, connection units
    Binding
      Mapping FSMD operations to specific units

## Slide 24: Behavioral synthesis
High-level synthesis
Converts single sequential program to single-purpose processor
  Does not require the program to schedule states
Key sub problems
  Allocation
  Binding
  Scheduling
    Assign sequential program’s operations to states
    Conversion template given in Ch. 2
Optimizations important
  Compiler
    Constant propagation, dead-code elimination, loop unrolling
  Advanced techniques for allocation, binding, scheduling

## Slide 25: System synthesis
Convert 1 or more processes into 1 or more processors (system)
  For complex embedded systems
    Multiple processes may provide better performance/power
    May be better described using concurrent sequential programs
Tasks
  Transformation
    Can merge 2 exclusive processes into 1 process
    Can break 1 large process into separate processes
    Procedure inlining
    Loop unrolling
  Allocation
    Essentially design of system architecture
      Select processors to implement processes
      Also select memories and busses

## Slide 26: System synthesis
Tasks (cont.)
  Partitioning
    Mapping 1 or more processes to 1 or more processors
    Variables among memories
    Communications among buses
  Scheduling
    Multiple processes on a single processor
    Memory accesses
    Bus communications
  Tasks performed in variety of orders
  Iteration among tasks common

## Slide 27: System synthesis
Synthesis driven by constraints
  E.g.,
    Meet performance requirements at minimum cost
      Allocate as much behavior as possible to general-purpose processor
        Low-cost/flexible implementation
      Minimum # of SPPs used to meet performance
System synthesis for GPP only (software)
  Common for decades
    Multiprocessing
    Parallel processing
    Real-time scheduling
Hardware/software codesign
  Simultaneous consideration of GPPs/SPPs during synthesis
  Made possible by maturation of behavioral synthesis in 1990’s

## Slide 28: Temporal vs. spatial thinking
Design thought process changed by evolution of synthesis
Before synthesis
  Designers worked primarily in structural domain
    Connecting simpler components to build more complex systems
      Connecting logic gates to build controller
      Connecting registers, MUXs, ALUs to build datapath
  “capture and simulate” era
    Capture using CAD tools
    Simulate to verify correctness before fabricating
  Spatial thinking
    Structural diagrams
    Data sheets

## Slide 29: Temporal vs. spatial thinking
After synthesis
  “describe-and-synthesize” era
  Designers work primarily in behavioral domain
  “describe and synthesize” era
    Describe FSMDs or sequential programs
    Synthesize into structure
  Temporal thinking
    States or sequential statements have relationship over time
Strong understanding of hardware structure still important
  Behavioral description must synthesize to efficient structural implementation

## Slide 30: Verification
Ensuring design is correct and complete
  Correct
    Implements specification accurately
  Complete
    Describes appropriate output to all relevant input
Formal verification
  Hard
  For small designs or verifying certain key properties only
Simulation
  Most common verification method

## Slide 31: Formal verification
Analyze design to prove or disprove certain properties
Correctness example
  Prove ALU structural implementation equivalent to behavioral description
    Derive Boolean equations for outputs
    Create truth table for equations
    Compare to truth table from original behavior
Completeness example
  Formally prove elevator door can never open while elevator is moving
    Derive conditions for door being open
    Show conditions conflict with conditions for elevator moving

## Slide 32: Simulation
Create computer model of design
  Provide sample input
  Check for acceptable output
Correctness example
  ALU
    Provide all possible input combinations
    Check outputs for correct results
Completeness example
  Elevator door closed when moving
    Provide all possible input sequences
    Check door always closed when elevator moving

## Slide 33: Increases confidence
Simulating all possible input sequences impossible for most systems
  E.g., 32-bit ALU
    232 * 232 = 264 possible input combinations
    At 1 million combinations/sec
    ½ million years to simulate
    Sequential circuits even worse
Can only simulate tiny subset of possible inputs
  Typical values
  Known boundary conditions
    E.g., 32-bit ALU
      Both operands all 0’s
      Both operands all 1’s
Increases confidence of correctness/completeness
Does not prove

## Slide 34: Advantages over physical implementation
Controllability
  Control time
    Stop/start simulation at any time
  Control data values
    Inputs or internal values
Observability
  Examine system/environment values at any time
Debugging
  Can stop simulation at any point and:
    Observe internal values
    Modify system/environment values before restarting
  Can step through small intervals (i.e., 500 nanoseconds)

## Slide 35: Disadvantages
Simulation setup time
  Often has complex external environments
  Could spend more time modeling environment than system
Models likely incomplete
  Some environment behavior undocumented if complex environment
  May not model behavior correctly
Simulation speed much slower than actual execution
  Sequentializing parallel design
    IC: gates operate in parallel
    Simulation: analyze inputs, generate outputs for each gate 1 at time
  Several programs added between simulated system and real hardware
    1 simulated operation:
      = 10 to 100 simulator operations
      = 100 to 10,000 operating system operations
      = 1,000 to 100,000 hardware operations

## Slide 36: Simulation speed
Relative speeds of different types of simulation/emulation
  1 hour actual execution of SOC
    = 1.2 years instruction-set simulation
    = 10,000,000 hours gate-level simulation
10,000,000
gate-level HDL simulation
register-transfer-level HDL simulation
cycle-accurate simulation
instruction-set simulation
throughput model
hardware emulation
FPGA
1 day
1 hour
4 days
1
10
100
1000
10000
100,000
1,000,000
IC
1.4 months
1.2 years
12 years
>1 lifetime
1 millennium

## Slide 37: Overcoming long simulation time
Reduce amount of real time simulated
  1 msec execution instead of 1 hour
    0.001sec * 10,000,000 = 10,000 sec = 3 hours
  Reduced confidence
    1 msec of cruise controller operation tells us little
Faster simulator
  Emulators
    Special hardware for simulations
  Less precise/accurate simulators
    Exchange speed for observability/controllability

## Slide 38: Reducing precision/accuracy
Don’t need gate-level analysis for all simulations
  E.g., cruise control
    Don’t care what happens at every input/output of each logic gate
  Simulating RT components ~10x faster
  Cycle-based simulation ~100x faster
    Accurate at clock boundaries only
    No information on signal changes between boundaries
Faster simulator often combined with reduction in real time
  If willing to simulate for 10 hours
    Use instruction-set simulator
    Real execution time simulated
      10 hours * 1 / 10,000
      = 0.001 hour
      = 3.6 seconds

## Slide 39: Hardware/software co-simulation
Variety of simulation approaches exist
  From very detailed
    E.g., gate-level model
  To very abstract
    E.g., instruction-level model
Simulation tools evolved separately for hardware/software
  Recall separate design evolution
  Software (GPP)
    Typically with instruction-set simulator (ISS)
  Hardware (SPP)
    Typically with models in HDL environment
Integration of GPP/SPP on single IC creating need for merging simulation tools

## Slide 40: Integrating GPP/SPP simulations
Simple/naïve way
  HDL model of microprocessor
    Runs system software
    Much slower than ISS
    Less observable/controllable than ISS
  HDL models of SPPs
  Integrate all models
Hardware-software co-simulator
  ISS for microprocessor
  HDL model for SPPs
  Create communication between simulators
  Simulators run separately except when transferring data
  Faster
  Though, frequent communication between ISS and HDL model slows it down

## Slide 41: Minimizing communication
Memory shared between GPP and SPPs
  Where should memory go?
  In ISS
    HDL simulator must stall for memory access
  In HDL?
    ISS must stall when fetching each instruction
Model memory in both ISS and HDL
  Most accesses by each model unrelated to other’s accesses
    No need to communicate these between models
  Co-simulator ensures consistency of shared data
  Huge speedups (100x or more) reported with this technique

## Slide 42: Emulators
General physical device system mapped to
  Microprocessor emulator
    Microprocessor IC with some monitoring, control circuitry
  SPP emulator
    FPGAs (10s to 100s)
  Usually supports debugging tasks
Created to help solve simulation disadvantages
  Mapped relatively quickly
    Hours, days
  Can be placed in real environment
    No environment setup time
    No incomplete environment
  Typically faster than simulation
    Hardware implementation

## Slide 43: Disadvantages
Still not as fast as real implementations
  E.g., emulated cruise-control may not respond fast enough to keep control of car
Mapping still time consuming
  E.g., mapping complex SOC to 10 FPGAs
    Just partitioning into 10 parts could take weeks
Can be very expensive
  Top-of-the-line FPGA-based emulator: $100,000 to $1mill
  Leads to resource bottleneck
    Can maybe only afford 1 emulator
    Groups wait days, weeks for other group to finish using

## Slide 44: Reuse: intellectual property cores
Commercial off-the-shelf (COTS) components
  Predesigned, prepackaged ICs
  Implements GPP or SPP
  Reduces design/debug time
  Have always been available
System-on-a-chip (SOC)
  All components of system implemented on single chip
  Made possible by increasing IC capacities
  Changing the way COTS components sold
    As intellectual property (IP) rather than actual IC
      Behavioral, structural, or physical descriptions
      Processor-level components known as cores
    SOC built by integrating multiple descriptions

## Slide 45: Cores
Soft core
  Synthesizable behavioral description
  Typically written in HDL (VHDL/Verilog)
Firm core
  Structural description
  Typically provided in HDL
Hard core
  Physical description
  Provided in variety of physical layout file formats
Behavior
Physical
Structural
Processors, memories
Registers, FUs, MUXs
Gates, flip-flops
Transistors
Sequential programs
Register transfers
Logic equations/FSM
Transfer functions
Cell Layout
Modules
Chips
Boards
Gajski’s Y-chart

## Slide 46: Advantages/disadvantages of hard core
Ease of use
  Developer already designed and tested core
    Can use right away
    Can expect to work correctly
Predictability
  Size, power, performance predicted accurately
Not easily mapped (retargeted) to different process
  E.g., core available for vendor X’s 0.25 micrometer CMOS process
    Can’t use with vendor X’s 0.18 micrometer process
    Can’t use with vendor Y

## Slide 47: Advantages/disadvantages of soft/firm cores
Soft cores
  Can be synthesized to nearly any technology
  Can optimize for particular use
    E.g., delete unused portion of core
      Lower power, smaller designs
  Requires more design effort
  May not work in technology not tested for
  Not as optimized as hard core for same processor
Firm cores
  Compromise between hard and soft cores
    Some retargetability
    Limited optimization
    Better predictability/ease of use

## Slide 48: New challenges to processor providers
Cores have dramatically changed business model
  Pricing models
    Past
      Vendors sold product as IC to designers
      Designers must buy any additional copies
        Could not (economically) copy from original
    Today
      Vendors can sell as IP
      Designers can make as many copies as needed
    Vendor can use different pricing models
      Royalty-based model
        Similar to old IC model
        Designer pays for each additional model
      Fixed price model
        One price for IP and as many copies as needed
      Many other models used

## Slide 49: IP protection
Past
  Illegally copying IC very difficult
    Reverse engineering required tremendous, deliberate effort
    “Accidental” copying not possible
Today
  Cores sold in electronic format
    Deliberate/accidental unauthorized copying easier
    Safeguards greatly increased
    Contracts to ensure no copying/distributing
    Encryption techniques
      limit actual exposure to IP
    Watermarking
      determines if particular instance of processor was copied
      whether copy authorized

## Slide 50: New challenges to processor users
Licensing arrangements
  Not as easy as purchasing IC
  More contracts enforcing pricing model and IP protection
    Possibly requiring legal assistance
Extra design effort
  Especially for soft cores
    Must still be synthesized and tested
    Minor differences in synthesis tools can cause problems
Verification requirements more difficult
  Extensive testing for synthesized soft cores and soft/firm cores mapped to particular technology
    Ensure correct synthesis
    Timing and power vary between implementations
  Early verification critical
    Cores buried within IC
    Cannot simply replace bad core

## Slide 51: Design process model
Describes order that design steps are processed
  Behavior description step
  Behavior to structure conversion step
  Mapping structure to physical implementation step
Waterfall model
  Proceed to next step only after current step completed
Spiral model
  Proceed through 3 steps in order but with less detail
  Repeat 3 steps gradually increasing detail
  Keep repeating until desired system obtained
  Becoming extremely popular (hardware & software development)
Behavioral
Structural
Physical
Waterfall design model
Behavioral
Structural
Physical
Spiral design model

## Slide 52: Waterfall method
Not very realistic
  Bugs often found in later steps that must be fixed in earlier step
    E.g., forgot to handle certain input condition
  Prototype often needed to know complete desired behavior
    E.g, customer adds features after product demo
  System specifications commonly change
    E.g., to remain competitive by reducing power, size
      Certain features dropped
Unexpected iterations back through 3 steps cause missed deadlines
  Lost revenues
  May never make it to market
Behavioral
Structural
Physical
Waterfall design model

## Slide 53: Spiral method
First iteration of 3 steps incomplete
Much faster, though
  End up with prototype
    Use to test basic functions
    Get idea of functions to add/remove
  Original iteration experience helps in following iterations of 3 steps
Must come up with ways to obtain structure and physical implementations quickly
  E.g., FPGAs for prototype
    silicon for final product
  May have to use more tools
    Extra effort/cost
Could require more time than waterfall method
  If correct implementation first time with waterfall
Behavioral
Structural
Physical
Spiral design model

## Slide 54: General-purpose processor design models
Previous slides focused on SPPs
Can apply equally to GPPs
  Waterfall model
    Structure developed by particular company
    Acquired by embedded system designer
    Designer develops software (behavior)
    Designer maps application to architecture
      Compilation
      Manual design
  Spiral-like model
    Beginning to be applied by embedded system designers

## Slide 55: Spiral-like model
Designer develops or acquires architecture
Develops application(s)
Maps application to architecture
Analyzes design metrics
Now makes choice
  Modify mapping
  Modify application(s) to better suit architecture
  Modify architecture to better suit application(s)
    Not as difficult now
      Maturation of synthesis/compilers
      IPs can be tuned
Continue refining to lower abstraction level until particular implementation chosen
Architecture
Application(s)
Mapping
Analysis
Y-chart

## Slide 56: Summary
Design technology seeks to reduce gap between IC capacity growth and designer productivity growth
Synthesis has changed digital design
Increased IC capacity means sw/hw components coexist on one chip
Design paradigm shift to core-based design
Simulation essential but hard
Spiral design process is popular

## Slide 57: Book Summary
Embedded systems are common and growing
  Such systems are very different from in the past due to increased IC capacities and automation tools
  Indicator: National Science Foundation just created a separate program on Embedded Systems (2002).
New view:
  Embedded computing systems are built from a collection of processors, some general-purpose (sw), some single-purpose (hw)
  Hw/sw differ in design metrics, not in some fundamental way
  Memory and interfaces necessary to complete system
  Days of embedded system design as assembly-level programming of one microprocessor are fading away
Need to focus on higher-level issues
  State machines, concurrent processes, control systems
  IC technologies, design technologies
There’s a growing, challenging and exciting world of embedded systems design out there. There’s also much more to learn. Enjoy!