## Slide 1: Chapter 1: Introduction
<number>

## Slide 2: Outline
<number>
Embedded systems overview
  What are they?
Design challenge – optimizing design metrics
Technologies
  Processor technologies
  IC technologies
  Design technologies

## Slide 3: Embedded systems overview
<number>
Computing systems are everywhere
Most of us think of “desktop” computers
  PC’s
  Laptops
  Mainframes
  Servers
But there’s another type of computing system
  Far more common...

## Slide 4: Embedded systems overview
<number>
Embedded computing systems
  Computing systems embedded within electronic devices
  Hard to define. Nearly any computing system other than a desktop computer
  Billions of units produced yearly, versus millions of desktop units
  Perhaps 50 per household and per automobile
Computers are in here...
and here...
and even here...
Lots more of these, though they cost a lot less each.

## Slide 5: A “short list” of embedded systems
<number>
And the list goes on and on
Anti-lock brakes
Auto-focus cameras
Automatic teller machines
Automatic toll systems
Automatic transmission
Avionic systems
Battery chargers
Camcorders
Cell phones
Cell-phone base stations
Cordless phones
Cruise control
Curbside check-in systems
Digital cameras
Disk drives
Electronic card readers
Electronic instruments
Electronic toys/games
Factory control
Fax machines
Fingerprint identifiers
Home security systems
Life-support systems
Medical testing systems
Modems
MPEG decoders
Network cards
Network switches/routers
On-board navigation
Pagers
Photocopiers
Point-of-sale systems
Portable video games
Printers
Satellite phones
Scanners
Smart ovens/dishwashers
Speech recognizers
Stereo systems
Teleconferencing systems
Televisions
Temperature controllers
Theft tracking systems
TV set-top boxes
VCR’s, DVD players
Video game consoles
Video phones
Washers and dryers

## Slide 6: Some common characteristics of embedded systems
<number>
Single-functioned
  Executes a single program, repeatedly
Tightly-constrained
  Low cost, low power, small, fast, etc.
Reactive and real-time
  Continually reacts to changes in the system’s environment
  Must compute certain results in real-time without delay

## Slide 7: An embedded system example -- a digital camera
<number>
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Single-functioned -- always a digital camera
Tightly-constrained -- Low cost, low power, small, fast
Reactive and real-time -- only to a small extent

## Slide 8: Design challenge – optimizing design metrics
<number>
Obvious design goal:
  Construct an implementation with desired functionality
Key design challenge:
  Simultaneously optimize numerous design metrics
Design metric
  A measurable feature of a system’s implementation
  Optimizing design metrics is a key challenge

## Slide 9: Design challenge – optimizing design metrics
<number>
Common metrics
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): The one-time monetary cost of designing the system
  Size: the physical space required by the system
  Performance: the execution time or throughput of the system
  Power: the amount of power consumed by the system
  Flexibility: the ability to change the functionality of the system without incurring heavy NRE cost

## Slide 10: Design challenge – optimizing design metrics
<number>
Common metrics (continued)
  Time-to-prototype: the time needed to build a working version of the system
  Time-to-market: the time required to develop a system to the point that it can be released and sold to customers
  Maintainability: the ability to modify the system after its initial release
  Correctness, safety, many more

## Slide 11: Design metric competition -- improving one may worsen others
<number>
Expertise with both software and hardware is needed to optimize design metrics
  Not just a hardware or software expert, as is common
  A designer must be comfortable with various technologies in order to choose the best for a given application and constraints
Size
Performance
Power
NRE cost
Microcontroller
CCD preprocessor
Pixel coprocessor
A2D
D2A
JPEG codec
DMA controller
Memory controller
ISA bus interface
UART
LCD ctrl
Display ctrl
Multiplier/Accum
Digital camera chip
lens
CCD
Hardware
Software

## Slide 12: Time-to-market: a demanding design metric
<number>
Time required to develop a product to the point it can be sold to customers
Market window
  Period during which the product would have highest sales
Average time-to-market constraint is about 8 months
Delays can be costly
Revenues ($)
Time (months)

## Slide 13: Losses due to delayed market entry
<number>
Simplified revenue model
  Product life = 2W, peak at W
  Time of market entry defines a triangle, representing market penetration
  Triangle area equals revenue
Loss
  The difference between the on-time and delayed triangle areas
On-time Delayed
entry entry
Peak revenue
Peak revenue from delayed entry
Market rise
Market fall
W
2W
Time
D
On-time
Delayed
Revenues ($)

## Slide 14: Losses due to delayed market entry (cont.)
<number>
Area = 1/2 * base * height
  On-time = 1/2 * 2W * W
  Delayed = 1/2 * (W-D+W)*(W-D)
Percentage revenue loss = (D(3W-D)/2W2)*100%
Try some examples
On-time Delayed
entry entry
Peak revenue
Peak revenue from delayed entry
Market rise
Market fall
W
2W
Time
D
On-time
Delayed
Revenues ($)
  Lifetime 2W=52 wks, delay D=4 wks
  (4*(3*26 –4)/2*26^2) = 22%
  Lifetime 2W=52 wks, delay D=10 wks
  (10*(3*26 –10)/2*26^2) = 50%
  Delays are costly!

## Slide 15: NRE and unit cost metrics
<number>
Costs:
  Unit cost: the monetary cost of manufacturing each copy of the system, excluding NRE cost
  NRE cost (Non-Recurring Engineering cost): The one-time monetary cost of designing the system
  total cost = NRE cost + unit cost * # of units
  per-product cost = total cost / # of units
  = (NRE cost / # of units) + unit cost
Example
  NRE=$2000, unit=$100
  For 10 units
    total cost = $2000 + 10*$100 = $3000
    per-product cost = $2000/10 + $100 = $300
Amortizing NRE cost over the units results in an additional $200 per unit

## Slide 16: NRE and unit cost metrics
<number>
Compare technologies by costs -- best depends on quantity
  Technology A: NRE=$2,000, unit=$100
  Technology B: NRE=$30,000, unit=$30
  Technology C: NRE=$100,000, unit=$2
But, must also consider time-to-market

## Slide 17: The performance design metric
<number>
Widely-used measure of system, widely-abused
  Clock frequency, instructions per second – not good measures
  Digital camera example – a user cares about how fast it processes images, not clock speed or instructions per second
Latency (response time)
  Time between task start and end
  e.g., Camera’s A and B process images in 0.25 seconds
Throughput
  Tasks per second, e.g. Camera A processes 4 images per second
  Throughput can be more than latency seems to imply due to concurrency, e.g. Camera B may process 8 images per second (by capturing a new image while previous image is being stored).
Speedup of B over S = B’s performance / A’s performance
  Throughput speedup = 8/4 = 2

## Slide 18: Three key embedded system technologies
<number>
Technology
  A manner of accomplishing a task, especially using technical processes, methods, or knowledge
Three key technologies for embedded systems
  Processor technology
  IC technology
  Design technology

## Slide 19: Processor technology
<number>
The architecture of the computation engine used to implement a system’s desired functionality
Processor does not have to be programmable
  “Processor” not equal to general-purpose processor
Application-specific
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control logic and State register
Data
memory
IR
PC
Single-purpose (“hardware”)
Datapath
Controller
Control
logic
State register
Data
memory
index
total
+
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory
General-purpose (“software”)

## Slide 20: Processor technology
<number>
Processors vary in their customization for the problem at hand
total = 0
for i = 1 to N loop
total += M[i]
end loop
General-purpose processor
Single-purpose processor
Application-specific processor
Desired functionality

## Slide 21: General-purpose processors
<number>
Programmable device used in a variety of applications
  Also known as “microprocessor”
Features
  Program memory
  General datapath with large register file and general ALU
User benefits
  Low time-to-market and NRE costs
  High flexibility
“Pentium” the most well-known, but there are hundreds of others
IR
PC
Register
file
General
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 22: Single-purpose processors
<number>
Digital circuit designed to execute exactly one program
  a.k.a. coprocessor, accelerator or peripheral
Features
  Contains only the components needed to execute a single program
  No program memory
Benefits
  Fast
  Low power
  Small size
Datapath
Controller
Control logic
State register
Data
memory
index
total
+

## Slide 23: Application-specific processors
<number>
Programmable processor optimized for a particular class of applications having common characteristics
  Compromise between general-purpose and single-purpose processors
Features
  Program memory
  Optimized datapath
  Special functional units
Benefits
  Some flexibility, good performance, size and power
IR
PC
Registers
Custom
ALU
Datapath
Controller
Program memory
Assembly code for:
total = 0
for i =1 to …
Control
logic and State register
Data
memory

## Slide 24: IC technology
<number>
The manner in which a digital (gate-level) implementation is mapped onto an IC
  IC: Integrated circuit, or “chip”
  IC technologies differ in their customization to a design
  IC’s consist of numerous layers (perhaps 10 or more)
    IC technologies differ with respect to who builds each layer and when
source
drain
channel
oxide
gate
Silicon substrate
IC package
IC

## Slide 25: IC technology
<number>
Three types of IC technologies
  Full-custom/VLSI
  Semi-custom ASIC (gate array and standard cell)
  PLD (Programmable Logic Device)

## Slide 26: Full-custom/VLSI
<number>
All layers are optimized for an embedded system’s particular digital implementation
  Placing transistors
  Sizing transistors
  Routing wires
Benefits
  Excellent performance, small size, low power
Drawbacks
  High NRE cost (e.g., $300k), long time-to-market

## Slide 27: Semi-custom
<number>
Lower layers are fully or partially built
  Designers are left with routing of wires and maybe placing some blocks
Benefits
  Good performance, good size, less NRE cost than a full-custom implementation (perhaps $10k to $100k)
Drawbacks
  Still require weeks to months to develop

## Slide 28: PLD (Programmable Logic Device)
<number>
All layers already exist
  Designers can purchase an IC
  Connections on the IC are either created or destroyed to implement desired functionality
  Field-Programmable Gate Array (FPGA) very popular
Benefits
  Low NRE costs, almost instant IC availability
Drawbacks
  Bigger, expensive (perhaps $30 per unit), power hungry, slower

## Slide 29: Moore’s law
<number>
The most important trend in embedded systems
  Predicted in 1965 by Intel co-founder Gordon Moore
  IC transistor capacity has doubled roughly every 18 months for the past several decades
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic transistors per chip
(in millions)
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2003
2005
2007
2009
Note: logarithmic scale

## Slide 30: Moore’s law
<number>
Wow
  This growth rate is hard to imagine, most people underestimate
  How many ancestors do you have from 20 generations ago
    i.e., roughly how many people alive in the 1500’s did it take to make you?
    220 = more than 1 million people
  (This underestimation is the key to pyramid schemes!)

## Slide 31: Graphical illustration of Moore’s law
<number>
1981
1984
1987
1990
1993
1996
1999
2002
Leading edge
chip in 1981
10,000
transistors
Leading edge
chip in 2002
150,000,000
transistors
Something that doubles frequently grows more quickly than most people realize!
  A 2002 chip can hold about 15,000 1981 chips inside itself

## Slide 32: Design Technology
<number>
The manner in which we convert our concept of desired system functionality into an implementation
Libraries/IP: Incorporates pre-designed implementation from lower abstraction level into higher level.
System
specification
Behavioral
specification
RT
specification
Logic
specification
To final implementation
Compilation/Synthesis: Automates exploration and insertion of implementation details for lower level.
Test/Verification: Ensures correct functionality at each level, thus reducing costly iterations between levels.
Compilation/
Synthesis
Libraries/
IP
Test/
Verification
System
synthesis
Behavior
synthesis
RT
synthesis
Logic
synthesis
Hw/Sw/
OS
Cores
RT
components
Gates/
Cells
Model simulat./
checkers
Hw-Sw
cosimulators
HDL simulators
Gate
simulators
Notes: RT= Register Transfer
<number>

## Slide 33: Design productivity exponential increase
<number>
Exponential increase over the past few decades
100,000
10,000
1,000
100
10
1
0.1
0.01
1983
1981
1987
1989
1991
1993
1985
1995
1997
1999
2001
2003
2005
2007
2009
Productivity
(K) Trans./Staff – Mo.

## Slide 34: The co-design ladder
<number>
In the past:
  Hardware and software design technologies were very different
  Recent maturation of synthesis enables a unified view of hardware and software
Hardware/software “codesign”
Implementation
Assembly instructions
Machine instructions
Register transfers
Compilers
(1960's,1970's)
Assemblers, linkers
(1950's, 1960's)
Behavioral synthesis
(1990's)
RT synthesis
(1980's, 1990's)
Logic synthesis
(1970's, 1980's)
Microprocessor plus program bits: “software”
VLSI, ASIC, or PLD implementation: “hardware”
Logic gates
Logic equations / FSM's
Sequential program code (e.g., C, VHDL)
The choice of hardware versus software for a particular function is simply a tradeoff among various design metrics, like performance, power, size, NRE cost, and especially flexibility; there is no fundamental difference between what hardware or software can implement.
Notes: ASIC=Application-Specific Integrated Circuit
<number>

## Slide 35: Independence of processor and IC technologies
<number>
Basic tradeoff
  General vs. custom
  With respect to processor technology or IC technology
  The two technologies are independent
General-purpose
processor
ASIP
Single-
purpose
processor
Semi-custom
PLD
Full-custom
General,
providing improved:
Customized,
providing improved:
Power efficiency
Performance
Size
Cost (high volume)
Flexibility
Maintainability
NRE cost
Time- to-prototype
Time-to-market
Cost (low volume)

## Slide 36: Design productivity gap
<number>
While designer productivity has grown at an impressive rate over the past decades, the rate of improvement has not kept pace with chip capacity
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic transistors per chip
(in millions)
100,000
10,000
1000
100
10
1
0.1
0.01
Productivity
(K) Trans./Staff-Mo.
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2003
2005
2007
2009
IC capacity
productivity
Gap

## Slide 37: Design productivity gap
<number>
1981 leading edge chip required 100 designer months
  10,000 transistors / 100 transistors/month
2002 leading edge chip requires 30,000 designer months
  150,000,000 / 5000 transistors/month
Designer cost increase from $1M to $300M
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic transistors per chip
(in millions)
100,000
10,000
1000
100
10
1
0.1
0.01
Productivity
(K) Trans./Staff-Mo.
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2003
2005
2007
2009
IC capacity
productivity
Gap

## Slide 38: The mythical man-month
<number>
The situation is even worse than the productivity gap indicates
In theory, adding designers to team reduces project completion time
In reality, productivity per designer decreases due to complexities of team management and communication
In the software community, known as “the mythical man-month” (Brooks 1975)
At some point, can actually lengthen project completion time! (“Too many cooks”)
10
20
30
40
0
10000
20000
30000
40000
50000
60000
43
24
19
16
15
16
18
23
Team
Individual
Months until completion
Number of designers
1M transistors, 1 designer=5000 trans/month
Each additional designer reduces for 100 trans/month
So 2 designers produce 4900 trans/month each

## Slide 39: Summary
<number>
Embedded systems are everywhere
Key challenge: optimization of design metrics
  Design metrics compete with one another
A unified view of hardware and software is necessary to improve productivity
Three key technologies
  Processor: general-purpose, application-specific, single-purpose
  IC: Full-custom, semi-custom, PLD
  Design: Compilation/synthesis, libraries/IP, test/verification