## Slide 1: Chapter 3 General-Purpose Processors: Software

## Slide 2: Introduction
General-Purpose Processor
  Processor designed for a variety of computation tasks
  Low unit cost, in part because manufacturer spreads NRE over large numbers of units
    Motorola sold half a billion 68HC05 microcontrollers in 1996 alone
  Carefully designed since higher NRE is acceptable
    Can yield good performance, size and power
  Low NRE cost, short time-to-market/prototype, high flexibility
    User just writes software; no processor design
  a.k.a. “microprocessor” – “micro” used when they were implemented on one or a few chips rather than entire rooms

## Slide 3: Basic Architecture
Control unit and datapath
  Note similarity to single-purpose processor
Key differences
  Datapath is general
  Control unit doesn’t store the algorithm – the algorithm is “programmed” into the memory
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status

## Slide 4: Datapath Operations
Load
  Read memory location into register
ALU operation
  Input certain registers through ALU, store back in register
Store
  Write register to memory location
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
10
+1
11
11

## Slide 5: Control Unit
Control unit: configures the datapath operations
  Sequence of desired operations (“instructions”) stored in memory – “program”
Instruction cycle – broken into several sub-operations, each one clock cycle, e.g.:
  Fetch: Get next instruction into IR
  Decode: Determine what the instruction means
  Fetch operands: Move data from memory to datapath register
  Execute: Move data through the ALU
  Store results: Write data from register to memory
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1

## Slide 6: Control Unit Sub-Operations
Fetch
  Get next instruction into IR
  PC: program counter, always points to next instruction
  IR: holds the fetched instruction
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
100
load R0, M[500]

## Slide 7: Control Unit Sub-Operations
Decode
  Determine what the instruction means
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
100
load R0, M[500]

## Slide 8: Control Unit Sub-Operations
Fetch operands
  Move data from memory to datapath register
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
100
load R0, M[500]
10

## Slide 9: Control Unit Sub-Operations
Execute
  Move data through the ALU
  This particular instruction does nothing during this sub-operation
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
100
load R0, M[500]
10

## Slide 10: Control Unit Sub-Operations
Store results
  Write data from register to memory
  This particular instruction does nothing during this sub-operation
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
100
load R0, M[500]
10

## Slide 11: Instruction Cycles
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
PC=100
10
Fetch ops
Exec.
Store results
clk
Fetch
load R0, M[500]
Decode
100

## Slide 12: Instruction Cycles
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
10
PC=100
Fetch
Decode
Fetch ops
Exec.
Store results
clk
PC=101
inc R1, R0
Fetch
Fetch ops
+1
11
Exec.
Store results
clk
101
Decode

## Slide 13: Instruction Cycles
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status
10
...
...
load R0, M[500]
500
501
100
inc R1, R0
101
store M[501], R1
102
R0
R1
11
10
PC=100
Fetch
Decode
Fetch ops
Exec.
Store results
clk
PC=101
Fetch
Decode
Fetch ops
Exec.
Store results
clk
PC=102
store M[501], R1
Fetch
Fetch ops
Exec.
11
Store results
clk
Decode
102

## Slide 14: Architectural Considerations
N-bit processor
  N-bit ALU, registers, buses, memory data interface
  Embedded: 8-bit, 16-bit, 32-bit common
  Desktop/servers: 32-bit, even 64
PC size determines address space
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status

## Slide 15: Architectural Considerations
Clock frequency
  Inverse of clock period
  Must be longer than longest register to register delay in entire processor
  Memory access is often the longest
Processor
Control unit
Datapath
ALU
Registers
IR
PC
Controller
Memory
I/O
Control
/Status

## Slide 16: Pipelining: Increasing Instruction Throughput
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Fetch-instr.
Decode
Fetch ops.
Execute
Store res.
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Wash
Dry
Time
Non-pipelined
Pipelined
Time
Time
Pipelined
pipelined instruction execution
non-pipelined dish cleaning
pipelined dish cleaning
Instruction 1

## Slide 17: Superscalar and VLIW Architectures
Performance can be improved by:
  Faster clock (but there’s a limit)
  Pipelining: slice up instruction into stages, overlap stages
  Multiple ALUs to support more than one instruction stream
    Superscalar
      Scalar: non-vector operations
      Fetches instructions in batches, executes as many as possible
        May require extensive hardware to detect independent instructions
      VLIW: each word in memory has multiple independent instructions
        Relies on the compiler to detect and schedule instructions
        Currently growing in popularity

## Slide 18: Two Memory Architectures
Processor
Program memory
Data memory
Processor
Memory
(program and data)
Harvard
Princeton
Princeton
  Fewer memory wires
Harvard
  Simultaneous program and data memory access

## Slide 19: Cache Memory
Memory access may be slow
Cache is small but fast memory close to processor
  Holds copy of part of memory
  Hits and misses
Processor
Memory
Cache
Fast/expensive technology, usually on the same chip
Slower/cheaper technology, usually on a different chip

## Slide 20: Programmer’s View
Programmer doesn’t need detailed understanding of architecture
  Instead, needs to know what instructions can be executed
Two levels of instructions:
  Assembly level
  Structured languages (C, C++, Java, etc.)
Most development today done using structured languages
  But, some assembly level programming may still be necessary
  Drivers: portion of program that communicates with and/or controls (drives) another device
    Often have detailed timing considerations, extensive bit manipulation
    Assembly level may be best for these

## Slide 21: Assembly-Level Instructions
opcode
operand1
operand2
opcode
operand1
operand2
opcode
operand1
operand2
opcode
operand1
operand2
...
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction Set
  Defines the legal set of instructions for that processor
    Data transfer: memory/register, register/register, I/O, etc.
    Arithmetic/logical: move register through ALU and back
    Branches: determine next PC value when not just PC+1

## Slide 22: A Simple (Trivial) Instruction Set
opcode operands
MOV Rn, direct
MOV @Rn, Rm
ADD Rn, Rm
0000
Rn
direct
0010
Rn
0100
Rm
Rn
Rn = M(direct)
Rn = Rn + Rm
SUB Rn, Rm
0101
Rm
Rn = Rn - Rm
MOV Rn, #immed.
0011
Rn
immediate
Rn = immediate
Assembly instruct.
First byte
Second byte
Operation
JZ Rn, relative
0110
Rn
relative
PC = PC+ relative
(only if Rn is 0)
Rn
MOV direct, Rn
0001
Rn
direct
M(direct) = Rn
Rm
M(Rn) = Rm

## Slide 23: Addressing Modes
Data
Immediate
Register-direct
Register
indirect
Direct
Indirect
Data
Operand field
Register address
Register address
Memory address
Memory address
Memory address
Data
Data
Memory address
Data
Addressing
mode
Register-file
contents
Memory
contents

## Slide 24: Sample Programs
int total = 0;
for (int i=10; i!=0; i--)
total += i;
// next instructions...
C program
MOV R0, #0; // total = 0
MOV R1, #10; // i = 10
JZ R1, Next; // Done if i=0
ADD R0, R1; // total += i
MOV R2, #1; // constant 1
JZ R3, Loop; // Jump always
Loop:
Next:
// next instructions...
SUB R1, R2; // i--
Equivalent assembly program
MOV R3, #0; // constant 0
0
1
2
3
5
6
7
Try some others
  Handshake: Wait until the value of M[254] is not 0, set M[255] to 1, wait until M[254] is 0, set M[255] to 0 (assume those locations are ports).
  (Harder) Count the occurrences of zero in an array stored in memory locations 100 through 199.

## Slide 25: Programmer Considerations
Program and data memory space
  Embedded processors often very limited
    e.g., 64 Kbytes program, 256 bytes of RAM (expandable)
Registers: How many are there?
  Only a direct concern for assembly-level programmers
I/O
  How communicate with external signals?
Interrupts

## Slide 26: Microprocessor Architecture Overview
If you are using a particular microprocessor, now is a good time to review its architecture

## Slide 27: Example: parallel port driver
Using assembly language programming we can configure a PC parallel port to perform digital I/O
  write and read to three special registers to accomplish this table provides list of parallel port connector pins and corresponding register location
  Example : parallel port monitors the input switch and turns the LED on/off accordingly
LPT Connection Pin
I/O Direction
Register Address
1
Output
0th bit of register #2
2-9
Output
0th bit of register #2
14,16,17
Output
1,2,3th bit of register #2
10,11,12,13,15
Input
6,7,5,4,3th bit of register #1

## Slide 28: Parallel Port Example
; This program consists of a sub-routine that reads
; the state of the input pin, determining the on/off state
; of our switch and asserts the output pin, turning the LED
; on/off accordingly
.386
CheckPort proc
push ax ; save the content
push dx ; save the content
mov dx, 3BCh + 1 ; base + 1 for register #1
in al, dx ; read register #1
and al, 10h ; mask out all but bit # 4
cmp al, 0 ; is it 0?
jne SwitchOn ; if not, we need to turn the LED on
SwitchOff:
mov dx, 3BCh + 0 ; base + 0 for register #0
in al, dx ; read the current state of the port
and al, f7h ; clear first bit (masking)
out dx, al ; write it out to the port
jmp Done ; we are done
SwitchOn:
mov dx, 3BCh + 0 ; base + 0 for register #0
in al, dx ; read the current state of the port
or al, 01h ; set first bit (masking)
out dx, al ; write it out to the port
Done: pop dx ; restore the content
pop ax ; restore the content
CheckPort endp
extern “C” CheckPort(void); // defined in // assembly
void main(void) {
while( 1 ) {
CheckPort();
}
}
LPT Connection Pin
I/O Direction
Register Address
1
Output
0th bit of register #2
2-9
Output
0th bit of register #2
14,16,17
Output
1,2,3th bit of register #2
10,11,12,13,15
Input
6,7,5,4,3th bit of register #1

## Slide 29: Operating System
Optional software layer providing low-level services to a program (application).
  File management, disk access
  Keyboard/display interfacing
  Scheduling multiple programs for execution
    Or even just multiple threads from one program
  Program makes system calls to the OS
DB file_name “out.txt” -- store file name
MOV R0, 1324 -- system call “open” id
MOV R1, file_name -- address of file-name
INT 34 -- cause a system call
JZ R0, L1 -- if zero -> error
. . . read the file
JMP L2 -- bypass error cond.
L1:
. . . handle the error
L2:

## Slide 30: Development Environment
Development processor
  The processor on which we write and debug our programs
    Usually a PC
Target processor
  The processor that the program will run on in our embedded system
    Often different from the development processor
Development processor
Target processor

## Slide 31: Software Development Process
Compiler
Linker
C File
C File
Asm. File
Binary File
Binary File
Binary File
Exec. File
Assembler
Library
Implementation Phase
Debugger
Profiler
Verification Phase
Compilers
  Cross compiler
    Runs on one processor, but generates code for another
Assemblers
Linkers
Debuggers
Profilers

## Slide 32: Running a Program
If development processor is different than target, how can we run our compiled code? Two options:
  Download to target processor
  Simulate
Simulation
  One method: Hardware description language
    But slow, not always available
  Another method: Instruction set simulator (ISS)
    Runs on development processor, but executes instructions of target processor

## Slide 33: Instruction Set Simulator For A Simple Processor
#include <stdio.h>
typedef struct {
unsigned char first_byte, second_byte;
} instruction;
instruction program[1024]; //instruction memory
unsigned char memory[256]; //data memory
void run_program(int num_bytes) {
int pc = -1;
unsigned char reg[16], fb, sb;
while( ++pc < (num_bytes / 2) ) {
fb = program[pc].first_byte;
sb = program[pc].second_byte;
switch( fb >> 4 ) {
case 0: reg[fb & 0x0f] = memory[sb]; break;
case 1: memory[sb] = reg[fb & 0x0f]; break;
case 2: memory[reg[fb & 0x0f]] =
reg[sb >> 4]; break;
case 3: reg[fb & 0x0f] = sb; break;
case 4: reg[fb & 0x0f] += reg[sb >> 4]; break;
case 5: reg[fb & 0x0f] -= reg[sb >> 4]; break;
case 6: pc += sb; break;
default: return –1;
}
}
return 0;
}
int main(int argc, char *argv[]) {
FILE* ifs;
If( argc != 2 ||
(ifs = fopen(argv[1], “rb”) == NULL ) {
return –1;
}
if (run_program(fread(program,
sizeof(program) == 0) {
print_memory_contents();
return(0);
}
else return(-1);
}

## Slide 34: Testing and Debugging
Implementation Phase
Implementation Phase
Verification Phase
Verification
Phase
Emulator
Debugger/ ISS
Programmer
Development processor
(a)
(b)
External tools
ISS
  Gives us control over time – set breakpoints, look at register values, set values, step-by-step execution, ...
  But, doesn’t interact with real environment
Download to board
  Use device programmer
  Runs in real environment, but not controllable
Compromise: emulator
  Runs in real environment, at speed or near
  Supports some controllability from the PC

## Slide 35: Application-Specific Instruction-Set Processors (ASIPs)
General-purpose processors
  Sometimes too general to be effective in demanding application
    e.g., video processing – requires huge video buffers and operations on large arrays of data, inefficient on a GPP
  But single-purpose processor has high NRE, not programmable
ASIPs – targeted to a particular domain
  Contain architectural features specific to that domain
    e.g., embedded control, digital signal processing, video processing, network processing, telecommunications, etc.
  Still programmable

## Slide 36: A Common ASIP: Microcontroller
For embedded control applications
  Reading sensors, setting actuators
  Mostly dealing with events (bits): data is present, but not in huge amounts
  e.g., VCR, disk drive, digital camera (assuming SPP for image compression), washing machine, microwave oven
Microcontroller features
  On-chip peripherals
    Timers, analog-digital converters, serial communication, etc.
    Tightly integrated for programmer, typically part of register space
  On-chip program and data memory
  Direct programmer access to many of the chip’s pins
  Specialized instructions for bit-manipulation and other low-level operations

## Slide 37: Another Common ASIP: Digital Signal Processors (DSP)
For signal processing applications
  Large amounts of digitized data, often streaming
  Data transformations must be applied fast
  e.g., cell-phone voice filter, digital TV, music synthesizer
DSP features
  Several instruction execution units
  Multiple-accumulate single-cycle instruction, other instrs.
  Efficient vector operations – e.g., add two arrays
    Vector ALUs, loop buffers, etc.

## Slide 38: Trend: Even More Customized ASIPs
In the past, microprocessors were acquired as chips
Today, we increasingly acquire a processor as Intellectual Property (IP)
  e.g., synthesizable VHDL model
Opportunity to add a custom datapath hardware and a few custom instructions, or delete a few instructions
  Can have significant performance, power and size impacts
  Problem: need compiler/debugger for customized ASIP
    Remember, most development uses structured languages
    One solution: automatic compiler/debugger generation
      e.g., www.tensillica.com
    Another solution: retargettable compilers
      e.g., www.improvsys.com (customized VLIW architectures)

## Slide 39: Selecting a Microprocessor
Issues
  Technical: speed, power, size, cost
  Other: development environment, prior expertise, licensing, etc.
Speed: how evaluate a processor’s speed?
  Clock speed – but instructions per cycle may differ
  Instructions per second – but work per instr. may differ
  Dhrystone: Synthetic benchmark, developed in 1984. Dhrystones/sec.
    MIPS: 1 MIPS = 1757 Dhrystones per second (based on Digital’s VAX 11/780). A.k.a. Dhrystone MIPS. Commonly used today.
      So, 750 MIPS = 750*1757 = 1,317,750 Dhrystones per second
  SPEC: set of more realistic benchmarks, but oriented to desktops
  EEMBC – EDN Embedded Benchmark Consortium, www.eembc.org
    Suites of benchmarks: automotive, consumer electronics, networking, office automation, telecommunications

## Slide 40: General Purpose Processors
Sources: Intel, Motorola, MIPS, ARM, TI, and IBM Website/Datasheet; Embedded Systems Programming, Nov. 1998

## Slide 41: Designing a General Purpose Processor
Not something an embedded system designer normally would do
  But instructive to see how simply we can build one top down
  Remember that real processors aren’t usually built this way
    Much more optimized, much more bottom-up design
Declarations:
bit PC[16], IR[16];
bit M[64k][16], RF[16][16];
Aliases:
op IR[15..12]
rn IR[11..8]
rm IR[7..4]
dir IR[7..0]
imm IR[7..0]
rel IR[7..0]
Reset
Fetch
Decode
IR=M[PC];
PC=PC+1
Mov1
RF[rn] = M[dir]
Mov2
Mov3
Mov4
Add
Sub
Jz
0110
0101
0100
0011
0010
0001
op = 0000
M[dir] = RF[rn]
M[rn] = RF[rm]
RF[rn]= imm
RF[rn] =RF[rn]+RF[rm]
RF[rn] = RF[rn]-RF[rm]
PC=(RF[rn]=0) ?rel :PC
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
PC=0;
from states
below
FSMD

## Slide 42: Architecture of a Simple Microprocessor
Storage devices for each declared variable
  register file holds each of the variables
Functional units to carry out the FSMD operations
  One ALU carries out every required operation
Connections added among the components’ ports corresponding to the operations required by the FSM
Unique identifiers created for every control signal
Datapath
IR
PC
Controller
(Next-state and control
logic; state register)
Memory
RF (16)
RFwa
RFwe
RFr1a
RFr1e
RFr2a
RFr2e
RFr1
RFr2
RFw
ALU
ALUs
2x1 mux
ALUz
RFs
PCld
PCinc
PCclr
3x1 mux
Ms
Mwe
Mre
To all input control signals
From all output control signals
Control unit
16
Irld
2
1
0
A
D
1
0

## Slide 43: A Simple Microprocessor
FSM operations that replace the FSMD operations after a datapath is created
RFwa=rn; RFwe=1; RFs=01;
Ms=01; Mre=1;
RFr1a=rn; RFr1e=1;
Ms=01; Mwe=1;
RFr1a=rn; RFr1e=1;
Ms=10; Mwe=1;
RFwa=rn; RFwe=1; RFs=10;
RFwa=rn; RFwe=1; RFs=00;
RFr1a=rn; RFr1e=1;
RFr2a=rm; RFr2e=1; ALUs=00
RFwa=rn; RFwe=1; RFs=00;
RFr1a=rn; RFr1e=1;
RFr2a=rm; RFr2e=1; ALUs=01
PCld= ALUz;
RFrla=rn;
RFrle=1;
MS=10;
Irld=1;
Mre=1;
PCinc=1;
PCclr=1;
Reset
Fetch
Decode
IR=M[PC];
PC=PC+1
Mov1
RF[rn] = M[dir]
Mov2
Mov3
Mov4
Add
Sub
Jz
0110
0101
0100
0011
0010
0001
op = 0000
M[dir] = RF[rn]
M[rn] = RF[rm]
RF[rn]= imm
RF[rn] =RF[rn]+RF[rm]
RF[rn] = RF[rn]-RF[rm]
PC=(RF[rn]=0) ?rel :PC
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
to Fetch
PC=0;
from states
below
FSMD
Datapath
IR
PC
Controller
(Next-state and control
logic; state register)
Memory
RF (16)
RFwa
RFwe
RFr1a
RFr1e
RFr2a
RFr2e
RFr1
RFr2
RFw
ALU
ALUs
2x1 mux
ALUz
RFs
PCld
PCinc
PCclr
3x1 mux
Ms
Mwe
Mre
To all input control signals
From all output control signals
Control unit
16
Irld
2
1
0
A
D
1
0
You just built a simple microprocessor!

## Slide 44: Chapter Summary
General-purpose processors
  Good performance, low NRE, flexible
Controller, datapath, and memory
Structured languages prevail
  But some assembly level programming still necessary
Many tools available
  Including instruction-set simulators, and in-circuit emulators
ASIPs
  Microcontrollers, DSPs, network processors, more customized ASIPs
Choosing among processors is an important step
Designing a general-purpose processor is conceptually the same as designing a single-purpose processor