## Slide 1: Chapter 4 Standard Single Purpose Processors: Peripherals

## Slide 2: Introduction
Single-purpose processors
  Performs specific computation task
  Custom single-purpose processors
    Designed by us for a unique task
  Standard single-purpose processors
    “Off-the-shelf” -- pre-designed for a common task
    a.k.a., peripherals
    serial transmission
    analog/digital conversions

## Slide 3: Timers, counters, watchdog timers
Timer: measures time intervals
  To generate timed output events
    e.g., hold traffic light green for 10 s
  To measure input events
    e.g., measure a car’s speed
Based on counting clock pulses
    E.g., let Clk period be 10 ns
    And we count 20,000 Clk pulses
    Then 200 microseconds have passed
    16-bit counter would count up to 65,535*10 ns = 655.35 microsec., resolution = 10 ns
    Top: indicates top count reached, wrap-around
16-bit up counter
Clk
Cnt
Basic timer
Top
Reset
16

## Slide 4: Counters
Counter: like a timer, but counts pulses on a general input signal rather than clock
  e.g., count cars passing over a sensor
  Can often configure device as either a timer or counter
16-bit up counter
Clk
16
Cnt_in
2x1 mux
Mode
Timer/counter
Top
Reset
Cnt

## Slide 5: Other timer structures
Top2
Time with prescaler
16-bit up counter
Clk
Prescaler
Mode
Interval timer
  Indicates when desired time interval has passed
  We set terminal count to desired interval
    Number of clock cycles = Desired time interval / Clock period
Cascaded counters
Prescaler
  Divides clock
  Increases range, decreases resolution
16-bit up counter
Clk
16
Terminal count
=
Top
Reset
Timer with a terminal count
Cnt
16-bit up counter
Clk
16-bit up counter
16
Cnt2
Top1
16/32-bit timer
Cnt1
16

## Slide 6: Example: Reaction Timer
indicator light
reaction button
time: 100 ms
LCD
/* main.c */
#define MS_INIT 63535
void main(void){
int count_milliseconds = 0;
configure timer mode
set Cnt to MS_INIT
wait a random amount of time
turn on indicator light
start timer
while (user has not pushed reaction button){
if(Top) {
stop timer
set Cnt to MS_INIT
start timer
reset Top
count_milliseconds++;
}
}
turn light off
printf(“time: %i ms“, count_milliseconds);
}
Measure time between turning light on and user pushing button
  16-bit timer, clk period is 83.33 ns, counter increments every 6 cycles
  Resolution = 6*83.33=0.5 microsec.
  Range = 65535*0.5 microseconds = 32.77 milliseconds
  Want program to count millisec., so initialize counter to 65535 – 1000/0.5 = 63535

## Slide 7: Watchdog timer
scalereg
checkreg
timereg
to system reset
or
interrupt
osc
clk
prescaler
overflow
overflow
/* main.c */
main(){
wait until card inserted
call watchdog_reset_routine
while(transaction in progress){
if(button pressed){
perform corresponding action
call watchdog_reset_routine
}
/* if watchdog_reset_routine not called every < 2 minutes, interrupt_service_routine is called */
}
watchdog_reset_routine(){
/* checkreg is set so we can load value into timereg. Zero is loaded into scalereg and 11070 is loaded into timereg */
checkreg = 1
scalereg = 0
timereg = 11070
}
void interrupt_service_routine(){
eject card
reset screen
}
Must reset timer every X time unit, else timer generates a signal
Common use: detect failure, self-reset
Another use: timeouts
  e.g., ATM machine
  16-bit timer, 2 microsec. resolution
  timereg value = 2*(216-1)–X = 131070–X
  For 2 min., X = 120,000 microsec.

## Slide 8: Serial Transmission Using UARTs
embedded device
1
0
0
1
1
0
1
1
Sending UART
1
0
0
1
1
0
1
1
Receiving UART
1
0
0
1
1
0
1
1
start bit
data
end bit
UART: Universal Asynchronous Receiver Transmitter
  Takes parallel data and transmits serially
  Receives serial data and converts to parallel
Parity: extra bit for simple error checking
Start bit, stop bit
Baud rate
  signal changes per second
  bit rate usually higher

## Slide 9: Pulse width modulator
clk
pwm_o
25% duty cycle – average pwm_o is 1.25V
clk
pwm_o
50% duty cycle – average pwm_o is 2.5V.
clk
pwm_o
75% duty cycle – average pwm_o is 3.75V.
Generates pulses with specific high/low times
Duty cycle: % time high
  Square wave: 50% duty cycle
Common use: control average voltage to electric device
  Simpler than DC-DC converter or digital-analog converter
  DC motor speed, dimmer lights
Another use: encode commands, receiver uses timer to decode

## Slide 10: Controlling a DC motor with a PWM
void main(void){
/* controls period */
PWMP = 0xff;
/* controls duty cycle */
PWM1 = 0x7f;
while(1){};
}
The PWM alone cannot drive the DC motor, a possible way to implement a driver is shown below using an MJE3055T NPN transistor.
Internal Structure of PWM
clk_div
cycle_high
counter
( 0 – 254)
8-bit
comparator
controls how fast the counter increments
counter < cycle_high,
pwm_o = 1
counter >= cycle_high,
pwm_o = 0
pwm_o
clk
Relationship between applied voltage and speed of the DC Motor
DC
MOTOR
5V
From processor

## Slide 11: LCD controller
E
R/W
RS
DB7–DB0
LCD controller
communications bus
microcontroller
8
void WriteChar(char c){
RS = 1; /* indicate data being sent */
DATA_BUS = c; /* send data to LCD */
EnableLCD(45); /* toggle the LCD with appropriate delay */
}

## Slide 12: Keypad controller
N1
N2
N3
N4
M1
M2
M3
M4
key_code
keypad controller
k_pressed
key_code
4
N=4, M=4

## Slide 13: Stepper motor controller
Red A
White A’
Yellow B
Black B’
MC3479P
1
5
4
3
2
7
8
6
16
15
14
13
12
11
10
9
Vd
A’
A
GND
Bias’/Set
Clk
O|C
Vm
B
B’
GND
Phase A’
CW’/CCW
Full’/Half Step
Stepper motor: rotates fixed number of degrees when given a “step” signal
  In contrast, DC motor just rotates when power applied, coasts to stop
Rotation achieved by applying specific voltage sequence to coils
Controller greatly simplifies this

## Slide 14: Stepper motor with controller (driver)
2 A’
3 A
10
7
B 15
B’ 14
MC3479P
Stepper Motor Driver
8051
P1.0
P1.1
Stepper
Motor
CLK
CW’/CCW
The output pins on the stepper motor driver do not provide enough current to drive the stepper motor. To amplify the current, a buffer is needed. One possible implementation of the buffers is pictured to the left. Q1 is an MJE3055T NPN transistor and Q2 is an MJE2955T PNP transistor. A is connected to the 8051 microcontroller and B is connected to the stepper motor.
void main(void){
*/turn the motor forward */
cw=0; /* set direction */
clk=0; /* pulse clock */
delay();
clk=1;
/*turn the motor backwards */
cw=1; /* set direction */
clk=0; /* pulse clock */
delay();
clk=1;
}
/* main.c */
sbit clk=P1^1;
sbit cw=P1^0;
void delay(void){
int i, j;
for (i=0; i<1000; i++)
for ( j=0; j<50; j++)
i = i + 0;
}

## Slide 15: Stepper motor without controller (driver)
Stepper
Motor
8051
GND/ +V
P2.4
P2.3
P2.2
P2.1
P2.0
A possible way to implement the buffers is located below. The 8051 alone cannot drive the stepper motor, so several transistors were added to increase the current going to the stepper motor. Q1 are MJE3055T NPN transistors and Q3 is an MJE2955T PNP transistor. A is connected to the 8051 microcontroller and B is connected to the stepper motor.
Q2
+V
1K
Q1
1K
+V
A
B
330
/*main.c*/
sbit notA=P2^0;
sbit isA=P2^1;
sbit notB=P2^2;
sbit isB=P2^3;
sbit dir=P2^4;
void delay(){
int a, b;
for(a=0; a<5000; a++)
for(b=0; b<10000; b++)
a=a+0;
}
void move(int dir, int steps) {
int y, z;
/* clockwise movement */
if(dir == 1){
for(y=0; y<=steps; y++){
for(z=0; z<=19; z+4){
isA=lookup[z];
isB=lookup[z+1];
notA=lookup[z+2];
notB=lookup[z+3];
delay();
}
}
}
/* counter clockwise movement */
if(dir==0){
for(y=0; y<=step; y++){
for(z=19; z>=0; z - 4){
isA=lookup[z];
isB=lookup[z-1];
notA=lookup[z -2];
notB=lookup[z-3];
delay( );
}
}
}
}
void main( ){
int z;
int lookup[20] = {
1, 1, 0, 0,
0, 1, 1, 0,
0, 0, 1, 1,
1, 0, 0, 1,
1, 1, 0, 0 };
while(1){
/*move forward, 15 degrees (2 steps) */
move(1, 2);
/* move backwards, 7.5 degrees (1step)*/
move(0, 1);
}
}

## Slide 16: Analog-to-digital converters
proportionality
Vmax = 7.5V
0V
1111
1110
0000
0010
0100
0110
1000
1010
1100
0001
0011
0101
0111
1001
1011
1101
0.5V
1.0V
1.5V
2.0V
2.5V
3.0V
3.5V
4.0V
4.5V
5.0V
5.5V
6.0V
6.5V
7.0V
analog to digital
4
3
2
1
t1
t2
t3
t4
0100
1000
0110
0101
time
analog input (V)
Digital output
digital to analog
4
3
2
1
0100
1000
0110
0101
t1
t2
t3
t4
time
analog output (V)
Digital input

## Slide 17: Digital-to-analog conversion using successive approximation
Given an analog input signal whose voltage should range from 0 to 15 volts, and an 8-bit digital encoding, calculate the correct encoding for 5 volts. Then trace the successive-approximation approach to find the correct encoding.
5/15 = d/(28-1)
d= 85
Successive-approximation method
0
1
0
0
0
0
0
0
Encoding: 01010101
½(Vmax – Vmin) = 7.5 volts
Vmax = 7.5 volts.
½(7.5 + 0) = 3.75 volts
Vmin = 3.75 volts.
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
½(7.5 + 3.75) = 5.63 volts
Vmax = 5.63 volts
½(5.63 + 3.75) = 4.69 volts
Vmin = 4.69 volts.
0
1
0
1
0
0
0
0
½(5.63 + 4.69) = 5.16 volts
Vmax = 5.16 volts.
0
1
0
1
0
0
0
0
½(5.16 + 4.69) = 4.93 volts
Vmin = 4.93 volts.
0
1
0
1
0
1
0
0
½(5.16 + 4.93) = 5.05 volts
Vmax = 5.05 volts.
0
1
0
1
0
1
0
0
½(5.05 + 4.93) = 4.99 volts
0
1
0
1
0
1
0
1