## Slide 1: Chapter 7 Digital Camera Example

## Slide 2: Outline
Introduction to a simple digital camera
Designer’s perspective
Requirements specification
Design
  Four implementations

## Slide 3: Introduction
Putting it all together
  General-purpose processor
  Single-purpose processor
    Custom
    Standard
  Memory
  Interfacing
Knowledge applied to designing a simple digital camera
  General-purpose vs. single-purpose processors
  Partitioning of functionality among different processor types

## Slide 4: Introduction to a simple digital camera
Captures images
Stores images in digital format
  No film
  Multiple images stored in camera
    Number depends on amount of memory and bits used per image
Downloads images to PC
Only recently possible
  Systems-on-a-chip
    Multiple processors and memories on one IC
  High-capacity flash memory
Very simple description used for example
  Many more features with real digital camera
    Variable size images, image deletion, digital stretching, zooming in and out, etc.

## Slide 5: Designer’s perspective
Two key tasks
  Processing images and storing in memory
    When shutter pressed:
      Image captured
      Converted to digital form by charge-coupled device (CCD)
      Compressed and archived in internal memory
  Uploading images to PC
    Digital camera attached to PC
    Special software commands camera to transmit archived images serially

## Slide 6: Charge-coupled device (CCD)
Special sensor that captures an image
Light-sensitive silicon solid-state device composed of many cells
When exposed to light, each cell becomes electrically charged. This charge can then be converted to a 8-bit value where 0 represents no exposure while 255 represents very intense exposure of that cell to light.
Some of the columns are covered with a black strip of paint. The light-intensity of these pixels is used for zero-bias adjustments of all the cells.
The electromechanical shutter is activated to expose the cells to light for a brief moment.
The electronic circuitry, when commanded, discharges the cells, activates the electromechanical shutter, and then reads the 8-bit charge value of each cell. These values can be clocked out of the CCD by external logic through a standard parallel bus interface.
Lens area
Pixel columns
Covered columns
Electronic circuitry
Electro-mechanical shutter
Pixel rows

## Slide 7: Zero-bias error
Manufacturing errors cause cells to measure slightly above or below actual light intensity
Error typically same across columns, but different across rows
Some of left most columns blocked by black paint to detect zero-bias error
  Reading of other than 0 in blocked cells is zero-bias error
  Each row is corrected by subtracting the average error found in blocked cells for that row
Covered cells
Before zero-bias adjustment
After zero-bias adjustment
Zero-bias adjustment

## Slide 8: Compression
Store more images
Transmit image to PC in less time
JPEG (Joint Photographic Experts Group)
  Popular standard format for representing digital images in a compressed form
  Provides for a number of different modes of operation
  Mode used in this chapter provides high compression ratios using DCT (discrete cosine transform)
  Image data divided into blocks of 8 x 8 pixels
  3 steps performed on each block
    DCT
    Quantization
    Huffman encoding

## Slide 9: DCT step
Transforms original 8 x 8 block into a cosine-frequency domain
  Upper-left corner values represent more of the essence of the image
  Lower-right corner values represent finer details
    Can reduce precision of these values and retain reasonable image quality
FDCT (Forward DCT) formula
  C(h) = if (h == 0) then 1/sqrt(2) else 1.0
    Auxiliary function used in main function F(u,v)
  F(u,v) = ¼ x C(u) x C(v) Σx=0..7 Σy=0..7 Dxy x cos(π(2u + 1)u/16) x cos(π(2y + 1)v/16)
    Gives encoded pixel at row u, column v
    Dxy is original pixel value at row x, column y
IDCT (Inverse DCT)
  Reverses process to obtain original block (not needed for this design)

## Slide 10: Quantization step
Achieve high compression ratio by reducing image quality
  Reduce bit precision of encoded data
    Fewer bits needed for encoding
    One way is to divide all values by a factor of 2
      Simple right shifts can do this
  Dequantization would reverse process for decompression
After being decoded using DCT
After quantization
Divide each cell’s value by 8

## Slide 11: Huffman encoding step
Serialize 8 x 8 block of pixels
  Values are converted into single list using zigzag pattern
Perform Huffman encoding
  More frequently occurring pixels assigned short binary code
  Longer binary codes left for less frequently occurring pixels
Each pixel in serial list converted to Huffman encoded values
  Much shorter list, thus compression

## Slide 12: Huffman encoding example
Pixel frequencies on left
  Pixel value –1 occurs 15 times
  Pixel value 14 occurs 1 time
Build Huffman tree from bottom up
  Create one leaf node for each pixel value and assign frequency as node’s value
  Create an internal node by joining any two nodes whose sum is a minimal value
    This sum is internal nodes value
  Repeat until complete binary tree
Traverse tree from root to leaf to obtain binary code for leaf’s pixel value
  Append 0 for left traversal, 1 for right traversal
Huffman encoding is reversible
  No code is a prefix of another code
144
5
3
2
1
0
-2
-1
-10
-5
-3
-4
-8
-9
6
14
1
1
2
1
1
2
1
2
2
4
3
5
4
6
5
9
5
10
5
11
5
14
6
17
8
18
15
29
35
64
1
Pixel frequencies
Huffman tree
Huffman codes

## Slide 13: Archive step
Record starting address and image size
  Can use linked list
One possible way to archive images
  If max number of images archived is N:
    Set aside memory for N addresses and N image-size variables
    Keep a counter for location of next available address
    Initialize addresses and image-size variables to 0
    Set global memory address to N x 4
      Assuming addresses, image-size variables occupy N x 4 bytes
    First image archived starting at address N x 4
    Global memory address updated to N x 4 + (compressed image size)
Memory requirement based on N, image size, and average compression ratio

## Slide 14: Uploading to PC
When connected to PC and upload command received
  Read images from memory
  Transmit serially using UART
  While transmitting
    Reset pointers, image-size variables and global memory pointer accordingly

## Slide 15: Requirements Specification
System’s requirements – what system should do
  Nonfunctional requirements
    Constraints on design metrics (e.g., “should use 0.001 watt or less”)
  Functional requirements
    System’s behavior (e.g., “output X should be input Y times 2”)
  Initial specification may be very general and come from marketing dept.
    E.g., short document detailing market need for a low-end digital camera that:
      captures and stores at least 50 low-res images and uploads to PC,
      costs around $100 with single medium-size IC costing less that $25,
      has long as possible battery life,
      has expected sales volume of 200,000 if market entry < 6 months,
      100,000 if between 6 and 12 months,
      insignificant sales beyond 12 months

## Slide 16: Nonfunctional requirements
Design metrics of importance based on initial specification
  Performance: time required to process image
  Size: number of elementary logic gates (2-input NAND gate) in IC
  Power: measure of avg. electrical energy consumed while processing
  Energy: battery lifetime (power x time)
Constrained metrics
  Values must be below (sometimes above) certain threshold
Optimization metrics
  Improved as much as possible to improve product
Metric can be both constrained and optimization

## Slide 17: Nonfunctional requirements (cont.)
Performance
  Must process image fast enough to be useful
  1 sec reasonable constraint
    Slower would be annoying
    Faster not necessary for low-end of market
  Therefore, constrained metric
Size
  Must use IC that fits in reasonably sized camera
  Constrained and optimization metric
    Constraint may be 200,000 gates, but smaller would be cheaper
Power
  Must operate below certain temperature (cooling fan not possible)
  Therefore, constrained metric
Energy
  Reducing power or time reduces energy
  Optimized metric: want battery to last as long as possible

## Slide 18: Informal functional specification
Flowchart breaks functionality down into simpler functions
Each function’s details could then be described in English
  Done earlier in chapter
Low quality image has resolution of 64 x 64
Mapping functions to a particular processor type not done at this stage
serial output
e.g., 011010...
yes
no
CCD
input
Zero-bias adjust
DCT
Quantize
Archive in memory
More 8×8 blocks?
Transmit serially
yes
no
Done?

## Slide 19: Refined functional specification
Refine informal specification into one that can actually be executed
Can use C/C++ code to describe each function
  Called system-level model, prototype, or simply model
  Also is first implementation
Can provide insight into operations of system
  Profiling can find computationally intensive functions
Can obtain sample output used to verify correctness of final implementation
image file
101011010110101010010101101...
CCD.C
CNTRL.C
UART.C
output file
1010101010101010101010101010...
CODEC.C
CCDPP.C
Executable model of digital camera

## Slide 20: CCD module
Simulates real CCD
CcdInitialize is passed name of image file
CcdCapture reads “image” from file
CcdPopPixel outputs pixels one at a time
char CcdPopPixel(void) {
char pixel;
pixel = buffer[rowIndex][colIndex];
if( ++colIndex == SZ_COL ) {
colIndex = 0;
if( ++rowIndex == SZ_ROW ) {
colIndex = -1;
rowIndex = -1;
}
}
return pixel;
}
#include <stdio.h>
#define SZ_ROW 64
#define SZ_COL (64 + 2)
static FILE *imageFileHandle;
static char buffer[SZ_ROW][SZ_COL];
static unsigned rowIndex, colIndex;
void CcdInitialize(const char *imageFileName) {
imageFileHandle = fopen(imageFileName, "r");
rowIndex = -1;
colIndex = -1;
}
void CcdCapture(void) {
int pixel;
rewind(imageFileHandle);
for(rowIndex=0; rowIndex<SZ_ROW; rowIndex++) {
for(colIndex=0; colIndex<SZ_COL; colIndex++) {
if( fscanf(imageFileHandle, "%i", &pixel) == 1 ) {
buffer[rowIndex][colIndex] = (char)pixel;
}
}
}
rowIndex = 0;
colIndex = 0;
}

## Slide 21: CCDPP (CCD PreProcessing) module
Performs zero-bias adjustment
CcdppCapture uses CcdCapture and CcdPopPixel to obtain image
Performs zero-bias adjustment after each row read in
#define SZ_ROW 64
#define SZ_COL 64
static char buffer[SZ_ROW][SZ_COL];
static unsigned rowIndex, colIndex;
void CcdppInitialize() {
rowIndex = -1;
colIndex = -1;
}
void CcdppCapture(void) {
char bias;
CcdCapture();
for(rowIndex=0; rowIndex<SZ_ROW; rowIndex++) {
for(colIndex=0; colIndex<SZ_COL; colIndex++) {
buffer[rowIndex][colIndex] = CcdPopPixel();
}
bias = (CcdPopPixel() + CcdPopPixel()) / 2;
for(colIndex=0; colIndex<SZ_COL; colIndex++) {
buffer[rowIndex][colIndex] -= bias;
}
}
rowIndex = 0;
colIndex = 0;
}
char CcdppPopPixel(void) {
char pixel;
pixel = buffer[rowIndex][colIndex];
if( ++colIndex == SZ_COL ) {
colIndex = 0;
if( ++rowIndex == SZ_ROW ) {
colIndex = -1;
rowIndex = -1;
}
}
return pixel;
}

## Slide 22: UART module
Actually a half UART
  Only transmits, does not receive
UartInitialize is passed name of file to output to
UartSend transmits (writes to output file) bytes at a time
#include <stdio.h>
static FILE *outputFileHandle;
void UartInitialize(const char *outputFileName) {
outputFileHandle = fopen(outputFileName, "w");
}
void UartSend(char d) {
fprintf(outputFileHandle, "%i\n", (int)d);
}

## Slide 23: CODEC module
Models FDCT encoding
ibuffer holds original 8 x 8 block
obuffer holds encoded 8 x 8 block
CodecPushPixel called 64 times to fill ibuffer with original block
CodecDoFdct called once to transform 8 x 8 block
  Explained in next slide
CodecPopPixel called 64 times to retrieve encoded block from obuffer
static short ibuffer[8][8], obuffer[8][8], idx;
void CodecInitialize(void) { idx = 0; }
void CodecDoFdct(void) {
int x, y;
for(x=0; x<8; x++) {
for(y=0; y<8; y++)
obuffer[x][y] = FDCT(x, y, ibuffer);
}
idx = 0;
}
void CodecPushPixel(short p) {
if( idx == 64 ) idx = 0;
ibuffer[idx / 8][idx % 8] = p; idx++;
}
short CodecPopPixel(void) {
short p;
if( idx == 64 ) idx = 0;
p = obuffer[idx / 8][idx % 8]; idx++;
return p;
}

## Slide 24: CODEC (cont.)
Implementing FDCT formula
C(h) = if (h == 0) then 1/sqrt(2) else 1.0
F(u,v) = ¼ x C(u) x C(v) Σx=0..7 Σy=0..7 Dxy x
cos(π(2u + 1)u/16) x cos(π(2y + 1)v/16)
Only 64 possible inputs to COS, so table can be used to save performance time
  Floating-point values multiplied by 32,678 and rounded to nearest integer
  32,678 chosen in order to store each value in 2 bytes of memory
  Fixed-point representation explained more later
FDCT unrolls inner loop of summation, implements outer summation as two consecutive for loops
static const short COS_TABLE[8][8] = {
{ 32768, 32138, 30273, 27245, 23170, 18204, 12539, 6392 },
{ 32768, 27245, 12539, -6392, -23170, -32138, -30273, -18204 },
{ 32768, 18204, -12539, -32138, -23170, 6392, 30273, 27245 },
{ 32768, 6392, -30273, -18204, 23170, 27245, -12539, -32138 },
{ 32768, -6392, -30273, 18204, 23170, -27245, -12539, 32138 },
{ 32768, -18204, -12539, 32138, -23170, -6392, 30273, -27245 },
{ 32768, -27245, 12539, 6392, -23170, 32138, -30273, 18204 },
{ 32768, -32138, 30273, -27245, 23170, -18204, 12539, -6392 }
};
static int FDCT(int u, int v, short img[8][8]) {
double s[8], r = 0; int x;
for(x=0; x<8; x++) {
s[x] = img[x][0] * COS(0, v) + img[x][1] * COS(1, v) +
img[x][2] * COS(2, v) + img[x][3] * COS(3, v) +
img[x][4] * COS(4, v) + img[x][5] * COS(5, v) +
img[x][6] * COS(6, v) + img[x][7] * COS(7, v);
}
for(x=0; x<8; x++) r += s[x] * COS(x, u);
return (short)(r * .25 * C(u) * C(v));
}
static short ONE_OVER_SQRT_TWO = 23170;
static double COS(int xy, int uv) {
return COS_TABLE[xy][uv] / 32768.0;
}
static double C(int h) {
return h ? 1.0 : ONE_OVER_SQRT_TWO / 32768.0;
}

## Slide 25: CNTRL (controller) module
Heart of the system
CntrlInitialize for consistency with other modules only
CntrlCaptureImage uses CCDPP module to input image and place in buffer
CntrlCompressImage breaks the 64 x 64 buffer into 8 x 8 blocks and performs FDCT on each block using the CODEC module
  Also performs quantization on each block
CntrlSendImage transmits encoded image serially using UART module
void CntrlSendImage(void) {
for(i=0; i<SZ_ROW; i++)
for(j=0; j<SZ_COL; j++) {
temp = buffer[i][j];
UartSend(((char*)&temp)[0]); /* send upper byte */
UartSend(((char*)&temp)[1]); /* send lower byte */
}
}
}
#define SZ_ROW 64
#define SZ_COL 64
#define NUM_ROW_BLOCKS (SZ_ROW / 8)
#define NUM_COL_BLOCKS (SZ_COL / 8)
static short buffer[SZ_ROW][SZ_COL], i, j, k, l, temp;
void CntrlInitialize(void) {}
void CntrlCaptureImage(void) {
CcdppCapture();
for(i=0; i<SZ_ROW; i++)
for(j=0; j<SZ_COL; j++)
buffer[i][j] = CcdppPopPixel();
}
void CntrlCompressImage(void) {
for(i=0; i<NUM_ROW_BLOCKS; i++)
for(j=0; j<NUM_COL_BLOCKS; j++) {
for(k=0; k<8; k++)
for(l=0; l<8; l++)
CodecPushPixel(
(char)buffer[i * 8 + k][j * 8 + l]);
CodecDoFdct();/* part 1 - FDCT */
for(k=0; k<8; k++)
for(l=0; l<8; l++) {
buffer[i * 8 + k][j * 8 + l] = CodecPopPixel();
/* part 2 - quantization */
buffer[i*8+k][j*8+l] >>= 6;
}
}
}

## Slide 26: Putting it all together
Main initializes all modules, then uses CNTRL module to capture, compress, and transmit one image
This system-level model can be used for extensive experimentation
  Bugs much easier to correct here rather than in later models
int main(int argc, char *argv[]) {
char *uartOutputFileName = argc > 1 ? argv[1] : "uart_out.txt";
char *imageFileName = argc > 2 ? argv[2] : "image.txt";
/* initialize the modules */
UartInitialize(uartOutputFileName);
CcdInitialize(imageFileName);
CcdppInitialize();
CodecInitialize();
CntrlInitialize();
/* simulate functionality */
CntrlCaptureImage();
CntrlCompressImage();
CntrlSendImage();
}

## Slide 27: Design
Determine system’s architecture
  Processors
    Any combination of single-purpose (custom or standard) or general-purpose processors
  Memories, buses
Map functionality to that architecture
  Multiple functions on one processor
  One function on one or more processors
Implementation
  A particular architecture and mapping
  Solution space is set of all implementations
Starting point
  Low-end general-purpose processor connected to flash memory
    All functionality mapped to software running on processor
    Usually satisfies power, size, and time-to-market constraints
    If timing constraint not satisfied then later implementations could:
      use single-purpose processors for time-critical functions
      rewrite functional specification

## Slide 28: Implementation 1: Microcontroller alone
Low-end processor could be Intel 8051 microcontroller
Total IC cost including NRE about $5
Well below 200 mW power
Time-to-market about 3 months
However, one image per second not possible
  12 MHz, 12 cycles per instruction
    Executes one million instructions per second
  CcdppCapture has nested loops resulting in 4096 (64 x 64) iterations
    ~100 assembly instructions each iteration
    409,000 (4096 x 100) instructions per image
    Half of budget for reading image alone
  Would be over budget after adding compute-intensive DCT and Huffman encoding

## Slide 29: Implementation 2: Microcontroller and CCDPP
CCDPP function implemented on custom single-purpose processor
  Improves performance – less microcontroller cycles
  Increases NRE cost and time-to-market
  Easy to implement
    Simple datapath
    Few states in controller
Simple UART easy to implement as single-purpose processor also
EEPROM for program memory and RAM for data memory added as well
8051
UART
CCDPP
RAM
EEPROM
SOC

## Slide 30: Microcontroller
Synthesizable version of Intel 8051 available
  Written in VHDL
  Captured at register transfer level (RTL)
Fetches instruction from ROM
Decodes using Instruction Decoder
ALU executes arithmetic operations
  Source and destination registers reside in RAM
Special data movement instructions used to load and store externally
Special program generates VHDL description of ROM from output of C compiler/linker
To External Memory Bus
Controller
4K ROM
128
RAM
Instruction Decoder
ALU
Block diagram of Intel 8051 processor core

## Slide 31: UART
UART in idle mode until invoked
  UART invoked when 8051 executes store instruction with UART’s enable register as target address
    Memory-mapped communication between 8051 and all single-purpose processors
    Lower 8-bits of memory address for RAM
    Upper 8-bits of memory address for memory-mapped I/O devices
Start state transmits 0 indicating start of byte transmission then transitions to Data state
Data state sends 8 bits serially then transitions to Stop state
Stop state transmits 1 indicating transmission done then transitions back to idle mode
invoked
I = 8
I < 8
Idle:
I = 0
Start: Transmit LOW
Data: Transmit data(I), then I++
Stop: Transmit HIGH
FSMD description of UART

## Slide 32: CCDPP
Hardware implementation of zero-bias operations
Interacts with external CCD chip
  CCD chip resides external to our SOC mainly because combining CCD with ordinary logic not feasible
Internal buffer, B, memory-mapped to 8051
Variables R, C are buffer’s row, column indices
GetRow state reads in one row from CCD to B
  66 bytes: 64 pixels + 2 blacked-out pixels
ComputeBias state computes bias for that row and stores in variable Bias
FixBias state iterates over same row subtracting Bias from each element
NextRow transitions to GetRow for repeat of process on next row or to Idle state when all 64 rows completed
C = 64
C < 64
R = 64
C = 66
invoked
R < 64
C < 66
Idle:
R=0
C=0
GetRow:
B[R][C]=Pxl
C=C+1
ComputeBias:
Bias=(B[R][11] + B[R][10]) / 2
C=0
NextRow:
R++
C=0
FixBias:
B[R][C]=B[R][C]-Bias
FSMD description of CCDPP

## Slide 33: Connecting SOC components
Memory-mapped
  All single-purpose processors and RAM are connected to 8051’s memory bus
Read
  Processor places address on 16-bit address bus
  Asserts read control signal for 1 cycle
  Reads data from 8-bit data bus 1 cycle later
  Device (RAM or SPP) detects asserted read control signal
  Checks address
  Places and holds requested data on data bus for 1 cycle
Write
  Processor places address and data on address and data bus
  Asserts write control signal for 1 clock cycle
  Device (RAM or SPP) detects asserted write control signal
  Checks address bus
  Reads and stores data from data bus

## Slide 34: Software
System-level model provides majority of code
  Module hierarchy, procedure names, and main program unchanged
Code for UART and CCDPP modules must be redesigned
  Simply replace with memory assignments
    xdata used to load/store variables over external memory bus
    _at_ specifies memory address to store these variables
    Byte sent to U_TX_REG by processor will invoke UART
    U_STAT_REG used by UART to indicate its ready for next byte
      UART may be much slower than processor
  Similar modification for CCDPP code
All other modules untouched
static unsigned char xdata U_TX_REG _at_ 65535;
static unsigned char xdata U_STAT_REG _at_ 65534;
void UARTInitialize(void) {}
void UARTSend(unsigned char d) {
while( U_STAT_REG == 1 ) {
/* busy wait */
}
U_TX_REG = d;
}
Rewritten UART module
#include <stdio.h>
static FILE *outputFileHandle;
void UartInitialize(const char *outputFileName) {
outputFileHandle = fopen(outputFileName, "w");
}
void UartSend(char d) {
fprintf(outputFileHandle, "%i\n", (int)d);
}
Original code from system-level model

## Slide 35: Analysis
Entire SOC tested on VHDL simulator
  Interprets VHDL descriptions and functionally simulates execution of system
    Recall program code translated to VHDL description of ROM
  Tests for correct functionality
  Measures clock cycles to process one image (performance)
Gate-level description obtained through synthesis
  Synthesis tool like compiler for SPPs
  Simulate gate-level models to obtain data for power analysis
    Number of times gates switch from 1 to 0 or 0 to 1
  Count number of gates for chip area
Power
VHDL simulator
VHDL
VHDL
VHDL
Execution time
Synthesis tool
gates
gates
gates
Sum gates
Gate level simulator
Power equation
Chip area
Obtaining design metrics of interest

## Slide 36: Implementation 2: Microcontroller and CCDPP
Analysis of implementation 2
  Total execution time for processing one image:
    9.1 seconds
  Power consumption:
    0.033 watt
  Energy consumption:
    0.30 joule (9.1 s x 0.033 watt)
  Total chip area:
    98,000 gates

## Slide 37: Implementation 3: Microcontroller and CCDPP/Fixed-Point DCT
9.1 seconds still doesn’t meet performance constraint of 1 second
DCT operation prime candidate for improvement
  Execution of implementation 2 shows microprocessor spends most cycles here
  Could design custom hardware like we did for CCDPP
    More complex so more design effort
  Instead, will speed up DCT functionality by modifying behavior

## Slide 38: DCT floating-point cost
Floating-point cost
  DCT uses ~260 floating-point operations per pixel transformation
  4096 (64 x 64) pixels per image
  1 million floating-point operations per image
  No floating-point support with Intel 8051
    Compiler must emulate
      Generates procedures for each floating-point operation
        mult, add
      Each procedure uses tens of integer operations
  Thus, > 10 million integer operations per image
  Procedures increase code size
Fixed-point arithmetic can improve on this

## Slide 39: Fixed-point arithmetic
Integer used to represent a real number
  Constant number of integer’s bits represents fractional portion of real number
    More bits, more accurate the representation
  Remaining bits represent portion of real number before decimal point
Translating a real constant to a fixed-point representation
  Multiply real value by 2 ^ (# of bits used for fractional part)
  Round to nearest integer
  E.g., represent 3.14 as 8-bit integer with 4 bits for fraction
    2^4 = 16
    3.14 x 16 = 50.24 ≈ 50 = 00110010
    16 (2^4) possible values for fraction, each represents 0.0625 (1/16)
    Last 4 bits (0010) = 2
    2 x 0.0625 = 0.125
    3(0011) + 0.125 = 3.125 ≈ 3.14 (more bits for fraction would increase accuracy)

## Slide 40: Fixed-point arithmetic operations
Addition
  Simply add integer representations
  E.g., 3.14 + 2.71 = 5.85
    3.14 → 50 = 00110010
    2.71 → 43 = 00101011
    50 + 43 = 93 = 01011101
    5(0101) + 13(1101) x 0.0625 = 5.8125 ≈ 5.85
Multiply
  Multiply integer representations
  Shift result right by # of bits in fractional part
  E.g., 3.14 * 2.71 = 8.5094
    50 * 43 = 2150 = 100001100110
    >> 4 = 10000110
    8(1000) + 6(0110) x 0.0625 = 8.375 ≈ 8.5094
Range of real values used limited by bit widths of possible resulting values

## Slide 41: Fixed-point implementation of CODEC
COS_TABLE gives 8-bit fixed-point representation of cosine values
6 bits used for fractional portion
Result of multiplications shifted right by 6
void CodecDoFdct(void) {
unsigned short x, y;
for(x=0; x<8; x++)
for(y=0; y<8; y++)
outBuffer[x][y] = F(x, y, inBuffer);
idx = 0;
}
static const char code COS_TABLE[8][8] = {
{ 64, 62, 59, 53, 45, 35, 24, 12 },
{ 64, 53, 24, -12, -45, -62, -59, -35 },
{ 64, 35, -24, -62, -45, 12, 59, 53 },
{ 64, 12, -59, -35, 45, 53, -24, -62 },
{ 64, -12, -59, 35, 45, -53, -24, 62 },
{ 64, -35, -24, 62, -45, -12, 59, -53 },
{ 64, -53, 24, 12, -45, 62, -59, 35 },
{ 64, -62, 59, -53, 45, -35, 24, -12 }
};
static const char ONE_OVER_SQRT_TWO = 5;
static short xdata inBuffer[8][8], outBuffer[8][8], idx;
void CodecInitialize(void) { idx = 0; }
static unsigned char C(int h) { return h ? 64 : ONE_OVER_SQRT_TWO;}
static int F(int u, int v, short img[8][8]) {
long s[8], r = 0;
unsigned char x, j;
for(x=0; x<8; x++) {
s[x] = 0;
for(j=0; j<8; j++)
s[x] += (img[x][j] * COS_TABLE[j][v] ) >> 6;
}
for(x=0; x<8; x++) r += (s[x] * COS_TABLE[x][u]) >> 6;
return (short)((((r * (((16*C(u)) >> 6) *C(v)) >> 6)) >> 6) >> 6);
}
void CodecPushPixel(short p) {
if( idx == 64 ) idx = 0;
inBuffer[idx / 8][idx % 8] = p << 6; idx++;
}

## Slide 42: Implementation 3: Microcontroller and CCDPP/Fixed-Point DCT
Analysis of implementation 3
  Use same analysis techniques as implementation 2
  Total execution time for processing one image:
    1.5 seconds
  Power consumption:
    0.033 watt (same as 2)
  Energy consumption:
    0.050 joule (1.5 s x 0.033 watt)
    Battery life 6x longer!!
  Total chip area:
    90,000 gates
    8,000 less gates (less memory needed for code)

## Slide 43: Implementation 4: Microcontroller and CCDPP/DCT
Performance close but not good enough
Must resort to implementing CODEC in hardware
  Single-purpose processor to perform DCT on 8 x 8 block
8051
UART
CCDPP
RAM
EEPROM
SOC
CODEC

## Slide 44: CODEC design
4 memory mapped registers
  C_DATAI_REG/C_DATAO_REG used to push/pop 8 x 8 block into and out of CODEC
  C_CMND_REG used to command CODEC
    Writing 1 to this register invokes CODEC
  C_STAT_REG indicates CODEC done and ready for next block
    Polled in software
Direct translation of C code to VHDL for actual hardware implementation
  Fixed-point version used
CODEC module in software changed similar to UART/CCDPP in implementation 2
static unsigned char xdata C_STAT_REG _at_ 65527;
static unsigned char xdata C_CMND_REG _at_ 65528;
static unsigned char xdata C_DATAI_REG _at_ 65529;
static unsigned char xdata C_DATAO_REG _at_ 65530;
void CodecInitialize(void) {}
void CodecPushPixel(short p) { C_DATAO_REG = (char)p; }
short CodecPopPixel(void) {
return ((C_DATAI_REG << 8) | C_DATAI_REG);
}
void CodecDoFdct(void) {
C_CMND_REG = 1;
while( C_STAT_REG == 1 ) { /* busy wait */ }
}
Rewritten CODEC software

## Slide 45: Implementation 4: Microcontroller and CCDPP/DCT
Analysis of implementation 4
  Total execution time for processing one image:
    0.099 seconds (well under 1 sec)
  Power consumption:
    0.040 watt
    Increase over 2 and 3 because SOC has another processor
  Energy consumption:
    0.00040 joule (0.099 s x 0.040 watt)
    Battery life 12x longer than previous implementation!!
  Total chip area:
    128,000 gates
    Significant increase over previous implementations

## Slide 46: Summary of implementations
Implementation 3
  Close in performance
  Cheaper
  Less time to build
Implementation 4
  Great performance and energy consumption
  More expensive and may miss time-to-market window
    If DCT designed ourselves then increased NRE cost and time-to-market
    If existing DCT purchased then increased IC cost
Which is better?

## Slide 47: Summary
Digital camera example
  Specifications in English and executable language
  Design metrics: performance, power and area
Several implementations
  Microcontroller: too slow
  Microcontroller and coprocessor: better, but still too slow
  Fixed-point arithmetic: almost fast enough
  Additional coprocessor for compression: fast enough, but expensive and hard to design
  Tradeoffs between hw/sw – the main lesson of this book!