## Slide 1: Chapter 9: Control Systems

## Slide 2: Control System
Control physical system’s output
  By setting physical system’s input
Tracking
E.g.
  Cruise control
  Thermostat control
  Disk drive control
  Aircraft altitude control
Difficulty due to
  Disturbance: wind, road, tire, brake; opening/closing door…
  Human interface: feel good, feel right…

## Slide 3: Tracking

## Slide 4: Open-Loop Control Systems
Plant
  Physical system to be controlled
    Car, plane, disk, heater,…
Actuator
  Device to control the plant
    Throttle, wing flap, disk motor,…
Controller
  Designed product to control the plant

## Slide 5: Open-Loop Control Systems
Output
  The aspect of the physical system we are interested in
    Speed, disk location, temperature
Reference
  The value we want to see at output
    Desired speed, desired location, desired temperature
Disturbance
  Uncontrollable input to the plant imposed by environment
    Wind, bumping the disk drive, door opening

## Slide 6: Other Characteristics of open loop
Feed-forward control
Delay in actual change of the output
Controller doesn’t know how well thing goes
Simple
Best use for predictable systems

## Slide 7: Close Loop Control Systems
Sensor
  Measure the plant output
Error detector
  Detect Error
Feedback control systems
Minimize tracking error

## Slide 8: Designing Open Loop Control System
Develop a model of the plant
Develop a controller
Analyze the controller
Consider Disturbance
Determine Performance
Example: Open Loop Cruise Control System

## Slide 9: Model of the Plant
May not be necessary
  Can be done through experimenting and tuning
But,
  Can make it easier to design
  May be useful for deriving the controller
Example: throttle that goes from 0 to 45 degree
  On flat surface at 50 mph, open the throttle to 40 degree
  Wait 1 “time unit”
  Measure the speed, let’s say 55 mph
  Then the following equation satisfy the above scenario
    vt+1=0.7*vt+0.5*ut
    55 = 0.7*50+0.5*40
  IF the equation holds for all other scenario
    Then we have a model of the plant

## Slide 10: Designing the Controller
Assuming we want to use a simple linear function
  ut=F(rt)= P * rt
  rt is the desired speed
Linear proportional controller
vt+1=0.7*vt+0.5*ut = 0.7*vt+0.5P*rt
Let vt+1=vt at steady state = vss
vss=0.7*vss+0.5P*rt
At steady state, we want vss=rt
P=0.6
  I.e. ut=0.6*rt

## Slide 11: Analyzing the Controller
Let v0=20mph, r0=50mph
vt+1=0.7*vt+0.5(0.6)*rt =0.7*vt+0.3*50= 0.7*vt+15
Throttle position is 0.6*50=30 degree

## Slide 12: Considering the Disturbance
Assume road grade can affect the speed
  From –5mph to +5 mph
  vt+1=0.7*vt+10
  vt+1=0.7*vt+20

## Slide 13: Determining Performance
Vt+1=0.7*vt+0.5P*r0-w0
v1=0.7*v0+0.5P*r0-w0
v2=0.7*(0.7*v0+0.5P*r0-w0) +0.5P*r0-w0 =0.7*0.7*v0+(0.7+1.0)*0.5P*r0-(0.7+1.0)w0
vt=0.7t*v0+(0.7t-1+0.7t-2+…+0.7+1.0)(0.5P*r0-w0)
Coefficient of vt determines rate of decay of v0
  >1 or <-1, vt will grow without bound
  <0, vt will oscillate

## Slide 14: Designing Close Loop Control System

## Slide 15: Stability
ut = P * (rt-vt)
vt+1 = 0.7vt+0.5ut-wt = 0.7vt+0.5P*(rt-vt)-w
  =(0.7-0.5P)*vt+0.5P*rt-wt
vt=(0.7-0.5P)t*v0+((0.7-0.5P)t-1+(0.7-0.5P)t-2+…+0.7-0.5P+1.0)(0.5P*r0-w0)
Stability constraint (I.e. convergence) requires
|0.7-0.5P|<1
-1<0.7-0.5P<1
-0.6<P<3.4

## Slide 16: Reducing effect of v0
ut = P * (rt-vt)
vt+1 = 0.7vt+0.5ut-wt = 0.7vt+0.5P*(rt-vt)-w
  =(0.7-0.5P)*vt+0.5P*rt-wt
vt=(0.7-0.5P)t*v0+((0.7-0.5P)t-1+(0.7-0.5P)t-2+…+0.7-0.5P+1.0)(0.5P*r0-w0)
To reduce the effect of initial condition
  0.7-0.5P as small as possible
  P=1.4

## Slide 17: Avoid Oscillation
ut = P * (rt-vt)
vt+1 = 0.7vt+0.5ut-wt = 0.7vt+0.5P*(rt-vt)-w
  =(0.7-0.5P)*vt+0.5P*rt-wt
vt=(0.7-0.5P)t*v0+((0.7-0.5P)t-1+(0.7-0.5P)t-2+…+0.7-0.5P+1.0)(0.5P*r0-w0)
To avoid oscillation
  0.7-0.5P >=0
  P<=1.4

## Slide 18: Perfect Tracking
ut = P * (rt-vt)
vt+1 = 0.7vt+0.5ut-wt = 0.7vt+0.5P*(rt-vt)-w
  =(0.7-0.5P)*vt+0.5P*rt-wt
vss=(0.7-0.5P)*vss+0.5P*r0-w0
(1-0.7+0.5P)vss=0.5P*r0-w0
vss=(0.5P/(0.3+0.5P)) * r0 - (1.0/(0.3+0.5P)) * wo
To make vss as close to r0 as possible
  P should be as large as possible

## Slide 19: Close-Loop Design
ut = P * (rt-vt)
Finally, setting P=3.3
  Stable, track well, some oscillation
  ut = 3.3 * (rt-vt)

## Slide 20: Analyze the controller
v0=20 mph, r0=50 mph, w=0
vt+1 = 0.7vt+0.5P*(rt-vt)-w
  = 0.7vt+0.5*3.3*(50-vt)
ut = P * (rt-vt)
  = 3.3 * (50-vt)
But ut range from 0-45
Controller saturates

## Slide 21: Analyze the controller
v0=20 mph, r0=50 mph, w=0
vt+1 = 0.7vt+0.5*ut
ut = 3.3 * (50-vt)
  Saturate at 0, 45
Oscillation!
  “feel bad”

## Slide 22: Analyze the controller
Set P=1.0 to void oscillation
  Terrible SS performance

## Slide 23: Analyzing the Controller

## Slide 24: Minimize the effect of disturbance
vt+1 = 0.7vt+0.5*3.3*(rt-vt)-w
  w=-5 or +5
39.74
  Close to 42.31
  Better than
    33
    66
Cost
  SS error
  oscillation

## Slide 25: General Control System
Objective
  Causing output to track a reference even in the presence of
    Measurement noise
    Model error
    Disturbances
Metrics
  Stability
    Output remains bounded
  Performance
    How well an output tracks the reference
  Disturbance rejection
  Robustness
    Ability to tolerate modeling error of the plant

## Slide 26: Performance (generally speaking)
Rise time
  Time it takes form 10% to 90%
Peak time
Overshoot
  Percentage by which Peak exceed final value
Settling time
  Time it takes to reach 1% of final value

## Slide 27: Plant modeling is difficult
May need to be done first
Plant is usually on continuous time
  Not discrete time
    E.g. car speed continuously react to throttle position, not at discrete interval
  Sampling period must be chosen carefully
    To make sure “nothing interesting” happen in between
    I.e. small enough
Plant is usually non-linear
  E.g. shock absorber response may need to be 8th order differential
Iterative development of the plant model and controller
  Have a plant model that is “good enough”

## Slide 28: Controller Design: P
Proportional controller
  A controller that multiplies the tracking error by a constant
    ut = P * (rt-vt)
  Close loop model with a linear plant
    E.g. vt+1 = (0.7-0.5P)*vt+0.5P*rt-wt
P affects
  Transient response
    Stability, oscillation
  Steady state tacking
    As large as possible
  Disturbance rejection
    As large as possible

## Slide 29: Controller Design: PD
Proportional and Derivative control
    ut = P * (rt-vt) + D * ((rt-vt)-(rt-1-vt-1)) = P * et+ D * (et-et-1)
Consider the size of error over time
Intuitively
  Want to “push” more if the error is not reducing fast enough
  Want to “push” less if the error is reducing really fast

## Slide 30: PD Controller
Need to keep track of error derivative
E.g. Cruise controller example
  vt+1 = 0.7vt+0.5ut-wt
  Let ut = P * et + D * (et-et-1), et=rt-vt
  vt+1=0.7vt+0.5*(P*(rt-vt)+D*((rt-vt)-(rt-1-vt-1)))-wt
  vt+1=(0.7-0.5*(P+D))*vt+0.5D*vt-1+0.5*(P+D)*rt-0.5D*rt-1-wt
  Assume reference input and distribance are constant, the steady-state speed is
    Vss=(0.5P/(1-0.7+0.5P)) * r
    Does not depend on D!!!
P can be set for best tracking and disturbance control
Then D set to control oscillation/overshoot/rate of convergence

## Slide 31: PD Control Example

## Slide 32: PI Control
Proportional plus integral control
  ut=P*et+I*(e0+e1+…+et)
Sum up error over time
  Ensure reaching desired output, eventually
  vss will not be reached until ess=0
Use P to control disturbance
Use I to ensure steady state convergence and convergence rate

## Slide 33: PID Controller
Combine Proportional, integral, and derivative control
  ut=P*et+I*(e0+e1+…+et)+D*(et-et-1)
Available off-the shelf

## Slide 34: Software Coding
Main function loops forever, during each iteration
  Read plant output sensor
    May require A2D
  Read current desired reference input
  Call PidUpdate, to determine actuator value
  Set actuator value
    May require D2A

## Slide 35: Software Coding (continue)
Pgain, Dgain, Igain are constants
sensor_value_previous
  For D control
error_sum
  For I control

## Slide 36: Computation
ut=P*et+I*(e0+e1+…+et)+D*(et-et-1)

## Slide 37: PID tuning
Analytically deriving P, I, D may not be possible
  E.g. plant not is not available, or to costly to obtain
Ad hoc method for getting “reasonable” P, I, D
  Start with a small P, I=D=0
  Increase D, until seeing oscillation
    Reduce D a bit
  Increase P, until seeing oscillation
    Reduce D a bit
  Increase I, until seeing oscillation
Iterate until can change anything without excessive oscillation

## Slide 38: Practical Issues with Computer-Based Control
Quantization
Overflow
Aliasing
Computation Delay

## Slide 39: Quantization & Overflow
Quantization
  Can’t store 0.36 as 4-bit fractional number
  Can only store 0.75, 0.59, 0.25, 0.00, -0.25, -050,-0.75, -1.00
  Choose 0.25
    Result in quantization error of 0.11
Sources of quantization error
  Operations, e.g. 0.50*0.25=0.125
    Can use more bits until input/output to the environment/memory
  A2D converters
Overflow
  Can’t store 0.75+0.50 = 1.25 as 4-bit fractional number
Solutions:
  Use fix-point representation/operations carefully
    Time-consuming
  Use floating-point co-processor
    Costly

## Slide 40: Aliasing
Quantization/overflow
  Due to discrete nature of computer data
Aliasing
  Due to discrete nature of sampling

## Slide 41: Aliasing Example
Sampling at 2.5 Hz, period of 0.4, the following are indistinguishable
  y(t)=1.0*sin(6πt), frequency 3 Hz
  y(t)=1.0*sin(πt), frequency of 0.5 Hz
In fact, with sampling frequency of 2.5 Hz
  Can only correctly sample signal below Nyquist frequency 2.5/2 = 1.25 Hz

## Slide 42: Computation Delay
Inherent delay in processing
  Actuation occurs later than expected
Need to characterize implementation delay to make sure it is negligible
Hardware delay is usually easy to characterize
  Synchronous design
Software delay is harder to predict
  Should organize code carefully so delay is predictable and minimized
  Write software with predictable timing behavior (be like hardware)
    Time Trigger Architecture
    Synchronous Software Language

## Slide 43: Benefit of Computer Control
Cost!!!
  Expensive to make analog control immune to
    Age, temperature, manufacturing error
  Computer control replace complex analog hardware with complex code
Programmability!!!
  Computer Control can be “upgraded”
    Change in control mode, gain, are easy to do
  Computer Control can be adaptive to change in plant
    Due to age, temperature, …etc
  “future-proof”
    Easily adapt to change in standards,..etc