## Slide 1: CLASSIFICATION OF AREA BY THEIR GEOGRAPHY
NETWORKS
PAN
LAN
WAN
MAN
CAN

## Slide 2: LOCAL AREA NETWORK(LAN)
LAN is a network which is designed to operate over a small physical area such as an office, factory or a group of buildings.
LAN’s are easy to design and troubleshoot
Exchange of information and sharing of resources becomes easy because of LAN.
In LAN all machines are connected to a single cable.
Different types of topologies such as star, tree, bus, ring, etc Can be used
It is usually a privately owned network.

## Slide 3: WIDE AREA NETWORK(WAN)
When network spans over a large distance or when the computers to be connected to each other are at widely separated locations a local area network cannot be used. A wide area network(WAN) is installed.
The communication between different users of WAN is established using leased telephone lines, satellite links and similar channels.
It is cheaper and more efficient to use the phone network for the link.
Most WAN networks are used to transfer large blocks of data between its users.

## Slide 4: PERSONAL AREA NETWORK(PAN)
A personal area network is a computer network organized around an individual person.
It generally consists of a mobile computer, a cell phone or personal digital assistant. PAN enables the communication among these devices.
It can also be used for communication among personal devices themselves for connecting to a digital level network and internet.
The PANs can be constructed using wireless or cables.

## Slide 5: CAMPUS AREA NETWORK(CAN)
The campus area network is made up of an interconnection of LAN with limited geographical area.
Network equipment's such as switches, routers and the transmission media i.e. optical fiber etc. are almost entirely owned by the campus owner.

## Slide 6: METROPOLITAN AREA NETWORK(MAN)
It is in between LAN & WAN technology that covers the entire city.
It uses similar technology as LAN.
It can be a single network such as cable TV network, or a measure of connecting a number of LAN’s o a large network so that resources can be shared LAN to LAN as well as device to device.

## Slide 9: NETWORK CLASSIFICATION BY THEIR COMPONENT ROLE
LOCAL AREA NETWORK
PEER TO PEER NETWORK
CLIENT SERVER NETWORK

## Slide 10: PEER TO PEER NETWORK
In peer to peer network each computer is responsible for making its own resources available to other computers on the network.
Each computer is responsible for setting up and maintaining its own security for these resources.
Also each computer is responsible for accessing the required network resources from peer to peer relationships.
Peer to peer network is useful for a small network containing less than 10 computers on a single LAN .
In peer to peer network each computer can function as both client and server.
Peer to peer networks do not have a central control system. There are no servers in peer networks.
Peer networks are amplified into home group.

## Slide 11: ADVANTAGES & DISADVANTAGES OF PEER TO PEER NETWORK
Advantages
Use less expensive computer hardware
Easy to administer
No NOS required
More built in redundancy
Easy setup & low cost
Disadvantages:
Not very secure
No central point of storage or file archiving
Additional load on computer because of resource sharing
Hard to maintain version control

## Slide 13: CLIENT/SERVER NETWORK
In client-server network relationships, certain computers act as server and other act as clients. A servers simply a computer, that available the network resources and provides service to other computers when they request it. A clients the computer running a program that requests the service from a server.
Local area network(LAN) is based on client server network relationship.
A client-server network is one n which all available network resources such as files, directories, applications and shared devices, are centrally managed and hosted and then are accessed by client.
Client serve network are defined by the presence of servers on a network that provide security and administration of the network.

## Slide 14: ADVANTAGES AND DISADVANTAGES OF CLIENT-SERVER NETWORK
Advantages:
Very secure
Better performance
Centralized backup
very reliable
Disadvantages:
requires professional administration
More hardware-intensive
More software intensive
Expensive dedicated software

## Slide 15: TYPES OF SERVERS
SERVERS
File Server
Print Server
Application Server
Message Server
Database Server

## Slide 16: TYPES OF SERVERS
File server: These servers provide the services for storing, retrieving and moving the data. A user can read, write, exchange and manage the files with the help of file servers.
Printer server: The printer server is used for controlling and managing printing on the network. It also offers the fax service to the network users.
Application server: The expensive software and additional computing power can be shared by the computers in a network with he help of application servers.
Message server: It is used to co-ordinate the interaction between users, documents and applications. The data can be used in the for of audio, video, binary, text or graphics.
Database server: It is a type of application server. It allows the uses to access the centralized strong database.