## Slide 1
Introduction of lift irrigation systems
& Design of lift irrigation systems
Malik Aamir Manzoor

## Slide 2
Irrigation Systems
Gravity Flow Irrigation System | Pressurized Irrigation System
Water flows under natural slopes | Water flows under external pressures
Consists of network of dams, head works, canals and watercourses | Consists of pumping unit, pipes, accessories and distributions boxes
Topographic conditions determine type of irrigation system | 
Plain terrains with positive gentle slopes provides feasibility for gravity flow irrigation systems | Undulating terrains with negative slopes require lift irrigation systems for conveyance of water to the fields
Large scale irrigation system | Small scale irrigation system
Initial cost very high | Initial cost very low
Operational cost very low | Operational cost higher

## Slide 3: Lift irrigation system
Definition
Parts
  Prime Mover
  Pumping unit
  Pipes
  Distribution box

## Slide 4: FEASIBILITY OF LIFT IRRIGATION SYSTEMS
Technical feasibility
  Water source at lower elevations
  Adjacent lands at higher elevations
Economic feasibility
  Converts already un irrigated lands to irrigated ones
  Benefits generated are many fold
  Detailed analysis should be carried out in case of long distant lift irrigation schemes

## Slide 5: Requirements
Purely technical job
Requires basic knowledge
  Soil water plant relationships
  Crop water requirements
  Pipe hydraulics
  Operation and maintenance of irrigation equipments
  Pipe installation

## Slide 6
DESIGN OF LIFT IRRIGATION SYSTEM
What is design
Purpose of design
  Purpose is to supply water to a farm to meet the peak crop water requirement with maximum efficiency and minimum cost
Design of lift irrigation system
  Involves making decisions about selection of certain parameters from the available farm resource data
    System capacity
    Irrigation depth
    Irrigation interval
    Daily operational hours of the pumping units
    Sizes of pumps and prime movers

## Slide 7
REVIEW OF TERMINOLOGY USED IN DESIGN PROCESS
  Discharge
The quantity of water passing through the given section of pipe in unit time is called discharge and can be calculated by the following formula
Q = AV
Discharge = Cross sectional area of pipe x velocity of water

## Slide 8
  PRESSURE
P = Force = F
Area A
P = Pressure in ponds per square inch
F = Force in ponds
A = Area in square inches

## Slide 9: HEAD OF WATER

## Slide 10
PRESSURE AND HEAD RELATIONSHIP
14.7 psi = 34 feet head of water
1 psi = 2.31 feet head of water
1 foot head of water = 0.433 psi

## Slide 11
HEAD LOSS IN PIPES

## Slide 12: HEAD LOSS BY PIPE FRICTION
1) Hf = K (Q/C)1.852 LD-4.87
Where
K = 1.21 X 1010
Q = Pipe Line discharge, (lps)
C= Friction Coefficient which is a function of pipe material characteristics.
L = Length of pipe (m)
D = Inside diameter of pipe (mm)
hf = Frictional Head Loss, m
2) Hf = f LV2
2gD
f = Friction factor
D = Pipe diameter in m
L = Length of pipe in m
V = Velocity of flow in m/sec
g = acceleration due to gravity, 9.81 m/sec2

## Slide 13: Design Procedure
Step 1: Collection of Basic Farm Resource Data
  Topo Graphic Map
  Data on Climate, Source of Water, Power Source, Crops and Soils
Step 2: Irrigation Depth
Id = TAW x MAD 100
Step 3: Irrigation Interval
Ii = Id____
Peak ETc

## Slide 14: Step 4: DESIGN SYSTEM CAPACITY
Q = 2.78 A X Id
Ii X H X E
where
Q = Discharge, (lps)
A = Area, (Hectares)
Id = Depth of Irrigation (mm)
Il = Irrigation Interval (Days)
H = Operation hours of pumping plant per day
E = Field application efficiency, (fraction)
2.78 = Conversion Factor

## Slide 15: Step 5: PIPE DIAMETER SELECTION
Maximum velocity approach
Maximum head loss method
Minimum cost approach

## Slide 16
i) Compute the dia of pipe on the basis of maximum velocity approach using the formula given below.
D = 63.25 Q___
v
where D = Pipe diameter in mm
Q = Discharge in lps
V = Velocity m/sec
63.25 = constant for conversion
The velocity range is 1-1.5 m/sec
The upper limit for the velocity may also be taken from manufacturer’s recommendations.
ii) Revise the diameter as judgment indicates keeping in view, the availability of sizes in market, operational and initial costs.
RECOMMENDED TECHNIQUE

## Slide 17
Step 6: SELECTION OF PUMP
Discharge and Head
Total Head
Elevation Head (Vertical distance from the center line of the pump to the highest field)
Friction losses
Pump suction lift
Minor losses (A figure of 10% to 15% of (b) above is normally used
Factor of safety
Ht = a + b + c + d + e

## Slide 19: Step 7: Calculation of Power
W.H.P = Q X Ht / 76
Q is in lps
Ht in meter
B.H.P = Q X Ht / 76 X Eff.
Where
W.H.P is water horsepower
B.H.P is the break horsepower
Eff. is the efficiency of the pumping system

## Slide 20: WORKED EXAMPLE
Step-1 Collection of Basic Farm Resource Data
Location Village Noorpur District Attock,
Barani Lands
Soil type Sandy loam
Cropping Pattern Wheat, Maize, Potato
Water Source Mini Dam
Power Source Diesel Engine
Area of Farm 25 Acres
Topography Undulating
Climate Falls in Zone V, Barani Lands

## Slide 21: WORKED EXAMPLE
Step-2 Irrigation Depth
AWHC of soil 125 mm/m
Rooting Depth 1.2 m
TAW 125X1.2 = 150 mm
MAD 50%
Id = TAW X MAD = 150X50 = 75 mm
  100 100

## Slide 22: WORKED EXAMPLE
Step-3 Irrigation Interval
Ii= Id___
Peak ETc
Ii = 75_ = 7.68 Say 8 days
9.77

## Slide 23: WORKED EXAMPLE
Step-4 Design System Capacity
Q = 2.78 x A x Id_
Ii x H x E
= 2.78X10X75 = 18.6 lps
8X20X0.70
Say = 18 lps
Qs = 18 lps

## Slide 24: WORKED EXAMPLE
D = 63.25 Q___
v
D = 63.25 18__ = 121.61mm = 4.78”
3.14X1.55
Say = 5”
Dia of Pipe = 5”
Step-5 Pipe diameter selection

## Slide 25: WORKED EXAMPLE
Total Head
a = Elevation Head = 8 m
b = Fiction Losses hf =1.21X1010(18 /150 )1.852 X435 = 5.89 m
(127)4.87
c = Minor Losses = (10-15%) of b = 0.88 Say = 1 m
d = Factor of safety = say 1 m
Ht = 8 + 5.89 + 1 + 1 = 15.89 Say = 16 m
Pump will be selected on basis of Q = 18 lps and Ht = 16 m
Step-6 Selection of pump

## Slide 26: WORKED EXAMPLE
W.H.P = QXHt = 18X16
76 76
B.H.P = QXHt__
76XEff
B.H.P = 18X16 9.47
76X0.4
Say = 12 H.P
Step-7 Calculation of power

## Slide 27: CLASS EXERCISE
A farm has an area of 5 acres with sandy clay soils. Total length of main pipe is 300m and length of two branches is 67 & 67 m originating at end of main pipe. The total elevation difference from water level to highest field is 9m. The pump is to be placed at an elevation of 4m from water source. Design a lift irrigation system for the farm. Ask/assume any data if missing.
[waterholding capacity=183 mm/m, peak Etc=8.5 mm/day, rooting depth=1.3m, application efficiency=0.6, flow velocity=1.5 m/sec, MAD=50%, operating hours per day=3, available discharge from stream=28 lps]