## Slide 2: QUALITY CONTROL TESTS
It includes the testing of following materials of aerosols
Propellants
Valves, Actuators and Dip Tubes
Containers
Weight Checking
Leak Testing
Spray Testing

## Slide 3: 1. PROPELLANTS :
Vapor pressure and density of the propellant are determined and compared with specification sheet.
Parameter
Identification
Tested By
Gas Chromatography IR Spectroscopy
Purity and acceptability
Moisture, Halogen,
Non-Volatile Residue determinations

## Slide 4: 2. VALVES , ACTUATORS AND DIP TUBES :
For metered dose aerosol valves ,test methods were developed by
‘Aerosol Specifications Committee’
‘Industrial Pharmaceutical Technology Section ‘Academy Of Pharmaceutical Sciences.
•
What is checked
Valve
Why valve is checked?
To test is the amount of valve delivery & degree of uniformity between individual valves of various containers.
•
How this test is done?
Standard test solutions were proposed to check variation in valve delivery.

## Slide 5: TEST SOLUTIONS
C’
Ingredients % w/w | Test Solutions ‘A’ | Test Solutions ‘B’ | Test Solutions ‘
Iso Propyl Myristate | 0.10% | 0.10% | 0.10%
Dichloro Difluoro methane | 49.95% | 25.0% | 50.25%
Dichloro tetrafluoro ethane | 49.95% | 25.0% | 24.75%
Trichloro monofluoro methane | - | - | 24.9%
Alcohol USP | - | 49.9% | -
Specific Gravity @ 25°c | 1.384 | 1.092 | 1.388

## Slide 6: Testing Procedure:
Take total 25 valves from the total valves
placed one valve on containers filled with specific test solution.(from list fill one solution only)
Actuator with 0.020 inch orifice is attached to container.
keepTemperature -25±1°C.
Now its a complete aerosol container
Valve is actuated to fullest extent for 2 sec and weight the container.
Again the valve is actuated for 2 sec and weight it.
Difference between them represents delivery in mg.
Repeat this procedure for all 25 valves.Apply formula
Individual delivery wt in mg.
Valve delivery per actuation in µL =
Specific gravity of test solution
Valve Acceptance:
Deliveries | Limit’s
54µL or less | ± 15%
55 to 200 µL | ± 10%

## Slide 7
For calculating delivery per actuation=weight of container after first delivery - weight of container after second delivery (Total 2 deliveries)
Of the 50 individual deliveries,(Two deliveries for each valves
If 4 or more are outside the limits : valves are rejected
If 3 deliveries are outside limits : another 25 valves are tested.
Lot is rejected if more than 1 delivery is outside the specifications.
If 2 deliveries from 1 valve are beyond limits : another 25 valves are tested.
Lot is rejected if more than1 delivery is outside specification.

## Slide 8: 3. CONTAINERS :
Containers are examined for defects in lining.
Quality control aspects includes degree of conductivity of electric current as measure of exposed metals.
Glass containers examined for Flaws.
4. WEIGHT CHECKING of product concentrate and propellant
Procedure for product concentrate weight checking
It is done in two steps
1. Tare the empty aerosol containers
2. filling with concentrate & weight.
Repeat this procedure for several containers randomly from the containers lined up for filling
Same procedure is used for checking weight of Propellants being added.

## Slide 9
5. LEAK TESTING :
It is a means of checking grooves of the valve and detect the defective containers due to leakage.
Is done by measuring the Crimp’s dimension & comparing.
Final testing of valve closure is done by passing the filled containers through water bath.
6. SPRAY TESTING :
•
•
•
Most pharmaceutical aerosols are 100% spray tested.
This serves to clear the dip tube of pure propellant and pure concentrate.
To check for defects in valves and spray pattern.

## Slide 10: EVALUATION TESTS
Flammability and combustibility :
  Flash point
  Flame Projection
Physicochemical characteristics :
  Vapor pressure
  Density
  Moisture content
  Identification of Propellants

## Slide 11: C. Performance:
Aerosol valve discharge rate
Spray pattern
Dosage with metered valves
Net contents
Foam stability
Particle size determination
D. Biological testing :
Therapeutic activity
Toxicity studies

## Slide 12: A. Flammability and combustibility
Flash point:
Apparatus : Tag Open Cup Apparatus Product is chilled to – 25°F and test liquid
temperature is allowed to increase slowly and the temperature at which vapors ignite is called as Flash Point .
Flame Projection:
Product is sprayed for 4 sec into a flame and the flame is extended ,exact length of the flame is measured with a ruler.

## Slide 13: B. Physicochemical characteristics:
Property Method
1. Vapor Pressure
» Pressure gauge
» Can Puncturing Device.
» Hydrometer,
» Pycnometer.
» Karl Fisher Method,
» Gas Chromatography.
» Gas Chromatography,
» IR Spectroscopy.
2. Density
3. Moisture
4. Identification of propellants

## Slide 14: C. Performance:
1. Aerosol valve discharge rate :
Contents of the aerosol product of known weight is discharged for specific period of time.
By reweighing the container after the time limit, the change in the weight per time dispensed gives the discharge rate ( g/sec).
2. Spray pattern :
The method is based on the impingement of spray on piece of paper that has been treated with Dye-Talc mixture.
The particles that strike the paper
cause the dye to go into solution and to be adsorbed onto paper giving a record of spray for comparison purpose.

## Slide 15: 3. Dosage with metered valves :
Reproducibility of dosage can be determined by:
»Assay techniques
»Accurate weighing of filled container followed by dispensing of several doses . Containers are then reweighed and difference in weight divided by number of doses dispensed gives average dose.
4. Net Contents :
•
Tared cans that have been placed onto the filling lines are reweighed and the difference in weight is equal to the net contents.
In Destructive method : weighing a full container and then dispensing as much of the content as possible . The contents are then weighed . This gives the net content.

## Slide 16
5. Foam stability :
Methods : » Visual Evaluation,
» Time for given mass to penetrate the
foam,
» Time for given rod that is inserted into
the
foam to fall ,
» Rotational Viscometer.
6. Particle Size Determination : Methods : » Cascade Impactor,
» Light Scattering Decay.

## Slide 17: a). Cascade Impactor :
Principle :
Stream of particles projected through a series of nozzles and glass slides at high velocity, larger particle are impacted first on lower velocity stage and smaller particles are collected
at higher velocity stage.
b). Light Scattering Decay :
Principle :
As aerosol settles under turbulent conditions, the change in the light intensity of a Tyndall beam is measured.

## Slide 18: D. Biological testing:
Therapeutic Activity :
» For Inhalation Aerosols : dosage of the product is determined and is related to the particle size distribution.
» For Topical Aerosols : is applied to test areas and adsorption of therapeutic ingredient is determined.
Toxicity :
» For Inhalation Aerosols : exposing test animals to vapors
sprayed from aerosol container.
» For Topical Aerosols
: Irritation and Chilling effects are determined.

## Slide 19: References:
“The Theory & Practice Of Industrial Pharmacy” by Leon Lachman , H.A.Lieberman.