## Slide 1: Soil and land pollution
Introduction:
Soil and land pollution >Third pollution
Causes:
Rapid growth of population
Large scale migration
Rapid industrialization
Soil and land pollution arise from varies human activities such as :
Urban community
Industrialists
Agriculturists
Scientists

## Slide 2: Definition Of Land And Soil
Definition of land:
According to Collins Concise English Dictionary (1992),
“The solid part of the surface of the earth as distinct from seas and lakes etc.”.
Enger and Smith(2000) defined the land as “The surface of the earth not covered by water”.
Definition of soil:
According to Collins Concise English Dictionary (1992),
“The top layer of the surface of the earth that is composed of disintegrated rock particles, humus, water and air”.

## Slide 3: Continued…
Enger and Smit (2000) defined the soil as:
“A mixture of mineral material, organic matter, air, water and living organisms that is capable of supporting plant growth”.
According to Enger and Smit (2000),another definition of soil is that it is:
“A thin covering over the land consisting of a mixture of minerals, organic materials, living organisms, air and water that together support of the growth of plant life”.

## Slide 4: Composition Of Soil
1:Minerals 2:Air 3:Water 4:Organic matter Total | 45% 25% 25% 5% 100%

## Slide 5: Soil Pollution
Farmer concern…
According to Dhaliwal (1998), “soil pollution results from excessive use of insecticides, herbicides, fertilizers and other chemicals which adversely affect the physical, chemical and biological properties of soil. Radioactive substances resulting from explosion of nuclear devices also penetrates the soil from where they enter the food chain and become concentrated into the body tissues”.
According to Hussain (1998) land pollution is defined as “The misuse of the land so as to render it unworthy of meeting the requirements of human and other living creatures”.

## Slide 6: Land And Soil Pollution

## Slide 7: Sources of soil and land pollution
Domestic effluents and wastes
Industrial effluents and wastes
Agricultural wastes
Municipal wastes
Pollution by natural disasters
Mining wastes
Water logging, salinity and sodicity
Soil erosion and degradation
Construction and demolition wastes
Atomic and nuclear wastes
Hospital and commercial wastes

## Slide 8: Domestic Effluents And Wastes
Putrescible
Also called combustible waste
Polythene bags
Papers
Small and large cartons
Wood
Leather
Plastic
Non putrescible
Also known as non combustible waste
Glass
Metals
Containers
Ceramics
Stones
Chemicals

## Slide 9: Domestic Effluents And Wastes
Provide permanent breeding places for flies, rats etc
Improper dumping of waste
Cause human disease like plague, malaria,cholera
Also cause environmental pollution

## Slide 10: Industrial Effluents And Wastes
Industrial toxic waste
Transmitted to man
From the soil through uptake by plants
Cause carcinogenic, mutagenic & teratogenic disease
Several industries such as
Oil refineries
Paper mills
Sugar mills
Fertilizer manufacturers
Alkali plants
Are the main source of land and soil pollution in this country

## Slide 11: Agricultural Wastes
Modernization of agriculture has resulted indiscriminate use of several chemicals to increase crop productivity
Thus modern agriculture is the main source of soil and land pollution
Pesticide and fertilizers are two major constituents of agricultural wastes

## Slide 12: Municipal wastes
Includes domestic wastes
Light industrial wastes
Commercial wastes
The waste is collected and transported to landfills by animal driven carts or vehicles.

## Slide 13: Pollution By Natural Disasters
Sources of soil pollution
Volcanoes
Floods
Earthquakes

## Slide 14: Pollution By Natural Disasters
Earthquake lead to demolition of buildings where dead bodies of human start polluting the environment
Floods provide breeding places for mosquitoes and bacteria
Volcanoes spread toxic materials on the soil causing environmental pollution

## Slide 15: Water Logging, Salinity And Sodicity
Water logging, salinity and sodicity deteriorate the soil texture and structure adversely.
These problems result into the spread of air and underground water pollution besides soil pollution.

## Slide 16: Soil Erosion And Degradation
Soil erosion and degradation also lead to soil pollution.
These problems are generally seen in areas where forests are cut extensively leaving the soil exposed for soil erosion and degradation through
High rainfalls, floods, winds storms
Large scale plantation in such areas can check problems.

## Slide 17: Sources of soil and land pollution
Mining wastes
Mining wastes are source of soil an land pollution.
For example waste extracted from the coal mines are generally spread on the surface of earth without proper destruction or disposal .

## Slide 19: Atomic and nuclear waste
With the increasing population and rapid industrialization atomic and nuclear wastes are becoming more and more important .
About 30 nations of the world are involved in carrying out nuclear an atomic waste.

## Slide 21: Hospital Wastes
Hospital waste require proper attention for collection , transport and disposal.
Hospital wastes generally includes used clothing, polythene bags, rubber gloves, tissues, used syringes, glass and plastics bottles cotton wool and discard body parts.
It is unfortunate that most of the hospital waste are dumped in the low-laying areas around the hospitals.

## Slide 23: Commercial Wastes
Commercial waste usually comes from hotels, restaurant, small industrial units, shopping plazas, schools, nursing homes, railway station, bus station , airports etc.
These waste are similar to domestic waste and municipal waste but contain large proportion of paper and cloth.

## Slide 25: Solid Waste
Definition
The material which arises from various human activities and which is normally discarded as useless unwanted.
Solid wastes are all waste arises from human and animal activities that are normally solids, semi-solids, liquids in containers and those are discarded as useless or unwanted.
Garbage from homes, wastes resulting from commercial and industrial activities and waste substances created by agriculture, mining and water purification plants.

## Slide 27: Classification Of Solid Wastes
Solid waste may be classified based partly on content and partly on moisture and heating value.
A typical classification suggested by RAO (1993) is reproduced as under
Garbage
Rubbish
Pathological waste
Industrial waste
Agricultural waste

## Slide 28: Garbage
It refers to the organic matter which can be decomposed with an offensive smell.
Solid waste constituents produced during the storage meat, fruits and vegetables.
These waste have moisture content of about 70%.
And heating value of around 6x106 j/Kg

## Slide 29: Rubbish
It refers to combustible or non combustible waste.
Combustible waste include paper, wood, scrap, rubber and leather etc.
Non-combustible wastes are metals and glass.
These wastes contain moisture content of 25%
And heating value is around 15x106 j/Kg.

## Slide 31: Pathological Wastes
Pathological wastes include dead animals and human waste etc.
The moisture content is 85% and there are 5% non-combustible solids.
The heating value is around 2.5x106 j/Kg

## Slide 33: Industrial Wastes
Industrial waste include various chemicals, paints, metal scrap, fibers, sewage and sludge.

## Slide 34: Soil And Land Pollution

## Slide 35: Composition Of Solid Waste
It varies with its sources like urban and industrial origin will be different like urban and industrial origin will be different
Hence source of solid waste has to kept in view before describing the components.

## Slide 36: Composition Of Urban Waste
Unfortunately no authentic information regarding composition of the urban waste of Pakistan is available and analysis of such waste has not be regularly by the concerned municipal corporations.
The waste is very heterogeneous in composition .
Composition vary from city to city and village to village due to geographical ,temporal cultural and seasonal variations.

## Slide 37: Composition Of Urban Waste
How ever waste from some urban areas of Pakistan consist of polythene shopping bags waste papers ,cartons , dust, vegetables, leaves, glass bottles , worn out tires , animals etc.

## Slide 38: Disease Related To Soil And Land Pollution
Soil and pollution also cause health hazards in human being the main risk to human health arises from multiplication of microorganisms (such is bacteria and disease vectors(mosquitoes are source of malaria ,flies cockroaches)
Bacteria are the cause of typhoid , cholera , diarrhea and dysentery .
Rat spread disease like plague ,rat bit fever etc.

## Slide 39: Soil Waste Management
Soil waste management is the discipline associated with control of generation, storage collection, transfer, transport and disposal of solid waste in a manner that is in accordance with the principles of public health, economics, engineering, conservation, aesthetic and other environmental considerations that are also responsible for public attitudes.
It includes all administration, financial, legal, planning and engineering function involve in the whole spectrum of solutions to problem of SW.
Three main activities involved in the SWM:
Collection
Disposal
Recycling and recovery

## Slide 40: Methods Of Disposal Of Solid Waste
Several methods are used in the different parts of the world and most important of these are given:
Source reduction
Open dumping
Ocean dumping
Composting
Sanitary land-filling
Incineration
Recycling

## Slide 41: 1.Source Reduction
The most important way to reduce waste is to prevent it from becoming waste in the first place It is defined as reducing the amount of solid waste generated by using less or converting from heavy packaging material to light weight once.
Followings are the ways can be adopted under source reduction:
Motivate the people to reduce the quantities of waste
Such things are purchased that are recyclable and reusable
Rechargeable batteries are used
Purchased items that are least packaging or no packaging
Purchase beverages in refillable glass
Use of lightweight aluminum and plastic bags for waste
Use sponges and washable napkins, towels and handkerchiefs instead of papers

## Slide 42: 2.Open Dumping
It is the method of disposal of waste, in this method generally low lying areas are selected around cities and large quantity of waste are disposed off there.
Merits Demerits
Cheap Makes an area unhealthy
Easy Waste are seen scattered
Less laborious Soil structure and texture of soil is affected
Low lying areas are filled Breeding sites for disease
Requires no planning Permanent source of bad smell

## Slide 43: Open Dumping

## Slide 44: 3.Ocean Dumping
Every years millions of tons of packaging, including bottles, cans and plastics containers, other municipal refuse, industrial waste, sewage and sewage sludge are dumped at sea, bridges, even in remote regions, are littered with large amount of non degradable materials from our industries.
The oceans are generally considered as waste area dumping our wastes ,but they are not so large that we can continue to treat them as carelessly as has been our habit.
Merits Demerits
Easy makes ocean ugly and dirty
Cheap causing environmental pollution
Economical toxic waste material containing heavy metals

## Slide 45: Ocean Dumping

## Slide 46: Sanitary Land Filling

## Slide 47: Definition
A method of disposal of solid waste on land without environmental damage and health hazard

## Slide 48: Land fills
According to Cunningham and Saigo (1955
Land fills are land disposal sites for solid waste and in the method of land filling the operators compact the waste and cover it with a layer of dirt to minimize rodent and insect infestation ,blowing of debris with wind and leaching by rain.
According to Enger and Smith (2000)
A method of disposing of solid waste that involves burying the waste in specially constructed sites.

## Slide 49: Method
It is a method of improving waste land .
Low lying and swampy areas are reclaimed by this method.
Cell
Solid waste is spread and compacted in thin layer within small area .it is called cell .
Its depth may not be more than 2 meter.
Cover
The cell is then covered with soil layer which is spread uniformly and then compacted .it is called cover .
It is usually 20 cm thick.

## Slide 50: Final cover
When number of cells reaches the final desired elevation a final cover of earth of about 1 meter is placed and compacted .
This final cover is essential to prevent entry of rodents through burrowing

## Slide 51: Phases Of Sanitary Land Filling
First phase
In first phase aerobic bacteria are dominant for aerobic decomposition. Bacteria deplete oxygen and therefor temperature is raised.
Second phase
In this phase anaerobic conditions or anaerobic bacteria take over resulting production of H2 and CO2 due to acidogenic activity of anaerobic bacteria.

## Slide 52
Third phase
In this phase methanogenic bacteria are product resulting commencement of methanogenic activity.
Fourth phase
In this phase methanogenic activity is established causing large scale production of CH4.
Fifth phase
Methanogenic activity is decreased representing depletion of organic matter. the process returns to aerobic condition within the landfill.
For this purpose escape vents are provided for gas .

## Slide 53: Merits
Public health problems are minimized as rats ,insect , and other pests are unable to breed due to compact final cover.
There is no air pollution and environmental damage.
There is less likelihood fire hazards.
This method is more economical .
Cost of this method was Rs.2 to 3 per tone .
By this method reclamation of land is achieved .

## Slide 54: Demerits
Danger of water pollution after raining due to leaching of toxic material.
However this drawback can be overcome by the use of plastic sheets or tight cement linings.

## Slide 55: Incineration
Incinerate means to burn up completely or reduce to ashes and incinerator means furnace.

## Slide 56: Definition
Complete combustion of the solid wastes at high temperature ranging from 900 to 1500 degree and reducing their volume and weight to from 10 to 15 percent.
Method or process:
Before incineration non combustible materials such as metals are removed by magnetic action or gravity .
Many of separated material like metals or glass can be recycled.
Require high temperature
Expensive method
Make it economical energy must be recovered .

## Slide 58: Merits
Helps in handling large load.
Small space is required for ultimately left over material.
Most of the industrial waste incinerated effectively.
Heat and electric energy can be recovered by this method

## Slide 59: Demerits
Expensive process
Involve very high level of maintenance and operating cost
Initial cost of the project is 3 to 4 times more than of sanitary land filling
Incineration leads to air pollution through evolution of gases like SO2 ,H2S hydrogen chloride , smoke, flyash, dust and organic acids etc.

## Slide 60: Composting

## Slide 61: Define
The organic matter of solid waste is handled in such way the natural accuring bacteria and other organism decompose it and produce a safe clean and soil like material is called compost.
That process is called composting
Other words the biological decomposition of organic matter is called composting .
Safe method than open dumping

## Slide 62
Saigo (1955) defined as “ The biological degradation of organic material under rich aerobic condition to produce compost which is a nutrient rich soil amendent and conditioner’’ .
Enger and Smith defined composting as “ a waste disposal system in which organic matter is allowed to decay to a usable product”.
Micro organism which decompose the organic matter are following
Bacteria : They decompose the material at all stages .
Fungi : They usually appear during the first week of decomposition.
Actionomycetes :They assist during the final stage.

## Slide 63: Process of Decomposition
First stage : mesophilic bacteria start the decomposition of organic matter and convert into carbon dioxide and generate heat up to 45C.
Second stage : thermophilic bacteria take over the process and raise the temperature up to 60 C .
Third stage :fungi appear in first week and assist the decomposition.
Forth stage :At this final stage the earth worm and actionomycetes assist and break down the organic matter.
Fifth stage : After 3 weeks the compost is establish and temperature is drop .
Compost gives earthy smell and dark brown color

## Slide 64: Measures
Organic matter turn to allow the oxygen penetration in all parts of waste .
For sustenance of aerobic life .
Moisture contents should be 55 % for biological activity.
Moisture is critical factor for decomposition.
Excess moisture makes aerobic life difficult .
Lower moisture inhibits the biological life

## Slide 65: Merits And Demerits
Merits
Compost is excellent for resorting organic contents of agriculture soils .
Use in rural areas because it is simple easy and economical method.
This is best method for disposal of putrescible materials.
Demerits:
Cost is 2 to 3 times higher then sanitary.
Non putrescible material should be removed .
Not suitable for urban areas

## Slide 66: Recycling

## Slide 67: Introduction
Solid wastes usually have significant amounts of valuable materials which should be separated and reused.
This would reduce the volume and weight of total solid wastes on the one hand & reuse the valuable materials giving income on the other.
Some important solid wastes
Paper
Glass
Metals
Plastics
Rubber

## Slide 68: Merits
It increases the income of waste collectors, artisans and suppliers.
The re-useable articles are converted into usable products with less cost.
It eases burden of wastes disposal services of Municipal Corporation.
E.g. 1. Similarly there is no sources of tin in the USA. However packagers reclaim about 2 kgs of tin from each 1000 kgs of metal food can.
2. The USA imports nearly all aluminum and recycles more than 60 percent of its aluminum beverage cans.

## Slide 69: Demerits
All the reusable constituents has to be separated for separate recycling such as paper, plastic, glass and metal etc. hence it may become expensive process.
Recycling of plastics is associated with technical and economic problems. This is because technologies for recycling differs from plastic to plastic and one plastic type has to be separated from others. For example
A milk container is a high density polyethylene.
An egg container is polystyrene.
A soft drink bottle is polyethylene terephthalate.