## Slide 1: Nuclear Energy:
Atomic nuclei when disintegrated produce energy which has tremendous potential is called nuclear energy.
Benefits of nuclear energy:
X-rays are now being used routinely to examine fractures/diseases of bones.
Radiation are used for the treatment of cancer called radiotherapy.

## Slide 2: Continued….
Nuclear power plants are generates 17% total electrical energy.
Preservation of food and agri. Products through irradiations.
Nuclear explosions are used to move large amounts of earth and rock in order to construct canals, dams, under ground storage facilities.

## Slide 3: Harmful Effects Of Nuclear Energy:
Nuclear energy also has tremendous potential to do harm to human being directly or indirectly.
For instance:
Nuclear bombs destroyed two cities i.e. Hiroshima and Nagasaki of Japan during world war 1.
Disposal of radioactive wastes has emerged a big problem now-a-days in account of increasing use of nuclear energy for military purposes.

## Slide 4: Terms/Concepts Used In Nuclear Energy:
Atom:
“The smallest entity of an element, composed of protons, neutrons and electrons that take part in chemical reaction”
Atom is a source of nuclear energy.
Atoms are composed of a central region called nucleus. which contains positively charged protons and neutrons having no charge.

## Slide 5: Continued…..
Small negatively charged electrons moves around the nucleus. As positively charged particles in the nucleus repel one another, therefore energy is required to hold protons and neutrons together.

## Slide 6: Isotopes:
“Those atoms of the same elements that have same atomic number but different numbers of neutrons(mass number)”.
Some isotopes of atoms are radioactive i.e. the nuclei of these atoms are unstable and decompose spontaneously.
Neutrons, electrons, protons and other large particles are released during nuclear disintegration along with considerable amount of energy.
The rate of decomposition is consistence for given isotopes.

## Slide 7: Continued…..
It is measured and expressed as radioactive half-life.
Radioactive half-life:
“The time taken for half of the radioactive material to decompose spontaneously”.

## Slide 8: Radiations:
Nuclear disintegration releases energy from the nucleus as radiations.
Types of radiations:
There are three major types of radiations:
Alpha radiations
Beta radiations
Gamma radiations

## Slide 9: Continued…..
Alpha Radiation:
“Alpha radiation is the type of radiation that consists of a particle with two neutrons and two protons”.
It travels through air for less than a meter and can be stopped by a sheet of paper or outer layer of skin.
It produces up to 20 times more damage to biological tissues than those of beta or gamma radiations.
Beta Radiation:
Beta radiation is a type of radiation that consists of electrons released from the nuclei of many fissionable atoms .
It travels more rapidly than alpha particles.it travels through air for a couple of meters and can be stopped by a layer of clothing, glass or aluminum

## Slide 10: Continued…..
Gamma Radiation:
Gamma radiation is a type of electromagnetic radiation that is released from the disintegrating atomic nuclei i.e. X-rays, light and radio waves.
Gamma radiation can pass through several millimeter of concrete.
It causes equal amount of damage to the biological tissues as that of beta radiations.

## Slide 11: Nuclear Fission:
“Nuclear fission is the decomposition of a nucleus of an atom with release of particles and energy”.
In other words, “Nuclear fission is the radioactive decay process in which isotopes split apart to create two smaller atoms”.

## Slide 12: Nuclear Chain Reaction
Nuclear chain reaction may be defined as “A continuous process in which a splitting nucleus releases neutrons that strike and split the nuclei of other atoms releasing nuclear energy”.
Uranium-235 and plutonium-239 are suitable for providing nuclear chain reactions.
Heavy atoms also produce large amount of energy from bombs or nuclear reactors.

## Slide 13: Nuclear Reactors:
“ Nuclear reactor is a device that permits a controlled nuclear fission chain reaction”.
Uranium-235 is a uranium isotopes that is used in nuclear fission reactors.
When the nucleus of fissionable heavy atom is splitted, it release 2 or 3 rapidly moving neutrons along with large amount of energy.
This energy(fuel) is very important product of nuclear fission reaction.

## Slide 15: Continued…..
Control rods:
“Nuclear reactors contain control rods that are used to control the rate of fission by absorbing neutrons”.
When control rods are lowered into a nuclear reactor, they absorbs the neutrons produce by fission ing uranium, few neutrons are left to continue nuclear chain reaction, hence the rate of fission is decreased.
When the control rods are withdrawn , more fission occurs and process continues through production of more particles, radiations and heat.

## Slide 16: Continued…..
Moderator:
Moderators is a material that absorbs the energy from neutrons released by fission hence it slows neutrons enabling them to split the nuclei of other atoms more effectively.
In nuclear reactors, water is used as moderator.
The fuel rods in the nuclear reactor are surrounded by water or some other moderator.
When uranium-235 undergoes fission, the energy of fast moving neutrons is transferred to water.
Due to this the neutrons slow down and the water is heated.

## Slide 17: Types Of Nuclear Reactor
Light water reactors
Heavy water reactors
Gass cooled reactors

## Slide 18: Light Water Reactors
Ordinary water is used as a coolant
The lightest isotope of hydrogen having atomic masses one
LWR make up about 90% of reactors working today
Two types of light water reactors.
Boiling water reactors
Pressurized water reactors

## Slide 19: Boiling Water Reactors
It produces steam in a reactor
Steam is transferred directly to turbine to produce electricity
Water acts as both moderator and reactor core coolant
Used in 20% nuclear reactors in the world.
Demerits
Steam passing to the turbine must be treated to remove any radiation
Even then some radioactive material is left in the steam

## Slide 20: Pressurized Water Reactors
Uses a stream generator to form steam.
Secondary loop is used to transfer this steam
Water is kept under high pressure and steam is not allowed to form in reactor.
Secondary loop transfers the heat to stream generator and this steam is used to turn the turbine to produce electricity

## Slide 21: Pressurized Water Reactors
Risk of radiation is reduced
Cost of construction is increased due to addition of secondary loop
It is used in over 70% of the nuclear reactors in the world.

## Slide 22: Heavy Water Reactor
In HWR water is used as reactant core coolant and moderator.
Heavy water is used containing deuterium isotope because it is better neutron moderator.
Steam generator is used to convert regular water to steam in a secondary loop.
Merits
HWR uses naturally occurring uranium isotopic mixtures as a fuel while LWR used enriched Uranium-235
Operating cost of HWR is low than LWR as it does not require enriched fuel

## Slide 23: Gas Cooled Reactors
Used graphite as a moderator and CO2 gas as the reactor-core coolant.
Steam generator forms steam and secondary loop is used to transfer steam to turbine
Natural isotopic mixture of uranium are used as fuel

## Slide 24: Nuclear Breeder Reactors
After nuclear fission development construction of breeder reactors were started.
A nuclear breeder reactor is a nuclear fission reactor that produces heat to be converted to steam to generate heat
Also forms a new supply of radio active isotopes.

## Slide 25: Nuclear Breeder Reactors
U-238
U-239
Np-239
Pu-239
A fast moving neutron hits U-238 nucleus, a series of reaction takes place with two intermediate atoms. i.e U-239 and Np-239
There is a release of beta particle from their nuclei.
While the Pu-239 is fissionable and can serve as nuclear fuel
Water is not used as a moderator because it slows down the neutrons and Pu-239 does not formed

## Slide 26: Process Of Nuclear Power Reactors
The important problem in the case emission of radioactive particles from a radioactive source and its ability to penetrate and damage tissues of human , animals and plant.
This property derived from spontaneous disintegration of nucleus of atom of heavy metals such as uranium , plutonium , radium , actinium and thorium etc.
Radio activity is measured in term of Becquerel.
A nuclear energy producing reactor is an assembly of equipment in which a nuclear reactions is sustained provides large quantity of heat.
With coal and oil heat comes from burning of fuel while in nuclear power its comes from splitting atoms of heavy radioactive metals like uranium

## Slide 27: Types Of Nuclear Power Plants
There are three main types of nuclear power point
Light water reactor
Boil water reactor
Power water reactor

## Slide 28: Merits Of NPPS
NPPS are friendly for environment
Because they don't generate greenhouse gasses
And their waste is very low in volume which can be easily disposed.

## Slide 29: Nuclear Accidents
Although there have been some accidents at nuclear power plants since their introduction.
Three mile island accident in 1979.
Chernobyl accident in 1986.
the effect include skin diseases ,deformed births and disturbed reproductive systems. In addition to human injuries many animals also died.

## Slide 30: Radiation And Their Effect
There are two main groups of radiations as under:
Non- ionizing radiation
Ionizing radiation

## Slide 31: Non-Ionizing Radiation
Non ionizing radiation are lethal to micro organisms.
They are capable of injuring surface of the tissues of higher animal and plants.
They have shorter wave-length and greater energy e.g. UV rays.

## Slide 32: Ionization Radiation
Ionizing radiation include:
Alpha
Beta
gamma
x-rays.

## Slide 33: Effects
They possess the following effects:
They break chromosomes
They induce mutation
Embryo's are more sensitive to ionizing radiation
Ionizing radiation effects the digestive tract resulting nausea, vomiting
Ionizing radiation can cause breast cancer leukemia
Nuclear accidents are frightens and cause immediate death due to involvement of large amount of energy

## Slide 34: Nuclear Power Plant In Pakistan
Pakistan has two nuclear plants under:
Karachi nuclear power plant
Chashma nuclear power plant

## Slide 35: Karachi Nuclear Power Plant
KANUPP is Pakistan's first nuclear power plant, inaugurated on November 28, 1972, with a total gross capacity of 137 MW.
The International Atomic Energy Agency safeguards and inspects the complex.
The plant is under construction by the Pakistan Atomic Energy Commission (PAEC) and is financed by the IAEA, the China Guangdong Nuclear Power Group, the China National Nuclear Corporation, and the China Atomic Energy Authority.
The Karachi Nuclear Power Plant (KANUPP) has a heavy water moderated and cooled natural uranium-fueled, horizontal pressure tube reactor.

## Slide 36: Chashma Nuclear Power Plant
The Chashma nuclear power plant or Chashma nuclear power complex, near Chashma colony and kundian town, mianwali district, Punjab, Pakistan, is a commercial nuclear power plant consisting of four operating units and one planned unit.
Chashma nuclear power plant reactors and other facilities are being built and operated by the Pakistan atomic energy commission (PAEC) with Chinese support under the approval and guidelines of international atomic energy agency.

## Slide 37: Nuclear Industry
Nuclear industry is producing considerable amount of waste.
This quantity is increasing steadily with the passage of time .
Some waste material are highly dangerous because of its radioactivity
However nuclear industry is relatively young one it is producing smaller quantity of nuclear waste as compared with other types of industrial waste.
The quantity of waste is also varies with every stage of nuclear fuel cycle ranging from mining, initial processing of uranium from the fuel after removal from the reactor.

## Slide 38: Rules For Nuclear Industry
Nuclear industry has been governed by strict national and international rules and regulation at all the stages . such as
Selection of safer sites for construction of nuclear power plant,
Installation operation,
Handling,
Storage,
Disposal of nuclear waste material including radioactive waste.

## Slide 39: Categories Of Nuclear Waste
On the bases of radioactivity and type of emission of radiation such as alpha , beta, gamma nuclear waste is categorized in to three levels.
Low level nuclear waste
Medium level nuclear waste
High level nuclear waste

## Slide 40: Low Level Nuclear Waste
This type of waste contain low radioactivity.
High volume because of its bulky nature.
waste contain protective clothing, rubber , gloves, tissues ,plastic bags and swabs, liquid effluents from sink and drain and radioactive gases found in ventilation system.

## Slide 41: Handling
During disposal low level of nuclear waste can be handled without shielding
Major part of low level of waste usually comes from medical uses non nuclear industries and agriculture and research activities.
the nuclear industry contributes only a miniscule 0.1 percent of the total radiation we receive
Although high doses of radiation are usually fatal but low doses are cumulative and lead to illness and finally it may develop cancer.
Large volume of low level waste is reduced by the compaction shredding and incineration

## Slide 42: Medium Level Nuclear Waste
It is more radioactive and hotter than low level type hence can not be handled or transported without shielding.
Such waste consist of reactor by products and other materials including equipment's and tools that have become radioactive.
So reactor resins , solidified chemical sludge's or used equipment are radioactive enough to need shielding during handling.

## Slide 43: Handling
It is encapsulated in cemented steel drums which are in turn kept in specially built stores for eventual disposal in underground caverns at selected sites.
Main demerit of underground burial is leakage problem as it may contaminate the ground water.

## Slide 44
High Level Nuclear Waste
It is sometime describe as heat generating waste because of warmth produced by decay of its highly concentrated radioactivity.
Produced into two ways
1) by reprocessing spent nuclear fuel to recover isotopes that can be used again as fuel.it is in the form of nitric acid containing fission products extracted from the components.
2) by merely using reactor fuel rod which contain long live isotopse when spent ,this waste is very hot at first.

## Slide 45: High Level Waste
Is created during the initial stages of reprocessing when uranium and plutonium are separated from spent fuel,
This solution is then diverted to stainless steel tanks, which are equipped with cooling system.
The liquid may also treated to neutralized it and precipitate the radioactive elements forming a sludge.
High level waste is the most radioactive and is in liquid form.
It is handled by converting liquid into solid after heating then they moved underground caverns for cooling .more secure handling is final burial in the sealed in appropriate corrosion resistant containers.

## Slide 46: Basic problem of nuclear waste
The basic problem of nuclear waste is that becomes harmless after million of years .
Plutonium, for example takes 25000 years for only half of its radioactivity to decay to a safe level and can take hundreds of thousand of more year to decay altogether.
Each nuclear reactor produces about 200kg of plutonium each year ,an amount that is enough to conflict cancer in every living human being.
Present world plans allow secure storage of high level waste for the next thousand years .

## Slide 48: Land Disposal Of Nuclear Waste
Land dumping of the nuclear waste is the other method of disposal low level and high level radioactive waste .
Radioactive waste buried deep in the ground where it hoped that it will remain unexposed to ground water .
Ten thousands of year required for decay of radioactive material to safe level.
There is possibility of migrating the waste over thousands of year due to leakage of metal canisters.
So experts believe that monitored retrievable storage is better approach for safe land disposal.

## Slide 49: Land Disposal Of Nuclear Waste
In this method the waste in underground mines surface facilities such a dry casks where it can be watched .
Storage sites are kept open and inspected regularly.
This method would be expensive .

## Slide 50: Decommissioning Old Nuclear Plants
Its means dismantling .
Life of plant 30 to 40 years.
Then each part of plant disposed safely.
Oceans to avoid environmental hazards .
In other words demolition is not so simple.
Preventing people from coming into contact wit the contaminated building.

## Slide 51: Steps For Decommissioning
All fuel rod removed
All water drained
Reactor and generator pipes are cleaned and flushed.
Drained water and material to clean pipes are radioactive hence stored safely and disposed of.
About 90% radioactivity is removed in that steps .

## Slide 52: Step II
Dismantle the plant as soon as it is closed down .
Put plant in mothballs so that material which has short life should be disintegrate.
Covering the plant with reinforced concrete and placing a barrio around the plant.
Packing
Transporting
Burying the waste
Cost of decommissioning a plant t is 200 to 400 million dollars.

## Slide 53: Thermal Pollution
It is defined as
“The waste heat that is released by the industries, automobiles, urban population and other miscellaneous sources into the environment.”
If nuclear power plant is efficient then is release low heat other wise high heat is released in the environment.
Water is used as cooling agent is that plants.

## Slide 54: Methods
Dilute and disperse
Delay and decay
Concentrate and contain
Vitrification
Ocean dumping of radioactive wastes
Land disposal
Decommissioning of nuclear plants

## Slide 55: Methods
Dilute and Disperse
Dilute to permissible levels for disperse
Diluted naturally when in the air, soil or water
Danger of their accumulation in food chain & environmental contamination
Delay and Decay
Radioactive material which has a relatively short life
Can be retained in receptacles for a long period until radioactivity disappears
Concentrate and Contain
Materials which has high radioactivity or long half life
Concentrated into small volumes and stored in the places far away from public and animal habitats

## Slide 56: Methods
Vitrification
Process in which high level liquid waste is converted into insoluble block of glass
At the same time, it also reduces the original volume of nuclear waste to about 2/3
The blocks are then cooled through naturally convected airflow and kept in containers
Containers are transferred to Vitrified Product Store (VPC) for at least 50 years
Ocean Dumping
It is the method to dump radioactive wastes in far off seas
Firstly it is started by Soviet Union in 1965 when they dumped 18 reactors in Kara Sea

## Slide 57: Methods
Land Disposal
It is another major method which is practicing by most of the countries in the world
The nuclear waste buried deep in the ground where it is hoped that they will remain unexpected to groundwater and earthquakes for the tens of thousands of the year
Decommissioning old nuclear plants
Decommissioning means dismantling
Some nuclear plants are designed for a life of only about 30-40 years
After that, it becomes brittle and untrustworthy
In these cases, such plants are to be dismantled
Its each part have to be disposed of safely either through monitored and retrievable storage sites