## Slide 1: MICROTOMY
Dr. Ahmad Ali
Lecturer in Zoology, IUB, Bahawalpur

## Slide 2: Introduction
Many living things are extraordinarily beautiful. The microscopist has a privileged view and this may be extended and enhanced by looking inside; this can be done by making very thin sections.

## Slide 3: Microtomy
The means by which tissue can be sectioned and attached to a surface for further microscopic examination.

## Slide 4: Microtome
Derived from the Greek mikros, meaning “small”, and temnein, meaning “to cut”)
It is a mechanical device for cutting thin uniform slices of tissue sections.

## Slide 5: History
The earliest form of microtomy was the freehand sectioning of fresh or fixed material using a sharp razor. The section produced, could, with practice, be quite thin and translucent.

## Slide 6
Santiago Ramón y Cajal managing the microtome, 1884-1887

## Slide 7
Charles Sedgwick Minot
(1852–1914)
Minot’s rotating microtome

## Slide 8: Types of microtomes
Based on the mechanism:
  Rocking
  Rotary Rocking
  Rotary
  Base-sledge
  Sliding
  Freezing
  Vibrating
  Saw
  Cryostat
  Ultra
  Laser

## Slide 9: Rocking microtome

## Slide 10
Name derived from the rocking action of the cross arm.
Oldest in design, cheap, simple to use, extremely reliable, minimum maintenance.
The Cambridge rocking microtome was the most popular microtome.

## Slide 11
Parts of a Rocking Microtome
Notes: 1 – Rocking arm; 2 – Micrometer screw; 3 – Operation lever; 4 –Knife holder; 5 – Sample holder base (the holder absent); 6 – Knife holder tightening screw; 7 – Sample holder screw; 8 – The safety lock mechanism.

## Slide 12: Mechanism of action
Knife is fixed, the block of the tissue moves through an arc to strike the knife.
Between strokes the block is moved towards the knife for the required thickness of sections by means of a ratchet operated micrometer thread.
Steady backward and forward movement of the handle gives ribbons of good sections.

## Slide 13
Advantages
1.Can cut sections from small blocks of any tissue type.
2.The mechanism is simple.
3.The machines literally last lifetime.
4.In emergency can be adapted for frozen sections by freezing the tissue with ethyl chloride spray

## Slide 14
Disadvantages
1.Size of block that can be cut is limited.
2.Sections are cut in a curved Plane.
3. Light instrument : advisable to fit it into a tray which is screwed to the bench , or to place it on a damp cloth to avoid movement during cutting.
4. The cutting angle of the knife cannot be adjusted
5. No serial section is possible.

## Slide 15: Rotary microtome

## Slide 16: Types of rotary microtome
Manual
Semi-automated
Fully automated

## Slide 17: Manual Rotary Microtome
Completely manipulated by the operator

## Slide 18: Semi-Automated Rotary Microtome
One motor to advance either the fine or coarse hand –wheel

## Slide 19: Fully Automated Rotary Microtome
Two motors that drive both the fine and the coarse advance hand-wheel

## Slide 20
Advantages of Rotary microtome
Ability to cut thin 2-3 mm sections.
Heavier, so more stable
Large and heavier knife used-less vibration when cutting hard tissue.
Cutting angle of knife is adjustable
Easy adaptation to all types of tissues ( hard, fragile, or fatty) sectioning.
Can cut celloidin-embedded sections by using a special holder to set the knife obliquely.
Ideal for cutting serial sections: large number of sections from each block.

## Slide 21: Parts of a Rotary microtome
BASE
(MICROTOME BODY)
KNIFE AND ITS HOLDER
BLOCK HOLDER

## Slide 22
Knife holder base: A part that anchors the knife holder to the microtome stage. The knife holder base can be moved toward or away from the block, but MUST be stationary and locked during microtomy.

## Slide 23
Knife holder: This part is comprised of several components including the blade clamp that holds the blade, the knife tilt for adjusting the knife angle, and the face plate that guides that ribbons away from the blade and towards the operator.

## Slide 24
Coarse handwheel: Moves the block holder either toward the knife or away from the knife.

## Slide 25
Micron adjustment: Micron settings for section thickness can range from 1 to 60 microns on most microtomes.

## Slide 26
Advancement handwheel: Turns in one direction and advances the block toward the knife at the specified microns.

## Slide 27
Safety Lock: Most handwheels are equipped with a safety lock to prevent the wheel from releasing and having the block holder come down towards the blade while a block is inserted or removed. It should be used anytime the microtomist is not actively sectioning paraffin blocks

## Slide 28: Rotary rocking microtome

## Slide 29
This is slightly more robust than the rocking microtome and has the advantage of producing a flat face to the tissue block.
Most of them have a retracting mechanism which takes the tissue block away from the knife on the upward stroke.
Although they can be used for paraffin wax work they are used more commonly in cryostats.

## Slide 30
Most widely used, also called Minot microtome, after its inventor Professor Minot.
The knife is stationary and the block is moved up and down in a vertical plane by the rotary action of the hand wheel
Suitable for paraffin embedded sections

## Slide 31: Mechanism of action
The hand wheel rotates through 360 degree moving the specimen vertically past the cutting surface and returning it to the starting position.
Block holder is mounted on a steel carriage which moves up and down in grooves and is advanced by a micrometer screw- cutting perfectly flat sections.

## Slide 32: Base sledge microtome

## Slide 33
Originally designed for cutting sections of very large blocks (whole brain)
In laboratories where very hard tissue or large blocks are usual, this type of microtome is favored
It is most commonly used in neuropathology and ophthalmic pathology

## Slide 34: Mechanism of action
The block holder is mounted on a steel carriage which slides backwards and forwards on guides against a fixed horizontal knife.

## Slide 35
Advantages
Heavy and stable with no vibrations
Angle of the knife is adjustable
Knife used is long(24 cms), hence requires less honing.
The knife holding clamps are adjustable and allow the tilt and the angle (slant) of the knife to be easily set.

## Slide 36
Disadvantages
Slower in use than rocking or rotary microtome.
With practice, sections from routine paraffin blocks can be cut as quickly as on any other type of microtome.

## Slide 37: Sliding microtome

## Slide 38
The knife or blade is stationary, the specimen slides under it during sectioning.
It was designed mainly for cutting celloidin embedded blocks of tissue.
It can also be used for paraffin wax embedded sections.

## Slide 39: Vibrating microtome

## Slide 40
Designed to cut fresh unfixed tissue
The name of the instrument derives from the high speed vibration produced in a safety razor blade to provide the cutting power.

## Slide 41
The amplitude of vibration is adjusted by altering electrical voltage applied to the 'knife'
Sections are thicker
Designed to cut tissues which has not been fixed , processed or frozen.
To prevent tearing, soft material is cut whilst immersed in a fluid which also aids in dissipating heat produced at the vibrating edge of the razor as it cuts.

## Slide 42
Advantages
Greatest application in enzyme histochemistry & ultra structure histochemistry.
Tissues are cut at very slow speed to avoid disintegration.

## Slide 43: Ultra Microtome

## Slide 44
These are used exclusively for electron microscopy .
Prepare ultrathin sections .
It has been reported that sections can be cut as thin as 10 nanometres.
Knives are usually made from glass, diamond or sapphire.
The block is brought to the knife edge under microscopical control and as each section is cut it is floated on to a water bath adjacent to the knife edge

## Slide 45: Freezing microtome

## Slide 46
The freezing microtome is equipped with a stage upon which tissue can be quickly frozen using either liquid carbon dioxide, from a cylinder, or a low temperature recirculating coolant.
To delay the thawing of sections on the knife and make it possible to transfer them directly from knife to slides.
The knife is moved whilst the tissue block remains static same as sliding microtome.

## Slide 47
Used for cutting thin to semi-thin sections of fresh, frozen tissue .
Although other microtome can be modified for cutting frozen section, this gives the best results & is used almost universally.

## Slide 48: Saw microtome

## Slide 49
Saw microtomes will cut sections from very hard material such as undecalcified bone, glass or ceramics.
The samples, commonly embedded in resins, are moved extremely slowly against a diamond coated saw rotating at approximately 600 rpm.
Sections of 20 µm or greater are possible providing the saw blade is in perfect condition.
Very thin sections are not possible.

## Slide 50: Cryostat microtome [Cryotome]

## Slide 51
Cryostat is a refrigerated cabinet in which a specialty microtome is housed.
All the controls for the cabinet are operated outside the cabinet.

## Slide 52
The introduction of fluorescent antibody staining techniques by Coons, Creech and Jones in 1941 led to a need for thin section(3-5 microns) of fresh frozen tissue free of ice crystal defect.
So it must be quick frozen at a very low temp , and section cut without allowing the tissue to thaw.

## Slide 53
Cryostat is primarily used for cutting sections of frozen tissue
Frozen sections were originally produced for histological techniques, but were later used to demonstrate soluble substance and the diagnosis or urgent biopsy specimens
Specimens are frozen and cut at 4-8 μm thickness in an cryo-microtome using an anti-roll plate

## Slide 54: Principle
When the tissue is frozen, the interstitial water turns into ice, tissue becomes firm and acts as an embedding medium.

## Slide 55: Improvements in design
electronic temperature control
electronically controlled advance and retraction of the block
specimen orientation facility
digital visualization of chuck and cabinet temperature
mechanical cutting speed control and section thickness
automatic defrost mechanism
automated decontamination and sterilization

## Slide 56: Freezing agents
liquefied nitrogen (−190°C)
isopentane (2-methylbutane) cooled by liquid nitrogen (−150°C)
dry ice (−70°C)
carbon dioxide gas (−70°C)
aerosol sprays (−50°C)

## Slide 57
USES –
rapid production of sections for intra-operative diagnosis
diagnostic and research enzyme histochemistry for labile enzymes
immunofluorescent methodology
immunohistochemistry techniques when heat and fixation may inactivate or destroy the antigens
diagnostic and research non-enzyme histochemistry, e.g. lipids and some carbohydrates
silver demonstration methods, particularly neuropathology

## Slide 58: Laser microtome

## Slide 59
Contact free slicing
Prior preparation of sample not required
Can also be used for very hard materials, such as bones or teeth as well as some ceramics
Thickness: 10-100 µm

## Slide 60
Principle:
The device operates using a cutting action of an infra-red laser. As the laser emits a radiation in the near infra-red, in this wavelength regime the laser can interact with biological materials.

## Slide 62: Microtome knives

## Slide 63
One of the important instruments used to cut uniform thin serial sections of the tissue.
For routine purpose wedge knife is used. It is plain on both sides. The size varies from 100 mm to 350 mm in length.

## Slide 64: Types of Knives
STEEL KNIVES
GLASS KNIVES
DIAMOND KNIVES
SAPPHIRE KNIVES

## Slide 65: Steel Knives
Manufactured from high quality carbon or tool grade steel which is heat treated to harden the edge.
The steel should be free from impurities, contain anti-corrosives and be rust-resistant.
The best knives are those that are fully hardened.
Those which are only surface hardened lose the cutting edge very quickly once the hardened area is removed through repeated re-sharpening.

## Slide 66: Based on compositon
Non-corrosive knives for cryostats
Tungsten carbide
Disposable blades

## Slide 67: Non-corrosive knives
These are manufactured from hardened, heat treated stainless steel free from all impurities and containing 12 to 15% chromium.

## Slide 68: Tungsten carbide knives
non corrosive
practically non magnetic
100 times harder than hardened tool steel.

## Slide 69
Excellent resistance to wear but are brittle because of their extreme hardness and should be handled carefully.
Up to 30,000 serial sections of undecalcified bone embedded in methacrylate per sharpening has been reported.

## Slide 70: Disposable blades
Manufactured from high quality stainless steel
different grades according to thickness
The edge of disposable blades can be coated with platinum6 or chromium7 to enhance strength and prolong cutting life.

## Slide 71
Teflon coated blades are particularly suitable for use in cryostats as these offer reduced cutting resistance and minimal friction.
Disposable blades need to be held rigid in a special holder to prevent vibration during the cutting stroke. These knives consistently produce high quality sections virtually free from compression.

## Slide 72: Knife profiles
Strongly planoconcave/Biconcave
Planoconcave
Wedge shaped
Plane shaped

## Slide 73: Biconcave Knife
Classical knife shape with concavity on both sides
Introduced by Heiffor
Rocking microtome and sledge microtome
Extremely sharp

## Slide 74
The Heiffor knife (used on rocking microtomes with a fixed handle)

## Slide 75: Parts of Heiffor knife
HEEL-Angle formed by the cutting edge and end of the knife nearest the handle.
TOE-Angle formed by the cutting edge and end of the knife farthest from the handle

## Slide 76
Length-100 to 250 mm
Less rigid
Prone to vibration
Used for cutting soft, celloidin embedded material.
To obtain the best result the knife should always be oblique to the object when cutting sections.
Not suitable for relatively hard materials, which cause the edge to vibrate and produce the phenomenon known as chattering.

## Slide 77: Planoconcave knife
One side of cutting surface is flat and the other is concave with different degrees of concavity.
Extremely sharp but delicate
Used for cutting soft samples like nitrocellulose embedded tissues.

## Slide 78
The plane surface is closest to tissue block.
Sledge and rotary microtome
This knife should be positioned obliquely to the material being sectioned.

## Slide 79: Wedge shaped knife
Used in all types of microtome to cut all type of materials
Both cutting surfaces are plane
Known as standard profile

## Slide 80
More rigid
Can be used for cutting harder materials.
Because of the extra thick nature of the wedge at the tip this type of knife cannot be ground as sharp as profile A or B knives.
With this style of knife the cutting plane is transverse to the object.

## Slide 81: Plane shaped knife
Wedge knife with steep cutting edge.
Hard objects (undecalcified bone).
Stouter to give rigidity.
Tungsten carbide coated edges.
Have detachable handle.

## Slide 82
Stable for long time.
Need more force to achieve the cut.
Varying lengths available
  80 mm-Freezing microtome
  240 mm-Base sledge microtome

## Slide 83: Angles of Knives
BEVEL ANGLE
RAKE ANGLE
CLEARANCE ANGLE

## Slide 84
Bevel angle/Facet angle/Cutting angle
Angle between the two facets that form the cutting edge
Usually varies between 27-32.
Smaller the bevel angle sharper is the knife, however too small bevel angle permits elastic distortion of the edge.
The width of the two facet which makes the cutting edge of knife has recommended from 0.1 to about 0.6mm.

## Slide 85
Clearance angle: angle formed by a line drawn along the block surface and the lower bevel of the knife.
Rake angle: angle between the upper bevel of the knife and a line at 90 degrees to the block surface.

## Slide 86
High rake angle and low clearance angle gives less compression to the tissue block and produces a smooth plastic flow type during sectioning.
High rake angles suitable for soft tissues and need to be reduced for harder tissues .
Clearance angle of 2 to 4° is used for paraffin and 5 to 7° for frozen sections.
Correct angle reduces friction preventing compression of the section.

## Slide 87: MICROTOME KNIFE SHARPENING
Done by two methods:-
Manual
    Honing
    Stropping
Automatic

## Slide 88: Honing
Microtome knives are sharpened against a special stone known as “Hone”.
Honing refers to grinding the cutting edge of the knife on a hard abrasive surface to sharpen the knife

## Slide 89
TYPES OF HONE
Belgian black vein
Arkansas
Aloxite
Tam’o Shanter Scotch
Carborundum
Plate glass

## Slide 90
Belgian Black Vein
fast, for coarse grinding and finishing.

## Slide 91
Arkansas
used to finish a knife after coarse honing on a coarse hone such as carborundum.

## Slide 92
Aloxite
fast but coarse , not for finishing

## Slide 93
Tam’o Shanter Scotch
good medium hone, very soft with short life. For removal of jagged edges and finishing.

## Slide 94
Carborundum
only for coarse work(large nicks in badly damaged knife)

## Slide 95
Plate glass
used as a hone by applying an abrasive (Aluminium oxide).
Used for all types of honing by changing the abrasive powder or paste.

## Slide 96: METHOD
Hone is placed on non skid surface
A damp cloth may be used-to prevent movement of the hone
Light lubricating Oil/soapy water is used for lubrication
Cutting edge facing away from the operator and the heel roughly at the centre of the nearest end of hone
Knife held between the thumb and fore finger, thumb on the back and forefinger on the front surface.

## Slide 97
The knife is pushed forward diagonally from heel to toe to the other end of the hone, turned over on its back and moved across the hone until the heel is in the centre with the cutting edge leading and then brought back diagonally. It is then turned across the hone to its original position

## Slide 99: Stropping
A process of polishing an already fairly sharp edge
May be flexible (hanging) or rigid
Before use & regularly (annually), strops must be oiled(vegetable oil) & dressed, with fine carborundum powder.

## Slide 100
The rigid type is a single leather strop stretched over a wooden frame of about 12×2×2 inches.

## Slide 101
Technique-Knife is laid on the near end of the strop with cutting edge towards the operator(opposite to honing).Knife held with forefinger and thumb.
Action is exact opposite to that of honing.

## Slide 102: Knife sharpening machines

## Slide 103
Despite high cost these machines are popular because less time consuming.
Mechanism:
Knife is held in the feeding mechanism and is sharpened by revolving cast iron wheels with both edges sharpened alternatingly.
Labolene is used as lubricant.

## Slide 104
Coarse lapping compound consisting of alumina suspension fluid and water is used first , followed by a compound containing a finer grade of alumina.
Lastly the suspension fluid is used alone to polish the edge
The time taken to traverse the whole of the cutting edge of knife should be about 25 seconds.
30 stroke in each direction should suffice with each grade of lapping compound.

## Slide 105: Glass knives

## Slide 106
Hard but brittle
Care is required while handling
These knives deteriorate with storage due to changes in the 'flow' or 'strain' of the glass after fracture and from oxidation impurities remaining in the hardened glass after manufacture.

## Slide 107
Knives should thus be prepared immediately before use.

## Slide 108: Diamond knives
Manufactured from gem quality diamonds.
Very expensive the knives are extremely durable, because of the hardness factor of the diamond, and are used primarily for cutting ultrathin, resin sections.

## Slide 109: Sapphire knives
Manufactured from one piece of solid sapphire artificially produced from an alumina monocrystal under computer controlled thermal conditions.

## Slide 110
Sapphire is harder than tungsten carbide or glass which ensures high durability of the cutting edge for all types of material.
The only restriction when using a sapphire knife is block size as the knife edge is limited to 11 mm. A special knife holder is required.

## Slide 111: Paraffin section cutting
Equipment required
  Water bath
  Drying oven or hot plate
  Fine pointed or curved forceps (130 cm in length)
  Small squirrel hair brush
  Clean slides
  Ice tray
  Pencil
  Teasing needle

## Slide 112
WATER BATH
The thermostatically controlled type is preferable. but if this is unavailable water from a hot water tap can be used, although this can give rise to air bubbles which may be trapped under cut sections.

## Slide 113
The temperature of the water should be about 5-6°C below the melting point of the paraffin wax.
Alcohol or small quantities of detergent may be added for reducing surface tension and allowing the section to flatten out with greater ease.

## Slide 114
HOT AIR OVEN
With a temperature setting at the melting point of the wax no obvious damage is done to the sections and drying is complete in 30 minutes.

## Slide 115
Too hot temperatures may cause:-
Dark pyknotic nuclei or nuclear bubbling
Cells that are completely devoid of nuclear detail

## Slide 116
HOT PLATE
For delicate tissues a lower temperature is desired for drying so as to avoid splitting and cracking of the section due to excess heat: 370C for 24 hours or longer is recommended
On Hot Stage which temperature is maintained at 45-50 degree 30 minute is sufficient.

## Slide 117
BRUSH AND FORCEPS
These instruments are necessary for the handling of sections during cutting and for the removal of folds and creases formed in the sections during floating out.

## Slide 118
SLIDES
For normal routine work 76 x 25 mm slides are universally used.
1.0-1.2 mm thick slides are preferred because they do not break easily.

## Slide 119
Larger size of slides are used for sections of eyes or CNS tissues when these will not fit on the regular size.
Identification details such as name or serial number have been traditionally inscribed on the slide by a diamond marker.

## Slide 120
Automatic slide labeling machines are now available and the increasing use of bar coding will reduce the number of transcription errors.

## Slide 121: Section adhesives
Most commonly used adhesive is Albumin.
Others are Starch paste and Chrome gelatin.
Albumin solution is prepared by mixing equal parts of glycerin, distilled water and white of eggs, then filtered through coarse filter paper and a crystal of Thymol is added .

## Slide 122
There are occasions when sections may tend to float from the slide and these are:
When sections are submitted to strong alkali solutions during staining.
Cryostat sections for immunofluorescence, immunocytochemistry and urgent diagnosis.
Tissues from the CNS.
When sections are submitted to high temperatures.
Tissues containing blood clot.
Tissues which have been decalcified.

## Slide 123
Disadvantages
Albumin retains some of the stain and gives a dirty background.
Thymol resistant organisms growing in the adhesive have been known to cause confusion in a gram-stained section.

## Slide 124
Two adhesives are favored:
Poly-L-lysine
This is bought as a 0.1 % solution which is further diluted for use(1 in 10 with distilled water). Sections are coated with this dilute poly-L-lysine and allowed to dry.
The ability of this substance to stick the section to the slide slowly loses its effectiveness. Therefore the coated slides should be used within a few days.

## Slide 125
3-aminopropyltriethoxysilane (APES)
This is by far the best section adhesive available and coated slides can be stored for a long time. Slides are dipped in 2% APES in acetone drained then dipped in acetone, drained again and finally dipped in distilled water.
Invaluable in cytology particularly for cytosine preparation of proteinaceous or bloody material.

## Slide 126: Charged or plus slides
Permanent positive charge by coating the slide with a basic polymer in which a chemical reaction occurs, leaving the amino groups linked by covalent bonds to the silicon atoms of the glass.
ADVANTAGE: Superior resistance to cell and tissue loss during staining or pre-treatments such as enzyme and antigen retrieval.

## Slide 127: Practical section cutting
BLOCK TRIMMING
Wax is removed with a sharp knife until 1/8th inch remains on all sides of the tissue.
Only small flakes of wax should be trimmed at a time
Attempts to trim large pieces can lead to splitting and exposure of tissue.

## Slide 128
TECHNIQUE OF CUTTING
Insert the knife in the knife-holder & screw tightly
Fix the block in the block holder & ensure it is secure.
Feed mechanism is adjusted until the wax block is almost touching the knife. Ensure that the whole surface of the block will move parallel to the knife so that straight ribbon of sections is obtained.

## Slide 129
All screws should be tight to avoid faulty sectioning.
For block trimming section thickness of 15µ with a rough knife is taken.
Sharp knife is used for sectioning.
Reset the thickness gauge to required thickness. 4-5 μ recommended for routine work.

## Slide 130
Apply ice to the block surface to make the wax hard which would have become soft by frictional heat.
There should be a smooth continuous plastic flow of the sections in the form of a ribbon

## Slide 131
When the ribbon comes off it is held gently with a fine moistened brush or forceps and then transferred to waterbath.
Section is then floated on water bath (temp 5-6° below melting pt. of wax) to remove creases

## Slide 132
Clean or albuminised slide is half submerged in water and section is picked up using a dissecting needle.
The slide is then set in an upright position to drain
Slides are kept in incubator (37° overnight for plain slides and 60° for 2 hours for albuminised ones).

## Slide 133: Cutting hard tissues
Since the introduction of disposable blades cutting hard tissues is now less difficult and the main reason for cutting difficulties is more likely to be poor fixation or processing.
Prolonged melting ice treatment of the block, or exposing the block surface to running tap water for 30 minutes, will often overcome almost every hard tissue.

## Slide 134
A slight reduction in the knife slant may also yield results.
If these remedies fail, softening fluids such as Mollifex (saturated into cotton, wool) can be used on the block surface. This will penetrate the block by some 15-20 µm and therefore it is essential to retrieve the immediate section.

## Slide 135: Surface decalcification
When a block has been trimmed to reveal the tissue surface, small foci of calcium may occasionally be removed.
The block can be removed from the chuck and placed face down on a pad of cotton wool saturated with 10% HCL. After treatment for approximately 1 hour, the block is relocated in the microtome and the first few sections can be cut before calcified tissue is re-encountered within the tissue.

## Slide 136: Precautions to be taken before section cutting
Fix Specimens Properly
No matter how much care is taken in processing and sectioning tissue specimens, essential morphologic detail will only be demonstrated if the tissue is promptly and adequately fixed.
Poorly fixed tissue will always produce inferior morphology even if optimally processed and carefully sectioned

## Slide 137
Process Tissue Properly
Specimens may be under-processed (specimen too large, schedule too short) or over-processed (schedule too long for size and nature of specimen). In both cases, they may be difficult or impossible to cut.
Considerable shrinkage of the specimen within the surrounding wax.
The tissue is soft and mushy and impossible to section.
Requires reprocessing

## Slide 138
Embed Specimens Carefully
Avoid under-filling the cassette as this can allow unstable clamping in the microtome and lead to cutting “thick then thin” sections and other problems.
Avoid over-filling cassettes as this can interfere with the correct alignment of the block face for sectioning.
Any excess wax on the outside of a cassette should be removed before clamping to ensure the block is firmly held during sectioning.

## Slide 139
Locate Microtome Appropriately
Position the microtome on a stable bench, away from air drafts, doorways and passing staff. Any air movement from air conditioners or other causes can make section handling very difficult.

## Slide 140
It is very important that staff are not distracted when using the microtome because of the risks of injury from extremely sharp blades.
It is preferable to have non-slip flooring in the vicinity of microtomes because inevitably, wax fragments will find their way onto the floor where they can produce a slippery surface.

## Slide 141
Utilize Safety Features Properly
Use forceps or brush instead of fingers to pick up sections or wax fragments from blade or block face.
Use handwheel lock when changing blocks.
The knife or blade should be removed from the microtome when the instrument is left unattended or when cleaning the instrument.

## Slide 142
Set Blade Clearance Angle Optimally
Blade clearance angle is adjustable and must be set for optimum performance
The clearance angle prevents contact between the knife facet and the face of the block.

## Slide 144
Maximize Blade Life
When cleaning the blade avoid dragging anything along the cutting edge. Even cellulose fibres can cause damage to the blade.
Avoid touching the edge with any hard objects such as forceps or brush.

## Slide 145
Orientate Specimen Appropriately
Intestine: blade passes through the mucosa last
Skin: blade passes through the epidermis last.
Cervix: it is better to present a point of dense tissue to the blade rather than a straight edge.

## Slide 146
Ensure Blocks are Cold
Sectioning is generally improved when the specimen and the wax are well matched in hardness.
Cold wax provides better support for the harder elements in a specimen allowing thinner sections to be obtained.

## Slide 147
Water penetrates a small distance into the block face, swelling tissues and making them more amenable to cutting. This is particularly important to over-dehydrated, dry or crumbly tissues.
Placing blocks in a freezer can cause surface cracking, where tissue separates from the surrounding wax.

## Slide 148: Precautions to ensure high quality thin section
Do not stop and restart during a cutting stroke as this will produce bands of different thickness across the section.
Use a section of blade that has not been used for rough trimming.
Re-chilling of the block may be required if the block face becomes warm or if deeper levels are required.
The application of warm, moist breath tends to make sections more cohesive, but it also causes thermal expansion thus making the section thicker.

## Slide 149
Float Out Sections Carefully
Flotation should expand the section to its original dimensions and ensure it is completely flat.
The temperature will need to be 5 - 9 ˚C below the melting point of the wax.

## Slide 150
Make sure the water is clean and free of bubbles and section waste (to avoid cross-contamination).
Place sections with the smooth (shiny) side down.
Place the sections onto the water surface with a gentle sweeping action.

## Slide 151
Sections are very easily damaged when dislodging wrinkles or bubbles with brush or forceps.
Leave the section on the water surface just long enough for it to flatten. Overexpansion can spoil the morphology in susceptible sections.
Skim the water surface with tissue paper between blocks to avoid the possibility of cross-contamination.

## Slide 152
To avoid any chance of a mix-up float out sections from one block at a time

## Slide 153
Dry Slides Adequately
Generally drying temperatures should not exceed
65 ˚C.
Excessive heat can cause droplets of water underneath a section to boil and this will cause damage.
Some delicate specimens will produce best results when dried at 37˚C for a longer time(24 hours).

## Slide 154
Clean and Maintain the Microtome Thoroughly
Do not clean the outer surfaces with alcohol or xylene as they are not resistant to these solvents.
No fluid must enter the inside of the instrument during cleaning.

## Slide 155: Faults
Section too thick
Wrong micrometer setting
Warm breath applied to cold block to facilitate sectioning
First section in ribbon chosen
Sectioning at too great a speed
Poor processing
Microtome needs recalibration

## Slide 156
Holes from rough
trimming
Block trimmed too quickly
Block surface not polished by cutting some thin sections after roughing
Inappropriate section thickness used when trimming
Block brittle (over-processed) or too cold when trimmed

## Slide 157
Knife lines
(vertical striations)
• Damaged knife or blade used
• Poor processing
• Hard material such as calcium in
block
• Debris in unfiltered wax
• Buffer salts precipitated in
specimens

## Slide 158
Disruption
Rough handling of specimen during grossing
Poor processing (incomplete dehydration, clearing or infiltration)
Vigorous treatment to dislodge wrinkles during flotation
Floating out for too long or using water that is too hot

## Slide 159
Fine cracks or micro-chatter
Tissue over-processed
Block too cold
Cutting too fast
Clamping mechanism not securely locked
Clearance angle needs adjustment

## Slide 160
Coarse chatter
CAUSES –
Clamping mechanism not securely locked
Very hard or large specimen
Poor processing
Insufficient clearance angle
Sectioning too rapidly
Worn microtome
Calcified areas in tissue
Over dehydration of the tissue

## Slide 161
SOLUTION –
Tighten blade and block holders
Reduce clearance angle
Use softening fluid
Rehydrate and surface decalcify
Re-embed in fresh paraffin
Replace or use new area of blade
Clean blade edge to clean excess paraffin

## Slide 162
Folds
Poor floatation technique
Poor fixation and/or processing (insufficient support)
Warm block
Section too thin
Clearance angle too great
Water bath too hot

## Slide 163
CAUSES –
Poor processing (insufficient support)
• Warm block
• Cutting too fast
• Dull cutting edge
• Clearance angle too great
• Paraffin too soft for processing
Excessive compression

## Slide 164
SOLUTION –
Replace blade
Cool block face and recut

## Slide 165
Bubbles under the section
Bubbles adhering to base and sides of floatation bath
Poor flotation technique trapping bubbles under section

## Slide 166
Over-expansion
during flotation
Temperature of bath too high
Section left for too long on water
Poor fixation and/or processing
(residual solvent)

## Slide 167
Section not flat
(poor adherence)
• Poor quality section (wrinkles, bubbles)
• Flotation bath too cold
• Use of an uncoated slide
• Section not drained thoroughly after flotation
• Insufficient drying time
• Drying temperature too low

## Slide 168
Dust present
Dirty slide
Floatation bath not skimmed or contaminated
Slides drained, dried or stored in a dusty environment
Fragments of pencil lead from labeling

## Slide 169
Knife is blunt
Tilt of knife is too great
Sections curl or roll up

## Slide 170
CAUSES :
Block edges are not parallel to each other
Block edges not parallel to the knife
Dull blade edge
Excessive paraffin
Tissue varying in consistency
Ribbons of section curved
PROBLEMS AND SOLUTIONS

## Slide 171
SOLUTION –
Trim block until parallel
Replace blade or move to a different area
Trim away excess paraffin
Re-orient block

## Slide 172: Thick and thin sections
CAUSES
Paraffin too soft for tissue or conditions
Insufficient clearance angle
Faulty microtome mechanisms

## Slide 173
SOLUTION –
Cool block with ice or re-embed in higher melting point wax
Increase clearance angle
Maintain microtome – Lubricate and calibrate.
Tighten block and blade

## Slide 174: Splitting of sections at right angle to knife edge
CAUSES –
Nicks in blade
Hard particles in tissue
Hard particles in paraffin

## Slide 175
SOLUTION –
Use different part of blade or replace
If calcium deposit, surface decal
If mineral or other particle, remove with fine sharp pointed scalpel.

## Slide 176: Sections do not form ribbons
CAUSES –
Paraffin too hard for sectioning conditions
Debris on knife edge
Incorrect clearance angle

## Slide 177
SOLUTION –
Re-embed in lower melting point paraffin
Clean with xylene moist cloth
Adjust clearance angle to optimal

## Slide 178: Sections attach to block on return stroke
CAUSES –
Insufficient clearance angle
Debris on blade edge
Debris on block edge
Static electricity on ribbon

## Slide 179
SOLUTION –
Increase clearance angle
Clean with xylene moist cloth
Trim edges of block
Humidify the air around the microtome, place static guard or dryer sheets near microtome

## Slide 180: Incomplete section
CAUSES –
Incomplete impregnation of the tissue with paraffin
Tissue incorrectly embedded
Sections superficially cut

## Slide 181
SOLUTION –
Re-process tissue block
Re-embed tissue, make sure orientation is correct and tissue is flat in mould
Re-face block, cut deeper into the tissue

## Slide 182: Sections expand or disintegrate in water bath
CAUSES –
Poor impregnation of tissue
Water temperature too high in flotation bath

## Slide 183
SOLUTION –
Reprocess tissue
Turn down the temperature of the flotation bath

## Slide 184: Sections roll into a coil instead of remaining flat on the knife edge
CAUSES –
Blade dull
Rake angle too small
Section too thick

## Slide 185
SOLUTION –
Use a new blade
Reduce blade tilt if clearance angle is excessive
Reduce section thickness

## Slide 186: THANK YOU