## Slide 1: Application of Computer
lecture # 06

## Slide 2: Topics
Ring Topology
Mesh Topology
Hybrid Topology

## Slide 3: Ring Topology
In ring topology each device is connected with the two devices on either side of it. There are two dedicated point to point links a device has with the devices on the either side of it. This structure forms a ring thus it is known as ring topology. If a device wants to send data to another device then it sends the data in one direction, each device in ring topology has a repeater, if the received data is intended for other device then repeater forwards this data until the intended device receives it.

## Slide 4: Ring Topology

## Slide 5: Hybrid Topology
A combination of two or more topology is known as hybrid topology. For example a combination of star and mesh topology is known as hybrid topology.
Advantages of Hybrid topology
1. We can choose the topology based on the requirement for example, scalability is our concern then we can use star topology instead of bus technology. 2. Scalable as we can further connect other computer networks with the existing networks with different topologies.

## Slide 6: Disadvantages of Hybrid topology
Disadvantages of Hybrid topology
1. Fault detection is difficult. 2. Installation is difficult. 3. Design is complex so maintenance is high thus expensive.

## Slide 7: Hybrid Topology

## Slide 8: Mesh Topology
Mesh Topology In mesh topology each device is connected to every other device on the network through a dedicated point-to-point link. When we say dedicated it means that the link only carries data for the two connected devices only. Lets say we have n devices in the network then each device must be connected with (n-1) devices of the network. Number of links in a mesh topology of n devices would be n(n-1)/2.

## Slide 9: Mesh Topology
Advantages of Mesh topology
1. No data traffic issues as there is a dedicated link between two devices which means the link is only available for those two devices. 2. Mesh topology is reliable and robust as failure of one link doesn’t affect other links and the communication between other devices on the network. 3. Mesh topology is secure because there is a point to point link thus unauthorized access is not possible. 4. Fault detection is easy.

## Slide 10: Mesh Topology