## Slide 1: Communication Medias And Topologies

## Slide 2: Communication Medias

## Slide 3: Classification of Medias

## Slide 4: Guided Media
Ethernet
  Ethernet is a way of connecting devices so that they can communicate with each other.
  Ethernet is most commonly used for LANs.
  Ethernet is also used in Wireless LANs.
  Normally Ethernet devices are not far from each other.
  Devices in Ethernet are connected over few meters, however new advancements have increased the range of communication of devices in an Ethernet Network.
  A medium is required for communication between devices

## Slide 5: Ethernet Terminologies
Segment
  Single shared medium is called segment.
  Multiple computers can be on the same segment.
Nodes
  Computers or devices attached to the segments are called Nodes
  Sometimes they are also called Stations.

## Slide 6: Ethernet Terminologies
Frame
  Nodes communicate in the form of short messages called Frames
  Frames have some rule
    Max. Min. length
    Source Destination addresses
    No two nodes on the segment can have same addresses

## Slide 7: Guided Media
It is a combination of two twisted copper wires.
Wires can cause interference with each other called Crosstalk.
To reduce crosstalk and outside interference, the cables are twisted with each other.
A twisted pair cable consists of two or more twister pairs in a common jacket.
Twister Pair Cable

## Slide 8: Twisted Pair Cable
It consists of twisted pairs with simple plastic casing
Commonly used for telephone systems.
Not very costly
Installation is easy just like telephone.
Bandwidth of around 100mbps
Nodes depend upon the limit of Hub etc.
EMI (Electromagnetic Interference)
  Susceptible to eaves dropping.
  Can be interfered by EM waves.
Unshielded Twisted Pair Cable
RJ-45
RJ-11

## Slide 9: Twisted Pair Cable
RJ-45 is used for 4 pair cables.
RJ-11 is used for 2 pair cables.
Categories are
  Category 1, 2 for voice communication
  Category 3, 4 and 5 for computer networks
  Category 6 are also available.
Unshielded Twisted Pair Cable

## Slide 10: Twisted Pair Cable
It consists of a shield of aluminum between wires and cover.
Cover normally protects from signal loss.
It prevents any signal from going out or coming in, so it has less interference.
Shielded Twisted Pair Cable

## Slide 11: Twisted Pair Cable
Expensive than UTP
A little difficult to install
Bandwidth of around 500mbps
Nodes depend upon the limit of Hub etc.
EMI
  Not interfered by any EMI
Shielded Twisted Pair Cable

## Slide 12: Coaxial Cable
Cable normally used by cable operator for TV channels
Less expensive than UTP and STP.
Installation is easy
Bandwidth of around 10mbps
Around 30 nodes.
EMI
  Not interfered by any EMI

## Slide 13: Coaxial Cable

## Slide 14: Fiber Optics
Optical fiber consists of thin glass fibers or plastic that can carry information at frequencies in the visible light spectrum and beyond. The typical optical fiber consists of a very narrow strand of glass called the core. Around the core is a concentric layer of glass called the cladding?
An optical transmission system has three basic components
(a) Light source
(b) Transmission medium (fiber optics)
(c) Detector

## Slide 15: Fiber Optics
Light source:
In such a system a pulse of light indicates bit 1 and the absence of light indicates bit 0. Light source can be an LED or a laser beam.
Transmission medium:
Transmission medium is the ultra-thin fiber of glass.
Detector:
A detector generates an electrical pulse when the light falls on it,

## Slide 16: Fiber Optics
Expensive
Difficult to install
Bandwidth of around 2gbps.
Nodes depends upon Hub.
EMI
  No EMI

## Slide 17: 10Mbps Ethernet
Different cables are available.
They use different signaling characteristics.
They share same Ethernet specs.
  10Mbps
  CSMA/CD
Some cables are
  10 Base 5
  10 Base 2
  10 Base T
  10 Base FL

## Slide 18: 10Mbps Ethernet
It is also called thicknet.
5 in base stands for maximum length, that is 500m
10 stands for 10Mbps
Coaxial cable is marked every 2.5m for connection points
  It means minimum length to connect a computer should not be less than 2.5m
  Since shorter distance degrades the signals
  Damaged Coaxial Cable is dangerous
Drilling is required to make a small hole into the cable.
10 Base 5

## Slide 19: 10Mbps Ethernet
Advantages
  Length can be increased using repeaters.
Disadvantages
  Large size
  High Cost
  Drilling is dangerous
  Difficult to use

## Slide 20: 10Mbps Ethernet
It is also called Thinnet Coax.
It is like coaxial cable for TV.
It is inexpensive.
Easy to handle.
A terminator must be used at each end.
One end of the cable must be grounded.
10 Base 2

## Slide 21: 10Mbps Ethernet
Advantages
  Length can be increased using repeaters.
  Less expensive
  Easy to use
Disadvantages
  High cost as compared to UTP
10 Base 2

## Slide 22: 10Mbps Ethernet
It is also called Twisted-Pair Ethernet
Used for only Unshielded Twisted Pair cable (UTP)
This specification does not support STP.
It is wired as star which means each device is connected to Hub with its own wires.
Normally used for connecting more than 1 device.
10 Base T

## Slide 23: 10Mbps Ethernet
FL in 10 Base FL means “Fiber Link”.
It uses Light to transmit data instead of Electricity.
It supports transmission over two fiber optics cables.
It uses a Hub or concentrator to receive the light signals.
Segment length is normally up to 2000m.
Normally used for connecting between buildings.
10 Base FL

## Slide 24: 100Mbps Ethernet
It is also sometimes referred as 100 Base T.
It is also called Fast Ethernet.
It is the most common type of network architecture within Ethernet.
It runs over cat 5 cable.
100 Base TX

## Slide 25: 100Mbps Ethernet
100 Base TX

## Slide 26: 1000Mbps Ethernet
It is also called Gigabit Ethernet.
It runs over cat 5 cable.
Currently in use at Corporate Sectors.
Since it runs on cat 5 cabling, so upgrade from 100 Mbps is not that difficult.
1000 Base TX

## Slide 27: Unguided Media
Wireless transmission is a form of unguided media. Wireless communication involves no physical link established between two or more devices, communicating wirelessly. Wireless signals are spread over in the air and are received and interpreted by appropriate antennas.
When an antenna is attached to electrical circuit of a computer or wireless device, it converts the digital data into wireless signals and spread all over within its frequency range. The receptor on the other end receives these signals and converts them back to digital data.

## Slide 28: Radio Transmission
Radio frequency is easier to generate and because of its large wavelength it can penetrate through walls and structures alike.
Frequency ranging from 3 KHz (Extremely Low Frequency) to 300 GHz
Radio waves are omnidirectional. When an antenna transmits radio waves, they are propagated in all directions. This means that the sending and receiving antennas do not have to be aligned. A sending antenna send waves that can be received by any receiving antenna.
AM and FM radio, television, maritime radio, cordless phones, and paging are examples of multicasting.

## Slide 29: Infrared Waves
Infrared waves, with frequencies from 300 GHz to 400 THz, can be used for short-range communication. Infrared waves, having high frequencies, cannot penetrate walls.
Infrared travels in a straight line hence it is directional by nature.
This same characteristic makes infrared signals useless for long-range communication.
it is for communication between devices such as keyboards, mouse, PCs and printers, television and it’s remote. .

## Slide 30: Micro Waves
Electromagnetic waves having frequencies between 1 and 300 GHz are called micro waves. Micro waves are unidirectional. When an antenna transmits microwaves, they can be narrowly focused. This means that the sending and receiving antennas need to be aligned.
Microwave propagation is line-of-sight. Since the towers with the mounted antennas need to be in direct sight of each other, towers that are far apart need to be very tall.
Very high-frequency microwaves cannot penetrate walls.
It is very costly
It is used in satellite networks

## Slide 31: Network Topology

## Slide 32: Network Topology
Topology
Layout of a network and how different nodes in a network are connected to each other and how they communicate.
Types of Topologies
Physical topology:
defines how the nodes of the network are physically connected
Logical topology:
How data is transmitted between nodes

## Slide 33: Types of Topologies
Bus
Ring
Star
Mesh
Tree
Hybrid

## Slide 34: Bus Topology
In this topology every workstation is connected to a main cable called the bus.
Single cable connects all network nodes without intervening
connectivity devices
• Devices share responsibility for getting data from one point to
another
Terminators stop signals after reaching end of wire
  Prevent signal bounce

## Slide 35: Bus Topology
When a device sends a message, it is broadcast down on the cable in both directions. Terminators at the end of the cable prevent the signal from reflecting back to the sender.
All devices on the cable constantly monitor for messages meant to them. When a device detects a message meant for it, it reads the message from the cable and the other devices will ignore it.

## Slide 36: Bus Topology
ADVANTAGES
Works well for small networks
Relatively inexpensive to implement
Easy to add to it
DISADVANTAGES
Difficult reconfiguration and fault isolation.
If any fault in backbone can stops all transmission.

## Slide 37: Ring Topology
In this topology, the workstations are connected in a closed loop
configuration. Adjacent pairs of workstations are directly connected.
Each node is connected to the two nearest nodes so the entire
network forms a circle
One method for passing data on ring networks is token passing
A message sent out from one node is passed along to each node in between until the target node receives the message.

## Slide 38: Ring Topology
Advantages:
1. Easy to install.
2. Easy to reconfigure.
Disadvantages:
1. Unidirectional traffic.
2. Break in a single ring can break entire network.
3. Fault identification is not easy.

## Slide 39: Star Topology
Here each device has a dedicated point-to-point link to the central controller called “Hub”(Act as an Exchange).
There is no direct traffic between devices.
The transmission are occurred only through the central “hub”.

## Slide 40: Star Topology
Advantages
Good option for modern networks
Easy to manage
Offers opportunities for expansion
Easy troubleshooting
Disadvantages
Hub is a single point of failure
• Requires more cable than the bus

## Slide 41: Mesh Topology
a network topology in which there is a direct link between all pairs of nodes.
Networks designed with this topology are usually very expensive to set up,
It provide a high degree of reliability due to the multiple paths for data that are provided by the large number of redundant links between nodes.
Total number of links can be calculated by n(n-1)/2

## Slide 42: Mesh Topology
Advantages
They use dedicated links so each link can only
carry its own data load. So traffic problem can be
avoided.
It is robust. If any one link get damaged it cannot
affect others.
It gives privacy and security.(Message travels along a dedicated link)
Fault identification and fault isolation are easy.

## Slide 43: Mesh Topology
Disadvantages
The amount of cabling and the number of I/O ports
required are very large. Since every device is connected
to each devices through dedicated links.
Hardware required to connected each device is highly expensive.

## Slide 44: Tree Topology
Alternatively referred to as a star bus topology.
Tree topology is one of the most common network setups that is similar to a bus topology and a star topology.
A tree topology connects multiple star networks to other star networks.
number of Star networks are connected using Bus.
This main cable seems like a main stem of a tree, and other star networks as the branches.

## Slide 45: Tree Topology
Advantages
Expansion of Network is possible and easy.
Divide the whole network into segments (star networks), which can be easily managed and maintained.
Error detection and correction is easy.
Each segment is provided with dedicated point-to-point wiring to
the central hub.
If one segment is damaged, other segments are not affected.

## Slide 46: Tree Topology
Disadvantages
Because of its basic structure, tree topology, relies heavily on the main bus cable, if it breaks whole network is crippled.
As more and more nodes and segments are added, the maintenance becomes difficult.

## Slide 47: Hybrid Topology
Hybrid networks use a combination of any two or more topologies, in such a way that the resulting network does not exhibit one of the standard topologies
hybrid topology is always produced when two different basic network topologies are connected. Two common examples for Hybrid network are: star ring network and star bus network

## Slide 48: Hybrid Topology
Advantages
Reliable: Unlike other networks, fault detection and troubleshooting
is easy in this type of topology. The part in which fault is detected can
be isolated from the rest of network and required corrective measures can be taken, WITHOUT affecting the functioning of rest of the network.
Scalable: Its easy to increase the size of network by adding new
components, without disturbing existing architecture.
Effective: Hybrid topology is the combination of two or more topologies, so we can design it in such a way that strengths of constituent topologies are maximized while there weaknesses are neutralized.

## Slide 49: Hybrid Topology
Disadvantages
Complexity of Design: One of the biggest drawback of hybrid topology is its design. Its not easy to design this type of architecture and its a tough job for designers. Configuration and installation process needs to be very efficient.
Costly Hub: The hubs used to connect two distinct networks, are very expensive. These hubs are different from usual hubs as they need to be intelligent enough to work with different architectures and should be function even if a part of network is down.
Costly Infrastructure: As hybrid architectures are usually larger in scale, they require a lot of cables, cooling systems, sophisticate network devices, etc.