## Slide 2: OSI Model
An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model.
It was first introduced in the late 1970s.
OSI is a set of protocols that allows any two systems to communicate regardless of their architecture
The OSI is not a protocol but it is a model for understanding and designing of flexible and robust network.

## Slide 4: Physical Layer / Layer 1
Physical layer is responsible for carrying bit stream over physical medium.
Functions of Physical Layer:
Bit representation – encodes the stream of bits into electrical or optical signals and also defines how bits are encoded into signals
Transmission rate – The number of bits sent each second
Physical characteristics of transmission media such as type of medium
Synchronization of bits: the sender and receiver clocks must be synchronized at the bit level

## Slide 5: Physical Layer / Layer 1
Transmission mode – physical layer defines the mode of transmission i.e. simplex, half-duplex, full duplex
Physical Topology – physical layer defines how devices are connected – ring, star, mesh, bus topology
Line Configuration – physical layer is concerned with the connection of devices to media which can be either point to point or multipoint.

## Slide 6: Data Link Layer/ Layer 2
It transforms raw bits into reliable link and make it appear error free to network layer.
Main functions of this layer are:
Framing – divides the stream of bits received from network layer into manageable data units called frames.
Physical Addressing – Add a header to the frame to define the physical address of the source and the destination machines.
Flow control – Impose a flow control –control rate at which data is transmitted so as not to flood the receiver reducing or increasing data flow

## Slide 7: Data Link Layer/ Layer 2
Error Control – Adds mechanisms to detect and retransmit damaged or lost frames. This is achieved by adding a trailer to the end of a frame
Access Control – checks whether the node has authority to access the requested data or not

## Slide 8: Network Layer / Layer 3
Main functions of this layer are:
Logical Addressing– when the packet has to cross the boundary of network logical addressing is required. For this purpose network layer adds a header to packets containing IP address of the sender and receiver.
Routing – Provide mechanisms to transmit data over independent
networks that are linked together.by providing the best path for transmission

## Slide 9: Transport Layer / Layer 4
Main functions of this layer are:
Responsible for source-to destination delivery of the entire message
Segmentation and reassembly –divide message into smaller segments, number them and transmit. Reassemble these messages at the receiving end.
Error control – make sure that the entire message arrives without
errors – else retransmit.

## Slide 10: Transport Layer / Layer 4
Connection Control – transport layer can be either connection oriented or connection less
  Connection oriented – connection oriented makes the connection with the transport layer first before sending the data packets.
  Connectionless – it treats the segment as independent packet and send it to destination machine.

## Slide 11: Session Layer/Layer 5
Session Layer is the network dialog controller. It establishes and maintains interaction among computers.
Dialog control – it creates a session and allows two systems to enter into a dialog with each other.
Synchronization – adds check points into stream of data.

## Slide 12: Presentation Layer/ Layer 6
Translation – it converts the data into a stream of bits before sending so that the destination computer can understand.
Compression – reduce number of bits to be transmitted. This makes the transmission efficient
Encryption – transform the original data into another format at the sending end for data security
Decryption – reverses the encryption process and converts it back into original data.

## Slide 13: Application Layer/Layer 7
Contains protocols that allow the users to access the network (FTP,
HTTP, SMTP, etc)
Does not include application programs such as email, browsers, word processing applications, etc.
Protocols contain utilities and network-based services that support email via SMTP, Internet access via HTTP, file transfer via FTP, etc

## Slide 14: OSI Layers with Protocols