## Slide 1: TCP/IP MODEL

## Slide 2: Computing Components
The TCP/IP protocol suite was developed prior to the OSI model. Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model.
The original TCP/IP protocol suite was defined as four software layersbuilt upon the hardware. Today, however, TCP/IP is thought of as a five-layer model with the layers named similarly to . the ones in the OSI model

## Slide 3: layers of tcp/ip model
Chart: 

## Slide 4: Application layer
The application layer in TCP/IP is equivalent to the combined session, presentation, and application layers in the OSI model
Application layer defines TCP/IP application protocols
How host programs interface with Transport layer services to use the network.
The application layer allows a user to access the services of our private internet or the global Internet
  electronic mail, file transfer, accessing the World Wide Web, etc.

## Slide 5: Application layer
It is include high level protocol that are used for wide verity application like:
TELNET(Terminal Network) : used for remote login.
FTP(File Transfer Protocol) : used for transfer of file from one system to another.
HTTP(Hyper Text Transfer Protocol)|: for fetching web pages

## Slide 6: Transport Layer
The purpose of Transport layer is to permit devices on the source and destination hosts to carry on a conversation.
The transport layer is responsible for delivering the whole message, which is called a segment from A to B
The transport layer was represented in the TCP/IP suite by two protocols:
  User Datagram Protocol (UDP)
  Transmission Control Protocol (TCP).

## Slide 7: Internet Layer
At the network layer (or, more accurately, the internetwork layer), TCP/IP supports the Internet Protocol (IP)
Internet layer pack data into data packets known as IP datagrams, which contain source and destination address (logical address or IP address)
The Internet layer is also responsible for routing of IP datagrams.

## Slide 8: Internet Layer
IP (Internet Protocol)
ICMP (Internet Control Message Protocol)
ARP (Address Resolution Protocol)
RARP (Reverse Address Resolution Protocol)
IGMP (Internet Group Management Protocol)

## Slide 9: Network Access Layer
Network Access Layer defines details of how data is physically sent through the network, including how bits are electrically or optically signaled by hardware devices that interface directly with a network medium, such as coaxial cable, optical fiber, or twisted pair copper wire.
CSMA/CD (Carrier Sense Multiple Access/Collision Detection)

## Slide 10: TCP
Transmission Control Protocol is considered as a reliable protocol.
Transmission Control Protocol (TCP) is responsible for breaking up the message (Data from application layer) into TCP Segments and reassembling them at the receiving side.

## Slide 11: HTTP
Hypertext Transfer Protocol (HTTP) is the protocol that enables the connection between a web server and a client. Hypertext Transfer Protocol (HTTP) is an application layer protocol for distributing information in the World Wide Web (WWW). Hypertext Transfer Protocol (HTTP) is based on the client–server architecture.

## Slide 12: IP
The Internet Protocol (IP) is the principal communications protocol in the Internet protocol suite for relaying data packets across network boundaries. Its routing function enables internetworking, and essentially establishes the Internet.

## Slide 13: CSMA/CD
Carrier-sense multiple access with collision detection (CSMA/CD) is a media access control method used most notably in early Ethernet technology for local area networking.
It uses a carrier-sensing scheme in which a transmitting station detects
collisions by sensing transmissions from other stations while transmitting a frame.

## Slide 14: Addrressssiing

## Slide 15: Physical address
The physical address, also known as the MAC address
It is included in the frame used by the data link layer.
It is the lowest-level address.
It is a 6-byte hexadecimal (48-bit) physical address.

## Slide 16: Logical Address
Logical addresses are necessary for universal communications that are independent of underlying physical networks
Physical addresses are not adequate in an internetwork environment where different networks can have different address formats
A universal addressing system is needed in which each host can be identified uniquely.

## Slide 17: Logical Address
A logical address in the Internet is currently a 32-bit address (IPv4) and a
128-bit address (IPv6), that can uniquely define a host connected to the Internet
No two publicly addressed and visible hosts on the Internet can have the same IP address

## Slide 18: Port Addresses
Computers are devices that can run multiple processes at the same time
The end objective of Internet communication is a process communicating with another process
For example, computer A can communicate with computer C by using TELNET, at the same time, computer A communicates with computer B by using the File Transfer Protocol (FTP)
In the TCP/IP architecture, the label assigned to a
process is called a port address A port address in TCP/IP is 16 bits in length (represented by one decimal number)

## Slide 19: Application-Specific Addresses
User-friendly addresses that are designed for specific application
Examples include the e-mail address (for example, tutun@stei.itb.ac.id) and the Universal Resource Locator (URL) (for example, www.itb.ac.id)