## Slide 1: High Voltage Engineering
EE.423
Dr. Rabia Shakoor

## Slide 2: Course outline
Introduction to HV technology, advantages of transmitting electrical power at high voltages, need for generating high voltages in laboratory. Important applications of high voltage.
Breakdown mechanism of gaseous , liquid ad solid materials
Mechanism of lightning
Shielding of overhead ground wires
Effect of lightning on a transmission line

## Slide 3: Introduction to HV technology
A high-voltage, direct current (HV) electric power transmission system uses direct current for the bulk transmission of electrical power, in contrast with the more common alternating current systems.
For long-distance distribution, HV systems are less expensive and suffer lower electrical losses. For shorter distances, the higher cost of DC conversion equipment compared to an AC system may be acceptable where other benefits of direct current links are useful.

## Slide 4: Advantages of high voltages
1) Reduces volume of conductor material:
Power in Three Phase Circuits P = √3 V I Cosθ
OR I = P / √3 V Cos θ (1)
Law’s of resistance = R = ρ (l /A) (2)
Power Loss in Three Phase Circuits = P = 3 I2R (3)
Putting the Values of I and R from Equation (1) and (2) into Equation (3).
P = 3 (P / √3 V Cos θ)2 x [ρ (l/A)]
P = 3 (P2/3 V2 Cos2 θ) x ρ (l /A)
P = W = P2 ρ l / V Cos2 θ A… OR … A = P2 ρ l / V2 Cos2θ W (4)
Volume of the conductor = Vol = 3A x Length (5)
Putting the value of “A” from Equation (4) into Equation (5)
Vol = 3 P2 ρ l / W V2 Cos2θ

## Slide 5: Advantages of high voltages
Increases Transmission efficiency:
Input power = P + total losses = P + P2 L / ( V2Cos2Ф A)
Let J be the current density, therefore A = I/ J Then input power = P + P2 L J / (V2Cos2Ф) * 1/I
Transmission efficiency = Output Power / Input Power = P / (P [ 1+√3 J L/ V cosФ])
Since J, ,L are constants, therefore transmissions efficiency increases when line voltage is increased.

## Slide 6: Advantages of high voltages
Decrease percentage line drop:
Line drop = IR = I * L / a = I * L * J/I = L J
% line drop = J L / V * 100
As J, and L are constants, therefore percentage line drop decreases when the transmission voltage increases.

## Slide 7: Advantages of high voltages
Undersea cables, where high capacitance causes additional AC losses.
Increasing the capacity of an existing power grid in situations where additional wires are difficult or expensive to install.
Power transmission and stabilization between unsynchronized AC distribution systems
Connecting a remote generating plant to the distribution grid.
Stabilizing a predominantly AC power-grid, without increasing prospective short circuit current .
Reducing line cost. HV needs fewer conductors as there is no need to support multiple phases. Also, thinner conductors can be used since HV does not suffer from the skin effect .
Facilitate power transmission between different countries that use AC at differing voltages and/or frequencies.

## Slide 8: Disadvantages of High voltage
HV is less reliable and has lower availability than AC systems, mainly due to the extra conversion equipment. Single pole systems have availability of about 98.5%, with about a third of the downtime unscheduled due to faults. Fault redundant bipole systems provide high availability for 50% of the link capacity, but availability of the full capacity is about 97% to 98%.
The required static inverters are expensive and have limited overload capacity.
In contrast to AC systems, realizing multi-terminal systems is complex, as is expanding existing schemes to multi-terminal systems.

## Slide 9: Disadvantages of High voltage
High voltage DC circuit breakers are difficult to build because some mechanism must be included in the circuit breaker to force current to zero, otherwise arcing and contact wear would be too great to allow reliable switching.
Operating a HV scheme requires many spare parts to be kept, often exclusively for one system as HV systems are less standardized than AC systems and technology changes faster.

## Slide 10: Applications of High Voltages:
High voltages are applied in laboratories in nuclear research, in particle accelerators and Van de Graff generators.
Voltages up to 100KV are used in electrostatic precipitators.
X-Ray equipment for medical and industrial application also uses high voltages.

## Slide 11: Energy sources and energy conversion
Apart from the direct conversion of solar energy to electricity due to the photo-voltaic effect, all the electricity in the world is generated, using Faraday’s Law. Water steam or wind energy causes rotation of the turbine and generator rotor.

## Slide 12: Generators
The rating of a typical large generator is between 500 to 900 MVA and the generator voltage is typically 24 kV. This results in a large full load current of the order of 10 to 20 kA.

## Slide 13: substations
The substations are the nodes in the power system where several lines and transformers are connected together.
Transmission substations serve as the interconnection nodes on the main transmission system. At these stations the voltage is raised to the levels of the transmission system and stepped down again to lower distribution levels when appropriate. Typically, distribution stations operate at voltages of 132 kV and below to distribute the power to the points of consumption. A typical distribution substation is shown in Fig

## Slide 14: Power lines and cables
High voltage feeders in the form of overhead power lines or underground cables interconnect high voltage substations. Typical high voltage overhead power lines are shown in Fig

## Slide 15: Bushings
It is sometimes required to take a high voltage conductor through a wall or the tank of a transformer. In such cases a bushing is required to support the high voltage conductor and to provide the necessary insulation in the axial and the radial directions.
The voltage gradient is also high close to the high voltage conductor and this could cause discharges in those regions. The use of conducting cylinders inside the bushing results in a more uniform voltage distribution as is shown in Fig.

## Slide 16: Bushings

## Slide 17: Power transformers
The power transformers transform the voltage from one level to another and must be able to handle the full power to be transformed, i.e. the copper windings must be rated to handle the full load current and short time over currents.
A transformer is equipped with a conservator to serve as an expansion tank to allow for the expansion of the oil when the transformer temperature increases.

## Slide 18: Power transformers

## Slide 19: Circuit breakers and fuses
The duty of circuit breakers and fuses is to rapidly interrupt fault current. When a short circuit occurs on the power system, currents of the order of tens of thousands of Ampere flow.
The presence of these power frequency fault currents are detected by the protection relays and the output contacts of the relays energize the circuit breaker trip coils.

## Slide 20: Surge arresters or lightning arresters
The power system is subject to transient overvoltages due to lightning and switching. Lightning arresters (also called surge diverters) are applied to limit the peak voltages to values that can not damage the equipment to limit overvoltage .
These overvoltages are limited by the use of nonlinear resistive elements. In conventional lightning arrestors silicon carbide elements are used.

## Slide 21: Conclusion
In this introduction the state of the art of high voltage power systems has been summarised. High voltage technology is of paramount importance to facilitate the transmission and utilisation of large amounts of electrical energy. Knowledge of the performance of the various types of electrical insulation systems depend on the magnitude of the electric fields in the materials. In the next lecture concepts relating to electric fields and their calculation will discuss.