## Slide 1: High Voltage Engineering
EE :423
Dr. Rabia shakoor

## Slide 2: Outline
Fields
Electric field
Magnetic field
Electrostatic Fields
Uniform fields
Non-uniform fields
Maximum field strengths for various arrangements
Electric field strength of three phase lines

## Slide 3: Fields
A field is formally described as a spatial distribution of a quantity, which may or may not be a function of time.
A typical example of such action-at-a- distance is gravitation: the fact that masses attract each other and that objects fall to earth.
Electric fields are caused by the voltage difference between electrodes while magnetic fields are caused by currents flowing in conductors.

## Slide 4: Electric fields
Electric fields are important in high voltage engineering due to the following effects:
- The performance of electric insulating materials is adversely affected by excessive electric field magnitudes. This is true for gaseous, liquid and solid insulating materials.
- The presence of electric fields causes induced voltages on non-earthed objects under high voltage conductors.
-Similarly, the charge at the base of a thundercloud causes an electric field near the earth surface that may induce charge on objects such as transmission lines. Under dynamic conditions, when the charges vary with time, currents flow in conducting objects.

## Slide 5: Magnetic fields
Magnetic fields do not have a direct effect on the properties of insulating materials but they affect the power system indirectly in the following way: - High AC currents cause time-varying magnetic fields that induce voltages in conducting loops. Similarly, high time-varying currents due to lightning may cause induced voltages. These overvoltages cause high electric fields in power system components that may cause failure of the insulation systems.
-A time-varying electric field is accompanied by a magnetic field and vice versa, forming an electromagnetic field. This interaction prevails at higher frequencies and can be used to explain the propagation of travelling waves along transmission lines. These travelling waves are of importance in high voltage engineering as overvoltage surges, caused by lightning, are propagated along the lines.

## Slide 6: Electrostatic Fields
The space around energised high voltage components is occupied by an electric field. The field has the same frequency as the voltage. The magnitude of these fields influences the behaviour of the insulation. It is therefore important to be able to estimate the electric field strength. The following sections discuss the methods available to analyse uniform and non-uniform fields.

## Slide 7: Uniform fields
If a voltage difference exist between two parallel plate electrodes of large dimensions, and the edge effects of the plates are ignored, the electrostatic field between the plates is uniform, as is shown in Figure

## Slide 8: Uniform fields
If 100 kV is connected between the plates, equipotential lines can be drawn as shown. If the distance between the plates is 10 cm, the electric field strength (intensity or gradient) is:
E = 100 kV / 10 cm = 10 kV/cm In general, the electric field strength is given by:
E =V/d
V=voltage between plates
D=distance between the plates.

## Slide 9: Uniform fields
If the edge effects are not ignored, the field strength will be higher at the sharp edges of the electrodes than in the central region, as shown in Fig. 2.2. The Rogowski "uniform field" gap is designed such that the field strength in the middle is E0 = V/d0, with d0 the minimum distance between the electrodes. Elsewhere the field strength is less than in the middle (E < E0). This is achieved by shaping the electrodes in such a way that they coincide with the equipotential lines obtained in Fig. 2.2, e.g. the 20% and 80% contours.

## Slide 10: Non-uniform fields
a) Concentric cylindrical and spherical arrangements
If the electrodes are curved, the field strength is not constant throughout the region. In Figure bellow a section through a concentric cylindrical configuration is shown

## Slide 11: Non-uniform fields
Note that the equipotential lines are much closer together near the inner conductor, resulting in higher field strength near the inner conductor. The field strength E is therefore not constant throughout the region and such a field is known as a non-uniform field.
V=voltage between the electrodes
b=outer radius a=inner radius, r=distance from center line
The maximum field strength occurs at the conductor surface, i.e. when r=a. The field strength of two concentric spheres, with a voltage V between them, can be derived by using Gauss's Law:
The maximum field strength occurs again at the surface, when r=a.

## Slide 12: Non-uniform fields
b) Cylinders and spheres: twin arrangements and conductors above a flat surface
Another practical arrangement that often occurs is that of a cylinder or a sphere with radius a at a height h above a flat conducting earthed plane as is shown in Fig.
In the case of such a cylinder above ground, the maximum field strength (at the conductor surface) is given by:

## Slide 13: Maximum field strengths for various arrangements

## Slide 14: The electric field strength of three phase lines
It is often necessary to know the electrical field strength under three phase lines or to know the maximum field strength at the surface of the conductors. In these cases the conductors are represented by line charges along their center lines. These line charges are obtained for the specific configurations by inverting the potential coefficient matrix. Once the line charges are available, the magnitudes of the field strength contributions of each line can be computed, using the following equation:
where r: distance between point where the field strength is required and the conductor q: line charge (C/m) ε0: absolute permittivity (F/m). These contributions are summed as vectors, bearing in mind the phase difference between the various phases.

## Slide 15: Capacitance formula
Although not directly associated with the maximum field strength, the following equations can be derived for various configurations: Two co-axial cylinders:

## Slide 16: Capacitance formula