## Slide 1: Cisco Switch & Router
Cisco switches and Routers
  Cisco switches and Routers uses 4 types of memories
  Flash
  NVRAM
  ROM
  RAM

## Slide 2: Cisco Switch & Router

## Slide 3: Cisco Switch & Router
Types of memories
ROM
  ROM ( Read only memory ) stores four components POST, Bootstrap program, ROMMON mode and Mini IOS
  POST ( Power on self-test ) is a low level diagnostic utility that performs various tests on hardware components. It verifies that all necessary components are present and operational

## Slide 4: Cisco Switch & Router
Bootstrap is the second utility in booting sequence. It controls the search and load process of IOS. Bootstrap program is responsible for bringing up the router, finding IOS on all possible locations and loading it in RAM
Mini-IOS is a fallback utility that contains a stripped down version of IOS. This is used in critical situations where IOS image in flash is not found. Mini-IOS contains only IP code that allows you to load IOS from other resources such as TFTP Server

## Slide 5: Cisco Switch & Router
Flash
  Flash is a nonvolatile memory. Data store in flash is not lost when you turn the router off
  You could assume flash as hard disk of router
  Router uses flash to store IOS image
  Flash memory stores fully functional Cisco IOS images and is the default location where the Router gets its Cisco IOS at boot time
NVRAM
  NVRAM is another permanent memory. Data stored in NVRAM is also remain safe
  Router & Switches use NVRAM to store configuration files in startup config file

## Slide 6: Cisco Switch & Router
RAM
  RAM is a temporary memory. Information stored in RAM does not remain in power off stage
  Everything in RAM is erased, when you turn off the router
  RAM is the fastest memory among these memories
    During the boot process IOS is copied and decompressed in RAM from Flash.
    Running configuration file is also copied in RAM from NVRAM
    RAM stores ARP, CDP neighbor, routing and other tables.
    Interface input and output buffers are also stored in RAM.

## Slide 7: Cisco Switch & Router
Boot Process
  When you first bring up a Cisco router or switch, it will run a power-on self test (POST), and if that passes, it will look for and load the Cisco IOS from Flash memory if a file is present
  Flash memory is an electronically erasable programmable read-only memory (EEPROM)
  If IOS not found in flash then locate IOS in TFTP server which is backup location on network where IOS backup image is stored

## Slide 8: Cisco Switch & Router
If not found TFTP server than go to ROM with help of bootstartp and load mini IOS which provide just working functionality of Router but not configurable
The IOS will load and then look for a valid configuration called startup-config that is stored by default in nonvolatile RAM (NVRAM)
If there is no configuration in NVRAM, then the router will bring up what is called setup mode

## Slide 9: Cisco Switch & Router

## Slide 10: Cisco Switch & Router
Setup Mode
  You actually have two options when using setup mode: Basic Management and Extended Setup
  Basic Management only gives you enough configurations to allow connectivity to the router, whereas Extended Setup allows you to configure some global parameters as well as interface configuration parameters

## Slide 11: Cisco Switch & Router
Cisco ISR (Integrated Service Router)
  ISR is that type of device has both functions of Router & Switch
  Support virtual application's
  Can run virtual machine inside the router
  Provide better security
  For accessing CLI mode to configure SWITCH or ROUTER; connect device to computer with console cable

## Slide 12: Cisco Switch & Router

## Slide 13: Cisco Switch & Router

## Slide 14: Cisco Switch & Router

## Slide 15: Cisco Switch & Router

## Slide 16: Cisco Switch & Router
Configuring the Terminal Emulator for the Console
  After the PC is physically connected to the console port, a terminal emulator software package must be installed and configured on the PC
  It accepts the text typed by the user and sends it over the console connection to the switch
  The emulator must be configured to use the PC’s serial port to match the settings on the switch’s console port settings

## Slide 17: Cisco Switch & Router
Emulator settings
  9600 bits/second
  No hardware flow control
  8-bit ASCII
  No parity bits
  stop bit

## Slide 18: Cisco Switch & Router

## Slide 19: Cisco Switch & Router
Initial configuration of ISR (Integrated Service Router)
  Would you like to enter the initial configuration dialog? [yes/no]: yes
  Would you like to enter basic management setup? [yes/no]: yes
  Enter host name [Router]: MCS
  Enter enable secret: meer
  Enter enable password: nicaas
  Enter virtual terminal password: test
  Configure SNMP Network Management? [no]: no
  Enter interface name used to connect to the management network from the above interface summary: Serial0/1/0

## Slide 20: Cisco Switch & Router
Configure IP on this interface? [yes]: yes
IP address for this interface: 200.200.200.200
Subnet mask for this interface [255.255.255.0] : 255.255.255.0
[0] Go to the IOS command prompt without saving this config.
[1] Return back to the setup without saving this config.
[2] Save this configuration to nvram and exit.
Enter your selection [2]: 2
MCS>enable
Password:
MCS#

## Slide 21: Cisco Switch & Router
Editing and Help Features
  By using a question mark (?) at any prompt, you can see the list of commands available from that prompt
  Router#?
  clear Reset functions
  clock Manage the system clock
  enable Turn on privileged commands

## Slide 22: Cisco Switch & Router
To find commands that start with a certain letter, use the letter and the question mark (?) with no space between them
Router#c?
Clear clock configure connect copy
To find the next command in a string, type the first command and then a question mark
Router#clock ?
set Set the time and date

## Slide 23: Cisco Switch & Router
By typing the command clock, then a space and a question mark, you will get a list of the next possible commands and what they do
Basic “show” commands
  Router#show history
  Use the command show history to see the last 10 commands entered on the router
  Router#show terminal
  To verify the terminal history size

## Slide 24: Cisco Switch & Router
Router#terminal history size ?
<0-256> Size of history buffer
Router#terminal history size 25
  Change the size of the history buffer
Basic Router Information
  The command show version will provide basic configuration for the system hardware as well as the software version, the names and sources of configuration files, and the boot images
  Router#show version

## Slide 25: Cisco Switch & Router
Router#show version
  Display information about router hardware and IOS software version
Router#show ip interface brief
  display all interfaces of router that router has like interface status in brief form (up or down), ip address (assigned or un-assigned)
Router# show interface fa 0/0
  Display information about specific interface in detail form like interface status, IP address with subnet mask, encapsulation, bandwidth etc

## Slide 26: Cisco Switch & Router
Setting the Passwords
  There are five passwords used to secure your Cisco routers
  The first two passwords are used to set your enable password (Enable Password and Enable Secret)
  This will prompt a user for a password when the command enable is used
  The other three are used to configure a password when user mode is accessed either through the console port, the auxiliary port, or Telnet

## Slide 27: Cisco Switch & Router
Enable Password & Enable Secrete
  Set the enable passwords & secret from global configuration mode
  Router(config)#enable password meer
  Router(config)#enable secret mazari
Password
  Is used to set the enable password on older versions (store in plain text form)
Secret
  Is the newer, encrypted password. Overrides the enable password (store in encrypted form)

## Slide 28: Cisco Switch & Router
Basic configuration of router
Configure router name (host name)
  Router(config)# hostname NICAAS (enter press)
  NICAAS(config)#
Configure Router as DHCP server
  Router(config)# ip dhcp pool test
  Router(config)# network 200.1.1.0 255.255.255.0
  Routerc(config)# default-router 200.1.1.100
note: black color is keyword of command & green color is using values

## Slide 29: Cisco Switch & Router
Configuring interface of Router
For configuring interface we go to specific interface
There are mostly two types of interfaces on router serial interface (using for serial link that provide connectivity with another router or with WAN ) & Fast Ethernet interface (used for LAN connectivity)
Ports Types with port number
  S0/0 (serial port with 0/0 number)
  S0/1
  Fa0/0 (Fast Ethernet port with 0/0 number)
  Fa0/1

## Slide 30: Cisco Switch & Router
Router(config)# interface s0/0
Router(config-if)# ip address 1.1.1.1 255.0.0.0
Router(config-if)# no shut
Router(config-if)# encapsulation ppp
Router(config-if)# clockrate 64000
Router(config-if)# speed 10
Configuring Default router & default route
Note: default router address is the address of default gateway and use IP address of LAN

## Slide 31: Cisco Switch & Router
Configuring Default route
Router(config)# ip default-network 0.0.0.0
Note:
Use the ip default-gateway command when ip routing is disabled on a Cisco router
Use the ip default-network command when ip routing is disabled on a Cisco router when we wants that our traffic use only this path