## Slide 1: GAS CHROMATOGRAPHY

## Slide 2: Introduction
Gas chromatography
It is a process of separating component(s)from the given sample by using a gaseous mobile phase.
It involves a sample being vaporized and injected onto the head of the chromatographic column.
The sample is transported through the column by the flow of inert, gaseous mobile phase.
The column itself contains a liquid stationary phase which is adsorbed onto the surface of an inert solid.

## Slide 3: Types of Gas Chromatography
Two major types
Gas-solid chromatography
(Stationary phase: solid)
Gas-liquid chromatography
(Stationary phase: immobilized liquid)

## Slide 4: Advantages of Gas Chromatography
The technique has strong separation power and even complex mixture can be resolved into constituents
The sensitivity of the method is quite high
It gives good precision and accuracy
The analysis is completed in a short time
The cost of instrument is relatively low and its life is generally long

## Slide 5: Components of Gas chromatography
Carrier gas
He (common), N2, H2, Argon
Sample injection port
Micro syringe
Columns
2-50 m coiled stainless steel/glass/Teflon
Detectors
Flame ionization (FID)
Thermal conductivity (TCD)
Nitrogen-phosphorus
Photo-ionization (PID)

## Slide 6: How a Gas Chromatography Machine Works
First: A vaporized sample is injected onto the chromatographic column.
Second: The sample moves through the column through the flow of inert gas.
Third: The components are recorded as a sequence of peaks as they leave the column

## Slide 7: Process Flow Schematic
Carrier gas (nitrogen or helium)
Sample injection
Long Column (30 m)
Detector (flame ionization detector or FID)
Hydrogen
Air

## Slide 8
Syringe
Injector
Detector
Carrier Gas Cylinder
Column
To Waste or Flow Meter
Flow Controller
Two-Stage Regulator

## Slide 9: Gas Chromatography Machine

## Slide 10: CHROMATOGRAPHIC ANALYSIS
The number of components in a sample is determined by the number of peaks.
The amount of a given component in a sample is determined by the area under the peaks.
The identity of components can be determined by the given retention times.

## Slide 11: Chromatogram of Gasoline
1. Isobutane 2. n-Butane 3. Isopentane 4. n-Pentane 5. 2,3-Dimethylbutane 6. 2-Methylpentane 7. 3-Methylpentane 8. n-Hexane 9. 2,4-Dimethylpentane 10. Benzene 11. 2-Methylhexane 12. 3-Methylhexane 13. 2,2,4-Trimethylpentane 14. n-Heptane 15. 2,5-Dimethylhexane 16. 2,4-Dimethylhexane 17. 2,3,4-Trimethylpentane 18. Toluene 19. 2,3-Dimethylhexane 20. Ethylbenzene 21. m-Xylene 22. p-Xylene 23. o-Xylene

## Slide 12: LIMITATION OF GC
Sample must be volatile
Dirty sample require clean up
Must use another instrument(eg.MS) for confirmation of identity
Some training /experience necessary
Hazards
Needles are sharp.
Detector coil is hot.
Carrier gas is flammable.