## Slide 1: UV-visual Spectrophotometer

## Slide 2: UV-visual Spectrophotometer:
Spectroscopy: It is the branch of science that deals with the study of interaction of matter with light.
Ultraviolet and visible(UV-Vis) absorption spectroscopy is the measurement of the attenuation of a beam of light after it passes through a sample or after reflection from a sample surface.
Absorption measurements can be at a single wavelength or over an extended spectral range.
UV–Vis absorption

## Slide 3: Principles of Spectroscopy
The principle is based on the measurement of spectrum of a sample containing atoms / molecules.
Spectrum is a graph of intensity of absorbed or emitted radiation by sample v/s frequency or wavelength.
Spectrometer is an instrument design to measure the spectrum of a compound.
The UV radiation region extends from 10 nm to 400 nm
The visible radiation region extends from 400 nm to 800 nm.
Near UV Region: 200 nm to 400 nm
Far UV Region: below 200 nm.
The common solvent used for preparing sample to be analyzed is either ethyl alcohol or hexane.

## Slide 4: History
In the 1930s, scientists found the phenomenon of absorpting of ultraviolet light on Vitamin A
The research finally lead out the commercial UV-Vis spectrophotometer in the early 1940s.
In 1941, Beckman Instruments Inc. launched the first commercial UV-visible spectrophotometer in the world, DU UV-Vis Spectrophotometer.
Although the modern UV-Vis spectrophotometer has been quite different then this historical one,
However, it measures the light flux difference before and after passing the sample, according to the amount of the light is absorbed by the liquid sample.

## Slide 5
Beckman Instruments Inc. launched the first spectrophotometer in the world.
UV-Vis spectrophotometer

## Slide 6: Schematic of UV- visible Spectrophotometer

## Slide 7: The Types of UV-Vis Spectrophotometer
UV / Vis spectrophotometer has two types,
Single-beam and dual-beam.
The single-beam UV-Vis spectrophotometer has only one cuvette
Therefore, the treatment group and the control group samples can one be measured one after the other.
With the double-beam UV-Vis spectrophotometer, you can measure the both groups simultaneously.
So, double beam UV-Vis spectrophotometer is more accurate, because you don’t need to recalibrate the instrument, before you measure the second sample.

## Slide 8: Single Beam
Composed by a single light source, a monochromator, a cuvette, and a detector. The simple structure brings the cheapest price.
Single Beam: Composed by a single light source, a monochromator, a cuvette, and a detector. The simple structure brings the cheapest price.

## Slide 9: Double Beam
There are two light sources, two cuvettes, and two detectors.
ACTTR Technology introduced UV1901 series
It has not only the excellent performance, but also the price is pretty economic.

## Slide 10: Applications
Qualitative & Quantitative Analysis: – It is used for characterizing aromatic compounds and conjugated olefins.
It can be used to find out molar concentration of the solute under study.
Detection of impurities: – It is one of the important method to detect impurities in organic solvents.
Detection of isomers are possible.
Determination of molecular weight using Beer’s law.