## Slide 1: Air Pollution

## Slide 2
Air is a mixture of various gases that envelops the earth to form the atmosphere.
Most of the atmosphere held close to earth because of pull of gravity.
Almost 99.99% of atmosphere mass remains within 80 Km of the earth’s surface.
The composition of air within 80 Km is remarkably constant.
Air and Atmosphere

## Slide 3: Atmosphere Composition
Atmospheric Composition (Major Constituents %)
  Nitrogen 78.08
  Oxygen 20.95
  Argon 0.93
  Carbon dioxide 0.04
Atmospheric Composition (Minor Constituents %)
  Neon 0.0018
  Helium 0.00052
  Methane 0.00015
  Hydrogen 0.0005
  Carbon monoxide 0.00001
  Ozone 0.000002

## Slide 4: Atmosphere as a Resource
Atmospheric ecosystem services
Atmosphere
  Provides O2 and CO2 (Medium of life)
  Blocks UV radiation
  Provides industrial and chemical raw material
  Moderates our climate
  Redistributes water (hydrologic cycle)

## Slide 5: What is the Nature of the Atmosphere?
The atmosphere is structured in layers, including the troposphere, which supports life, and the stratosphere, which contains the protective ozone layer.
Atmosphere varies in
  Density
  Atmospheric pressure
Thermosphere
Mesosphere
Ozone Maximum
Stratosphere
Troposphere
Temperature

## Slide 6: Air Movements in the Troposphere Play a Key Role in Earth’s Weather and Climate
Troposphere
  75–80% of the earth’s air mass
  Closet to the earth's surface
  Chemical composition of air
  Rising and falling air currents: weather and climate
  Involved in chemical cycling

## Slide 7: The Stratosphere is Our Global Sunscreen
Stratosphere
  Similar composition to the troposphere, with 2 exceptions
    Much less water
    O3, ozone layer, filters UV

## Slide 8: What is Air Pollution
When different Chemicals or substances added into the atmosphere by natural or human activities in high concentrations enough to be harmful for life on earth, it is Air Pollution.

## Slide 9
Indicates whether pollutant levels in air may cause health concerns or not.
Ranges from 0 (least concern) to 500 (greatest concern)
AQI: Air Quality Index

## Slide 10
Air Quality | Air Quality Index | Protect Your Health
Good | 0-50 | No health impacts are expected when air quality is in this range.
Moderate | 51-100 | Unusually sensitive people should consider limiting prolonged outdoor exertion.
Unhealthy for Sensitive Groups | 101-150 | Active children and adults, and people with respiratory disease, such as asthma, should limit prolonged outdoor exertion.
Unhealthy | 151-200 | Active children and adults, and people with respiratory disease, such as asthma, should limit prolonged outdoor exertion.
Very Unhealthy (Alert) | 201-300 | -do-
AQI: Air Quality Index

## Slide 11: Impact of Air Pollution
The World Health Organization (WHO) estimates
A billion people live in places where the air is substandard.
Air pollution kills 8,000 people a day worldwide.
About 90% of the deaths occur in developing countries.
Air pollution can cause the following harms
  Teratogenic effects
  Carcinogenic effects
  Mutagenic effects
  Respiratory effects

## Slide 12: Air Pollution Comes from Natural and Human Sources
Natural sources
  Wind blown dust
  Pollen grains
  Salt particles from active oceans
  Pollutants from wildfires and volcanoes
  Volatile organics released by plants
Man made sources
  Anthropogenic sources (all human activity)

## Slide 13: Air Pollutants
The substances (organic, inorganic, biological or radioactive) released into the atmosphere by natural or human activities in concentrations enough to change the quality of air and to be harmful to life.
Types of Air Pollutants:
Primary Air Pollutant
Harmful substance that is emitted directly into the atmosphere (unmodified).
Secondary Air Pollutant
Harmful substance formed in the atmosphere when primary air pollutants react with substances normally found in the atmosphere or with other air pollutants (modified).

## Slide 14: Primary and Secondary Air Pollutants

## Slide 15: Primary and Secondary Air Pollutants
Fig. 18-4, p. 472
Primary Pollutants
CO
CO2
Secondary Pollutants
SO2
NO
NO2
Most hydrocarbons
SO3
Most suspended particles
HNO3
H2SO4
H2O2
O3
PANs
Sources
Natural
Stationary
Mobile
Most NO3− and SO42− salts

## Slide 16: Major Air Pollutants

## Slide 17: Chemical Reactions that Form Major Outdoor Air Pollutants

## Slide 18: Carbon Monoxide (CO)
  Colourless & odourless gas
  Highly toxic air pollutant
  WHO standard up to 9 ppm
  200 million tones is added into air every year.
  Level maintains by conversion into CO2 & removal by plants
  In complete combustion reactions gives CO as end product
  At higher temperatures, CO2 dissociates or reacts with C to form CO also

## Slide 19: Fate of CO in Nature
  Atmospheric reactions keep CO low
    2CO + O2 → 2CO2
  Microbial Utilization
  Soil Sink (5 times faster than discharge of CO into air)
  Migration of CO to stratosphere and reactions with OH
    CO + OH→CO2 + H

## Slide 20: Source of CO
  Natural Source
    Natural source counts 90% of total CO entry
    Volcanic eruptions
    Decomposition of carbon or organic materials
    Oxidation of methane in nature
  Man made Source
    Incomplete combustion or burning of Carbon products
    Vehicular CO emissions (60% of total man made)
    Industrial activities
    Smoking (400 ppm)

## Slide 21: Effects of CO Pollution
  Effects on haemoglobin (Asphyxiation)
    Hb performs two way transportation
    Carries Oxygen as O2Hb from lungs to body cells
    Carries CO2 as CO2Hb from body cells to lungs
    CO has 210 times more tendency to combine with Hb to make COHb
    Reduction in O2 carrying capacity of blood
    Breathing problems

## Slide 22: Effects of CO Pollution
  Breathing Problems
    2% COHb level in blood is safe
    ˃ 2.5% of COHb level causes psychomotor dysfunction and visual acuity
    ˃ 10% of COHb level causes dizziness and headache
    ˃ 50% of COHb level leads to death
    Myocardial infractions (Heart attacks to CO)

## Slide 23: Control measures for CO Pollution
    CO is not persistent under natural system and non harmful compounds
    Mild adverse effects are temporary (removable by breathing in clean air)
    Incomplete combustions should be avoided
    Good maintenance of traffic vehicles
    No smoking

## Slide 24: Oxides of Nitrogen
Nitrous oxides (N2O)
Nitric oxide (NO)
Nitrogen dioxide (NO2)
Nitrates (NO3)
Nitric acid (HNO3)
Ammonia (NH3)
  Only first 3 occur in atmosphere
  N2O mainly comes from soil bacteria and is the most abundant
  NO and NO2 are made from anthropogenic actions
  NO and NO2 are air pollutants but NO2 is the most toxic to plants
  NO2 concentration must be below 0.50 ppm
  Increasing global use of fertilizers is increasing N2O as well

## Slide 25: Sources of oxides of Nitrogen
Man made sources
Natural sources
  Motor vehicle exhust
  Soft coal burning
  Acid manufacturing
  Industrial emmssions
  60% of NOx comes from nature
  Lightening fixation
  Soil bacteria fixation
  Biological activities & reactions
  Lightening fixation (1600 K)
    N2 + O2 2NO
    2NO + O2 2NO2
  NO2 reacts with other compunds to form photochemical smog
  Soil bacteria fixation produce N2O whcih reacts with O and O3
    N2O + O 2NO
    NO + O3 NO2 + O2
  Biological activities & reactions from
    Nitrates
    Nitrites
    Electronic storms
    Chemical conversions of ammonia

## Slide 26: Effects of oxides of Nitrogen
  N2O is an oxidizing agent and form nitrates and nitrites.
  Nitrates and nitrites convert into nitric acid in the presence of moisture and O2 resulted into acid rains which cause.
    Many diseases like skin and eye irritations.
    Metal corrosions
    Photochemical smog by reacting with hydrocarbos leads to heart and lung problems
  Effects on plants
      Chlorosis
      Necrosis
      Vegetation damage
  Effects on human health (Threshold level is 25µl/L for NO and 2µl/L for NO2)
      Coughing, headache, chest tightness
      Circulatory collapse in lungs (lung cancer)
      RBC damages (Methemoglobinemia)
      Accumulation of tissue fluids
      Methemoglobinemia (blue baby syndrome)

## Slide 27: Oxides of Sulphur
Sulphur dioxides (SO2)
Sulphur Trioxides (SO3)
  SO2 is the most damaging
  SO2 is colourless gas with suffocating and pungent odour
  Reacts with water to form sulphuric acids which is more harmful
  Environmental sulphuric acid concentration is 4x than standard
  Poisoning is almost 80 million tonns every year
Source
  Combustion reactions of coal and fossil fuels burning
    S + O2 SO2
  Fuels may have 1% to 4% sulphur
  Industrial emmisions of SO2
  About half of SO2 is coming from oxidation of H2S
    H2S + O3 H2O + SO2
  Volcanic emmsions
  Metallurgical operations during smelting of metal ores of sulphides

## Slide 28: Effects of oxides of Sulphur
  Effects on plants
      Plant damages by acid rains
      Inhibition of photosythesis (choloroplast disburance)
      Chlorosis
      Changes in growth and low yeilds
      Monocotylednous plants are more sensitive
  Effects on human health
      SO2 and its derivatives produce strong eye and nasal irritations
      Coughing, chronic bronchitis and asphyxiation
      Non fatal accidental exposure cause inflamations of eyes, nausea, vomiting, abdominal pain, sore throat, pneumonia
      Higher levels can cause lung cancer, shorter lives
      Poor health of workers