## Slide 1: Particulate Materials (PM)
Wide variety of airborne material consists of materials that are directly emitted into the air or result from the transformation of gaseous pollutants.
  Small solid particles and liquid droplets together
  Includes: soil particles, soot, lead, asbestos, sea salt, and sulfuric acid droplets
  Dust, fumes, mist, smoke particles, pollens, fog, bacteria, viruses, aerosoles etc.
  50% natural dust in air
  Suspended particulate matter (SPM)
  Size ranges from 0.0002 µm to 500 µm
  Smaller particles (‹2.5 µm) are more dangrous
  Dangerous for 2 reasons
    May contain materials with toxic or carcinogenic effects
    Extremely small particles can become lodged in lungs

## Slide 2: Particulate Materials (PM)
Particulates Sources
  Ntural
    Forest fires
    Sea salt diffusion into air
    Volcanic eruptions
    Wind blown dusts
    Plant sources
  Anthropogenic
    Indutrial processings
    Transportation
    Constructions works
    Agricultural operations
Chemcial compositions of PM depends upon
the source, eg. One third of fly ash could be Carbon

## Slide 3: Particulate Materials (PM)
Mobile Sources
(vehicles)
VOCs, NO2, PM
Stationary Sources
(power plants, factories)
NO2, SO2, PM
Area Sources
(drycleaners, gas stations)
VOCs
Natural Sources
(forest fires, volcanoes)
PM
Imporatnce
PM is one of the six harmful pollutants to public health and the environment. (The other five are ozone, sulfur dioxide, nitrogen dioxide, carbon monoxide, and lead.)

## Slide 4: Particulate Materials (PM)
PM
VOCs
NO2
SO2
Sources may emit PM directly into the environment or emit precursors such as sulfur dioxide (SO2), nitrogen dioxide (NO2), and volatile organic compounds (VOCs), which are transformed through atmospheric chemistry to form PM.
Ammonia (NH3)
Ammonia (NH3)
Where Does PM Originate?

## Slide 5: Determinants of PM Concentration
Weather patterns
Wind
Stability (vertical movement of air)
Turbulence
Precipitation
Topography
Smokestack height and temperature of gases
Nearby natural and built structures may lead to downward moving currents causing aerodynamic or building downwash of smokestack emissions.

## Slide 6
The Role of Inversions
An inversion is an extremely stable layer of the atmosphere that forms over areas.
Temperature inversions trap pollutants close to the ground. These inversions involve layers of hot air sitting above cooler air near ground level. When particles accumulate in the air layer, they are unable to rise into the atmosphere where winds will disperse them.
Source: http://www.epa.gov/apti/ course422/ ce1.html

## Slide 7
Image: PM2.5. By D. Hershey. From New York State Department of Environmental Conservation. http://www.dec.state.ny.us/website/dar/baqs/micro/two.html
Particulate Matter
Size is important to the behavior of PM
Particles larger than 10 µm are trapped in the nose and throat
Particles between 5 and 10 µm are removed by physical processes in the throat.
Particles smaller than 5 µm reach the bronchial tubes.
Particles 2.5 µm or smaller are breathed into the deepest portions of the lungs.
Importance of Size

## Slide 8
Types of Particulates
  Ntural particulates
  Natural air born PM cause alergic responses may lead to asthma or hay fever
    Pollens
    Aerosoles
  Anthropogenic
    Aerosoles
Particulate Materials (PM)
  Pollens
    Peculiar irritating characters
    Trees, shrubs, crops, grasses and weed source
    General size range is 10-50 µm
    Effects
      Sensitivity leads to asthma and hay fever
      Susceptiblity leads to bronchitis, bronchl asthma and dermatitis

## Slide 9
Types of Particulates
  Aerosols
    Colloidal dispersion of microscopic soild or liquid particles in air medium
    Variable in size (0.01-100 µm)
    Types
      Dust (mainly in summer, 1-200 µm)
      Smoke (Carbon particles, 0.05- 1.0 µm)
      Mists (liquid particles of large size, 40-500 µm)
      Fog (dispersed water near earth, 1-40 µm)
      Fumes (gaseous condensations)
Particulate Materials (PM)

## Slide 10
Types of Particulates
Particulate Materials (PM)

## Slide 11
Human health
  Premature death
  Lung cancer
  Development of chronic lung disease
  Heart attacks
  Respiratory symptoms and medication use in people with chronic lung disease and asthma
  Decreased lung function
  Pre-term birth
  Low birth weight
Plant effects
  Depends upon chemical composition and concentrations
  Dust on vegetations leads towards low photosynthesis
Adverse effects of PM

## Slide 12
Several theories have been advanced as to the mechanism of action. It is likely that more than one mechanism is involved in causing PM-related health effects. Theories include the following:
PM causes inflammation of lung tissue, resulting in the release of chemicals that impact heart function;
PM causes changes in blood chemistry that results in clots that can cause heart attacks.
PM leads to lung irritation which leads to increase permeability in lung tissue;
PM increases susceptibility to viral and bacterial pathogens leading to pneumonia in vulnerable persons who are unable to clear these infections;
PM aggravates the severity of chronic lung diseases causing rapid loss of airway function;
How Does PM Cause Health Effects?